|  | International Civil Aviation Organization WORKING PAPER | ACP-WGM16/WP-08 17 May 2010 |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

16th MEETING OF WORKING GROUP M (Maintenance)

Paris, France  17-19 May 2010

| Agenda Item 3a: | ATN/OSI Document 9880 Update Status – Security Updates |
| --- | --- |

ATN/OSI Doc. 9880 Security Validation Report

(Presented by Michael Olive, Honeywell International Inc., United States)

SUMMARY

This working paper includes, as an appendix, a report containing detailed validation of ATN/OSI security provisions in Doc. 9880 Part IV-B. The ATN/OSI security validation was conducted by the Aerospace Advanced Technology organization of Honeywell International Inc. under contract to the FAA and in support of the FAA DataComm Program Office.

ACTION

The working group is invited to review the ATN/OSI Security Validation results and consider recommended improvements to Part IV-B.

INTRODUCTION

This working paper includes, as an appendix, a report that presents the detailed results of validation analysis of the ATN/OSI security provisions in Doc. 9880 Part IV-B as proposed in WGM14/IP05.

The ATN/OSI security validation activity was conducted by the Aerospace Advanced Technology organization of Honeywell International Inc. under contract to the FAA and in support of the FAA DataComm Program Office.

DISCUSSION

The scope of the validation report includes validation by inspection and analysis of the ATN/OSI security provisions contained in the following chapters of Doc. 9880 Part IV-B as proposed in WGM14/IP05:

- Chapter 2 – ATN Generic Security Services,

- Chapter 4 – ATN Public Key Infrastructure (PKI),

- Chapter 5 – ATN Cryptographic Infrastructure,

- Chapter 6 – ATN System Security Object.

These chapters contain the detailed ATN/OSI security provisions.

The validation approach leverages:  1) ARINC Specification 823, the industry standard for ACARS Message Security (AMS) which is based directly on ATN/OSI security documented in Sub-volume VIII of ICAO Doc. 9705 and the security enhancements specified in Part IV-B of ICAO Doc. 9880; and 2) Honeywell Secure ACARS, which is an existing ARINC 823-compliant implementation of AMS.  These artifacts are used to show, by analysis and inspection, that:

- There is substantial alignment between the AMS provisions in ARINC 823 and the ATN/OSI security provisions specified in Part IV-B of ICAO Doc. 9880.

- Given that alignment, Secure ACARS is a representative implementation of the technical security solution specified in Part IV-B of ICAO Doc. 9880.

- Consequently, successful system-level testing and flight demonstration of the Secure ACARS implementation in a representative, operational communications environment satisfies high-level ATN security validation objectives and provides confidence in the technical security solution specified in Part IV-B of ICAO Doc. 9880.

Since Doc. 9880 Part IV-B is intended to update and supersede ICAO Doc. 9705 Sub-volume VIII, the validation analysis re-uses the same high-level validation objectives that were applied previously during validation of the security provisions in Doc. 9705 Sub-volume VIII.

In general, the validation analysis results provide a high-degree of confidence that the ATN/OSI security provisions in Part IV-B are:

- Complete, unambiguous, consistent, and necessary.

- Sufficient to accommodate all security users.

- Sufficient to accommodate both mobile and fixed users.

- Implementable and implementation independent.

The validation effort identified only minor defects and typographical errors.  In addition, based on the implementation and test verification experience with ARINC 823 and Secure ACARS, the following bullets summarize areas where potential improvements can be made to ICAO Doc. 9880 Part IV-B:

- Chapter 4 – Consider replacing the detailed provisions for certificate and certificate revocation list profiles with pointers to industry standards that represent best practice.  This approach is consistent with the approach taken in ICAO Doc. 9896, Technical Manual for the ATN using IPS.

- Chapter 4 – Consider removing compressed certificates, which are a non-standard, ATN-unique format.  Furthermore, compressed certificates impose significant constraints on uncompressed certificates, and these requirements may be difficult to achieve since they do not reflect industry standard practice for Public Key Infrastructures (PKI) and Certificate Authorities (CA).

- Chapter 5 – Re-consider the requirement for compressed elliptic curve points.  Although point compression offers some bandwidth efficiency, it requires additional computation and the implementation itself may require licensing of third-party intellectual property and consequently it may not be widely supported by certificate providers and cryptographic toolkit vendors.

- Chapter 5 – Consider specifying a single public/private key pair for both key agreement and digital signature, rather than a separate key pair for each.  ARINC 823 specifies, and Secure ACAR implements, a single key pair based on feedback from airlines, which are striving to minimize the numbers and types of aircraft certificates that need to be procured and managed.

The detailed defect summary and recommendations may be found in Section 5 in the ICAO Doc. 9880 Part IV-B Security Validation Report, which is included as Appendix A to this working paper.

ACTION BY THE MEETING

The ACP WG-M is invited to:

      - Review the detailed ATN/OSI Security Validation results and consider recommended improvements to Part IV-B presented in the ICAO Doc. 9880 Part IV-B Security Validation Report, which is included as Appendix A to this working paper.

APPENDIX A

ICAO Doc. 9880 Part IV-B Security Validation Report

(embedded PDF file)