AMCP WG-M/2-Appendix F

Amendments to the draft VDL Mode 3 manual on detailed technical specifications

Paragraph 5.7.2.5.2 Data-Capable System Configurations

If the radio is operating in a system configuration supporting data service, upon receiving the uplink Reservation Response field of the Recovery message indicating that it is granted a slot to transmit, the aircraft shall downlink a CTRL_CMD frame containing an Expedited Recovery XID, per Section 5.7.3.3.4.2.1, and a Network Initialization XID, per Section 5.7.3.3.4.1.3 and use an ICAO Address of 0xFFFFFF in place of the Aircraft Station Address of the DLS header, per Section 5.6.2.2.1, so that the ground station may easily extract the FCS.  The Expedited Recovery XID indicates the actual aircraft addressing information as well as information needed to recover the data scheduler.  The Network Initialization XID indicates the desired subnetwork connection.  The aircraft shall only transmit those network information and network subparameters needed to initialize the network.  The CTRL_CMD frame downlinked shall be limited to a single burst transmission so that the ground system can deterministically schedule access during recovery.  Additional parameters and network connections should be negotiated after the recovery process is complete.

-----------------

5.7.2.1.2    Net Entry. The net entry procedure shall begin with the aircraft station transmitting a Net Entry Request message following a successful net initialization.  The transmission of the Net Entry Request message and the subsequent retransmission, if enabled, shall follow the procedures described in Appendix D. The Net Entry retransmission shall continue until a Net Entry Response message is received or the number of retransmissions reaches NL1.  After NL1 retries (Table 5-60a), the SN-SME shall be notified.  If a Net Entry Response message is received, the aircraft station shall transmit a Poll Response message in the next MAC cycle.  If the Net Entry Response message is of type "previous link preserved," the aircraft TL3 timer (Table 5-60a) shall be stopped.

Note.( All configurations that offer one or more data circuit(s) must support net entry (3V1D, 2V2D, 2V1D, 3T).  The voice only configurations (3V, 4V, 3S and 2S1X) may support net entry if discrete addressing is enabled by the ground user.

Upon receiving a Net Entry Request message, the ground shall check the aircraft ICAO address.  If this address has been assigned a Local ID and the TL3 timer has not been started, the ground shall transmit the Net Entry Response message of type “previous link preserved.”  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.

If the aircraft ICAO address has not been assigned a Local ID, the ground shall assign the next available Local User ID to the requesting aircraft and the pending disconnect link table shall be examined.  If the aircraft ICAO address is found in the table, the link status shall be reinstated, the TL3 timer shall be stopped, and the link port address shall be changed to the new radio station port address.  The ground shall transmit the Net Entry Response message of type "previous link preserved."  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.

If the aircraft ICAO address is not found in the table and a Local ID has been assigned, the ground shall transmit the Net Entry Response message of type "no previous link."  When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response message to the entering aircraft during the next MAC cycle.  This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” message if no data slots were requested.  If an aircraft receives a Net Entry Response message of type "no previous link", it shall also form a join event message, as required by the supported network stack, and deliver it to the air router.

If there are already 60 aircraft in the net when the Net Entry Request message is received, the ground LME shall respond with a Net Entry Response message with the local identifier field set to 0 indicating that the net is currently full. The aircraft shall then use an Aircraft ID of 61 to indicate that it has not entered the net, when communicating with the ground station and other aircraft.

If a duplicate Net Entry Request message is received it shall be discarded.

If the requesting aircraft does not receive a Reservation message from the ground in the next MAC cycle after transmitting the Poll Response message, it shall restart the net entry procedure.

Note 1. ( The GNI provides a connection management function across multiple ground stations such that the same subnetwork connections are maintained with aircraft served by those ground stations.  A description of the GNI function is provided in the Implementation Aspects for VDL Mode 3.

Note 2. – A Net Entry Request message is considered to be a duplicate if a ground station receives a retransmitted Net Entry Request while it is still processing a previously received Net Entry Request from the same aircraft.

Note 3. – Aircraft receiving a “Net Full” indication in the Net Entry Response message are expected to operate in a limited manner until the pilot manually directs the LME to re-initiate the Net Entry Process.

-----------------------------

Table 5-59a.  XID Parameters

|  |  | Air initiated Link establishment | Link connection rejection |
| --- | --- | --- | --- |
|  | Source | Aircraft | New ground Station | Any station |
|  | Destination | Proposed ground station | Aircraft | Any station |
| XID parameters | GI | PI | CTRL_CMD_LE | CTRL_RSP_LE | CTRL_RSP_LCR CTRL_CMD_LCR |
| Public parameters (8885:1993:Mode 3) |  |  |  |  |  |
| Parameter set ID | 80h | 01h | N/A | O | N/A |
| N1-downlink | 80h | 05h | N/A | O | N/A |
| N1-uplink | 80h | 06h | N/A | O | N/A |
| Counter N2 | 80h | 0Ah | N/A | O | N/A |
| Timer T1 | 80h | 09h | N/A | O | N/A |
| T-ack | 80h | 08h | N/A | 0 | N/A |
| Private parameters (V) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | M |
| SQP | F0h | 02h | O | O | N/A |
| LCR cause | F0h | 06h | N/A | N/A | M |
| Modulation support | F0h | 81h | O | N/A | N/A |
| Private parameters (W) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | M | M | O |
| Algorithm version number | F0h | 01h | O | O | O |
| Network initialization | F0h | 02h | M | M | N/A |
| Connection check | F0h | 03h | N/A | N/A | N/A |
| Version | F0h | 04h | O | O | O |
| Authentication | F0h | 05h | O | O | O |
| Subnetwork User Data | F0h | 06h | O | O | O |
| NM1 | F0h | 42h | N/A | O | N/A |
| RR | F0h | 43h | N/A | O | N/A |
| WR | F0h | 44h | N/A | O | N/A |
| RE | F0h | 46h | N/A | O | N/A |
| RL | F0h | 47h | N/A | O | N/A |
| Timer T3 | F0h | 48h | N/A | O | N/A |
| NL1 | F0h | 49h | N/A | O | N/A |
| Timer TL3 | F0h | 4Ah | N/A | O | N/A |
| Timer TL4 | F0h | 4Bh | N/A | O | N/A |
| WE | F0h | 4Ch | N/A | O | N/A |
| Operative_GNIp | F0h | 4Fh | O | O | N/A |
| Aircraft_TMbB | F0h | 50h | O | O | N/A |
| MbB_Operations_Permitted | F0h | 51h | O | O | N/A |
| Expedited recovery | F0h | 80h | O | N/A | N/A |
| t | F0h | 81h | O | N/A | N/A |
| f | F0h | 82h | O | N/A | N/A |
| Former_GNIp | F0h | 83h | O | O | N/A |
| Counter NL2 | F0h | C1h | N/A | O | N/A |

Table 5-59b. XID Parameters

|  |  | Addressed link parameter modification | Broadcast link parameter modification |
| --- | --- | --- | --- |
|  | Source | Current ground station | Aircraft | Current ground station |
|  | Destination | Aircraft | Current ground Station | Aircraft |
| XID parameters | GI | PI | CTRL_CMD_LPM | CTRL_RSP_LPM | CTRL_CMD_LPM (GSIF) |
| Public parameters (8885:1993:Mode3) |  |  |  |  |  |
| Parameter set ID | 80h | 01h | O | N/A | O |
| N1-downlink | 80h | 05h | O | N/A | O |
| N1-uplink | 80h | 06h | O | N/A | O |
| Counter N2 | 80h | 0Ah | O | N/A | O |
| Timer T1 | 80h | 09h | O | N/A | O |
| T-ack | 80h | 08h | N/A | 0 | N/A |
| Private parameters (V) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | O |
| SQP | F0h | 02h | O | O | O |
| LCR cause | F0h | 06h | N/A | N/A | N/A |
| Modulation support | F0h | 81h | N/A | N/A | N/A |
| Private parameters (W) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | O |
| Algorithm version number | F0h | 01h | O | N/A | O |
| Network initialization | F0h | 02h | O | O | O |
| Connection check | F0h | 03h | O | O | O |
| Version | F0h | 04h | N/A | N/A | O |
| Authentication | F0h | 05h | O | O | O |
| Subnetwork User Data | F0h | 06h | O | O | O |
| NM1 | F0h | 42h | O | N/A | O |
| RR | F0h | 43h | O | N/A | O |
| WR | F0h | 44h | O | N/A | O |
| RE | F0h | 46h | O | N/A | O |
| RL | F0h | 47h | O | N/A | O |
| Timer T3 | F0h | 48h | O | N/A | O |
| NL1 | F0h | 49h | O | N/A | O |
| Timer TL3 | F0h | 4Ah | O | N/A | O |
| Timer TL4 | F0h | 4Bh | O | N/A | O |
| WE | F0h | 4Ch | O | N/A | O |
| Operative_GNIp | F0h | 4Fh | O | O | O |
| Aircraft_TMbB | F0h | 50h | O | O | O |
| MbB_Operations_Permitted | F0h | 51h | O | O | O |
| Expedited recovery | F0h | 80h | N/A | N/A | N/A |
| t | F0h | 81h | O | N/A | O |
| f | F0h | 82h | O | N/A | O |
| Former_GNIp | F0h | 83h | O | O | O |
| Counter NL2 | F0h | C1h | O | N/A | O |

----------------------------

5.7.3.3.4.1.7 Subnetwork User Data parameter.   The subnetwork user data parameter allows for any subnetwork or network level messages to be combined with the CTRL frame exchange, such as ISH packets.  The subnetwork user data parameter format shall be as defined in Table 5-67f.  If included as a subparameter in the Network Initialization parameter, the content of the value field shall be forwarded to the subnetwork interface for which this is a subparameter.  Otherwise, the content of the value field shall be forwarded to the raw subnetwork interface.

Table 5-67f:  Subnetwork User Data Parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 0 | 1 | 1 | 0 | User Data |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 |  | n4 | n3 | n2 | n1 |  |
| Parameter value | v8 | v7 | v6 | v5 |  | v4 | v3 | v2 | v1 | Value |

6.7.2.2    CLNP compression.  The compression technique to be used for CLNP packets shall be defined in ICAO Doc 9705 (3rd Edition), Sub-Volume V, Section 5.7.9.  The Type-Specific Information subfield of the Payload octet shall be encoded per Table 5-1 of the referenced document.  For non-compressed CLNP, the Type-Specific Information subfield shall be binary 0000.

-------------------------------

Insert the following new section:

6.7.4    Router Interface Recommendation

The subnetwork should forward pertinent XIDs to the router, so as to prevent the need for the router to communicate additional information as separate messages and incur additional overhead.

----------------------------------------

7.2.3.2.5	 CLNP Compression.

Compression of CLNP packets within the frame-based SNDCF shall be supported. Compression of CLNP packets shall be performed whenever ATN connectivity is specified and shall be performed according to the procedures defined in ICAO Doc 9705 (3rd Edition), Sub-Volume V, Section 5.7.9. Compression shall be performed on both broadcast and unicast packets. The use of compression shall be signaled during net entry, using the procedures described in Section 5.7.3.3.4.1.3. The compression status of each CLNP packet shall be indicated according to the procedures defined in Section 6.7.1.

--------------------------------

5.5.4.2 Voice operation support. The aircraft VDL shall grant media access on a MAC cycle-by-MAC cycle basis based on the timing state and the voice signaling information received in the M uplink burst of the previous MAC cycle. The rules for media access shall be as described in Table 5-55. The conditions of both the timing state and the signaling shall be met in order to be granted access in a given MAC cycle.

The Voice Unit (Section 8) shall be notified of the timing state during each MAC cycle.

The maximum duration of an aircraft PTT event shall be limited to no more than 35 seconds (approximately 145 MAC cycles). Aircraft VDL shall automatically terminate the PTT event upon reaching this limit.

Any aircraft VDL transmitting a voice signal shall cease transmitting if it receives a valid uplink M channel signal with the Voice Signal code set to any value other than 012 (occupied). (See Section B.2.1.3.) This rule shall apply for the duration of the PTT event, starting 2 cycles after the first voice burst transmission.

-------------------------------------

Insert a new Section 9.8 in the Manual on the Implementation of the VDL Mode 3 as follows:

9.8 DLS State Forwarding During Handoff

It is optional whether the ground station needs to forward the current state information of the Data Link Service entity to a new ground station when an aircraft hands-off between ground stations.  The Transport Layer should eventually recover any lost information that may be queued with the old ground station DLS entity.  To improve the efficiency of operation, the ground system may forward the queue states to the new ground station during the handoff operation, so that data may flow unperturbed.

If the router is using the optional DEFLATE stream-mode compression, then it is strongly recommended that the ground system support this optional capability of forwarding the state information.  Otherwise, the compressor will need to reset upon every handoff, which will reduce the efficiency of the compressor and may degrade the system efficiency.