# WG M2 Appendix L

PROPOSED CHANGES TO Annex 10, Volume I, CHAPTER 4 on AMSS SARPs

Note: these are draft amendments which will be considered on the basis of submission of further material in the future.

1	Add a new section 4.2.3.4.6. which will address the receiver’s interference susceptibility:

1.1	New Text:

Receiver Interference Susceptability. Receivers meeting the requirements of these SARPs shall operate satisfactorily in the presence of interference at RF levels at the receivers input port not exceeding the following tabulated levels.

Frequency Range		Maximum Interference Level

470 to 1450 MHz		+3 dBm

1450 to 1529 MHz		Decreases linearly in decibels from

+3 dBm at 1450 MHz to -72 dBm

at 1529 MHz

1529 to 1560 MHz		-163.3 dBm

1560 to 1626.5 MHz		Increases linearly in decibels from

-72 dBm at 1560 MHz to +3 dBm

at 1626.5 MHz.

1626.5 to 1660.5 MHz		+47.8 dBm

1660.5 to 18000 MHz		+3 dBm

1.2.	Discussion: Modern aircraft are now operating with many different transmitting equipment onboard, and in environments where there are many external transmitters. Determining the whether a piece of equipment can be certified to operate in the environment it is being placed in will be made easier if the receiver interference susceptibility is known by the certifying agency. To facilitate this, all SARPs should state this parameter.

2	Modify Table 4-3. Maximum harmonics, discrete spurious and noise density levels.

2.1	New table.

Table 4-3. Maximum harmonic, discrete spurious and noise density levels.

Frequency (MHz)		Power Density

0.01 to 15251	-135	dBc/4 kHz

1525 to 1559	-203	dBc/ 4kHz

1559 to 1585	-155	dBc/MHz

1585 to 1605	-143	dBc/MHz

1605 to 1610	-117	dBc/MHz

1610 to 1610.6	  -95	dBc/MHz

1610.6 to 1613.8	  -80	dBW/MHz5,7

1613.8 to 1614	  -95	dBc/MHz

1614 to 1626.5	  -70	dBc/4 kHz

1626.5 to 1660	  -70	dBc/4 kHz2,3,4,5,6

1660 to 1660.5	-49.5	dBW/20 kHz2,3,4,5,6,7

1660.5 to 1670	-49.5	dBW/20 kHz4,5,7

1670 to 1735	  -60	dBc/4 kHz

1735 to 12000	-105	dBc/4 kHz

12000 to 18000	  -70	dBc/4 kHz

1.	AMSS operations are permitted in the MMS (maritime) band which has been extended to include 1525-1530 MHz.

2.	Within the transmit band, excluding the frequency band within (35 kHz of the carrier.

3.	The –55 dBc/4kHz spectrum level in this table is equivalent to –55 – 10 log10(4000/SR) dBe (relative to the maximum envelope) under the definitions in Section 2.2.4.2.16.

4.	For wide band spurious the limit is –39.5 dBW/MHz.

5.	This level is not applicable for intermodulation products

6.	The upper limit for the excess power for any narrow-band spurious emission (excluding intermodulation products) within a 30 kHz measurement bandwidth shall be 10 dB above the power limit in this table.

7.	Note that the power density is expressed in terms of absolute power (dBW) in some instances, and in terms relative to carrier power (dBc) in other instances.

2.2	Discussion. In the months since AMCP/6, interference issues have been discussed in detail, and the table in section 2.2.1 reflects the latest values that have been adopted by the RTCA. However, discussions are still ongoing, particularly for the 1610.6 to 1613.8 MHz Radio Astronomy band. It would be expected that some if these values will change again in the future.

3	Insert a new section of text to introduce an intermodulation requirement for the transmitter.

3.1	New section:

4.2.3.5.7.4	For multicarrier AES, when transmitting two equal carriers with a total power equal to the maximum allowable operating EIRP of the AES, the power level of each of the intermodulation products shall not exceed the levels specified in table 4-3 bis.

4.1	New table 4-3 bis Maximum Intermodulation Product levels.

Frequency MHz				IM Level

Below 1610				<-70 dBc

1610 to 1614				-64 dBc

1614 to 1671.25			-24 dBc

1671.25 to 1711			-29 dBc

1711 to 1735				-34 dBc

1735 to 18000				<-70 dBc

4.1.1		Discussion: A Class 4 AES is capable of transmitting at least 1 C-channel through a common High Power Amplifier. This will result in intermodulation products being produced at the output of the HPA due to non-linearities within the HPA. These intermodulation products are a spurious emission, but need to be treated differently from other types of spurious emission. The level of the intermodulation product, when they fall outside the transmit pass band of the terminal, will be affected by the filtering employed in the diplexer. The values above can be met by appropriate HPA design, and diplexer filter rejection.

5	Add corrections to Table 4-30. DTE effect on DCE restart states.

5.1	In Table 4-30, Note 3 should be modified to read as follows:

3.	The received packet is not forwarded to the IWF.

5.1.1	Discussion: For most ERROR conditions in the r2 DTE RESTART REQUEST states,

the MOPS and SARPs  reference Note 3. The RTCA DO210D MOPS Note 3 actually states "The received packet is not forwarded to the SSNIW", which is consistent with 8208 and X.25. SARPs Note 3 actually states "No action is taken by the DCE." This is obviously incorrect, since a state transition occurs, a diagnostic code is declared, etc. SARPs Note 3 needs to be corrected.

6..	In Table 4-30, the row labled “Restart request”, the r1 column should not reference “Note 1” but “(4.2)". The r3 column should reference “(4.3)”, not “(4.2)”.

6.1	Discussion: The SARPs table contains parenthetical references to ISO 8208 for the Normal responses by the DCE. e.g., it has the correct reference to 8208 Section 4.4 for the r3 case of receipt of  Restart Confirmation packet (row 7). However, the SARPs is lacking a reference to Section 4.2 for the r1 case of receipt of a Restart Request (back in row 6); where such a reference is expected, there is instead the unnecessary redundant reference to Note 1. For the r3 case in row 6, the SARPs incorrectly references 8208 Section 4.2. This is the "restart collision" case (the DCE and DTE both indicating/requesting a restart at the same time), which should reference 8208 Section 4.3 ("Restart collision") rather than 4.2 ("Receiving a restart indication").

7.	In table 4-30, last column, for the row starting “Restart request or restart confirmation packet with format error”, after the entry “A = ERROR D = 38, 39, 81 or 82”, add (see Note 3).

7.1	Discussion: Should such a packet be received with a format error, the DCE should not  forward it to the IWF. This is made clear by referencing Note 3.

8.	In Table 4-30, third column. For the row starting “ Packets having a packet type identifier shorter than one byte…”, after the entry “A = ERROR S = r3 D = 38” add (see Note 3).

8.1	Discussion: Should such a packet be received with these parameters, the DCE should not forward it to the IWF. This is made clear by referencing Note 3.

9.	In Table 4-30, third column. For the row starting “Call setup, call clearing, data, interrupt, flow control…”, after the entry “A = ERROR S = r3 D = 18” add (see Note 3).

9.1	Discussion: Should such a packet be received with these parameters, the DCE should not forward the packet to the IWF. This is made clear by referencing Note 3.

10	In Table 4-30, the last row, column r2 the reference to note 4 should be changed to Note 3.

10.1	Discussion: Note 4 applies to the entire column. In this cell, there should be a reference to Note 3, which is more explicit.

11.	Table 4-30, Note 1 is basically correct, but could benefit from some clarification, and should be similar to the corresponding note in the MOPS. The proposed new note should be re written to read:

1. The AES subnetwork has no restart states. Receipt of a restart request causes the DCE to respond with a restart confirmation. This restart request packet is forwarded to the IWF, which responds by executing a connection release procedure for each VC associated with the DTE/DCE interface. This is equivalent to the originating DTE separately issuing a clear request for each VC, i.e. the equivalent of a restart  request.

11.1	Discussion: What the SSNL in the DCE does in response to a RESTART REQUEST from the DTE is to execute a separate connection release procedure for each VC associated with the originating DTE (reference ARINC 741 Part 2 Section 4.3.4.2.1). Per MOPS Note 1, the received RESTART REQUEST packet is forwarded by the DCE to the SSNIW sublayer (known as the IWF in the SARPs). What is specified in the earlier referenced SDM material (in Module 1 Appendix 10 Sections 4.1.5.x) is that the SSNIW is to issue an SN-DISCONNECT request primitive for each VC. The SN-DISCONNECT primitives map to CONNECTION RELEASED SNPDUs, which are sent to the GES (reference SDM Section 7.3.2.1 and MOPS Figure 2-2). This in turn ultimately results in CLEAR INDICATION packets being delivered to the far-end DTE for each applicable VC. The DCE also sends a RESTART CONFIRMATION packet to the originating DTE, indicating that it effectively performed the RESTART REQUEST function. The SARPs version of Note 1 states "Receipt of a restart request packet causes the DCE to issue a clear request packet to the IWF for each VC associated with the DCE entity." It could be implemented this way, but the MOPS more logically states that the received RESTART REQUEST packet itself (not a series of CLEAR REQUEST packets) is forwarded to the SSNIW (or IWF) (which then performs the necessary interworking functions). The SARPs note would thus be corrected and clarified if it is replaced by the MOPS version (aligned to the SARPs style and usage peculiarities).

12	Table 4-30 Note 4 should be rewritten to read:

4. If the DCE enters the r3 state, then the restart confirmation is not sent.

12.1	Discussion: The text of the existing version of the SARPs Note 4 is incorrect ("The restart request packet is not forwarded to the IWF") -- in fact, the MOPS Table 2-4 Note 1 states just the opposite: "The RESTART REQUEST packet is forwarded to the SSNIW ...", which makes sense (since the received packet has to be processed internally on the SSNIW/SSND side as well as on the DTE side). Since both documents reference Note 4 in their r2 state (3rd) column header, the SARPs should use the MOPS form of Note 4: "If the DCE enters the r3 state, then the RESTART CONFIRMATION is not sent." This note gives pertinent information regarding the r2 state, in which the DCE normally DOES send a RESTART CONFIRMATION, but not when it first enters the r3 state from the r2 state.

13	In the notes of table 4-30, Note 5 needs to be modified as follows:

5. The DCE upon entering the r3 state, checks for the completion of the r2 processing. If the r3 state is entered via the r2 state, the DCE discards the received packet and indicates a restart by transmitting to the DTE a restart indication packet with the cause ‘local procedure error’ and the appropriate diagnostic code. If the r3 state is not entered via the r2 state, the DCE performs all of the actions normally performed when entering r2 and issues an ISO 8208 restart indication packet to the DTE, and sends a restart request packet to the IWF (the equivalent of a clear request packet for each VC associated with the DCE entity).

13.1	See discussion in section 2.4.7.1 above.

14	Table 4 –34

14.1	The reference to REJECT Packets in Note 6 should be removed.

14.2	Discussion: Since the Packet Retransmission facility is not supported, the REJECT packet will never be received, so all the Reject Packet references should be removed from the SARPs.

14.3	There are no references to note 1 in the table. This is corrected by amending the text in the heading of the second part of the table. The existing text for the table which reads:

“DCE flow control transfer states (see Notes 2 and 3)”

should read:

“DCE flow control transfer states (see Notes 1, 2 and 3)”.

14.4	The 4 occurrences of references to the ISO8208 document sections 7.1.5 and 7.1.6, in the last two rows of Table 4-34, are incorrectly prefixed with a “4”. This “4” should be deleted in the 4 instances.