AMCP WG M2 Appendix M

VHF Datalinks for point to point Communications

# Introduction

## Background

The 7th meeting of the AMC Panel approved SARPs for the VDL Mode 4 system “to support ATN compliant subnetwork services for surveillance applications”. The VDL Mode 4 system was validated in ICAO for surveillance applications (ADS-B and ADS-C). However, the VDL Mode 4 system is capable to support other applications and in particular ATS point to point communications (i.e. CPDLC).

AMCP/WGC in its first meeting (October 2000) discussed the additional capabilities of VDL Mode 4 and has recognised the potential for VDL Mode 4 to support time-critical communication services as an ATN sub network as well as broadcast communications. Therefore, AMCP/WGM was invited to identify the activities and steps necessary to validate this position and to identify the appropriate actions to include communication functions within the VDL Mode 4 SARPs.

AMCP/WGM decided in its first meeting (December 2000) to establish a subgroup to examine further the issue. In particular the examination will address two aspects. The first one is the resolution of a number of issues as identified in Appendix O of the report of the 1st meeting of WGM. The second one is a comparative analysis of the performance of the different candidate systems to support point to point communications.

## Scope and methodology

This report considers the second aspect of the above discussion in the WGM activities: the comparative analysis of the performance of the systems for point to point communications. Furthermore, the emphasis is put on the datalink systems operating in the VHF band that have been approved by ICAO and have a potential to support COM applications. There are (or soon to be) three VHF systems in Annex 10 that can support COM applications: VDL Mode 2, VDL Mode 3, and VDL Mode 4. These are the systems that this report is concerned with.

There are other ICAO systems that can support COM services (i.e. Mode S datalink and SATCOM). Furthermore, there may be other systems that have a potential to support point to point communications. Indeed, AMCP/WGC has already begun discussions about a future aeronautical communication system (e.g. CDMA systems have been mentioned). However, none of these systems are within the current scope of the analysis in this report.

It was decided to examine, at least in a first step, the most likely candidates. If required the analysis may be expanded to consider these non-VHF systems. Nevertheless, some remarks on the potential usage of these systems will be provided.

Recognising the difficulties in “comparing” these different technologies, which in any case were not designed to fulfil the same functionality, this report will bring together the material from different studies that have been carried out to examine the performance of these datalink systems.

This report is based on the following material:

[1]:	“Assessment of CNS Digital links against operational requirements and an overview of the performance characteristics of these digital links”, 8th meeting AMCP/WGD, 1997.

[2]:	“COM.ET2.ST15: Analyse options for initial a/g data networks”, Eurocontrol 1998.

[3]:	“COM.ET2.ST12: Future VHF Systems – Architecture Implementation Study”, Eurocontrol, 2000.

[4]:	“European ATN simulation, VDL Mode 2 simulation report”, Eurocontrol, 2000.

Section 2 of this report describes the status and the performance of the VDL Mode 2 system. Section 3 deals with the VDL Mode 3 system and Section 4 deals with the VDL Mode 4 system. Section 5 examines briefly some other systems. Finally section 6 provides a summary.

# VDL Mode 2

## Performance

The VDL Mode 2 performance was analysed in [2]. This study calculated the useful throughput that the VDL Mode 2 subnetwork would support to 5,355 Kbps (out of the 31,5 Kbps channel rate) under the assumption of short messages (16 octets). For longer messages the link overhead will be relatively smaller, increasing thus the useful throughput. However the length of 16 octets is an average ATC message, and therefore the corresponding throughput is an appropriate indicator of the throughput performance.

The same study ([2]), highlighted the limitation of VDL Mode 2 in high density environments in terms of transfer delay. The VDL Mode 2 system is not designed to support time critical applications. Due to the access mechanism (CSMA-CD) it exhibits a non deterministic behaviour and it can not guarantee the required performance level in terms of transfer delay. Therefore, at low traffic levels the transfer delay will be small, but as the traffic increases, the transfer delay will also increase (due to increased failed transmission attempts because of collisions) until a breaking point in the system performance. However this can be avoided by dividing the traffic among additional frequency channels

Some further analysis based on the assumptions and work in reference [2] estimated the required throughput to support the first set of datalink applications considered by the LINK2000+ programme (DLIC, FLIPCY, ACM, ACL, DSC and AOC). This analysis estimated that in the 2010 timeframe, for about 850 aircraft equipped with VDL Mode 2 and in a radius of 230 nm around a VDL Mode 2 ground station, 15 to 18 Kbps of useful throughput would be required to support the considered applications. This throughput corresponds to 3 to 4 VDL Mode 2 frequencies (assuming 5.3 Kbps per frequency channel).

Finally, in a simulation study, [4], there were significant differences recorded in the performance of the VDL Mode 2 subnetwork between different environments (airport, TMA and enroute). The simulated performance in the enroute environment is lesser than performance in TMA and the airport  environment and lesser than the performance calculated in [2]. This is attributed to the hidden terminal problem. The higher an aircraft is, the more is seen (and heard) by ground stations not intended to communicate with, contributing thus to collisions and retransmissions. As a result the actual performance is reduced when compared to theoretical estimates.

## Implementation Plans

In 1999, industry proposed a two step implementation of VDL Mode 2 services. In a first step the existing ACARS messages will be transmitted using the minimum of VDL Mode 2:(ACARS over AVLC, AOA). This step foresees the deployment of a VDL 2 air-ground segment with a protocol stack limited to the functions required for delivering higher performance to unchanged ACARS applications. Service Providers are committed to start AOA operation with a few airlines in summer 2001, both in Europe and in USA. The required product development and adaptation of relevant AEEC standards are taking place in time for this to happen. However for advanced datalink applications, compliant with the ICAO/FANS concept, additional ATN components will be required.

This is the second step of implementing the VDL Mode 2 services: VM2/ATN. In this direction the Eurocontrol Petal II Extension project with American Airlines will operate 4 aircraft equipped with ATN on top of VDL 2 from May 2001 onwards, in order to evaluate operational issues of datalink. Furthermore both EUROCONTROL and FAA have set up respective projects (Link2000+, Build1 and 1A) that co-ordinate the deployment of ATS datalink services based on ATN and VDL 2.

<to provide more info on these programmes>

In the US in the frame of the NEXCOM discussions (see section 3.2) the option of implementing VDL Mode 2 for data and 8.33 KHz for voice is evaluated instead of VDL Mode 3 for both voice and data.

## Other issues

<?>

# VDL Mode 3

## Performance

The performance of the air/ground data point-to-point capability of the VDL mode 3 system was evaluated in the frame of the study [3]. The simulations considered different equipage scenarios and different types of airspace, i.e. landing (CTR), approach (TMA) and enroute (ACC). A number of assumptions and simplifications have been made in order to make the simulations feasible. These are detailed in the full report. The study considered the traffic scenarios for 2015 in the Frankfurt FIR. For this purpose real radar data from 1998 were used and extrapolated using two assumption: 1% traffic growth per year resulting in 18% increase in traffic in 2015 and 3,8% traffic growth per year resulting in 89% traffic increase in 2015.

VDL mode 3 is the only considered system that supports both voice and data applications. For this evaluation the data only capability of VM3 is of interest. However, the study [3] assumed mixed configurations for CTR and TMA and data configuration for enroute. This is more realistic in a real operational concept. Nevertheless, it may be interesting to examine the performance of the system in an only data mode. The study [3] assumed that the 3V1D or 2V2D configurations will be used for CTR and TMA, and the 3T configuration will be used for ACC. The following number of channels have been assumed for the simulations:

- 4VHF channels for CTR (configuration 3V1D)

- 1 or 2 VHF channels for CTR (2V2D)

- 4 VHF channels for TMA (3V1D)

- 1 or 2 VHF channels for TMA (2V2D)

- 2, 3 or 4 channels for ACC (configuration 3T)

The following table summarises the results from the VDL Mode 3 simulations for the CTR, TMA and ACC airspace.

|  |  |  | CTR (not 3T) | TMA (not 3T) | ACC (3T only) |
| --- | --- | --- | --- | --- | --- |
| Service | Required 95% end-to-end delay (s) | Number of channels | Max 95% end-to-end delay (s) | Success Probabi-lity (%) | Max 95% end-to-end delay (s) | Success Probabili-ty (%) | Max 95% end-to-end delay (s) | Success Probabili-ty (%) |
| DLIC | 15 | 4 (3V1D, 3T) | 1.8 | 100 | 2.55 | 100 | 2.4 | 100 |
|  |  | 3 (3T) |  |  |  |  | 6.9 | 99.8 |
|  |  | 2 (2V2D, 3T) | 1.8 | 100 | 2.1 | 100 | > 15 | 69.6 |
|  |  | 1 (2V2D) | 2.4 | 100 | 5.25 | 100 |  |  |
| ACM / VCI | 10 | 4 (3V1D, 3T) | 1.7 | 98.4 | 2.05 | 100 | 2.2 | 100 |
|  |  | 3 (3T) |  |  |  |  | 6.15 | 99.9 |
|  |  | 2 (2V2D, 3T) | 1.6 | 98.8 | 1.85 | 100 | > 15 | 58.6 |
|  |  | 1 (2V2D) | 2.4 | 98.4 | 4.45 | 99.8 |  |  |
| DCL | 15 | 4 (3V1D, 3T) | 1.2 | 100 | 1.2 | 100 |  |  |
|  |  | 3 (3T) |  |  |  |  |  |  |
|  |  | 2 (2V2D, 3T) | 1.2 | 100 | 1.2 | 100 |  |  |
|  |  | 1 (2V2D) | 1.8 | 100 | 1.8 | 100 |  |  |
| D-OTIS | 15 | 4 (3V1D, 3T) | 1.0 | 100 | 1.0 | 100 | 2.0 | 100 |
|  |  | 3 (3T) |  |  |  |  | 6.5 | 99.8 |
|  |  | 2 (2V2D, 3T) | 1.0 | 100 | 1.0 | 100 | > 15 | 82.8 |
|  |  | 1 (2V2D) | 2.0 | 100 | 2.0 | 100 |  |  |
| SIGMET | 15 | 2 (3T) |  |  |  |  | >15 | 82.6 |
|  |  | 3 (3T) |  |  |  |  | 6.5 | 99.8 |
|  |  | 4 (3T) |  |  |  |  | 2.0 | 100 |
| FLIPCY | 10 | 4 (3V1D, 3T) | 2.6 | 100 | 3.6 | 100 | 3.0 | 100 |
|  |  | 3 (3T) |  |  |  |  | 7.2 | 98.3 |
|  |  | 2 (2V2D, 3T) | 2.8 | 100 | 3.0 | 100 | >15 | 42.3 |
|  |  | 1 (2V2D) | 3.4 | 100 | 6.0 | 99.6 |  |  |
| AOC_IN |  | 4 (3V1D) | 1.9 | 100 | 3.0 | 99.9 |  |  |
|  |  | 2 (2V2D) | 1.8 | 100 | 2.85 | 99.9 |  |  |
|  |  | 1 (2V2D) | 2.6 | 100 | 4.65 | 99.9 |  |  |
| AOC_UL2 |  | 4 (3T) |  |  |  |  | 2.1 | 99.8 |
|  |  | 3 (3T) |  |  |  |  | 6.45 | 99.8 |
|  |  | 2 (3T) |  |  |  |  | >15 | 99.4 |
| 4D_NEG (EQ_SC_3) |  | 4 (3T) |  |  |  |  | 1.4 | 97.6 |
|  |  | 3 (3T) |  |  |  |  | 2.8 | 97.8 |
|  |  | 2 (3T) |  |  |  |  | 12.0 | 41.4 |
| 4D_INIT (EQ_SC_3) |  | 4 (3V1D) | 1.2 | 100 | 1.4 | 100 |  |  |

|  | : Not simulated |
| --- | --- |

For the enroute case it was found that three VHF frequencies are needed in order to handle the whole data traffic. With these frequencies all requirements could be met and the success probability for ATS applications was very close to 100 %.

With respect to the performance evaluation the capacity assessments for the year 2015 with four 3V1D channels for CTR and TMA showed that all data requirements in a high dense airport like Frankfurt could be met. Further investigations using 2V2D showed that even with two 2V2D frequencies (one for CTR and one for TMA), the delay requirements for data could be met with a success probability very close to 100 %. Capacity assessments for the year 2015 with 3T configuration for the enroute case showed that with four VDL frequencies all data requirements in a high dense airspace like FIR Frankfurt could be met. In case three frequencies are used the success probability is no longer 100 % but still very close. Therefore three frequencies are considered to provide sufficient capacity to handle the data traffic assumed. Capacity assessments for the year 2015 for the non core area region FIR Brindisi and the enroute case restricting to ADS-C-application showed, that requirements could be met with two 3T frequencies.

## Implementation Plans

FAA has announced a planning for the VDL Mode 3 implementation. These plans address only the voice capability. The plans indicate that the voice capability will be initially operational in 2009. The full scale operation will be later, but no date has been announced. No dates have been specified for the data capability of the system.

These plans are under the umbrella of the US NEXCOM programme, which will transition the current ATC system to the future one. Recently, the NEXCOM Aviation Rulemaking Committee (NARC) decided to investigate the following options in terms of technology:

- VM3 for voice and data

- VM3 for voice and VM2 for data

- 8.33 KHz for voice and VM2 for data.

The business case of these options is established and it is expected that a decision on the technology will be made in mid 2001.

## Other issues

<voice capability>

# VDL Mode 4

## Performance

The VDL Mode 4 performance was analysed in [2]. Based on the calculations of this study the useful throughput for one fully loaded channel is 8,9 Kbps (out of the 19,2 Kbps channel rate) under the assumption of short messages (16 octets). Since VDL Mode 4 is a slotted system it may be more appropriate to calculate the throughput assuming a full slot (around 21 octets), which would increase the useful throughput. However for consistency to the previous sections the length of 16 octets is used to report the useful throughput.

The study in [2] did not identify any issues in relation to the transfer delay. Indeed, VDL Mode 4 (as is VDL Mode 3) is a slotted system (TDMA) with deterministic behaviour, and which can support time critical applications. This was demonstrated in the extensive simulations that were carried in the frame of the study [3].

From this study, which covered many different aspects of the future VHF system, the performance evaluation of the air/ground point-to-point capability of VDL Mode 4 is of interest. The simulations considered different equipage scenarios and different types of airspace, i.e. landing (CTR), approach (TMA) and enroute (ACC). A number of assumptions and simplifications have been made in order to make the simulations feasible. These are detailed in the full report. The study considered the traffic scenarios for 2015 in the Frankfurt FIR. For this purpose real radar data from 1998 were used and extrapolated using two assumption: 1% traffic growth per year resulting in 18% increase in traffic in 2015 and 3,8% traffic growth per year resulting in 89% traffic increase in 2015. The traffic environment is the same as with the traffic environment for the VDL Mode 3 simulations presented in section 3.

For VDL Mode 4 the following number of channels have been assumed for the simulations:

- 1 frequency for CTR

- 1 frequency for TMA

- 1, 2, 3 or 4 frequencies for ACC

Delay performance values for a subset of selected datalink applications are outlined in the following table for CTR, TMA and ACC and compared to the required values

|  |  |  | CTR | TMA | ACC |
| --- | --- | --- | --- | --- | --- |
| Service | 95% e/e delay (s) | # frq | Max 95% e/e delay (s) | Success Probability (%) | Max 95% e/e delay (s) | Success Probability (%) | Max 95% e/e delay (s) | Success Probability (%) |
| DLIC | 15 | 1 | 1.5 | > 99 | 2 | > 98 | 8.55 | 75.6 |
|  |  | 2 |  |  |  |  | 5.55 | 90.4 |
|  |  | 3 |  |  |  |  | 3.75 | 94.9 |
|  |  | 4 |  |  |  |  | 3.0 | 97.2 |
| ACM / VCI | 10 | 1 | 1.5 | > 99 | 2 | > 97 | 8.4 | 71.2 |
|  |  | 2 |  |  |  |  | 5.4 | 90.3 |
|  |  | 3 |  |  |  |  | 3.75 | 96.0 |
|  |  | 4 |  |  |  |  | 2.85 | 97.7 |
| DCL | 15 | 1 | 1.6 | > 98 |  |  |  |  |
| D-OTIS | 15 | 1 | 1.45 | > 89 |  |  | 7.75 | 20.2 |
|  |  | 2 |  |  |  |  | 5.25 | 37.9 |
|  |  | 3 |  |  |  |  | 3.75 | 52.1 |
|  |  | 4 |  |  |  |  | 2.75 | 63.1 |
| SIGMET | 15 | 1 |  |  |  |  | 8.25 | 19.8 |
|  |  | 2 |  |  |  |  | 5.25 | 38.2 |
|  |  | 3 |  |  |  |  | 3.75 | 52.9 |
|  |  | 4 |  |  |  |  | 3.0 | 62.7 |
| FLIPCY | 10 | 1 | 2 | > 99 | 2.5 | > 98 | 8.6 | 75.9 |
|  |  | 2 |  |  |  |  | 6.0 | 90.2 |
|  |  | 3 |  |  |  |  | 4.4 | 94.9 |
|  |  | 4 |  |  |  |  | 3.4 | 97.1 |
| AOC_IN |  | 1 | 1.5 | > 98 |  |  |  |  |
| AOC_UL2 |  | 1 | 1.5 | > 98 | 2.7 | > 96 | 8.1 | 79.0 |
|  |  | 2 |  |  |  |  | 5.7 | 88.6 |
|  |  | 3 |  |  |  |  | 4.35 | 92.6 |
|  |  | 4 |  |  |  |  | 3.45 | 95.0 |
| 4DINIT EQSC3 |  | 1 | 1.7 | > 98 |  |  |  |  |
| 4DNEG EQSC3 |  | 1 | 1.7 | > 98 | 1.7 | > 98 | 7.8 | 65.9 |
|  |  | 2 |  |  |  |  | 4.8 | 84.8 |
|  |  | 3 |  |  |  |  | 3.4 | 91.6 |
|  |  | 4 |  |  |  |  | 2.8 | 94.1 |

It could be seen in the simulations, that due to the assumption of one dedicated frequency inside the CTR and TMA the success probability is very close to 100%. For the enroute case (ACC) success probability may become very low in case of only one VDL frequency. Even in case of four available VDL frequencies success probability is not close to 100 percent for certain applications like D-OTIS and FLIPCY. This is due to the fact that the VDL Mode 4 Specific Services (VSS) retransmission parameter setting as defined in the VDL Mode 4 SARPS are not optimised regarding the considered scenario. Additional simulation work is needed in order to provide simulation results with an optimised setting of these parameters to allow for a comparison of the results.

With respect to the performance evaluation the capacity assessments for the year 2015 with one VDL frequency for CTR and TMA showed that all requirements in an high dense airport like Frankfurt could be met. Further investigations using one frequency for shared use within CTR and TMA might be useful. Capacity assessments for the year 2015 and the enroute case showed that using three VDL frequencies does not allow to fulfil the requirements due to the fact that success probability is too low. Even in the case of four frequencies the success probability for some services like D-OTIS or FLIPCY is less than 70 %. Capacity assessments for the year 2015 for the low density traffic FIR Brindisi and the enroute case restricting to ADS-C-application showed, that all requirements could be met with one frequency. By artificially increasing the mean number of instantaneous aircraft from 30 to 730 (ICAO ADSP requirement) results showed that capacity limit of the system with one frequency has been reached. It is likely that in such a high dense scenario two frequencies should be sufficient.

## Implementation Plans

<add info about following programmes>

<M-ADS: built of VM4 ATN services for ADS-C and CPDLC services for helicopters in North Sea>

<MEDUP>

<MA-AFAS: avionics development for VM4>

<Norwegian implementation of M-ADS over VDL Mode 4 /ATN.>

## Other issues

<expand: VM4 is able to support autonomous operations in an air to air environment>

# Other systems

For the Mode S datalink, a significant emerging issue that needs very careful consideration is the self interference limitation. The frequency band is heavily loaded with interrogations/transmissions form other systems using the same frequency (Mode S radars, TCAS, Extended Squitter). Simulations to evaluate the performance of the ADS-B functionality of the Mode S (Extended Squitter) indicate that additional datalink activity may be very difficult due to interference limitations. Furthermore, in the analysis in [2], transfer delay and coverage considerations were highlighted as potential issues.

The SATCOM system was also considered in [2]. This study investigated the feasibility of this system as a complementary system to a main subnetwork. Among the relating conclusions is that the system could meet the throughput requirements for a subset of the a/c population (assuming a 10% of equipped a/c among the projected a/c in 2005). However, the study also indicated that it would be unlikely that this system would meet the transfer delay requirements for many applications (simulations showed a 95% 20 sec transfer delay in the air to ground direction). Furthermore, availability, reliability and continuity of service requirements may also become issues.

As for a new system, it is likely that the development of such a system would require a significant time. It is highly debatable that such a system could be operationally available before 2012 at the earliest.

The above considerations are the main rationale that these systems were not considered more in-depth in the evaluation in this report.

# Summary – Status

<collection of points/thoughts, to be refined>

Today, there are plans for the implementation of a VDL Mode 2 subnetwork. It is planned to have datalink services implemented over VDL Mode 2 by 2005.

However, the VDL Mode 2 subnetwork is not designed to support time critical applications. Due to the access mechanism (CSMA) it exhibits a non deterministic behaviour and it can not guarantee a required performance level in terms of transfer delay.

It is expected that at some time in the future, there will be operational requirements for time critical applications with stringent QoS parameters. However, it is not possible to predict or agree when these applications will be required.

Therefore, at some future time, there will be the need for a new system to support these new requirements. This system could complement and eventually may replace the deployed (at that time) VDL Mode 2 network. All users and especially airlines will want to maximise benefetis/gain from an installed system before introducing a new one (example of ACARS).

Experience (in the VDL mode 2 case) shows that it takes a long time after the SARPs approval to be able to plan an implementation and deployment of datalink services.

Analysis that have been carried out, shows that the new system able to support the more demanding applications, could be either VDL Mode 3 or VDL Mode 4. Both these systems can support the applications considered in the time frame up to 2015.

However only the VDL Mode 3 SARPs support, as currently approved, point to point ATN communications. The VDL Mode 4 SARPs as approved in ICAO are validated for surveillance only applications.

Currently there are no dates identified for plans to implement data communication services using VDL Mode 3.

In all the studies that analysed the considered systems, it became clear that it very difficult to compare these systems, as they were not designed to meet the same objectives. Therefore a comparative analysis will not be able to identify a clear winner. Previous discussions in AMCP in similar subjects have resulted in clear disagreements.

<Proliferation of datalinks versus flexibility and availability of options>

<Availability of other required standards: EUROCAE/RTCA, AEEC>

<To be considered:  Frequency issues>

# Recommendations

WGM is invited to:

- take note of this analysis,

- provide comments on the analysis, and

- provide advice on how to progress the work of examining the use of VDL Mode 4 for ATS point to point communications.

# Footnotes

[2] assumed a 75% loaded channel. The numbers presented in this report assume 100% loaded channel the same as for the other systems: VM2 and VM3.