AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

ARINC Response to ICAO/AMCP WG-M/1 proposals

SUMMARY

This paper contains ARINC’s response and evaluation of the VDL Mode 2 Technical Manual amendment proposals presented at the ICAO/AMCP WGM meeting in Malmo Sweden December 2000.  This paper will also be presented to the RTCA SC 172 committee and AEEC VDL subcommittee for consideration.

Presented By

Bassam Farroha

ARINC Incorporated

bfarroha@arinc.com

Tele: (410) 266-2160

Fax: (410) 266-4040

This paper contains the ARINC reviews and positions regarding the Amendment proposals that were presented in the ICAO/AMCP WGM/1 in Malmo, Sweden.  Each issue is identified by its Working Paper (WP) number and a brief description.  The official position and reasoning are also presented.  The description of the issues can be found in the ICAO/AMCP WGM/1 report Appendix H and in the submitted working papers.

## ARINC Response to ICAO/AMCP WG-M/1 proposals Cross Reference

| WP # | Name or Description | ARINC Position | Reason |
| --- | --- | --- | --- |
| 37 | Addition of Timer T27 | Support | Needed for 8208 Protocol to remove possible deadlock states |
| 38 | HDLC Public parameter ID | Support | SARPs Editorial error |
| 39 | Timer T1 Calculation has TD instead of TD(( | Support | SARPs Editorial error |
| 40 | Change the title of Table 5-9 to Private Parameter set ID | Support | Make the distinction between the Private and Public parameters more obvious |
| 52 | Remove requirement to initialize aircraft DCE | Support | Conflict within SARPs. Removing the referenced sentence will fix the problem. |
| 36 | Add T24, and T25 | Support | They can be optional timers for the implementations that need them. Use the ISO 8208 defaults as the VDL defaults until better numbers are available. |
| 41 | Make the NET parameter mandatory in all XID | Reject | It is not always needed. This is additional overhead that is not necessary. The value can be obtained by the avionics from previous transactions i.e. GSIF??? |
| 42 | Remove reference to CALL REQUEST from the ground | Reject | It is needed for Expedited Ground Initiated Handoffs |
| 43 | Make System Mask mandatory on all XID | Reject | It is not always needed. This is additional overhead that is not necessary. The value can be obtained by the avionics from previous transactions i.e. GSIF??? |
| 44 | T3 Definition | Support | Acknowledgement delay for XID |
| 45 | Make Public parameter Set ID, Procedure Class and HDLC Options mandatory on XID_CMD_HO and XID_RSP_HO | Reject | It is not always needed. This is additional overhead that is not necessary. The value can be obtained by the avionics from previous transactions i.e. GSIF???? |
| 46 | Addressing type?? | Reject | Need to be reworded, also method 2 is the preferred option |
| 47 | Join and Leave events not reported to ATN Router | Support, need additional text | Partial response, additional work is needed. |
| 48 | Add requirement for VME to generate a handoff event to IS-SME | More research is needed | Is this mixing VDL and ATN?? |
| 50 | Remove the word Minimum from the name of TG1 to name it “Frequency Dwell Timer” | Reject | The timer is designed to have the dwelling continue for at least X time units |
| 51 | Remove Call Request from the Ground | Reject | Need to keep the Call Request from the ground and make it an option. This is used for Expedited Ground Initiated handoffs |
| 64 | VSDA definition | Support | Definition and description of addressing types |
| 53 | Subnetwork Entity Initialization | Support | This feature is used to support Call Ground Initiated Expedited Handoff |
| 65 | Subnetwork Connection Establishment and Maintenance | Support | Additional wording to include a method for using VSDA. Original SARPs mentions only X.121, and assumes the rest is clear. This is only a clarification. |
| 66 | AOA | Support | Need to take out the details of AOA, will only mention 8208 and non-8208 services. |
| 49 | Ground System definition | Reject | Ground System is well defined in the SARPs. The original ARINC response shows the details. We do not need any additional definitions |