The base material for the below was taken from TM_AMCP_rev1 cv5, all redline/strikeout is against section 3..7.2 (which I believe is the latest draft).

Besides fixing a few editorial things, I have made the following changes:

- added a parameter block to enable the dynamic changing of QOS and VSS parameters

- added an arc-based regional broadcast destination

- added a requirement for sequential processing to enable exceptions / regional cut-outs / and other similar operations

Because of the tour-de-force known as Microsoft Word, these paragraph numbers begin with 1.1.1 instead of 3.7.2

    - Channel management XID

The channel management XID parameter shall be divided into component blocks as described in Table 3-25.  A station that matches a destination in a channel management XID parameter shall not process subsequent channel management XID parameters with the same command set ID in the same XID.  A station receiving a channel management XID parameter with a script that matches an active command set shall update the script duration but otherwise not modify its transmissions.

[Author’s Note:  Do we need to specifically state that a station that is operating under a received broadcast (regional or otherwise) script and who receives a second such script should compare the two and, if they are the same, ignore the command rather that stop and restart the streams?  I added a sentence at the end of the paragraph to address this concern.]

# Table 3-25. Component blocks of channel management XID

| Blocks | Description |
| --- | --- |
| Header block | Contains the XID header and the non-repetitive information for each of the sub-elements. |
| Destination block | Contains a list of zero or more destinations, along with the timeout and slot offset from the current slot to the start of the script (zero destinations included implies broadcast.) |
| Transmission definition block | Contains from 0 to 15 transmission definitions in an unordered list. Each definition describes a particular desired transmission (one not already specified in SARPs) and all relevant options. The location of a particular transmission block in this list defines an implicit pointer used in the script block (i.e., thereby specifying a particular message). |
| Frequency block | Contains from 1 to 7 frequencies in an ordered list and optional sleep parameters to use on each frequency. The location of a particular frequency block in this list defines an implicit pointer used in the script block (i.e., thereby specifying a particular frequency). |
| Parameter block | Contains QOS and other transmission parameters to use with the elements of this script. |
| Script block | Contains a repeat rate and from 1 to N script elements in an ordered list. Each script element consists of an optional repeat count, a frequency block pointer, and a transmission block pointer. |

      - Header block encoding

The channel management XID parameter header block shall be encoded as defined in Table 3-26 with subfield encodings as defined in Table 3-27.

# Table 3-26. Header block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| XID parameter ID | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 |
| XID length | 2 | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |
| directed timeout (dt) | 3 | dt4 | dt3 | dt2 | dt1 | do12 | do11 | do10 | do9 |
| directed offset (do) | 4 | do8 | do7 | do6 | do5 | do4 | do3 | do2 | do1 |
| destination count (dc) | 5 | dc8 | dc7 | dc6 | dc5 | dc4 | dc3 | dc2 | dc1 |
| command set ID (csid), transmission definition count (tc) | 6 | csid4 | csid3 | csid2 | csid1 | tc4 | tc3 | tc2 | tc1 |
| frequency count (fc), script duration type (styp), script rate (sr) | 7 | fc3 | fc2 | fc1 | styp | sr4 | sr3 | sr2 | sr1 |
| Transmit parameter count (pc) | 8 | res | res | pc6 | pc5 | pc4 | pc3 | pc2 | Pc1 |
| script count (sc) | 9 | sc8 | sc7 | sc6 | sc5 | sc4 | sc3 | sc2 | sc1 |

# Table 3-27. Header block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| directed timeout (dt) | See Table 1-35 |  |
| directed offset (do) | 0 or 2 to 212 – 1 do = 1: invalid | do = 0 implies directed rate reservation. Do >1 implies directed slot reservation. For do >1, do = the first slot in which to transmit. |
| destination count (dc) | 0-255 | Number of bytes in the destination block. 0 implies broadcast. |
| Command set ID (csid) | 0-15 | ID specifying this command* |
| transmission definition count (tc) | 0-15 | The number of elements in the transmission definition block. |
| Frequency count (fc) | 1-7 | The number of elements in the frequency block. |
| Script duration type (styp) | styp = 0: interpret sr as the number of times the entire script repeats per minute; styp = 1: interpret sr as the number of minutes until script repeats. |  |
| Script rate (sr) | 0-15. Interpreted based on styp. For styp = 0, sr is encoded per Table 1-33. For styp = 1, sr is encoded as minutes between 2 (encoded as 0) and 17 minutes. |  |
| Script count (sc) | 1 (encoded as 0) – 256 | Number of bytes in script block. |
| Transmit parameter count (pc) | 0-63 | Number of bytes in the transmit parameter block. |

Note 1:- The command set ID allows a ground station to uplink several (up to 16) separate commands to each aircraft or set of aircraft (including all aircraft in view) which are each processed separately.  A transmission with csid = x overrides operations specified in a previous transmission with csid = x, but does not affect operations dictated by previous transmissions with csid ( x.  Hence a ground station can command multiple sets of messages (each set containing various types of transmissions), and the transmissions can have different report periods from one set to another.

The number of elements in the script (total number of transmissions over one repeat cycle) shall be designated NES.  The number of transmissions per minute shall be designated NTM.  A repeat cycle can be less than a sub-multiple of one minute, exactly one minute, or multiple minutes.

# Note 2:- The NES  can be greater than sc because of the repeat capability.

Note 3. –The length of a single channel management XID parameter is limited by ISO 8885 to 255 bytes.

      - Destination block encoding

The destination block consists of zero destinations (a broadcast), one or more destinations, or a regional definition.

# 1.1.1.2.1  Broadcast Destination

If the destination count (dc) in the header block is zero, then the channel management XID parameter applies to all stations.

# 1.1.1.2.2  Addressed Destination

If bit 8 of octet 1 of the destination block is a zero, then the destination block consists of one or more addresses per Table 3-28 with encodings defined in Table 3-29.  If none of the addresses matches the receiver, then further processing of this parameter shall terminate.

# Note: -- The individual offset for the first destination is limited to 0-15 and not 0-31.

# Table 3-28. Addressed destination block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Individual offset (ido) | 1 | ido5 | ido4 | ido3 | ido2 | ido1 | d27 | D26 | d25 |
| Destination address (d) | 2 | d24 | d23 | d22 | d21 | d20 | d19 | D18 | d17 |
|  | 3 | d16 | d15 | d14 | d13 | d12 | d11 | D10 | d9 |
|  | 4 | d8 | d7 | d6 | d5 | d4 | d3 | D2 | d1 |

# Table 3-29. Addressed destination block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| Individual offset (ido) | Per Section 1.4.2.1 |  |
| Destination address (d) | 0-31 | See description of usage below. |

# 1.1.1.2.2.1		Directed rate operations

If the directed offset is set equal to 0, then the addressed stations shall operate in directed rate mode. The individual offset parameter ido shall be set to 0 on transmit for each addressed station. All stations that are not individually addressed shall operate in directed rate mode.

# 1.1.1.2.2.2		Directed slot operations

If the directed offset is not set equal to 0, then the addressed stations shall operate in directed slot mode. The individual offset parameter ido for each addressed station shall be set to the number of slots by which the transmissions of that station are to be offset from do after the first slot of the XID command.

A station transmitting a channel management XID parameter for which the directed offset is not set equal to 0 shall first ensure that the slots which will be used by addressed stations have first been reserved using block reservation protocols (see section 1.3.17) or ground quarantine (see section 1.3.6.4).

# 1.1.1.2.3  Regional multicast

If bit 8 of octet 1 of the destination block is a one, then the destination block consists of a regional multicast per Table 3-xx with encodings defined in Table 3-yy.  If the station is not in the defined region, then further processing of this parameter shall terminate.  A station is in the defined region if all of the following are true:

- its altitude (using baro altitude if available, otherwise geo altitude) is greater than or equal to the lower altitude and less than or equal to the upper altitude

- if it is on a listed radial, then its distance to the region center is less than the distance listed on either side of the radial (or, for the first radial, the first and last distance in the list)

- if it is not on a listed radial, then its distance to the region center is less than the distance listed between the radials that straddle it (if the radial that the station is on is less than the first radial or greater than the last radial, then the station must be less than the last distance listed)

# Table 3-xx. Regional multicast block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Vertex count (vc) | 1 | 0 | res | lon14 | lon13 | Vc4 | Vc3 | Vc2 | Vc1 |
| center | 2 | lon8 | lon7 | lon6 | lon5 | lon4 | lon3 | lon2 | lon1 |
|  | 3 | lon12 | lon11 | lon10 | lon9 | lat12 | lat11 | lat10 | lat9 |
|  | 4 | lat8 | lat7 | lat6 | lat5 | lat4 | lat3 | lat2 | lat1 |
|  | 5 | lon44 | lon43 | lon42 | lon41 | lat44 | lat43 | lat42 | lat41 |
| Lower altitude | 6 | Lalt8 | Lalt7 | Lalt6 | Lalt5 | Lalt4 | Lalt3 | Lalt2 | Lalt1 |
| Upper altitude | 7 | ualt8 | Ualt7 | Ualt6 | Ualt5 | Ualt4 | Ualt3 | Ualt2 | ualt1 |
| Vertex 1 | Radial 1 | 8 | R18 | r17 | R16 | r15 | R14 | r13 | r12 | r11 |
|  | Distance 1 | 9 | d18 | d17 | d16 | d15 | d14 | d13 | d12 | d11 |
| Vertex 2 (as needed) | Radial 2 | 10 | R28 | R27 | R26 | R25 | R24 | R23 | R22 | R21 |
|  | Distance 2 | 11 | D28 | D27 | D26 | D25 | D24 | D23 | D22 | D21 |

# Table 3-yy. Regional multicastblock field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| Lat | Lat, lon, lat4, lon4 are CPR encoded per Section 4. | Sent using type=0, reference position is location of station transmitting this XID. |
| long |  |  |
| Lower altitude | 0: alt <= -1 500 feet 1: –1 500 < alt <= 1 250 feet 2-254: 250 linear increments 255: alt >= 62 500 feet | Station only matches the broadcast if its altitude (baro if available, otherwise geo) is between lower and upper altitudes |
| Upper altitude |  |  |
| distance | See table 3-zz. | Vertex blocks are listed in monotonically increasing radial order. |
| radial | due North coded as 0. Resolution is 360/256 degrees, linear |  |

# Table 3-zz. Vertex distance encoding

| Transmitted value of distance (decimal equivalent of field) | Within region if: |
| --- | --- |
| 0 | Distance < 0.5 nmi |
| 1 | Distance < 1.0 nmi |
| ( | ( |
| 59 | Distance < 29.5 nmi |
| 60 | Distance < 30 nmi |
| 61 | Distance < 31 nmi |
| ( | ( |
| 89 | Distance < 59 nmi |
| 90 | Distance < 60 nmi |
| 91 | Distance < 62 nmi |
| ( | ( |
| 119 | Distance < 118 nmi |
| 120 | Distance < 120 nmi |
| 121 | Distance < 124 nmi |
| ( | ( |
| 254 | Distance < 656 nmi |
| 255 | Distance < 660 nmi |

Note. – As indicated in Section 1.1.1.2.2.1, a station that matches the regional broadcast filter operates per the directed rate mechanism.

      - Channel management XID reception procedures

Upon receipt of a channel management XID command the station shall establish NTM streams. If styp = 0, then NTM shall equal NES * nr (where nr is the result of looking up the encoded sr in Table 1-33). If styp = 1, then NTM shall equal NES / (2 + sr). If styp=1 and NES is not a multiple of (2 + sr), then periodic streams cannot be defined according to the indicated script, the message shall be judged invalid, and the entire XID parameter shall be discarded without further processing.

The receiving station shall update its reservation table and carry out the actions as specified in Table 3-30. The mth individual offset idom shall correspond to the mth destination address matching that of the receiving station.

# Table 3-30. Action on receipt of a channel management XID

| Directed offset (do) | Directed timeout (dt) | Action |
| --- | --- | --- |
| 0 | any | See 1.3.16.5.2. |
| 1 | any | Invalid |
| do > 1 | dt < 15 | Reserve the following slots for the destination to broadcast: for j equal to 0 to 3 and k equal to 0 to NTM - 1, the slots equal to truncate (do + idom + (k * M1/NTM) + j * M1) through (lg + truncate (do + idom + (k * M1/NTM) + j * M1)) after the first slot of the received burst |
| do > 1 | dt = 15 | Reserve the following slots for the destination to broadcast: for k equal to 0 to NTM - 1, the slots equal to truncate (do + idom + (k * M1/NTM)) through (lg + truncate (do + (k * M1/NTM))) after the first slot of the received burst |

Upon receipt of a burst containing an autotune reservation (pr_flag = 0), the station shall update its reservation table  and carry out the actions as specified in Table 1-39.

        - Response to a channel management XID with do = 0

If the directed offset subfield is equal to 0, the responder station shall operate autonomously using the periodic broadcast procedures with the nominal periodic rate (V11) set to NTM in the autotune reservation transmission for the next dt * M1 slots, with the first two bits of the message ID field set to “00”. The nominal slots shall be spaced such that the nominal slot for the kth element identified in the script occurs

truncate ((k-1)*M1/NTM) slots

after the nominal slot for the first element identified in the script. Upon cessation of directed transmissions, the responder shall resume default autonomous behaviour on the GSCs, reserving new slots as required.

        - Response to a channel management XID with do > 1

On receipt of an XID command with the mth destination address matching that of the receiving station and with the directed offset subfield (do) greater than 1, the responder station shall begin the transmission of the first script element at T0m slots after the first slot of the XID command where T0m = do + idom. Subsequent transmission slots shall be spaced such that the slot for the kth element identified in the script occurs

truncate ((k-1)*M1/NTM) slots

after the specified slot for the first element identified in the script.

        - Setting of TV11 timer

Upon receipt of a channel management XID command the station shall set the TV11 timer (see Section 1.3.10.2.1) equal to the value of the directed timeout (dt) subfield for each of the slots indicated in the XID transmission. The responder station shall transmit in each of the reserved slots. Each response burst shall contain the periodic broadcast reservation field with the periodic offset (po) subfield set to 0 and the periodic timeout (pt) subfield set to min(3, TV11-1). After transmission, the timer TV11 shall be decremented. When TV11 reaches zero, the responder shall not transmit a response to the directed request. Upon cessation of directed transmissions, the responder shall resume default autonomous behaviour on the GSCs, reserving new slots as required.

        - Sharing streams

If styp = 1, then the transmissions in successive minutes shall share streams with those script elements that are NTM (modulo NES) apart.  If all of the elements that share a stream are not transmitted on the same frequency, then the message shall be judged invalid and the entire XID parameter shall be discarded. If all of the elements that share a stream are not of the same length, then a basic sync burst shall be transmitted for all elements in that stream.

If a station receives a plea request, it shall use NTM as the default reporting rate for the frequency to construct the plea response.

      - Cancellation of channel management XID command

A station shall cancel a channel management XID command by transmitting a channel management XID with the directed timeout subfield set to 15, the directed offset (do) to the offset from the first slot of the cancellation XID to the first slot for which the reservation shall be cancelled, and all other subfields set to the same values as in the original burst to be cancelled.

      - Cancellation of autonomous streams

If the responder was transmitting autonomously the VSS user data for which a channel management XID command was received, then it shall cancel its existing reservations in accordance with paragraph 1.3.10.5.9, and operate in accordance with the parameters of the XID command.

        - Command set ID parameter

A station that receives a channel management XID parameter with csid = 0 shall terminate any previous default sync burst operations and initiate operations in accordance with the current XID parameter.

A station that receives a channel management XID parameter with csid matching a previously-received XID parameter shall terminate any previous operations commanded by the previous XID parameter and initiate operations in accordance with the current XID parameter.

A station that does not receive a new XID parameter block with csid = 0 within (dt * M1) slots, with dt as specified in the XID parameter block with csid = 0, shall revert to default operations.

A station that does not receive a new XID parameter block with csid > 0 within (dt * M1) slots, with dt as specified in the XID parameter block with csid > 0, shall terminate the operations indicated in the associated XID parameter block.

      - Transmission block encoding

        - Transmission block definitions in SARPs

The SARPs contain the following ordered list of standard transmission blocks (id = 0 through 15) which can be referenced by id without explicitly describing the referenced formats in the uplink XID. If a station receives an XID parameter containing a standard transmission definition (id = 0 through 15) that it does not recognize, it shall transmit a basic sync burst.

# Table 3-30. Transmission block definitions in SARPs

| Encoding | Transmission definition |
| --- | --- |
| 0 | Sync burst with baro altitude, no sleep parameters, basic variable field, baro alt rate |
| 1 | Sync burst with geo altitude, no sleep parameters, basic variable field, geo alt rate |
| 2 | Sync burst with baro altitude, no sleep parameters, full position variable field, baro alt rate |
| 3 | Sync burst with baro altitude, no sleep parameters, aircraft data variable field |
| 4 – 15 | reserved |

        - Transmission block definitions not predefined in SARPs

The XID can contain explicit definitions of transmission blocks (i.e., if a desired transmission block is not contained in the ordered list in SARPs but is still describable using internationally standardized elements).  Zero to fifteen such transmission blocks can be defined in the transmission block definition section (as indicated by the tc field) and shall be encoded as defined in Tables 3-31 and 3-33.

# Table 3-31. Sync burst block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Boolean ID (id) | 1 | id4 | id3 | id2 | id1 | aux | b/g | res | 0 |
| ID-extension (if required) | 2 | id14 | id13 | id12 | id11 | id24 | id23 | id22 | id21 |

# Table 3-32. Sync burst block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| baro/geo selection (b/g) | b/g = 0: send baro b/g = 1: send geo | If the preferred altitude encoding is not available, then send the other if it is available. |
| variable field ID (and extensions) | Per Table 3-2 | Octet 2 is only included when necessary |
| auxiliary selection (aux) | For those variable fields with a selection (e.g, basic, high dynamic, TCP), send selection = aux. | If the requested data is not available, but the alternate is, then send the alternate. As an example, for the basic variable field, aux=0 means send baro rate. |

If the mobile is travelling greater than 3069 knots (i.e., bit gs12=1), then the mobile shall transmit a high dynamic variable field whenever it otherwise would have transmitted a basic, full position, or high resolution variable field.

# Table 3-33. Non-sync burst block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| message ID (mid), more bit (mb) | 1 | mb | mid7 | mid6 | mid5 | mid4 | mid3 | mid2 | mid1 |
| length (len), application specific (app) | 2 | app | app | app | app | len4 | len3 | len2 | len1 |

# Note. – Octets 3 through len+2 are all application specific.

# Table 3-34. Non-sync burst block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| application specific data (app) |  | Defined by the application specified by the message ID |
| length (len) | 0-15 | Number of bytes following the length (i.e., an application requiring only 4 bits of parameters would encode a 0 for length) |
| message ID (mid) | Per Table 1-6 |  |
| more bit (mb) | mb = 0: octet 2 not included mb = 1: octet 2 (and possibly more follow) |  |

Whenever the mobile cannot transmit the requested information (either a new message ID, variable field, or other option was defined that the mobile does not understand or the mobile does not have the requested information), then the mobile shall transmit a sync burst with a basic variable field.

1.1.1.7		Frequency block encoding

One to seven frequencies are included in the frequency block section (as indicated by the fc field).  A single frequency shall be encoded as defined in Table 3-39 with subfield encodings as defined in Table 3-40:

# Table 3-39. Frequency block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| flags | 1 | sleep | auto | rcv | res | f12 | f 11 | f 10 | f 9 |
| freq | 2 | f 8 | f7 | f6 | f5 | f4 | f3 | f2 | f1 |

# Table 3-40. Frequency block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| frequency (f) | Per Section 1.3.15.1 |  |
| must receive (rcv) | rcv = 0: reception on this frequency is optional rcv = 1: reception on this frequency is mandatory | As the list is ordered in priority, a station receiving a list with a frequency with rcv=0 before a frequency with rcv=1 shall discard the entire XID parameter. |
| sleep and auto | Per section 3.4.3 | If the respective bit is set, then the respective block is appended per Section 3.4.3 |

The list of frequencies is ordered. A station with k available receivers shall monitor the first min(k, number of mandatory frequencies) frequencies in the frequency list.

        - Recommendation.

A station with spare receivers should monitor the remaining frequencies in the list.

1.1.1.8Transmission parameter block definition

The station shall transmit all of the streams defined in the script using the parameters defined in Table 3-aa with subfield encodings as defined in Section 1 for the appropriate variable.  The station shall use the first transmit parameter count (pc) octets from Table 3-aa instead of the default values for those parameters.  If pc is greater than the length of Table 3-aa, then the station shall ignore all octets beyond the length.  These parameters shall be ignored for directed slot operations.

Note. – PC would be greater than the length of Table 3-aa if more parameters were added after the software was released.

# Table 3-aa. Transmission parameter block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| Q1, Q4 | 1 | Q12 | Q11 | res | Q45 | Q44 | Q43 | Q42 | Q41 |
| Q2a | 2 | Q2a8 | Q2a 7 | Q2a 6 | Q2a 5 | Q2a 4 | Q2a 3 | Q2a 2 | Q2a 1 |
|  | 3 | Q2a 12 | Q2a 11 | Q2a 10 | Q2a 9 | Q2b 12 | Q2b 11 | Q2b 10 | Q2b 9 |
| Q2b | 4 | Q2b 8 | Q2b 7 | Q2b 6 | Q2b 5 | Q2b 4 | Q2b 3 | Q2b 2 | Q2b 1 |
| Q2c | 5 | Q2c8 | Q2c 7 | Q2c 6 | Q2c 5 | Q2c 4 | Q2c 3 | Q2c 2 | Q2c 1 |
|  | 6 | Q2c 12 | Q2c 11 | Q2c 10 | Q2c 9 | Q2d 12 | Q2d 11 | Q2d 10 | Q2d 9 |
| Q2d | 7 | Q2d 8 | Q2d 7 | Q2d 6 | Q2d 5 | Q2d 4 | Q2d 3 | Q2d 2 | Q2d 1 |
| TV11min, TV11max | 8 | TV11min4 | TV11min3 | TV11min2 | TV11min1 | TV11max4 | TV11max3 | TV11max2 | TV11max1 |
| V11 | 9 | res | Res | V116 | V115 | V114 | V113 | V112 | V111 |
| V12 | 10 | Res | V127 | V126 | V125 | V124 | V123 | V122 | V121 |
| VS2 | 11 | res | Res | VS26 | VS25 | VS24 | VS23 | VS22 | VS21 |
| VS4 | 12 | res | VS47 | VS46 | VS45 | VS44 | VS43 | VS42 | VS41 |

1.1.1.9		Script block definition

The channel management XID parameter script shall be encoded as defined in Table 3-41 with subfield encodings as defined in Table 3-42.

# The script block shall contain one or more script elements. There are two types of script elements.

# Table 3-41. Script block bit encoding

| Description | Octet | Bit number |
| --- | --- | --- |
|  |  | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |
| freq index (frq), transmission definition index (txd) | 1 | frq3 | frq2 | frq1 | nsd | txd4 | txd3 | txd2 | txd1 |
|  |  |  |  |  | or |  |  |  |  |
| repeat count (rpt) | 1 | 1 | 1 | 1 | rpt5 | rpt4 | rpt3 | rpt2 | rpt1 |
| freq index (frq), transmission definition index (txd) | 2 | frq3 | frq2 | frq1 | txdt | txd4 | txd3 | txd2 | txd1 |

# Table 3-42. Script block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| frequency index (frq) | 0-6 | The offset from the beginning of the frequency list. (An encoding of 0 refers to the first element in the frequency block.) |
| non-standard definition (nsd) | nsd = 0: defined in SARPs. nsd = 1: defined in XID transmission definition list |  |
| transmission definition index (txd) | 0-15 | The offset from the beginning of the transmission definition list (An encoding of 0 refers to the first element in the list.) |
| repeat count (rpt) | 3 (encoded as 0) to 34 | The number of times to repeat the frequency/vfd listed in octet 2. |

Example:

# The picture above shows five regions:

| Region | Number | Operations |
| --- | --- | --- |
| Airport Movement Area | R1 | Ground freq (sleep command only by addressed direction) |
| Approach/Departure | R2 | Ground freq, local freq |
| Terminal Area | R3 | Local freq and GSCs |
| Another Airport | R4 | Second local freq and GSCs |
| Default | R5 | GSCs |

Whether this scheme would actually work (given that we have given one minute for an aircraft to update its script, the transition from terminal area to approach to ground may be too short and the aircraft may penetrate too far into the next region with a regional update) is not relevant to the purpose of the example.

The XID would consist of (potentially other parameters, plus five channel management parameters), and will have the following basic structure:

| Field | Size |
| --- | --- |
| Header (Source Address, Compressed Frame Message ID, XID header and parameter set ID) | About 10 |
| Channel Management – R1 | About 20 + 9 |
| Channel Management – R2 | About 20 + 11 |
| Channel Management – R3 | About 20 + 9 |
| Channel Management – R4 | About 20 + 9 |
| Channel Management – R5 | About 20 + 0 |
| Reservation data, CRC | 3 |

The size of the channel management parameters depends on the degree of configuration.  If only the default parameters are included on two frequencies with a simple script, then the parameter will be only 13 bytes plus the script.

The encodings of R1, R3, and R4 are the basically the same:

| Description | Octet | R1 | R3 | R4 |
| --- | --- | --- | --- | --- |
| Vertex count (vc) | 1 | 0x01 | 0x01 | 0x01 |
| center | 2 | Center of region | Center of region | Center of region |
|  | 3 |  |  |  |
|  | 4 |  |  |  |
|  | 5 |  |  |  |
| Lower altitude | 6 | 0x00 | 0x00 | 0x00 |
| Upper altitude | 7 | FL0 (0x06) | FL180 (0x4E) | FL180 (0x4E) |
| Vertex 1 | Radial 1 | 8 | 0x00 | 0x00 | 0x00 |
|  | Distance 1 | 9 | 1 nmi (0x01) | 30 nmi (0x3C) | 30 nmi (0x3C) |

R2 is a keyhole encoded as:

| Description | Octet | R1 |
| --- | --- | --- |
| Vertex count (vc) | 1 | 0x02 |
| center | 2 | Center of region |
|  | 3 |  |
|  | 4 |  |
|  | 5 |  |
| Lower altitude | 6 | 0x00 |
| Upper altitude | 7 | FL50 (0x1A) |
| Vertex 1 | Radial 1 | 8 | 225 degrees (0xA0) |
|  | Distance 1 | 9 | 5 nmi (0x0A) |
| Vertex 2 | Radial 2 | 10 | 315 degrees (0xE0) |
|  | Distance 2 | 11 | 1 nmi (0x01) |

R5 is the default area and is encoded by setting the destination count field in the header to zero.  Alternatively, to prevent ducting or other propagation anomalies from affecting arbitrary aircraft, the same encoding as R1 may be used, but with a larger radius.

# Text boxes

SFC

FL50

FL180

R1

R2

R3

30 mi

5 mi

R5

30 mi

1 mi

R2

R1

R3

R4

R5