# WP # 22

# Changes to HFDL SARPs

(Annex 10, Section III, Chapter 11)

Change to paragraph 11.3.1.6 TRANSMITTER STABILITY.

This paragraph is incorrect, as it does not reflect that the “actual carrier of the PSK transmission” is actually 40Hz above the SSB assigned frequency.

Original Paragraph:

      - TRANSMITTER STABILITY

The basic frequency stability of the transmitting function shall be such that the difference beween the actual carrier of the PSK transmission and the SSB assigned frequency shall not exceed:

- 20Hz for HFDL aircraft station sub-systems; and

- 10Hz for HFDL ground station sub-systems.

New Paragraph:

      - TRANSMITTER STABILITY

The basic frequency stability of the transmitting function shall be better than:

- 20Hz for HFDL aircraft station sub-systems; and

- 10Hz for HFDL ground station sub-systems.

Change to the Note following paragraph 11.3.1.10  ASSIGNED FREQUENCY.

Original Note:

Note. – The HFDL assigned frequency is offset from the SSB carrier (reference) frequency by 1400.  The digital modulation is fully contained within the same over-all channel bandwidth as the voice signal and complies with the provisions of Appendix S27 to the ITU Radio Regulations.

Modified Note:

Note. – By convention, the HFDL assigned frequency is offset from the SSB carrier (reference) frequency by 1400 Hz.  The HFDL M-PSK carrier of the digital modulation is offset from the SSB carrier (reference) frequency by 1440 Hz.  The digital modulation is fully contained within the same over-all channel bandwidth as the voice signal and complies with the provisions of Appendix S27 to the ITU Radio Regulations.

Figure 11-1:

The location of the text “SSB carrier (reference) frequency” is incorrect.  This text should be moved to be directly beneath the vertical dashed line which is 1400 Hz to the left of the vertical dashed line in the middle of the spectrum mask showed.