AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

STNA Response to ICAO/AMCP WG-M/1 proposals

SUMMARY

This paper contains STNA’s response and evaluation of the VDL Mode 2 Technical Manual amendment proposals presented at the ICAO/AMCP WGM meeting in Malmo Sweden December 2000.

Presented By

STNA

This paper contains the STNA reviews and positions regarding the Amendment proposals that were presented in the ICAO/AMCP WGM/1 in Malmo, Sweden.  Each issue is identified by its Working Paper (WP) number and a brief description.  The description of the issues can be found in the ICAO/AMCP WGM/1 report Appendix H and in the submitted working papers.

## STNA Response to ICAO/AMCP WG-M/1 proposals Cross Reference

| WP # | Name or Description | STNA Position | Comments |
| --- | --- | --- | --- |
| 37 | Addition of Timer T27 | Support |  |
| 38 | HDLC Public parameter ID | Support |  |
| 39 | Timer T1 Calculation has TD instead of TD(( | Support |  |
| 40 | Change the title of Table 5-9 to Private Parameter set ID | Support |  |
| 52 | Remove requirement to initialize aircraft DCE | Support |  |
| 36 | Add T24, and T25 | Support |  |
| 41 | Make the NET parameter mandatory in all XID | Reject | The NET parameter is optional, only in the Air Initiated and in the Ground Requested Handoffs. The later shall lead to an Air Initiated Handoff. The question is: is it possible for an airborne user, and if yes, in which case, to initiate a Handoff without having received a valid GSIF before, where this parameter is mandatory? If it is, see WP 43 commentary. |
| 42 | Remove reference to CALL REQUEST from the ground | Support | As it is not possible to initiate sub network connections from the ground, we agree this amendment. Solution exposed in ARINC 631-3 section 9.4.1.1 is acceptable. |
| 43 | Make System Mask mandatory on all XID | Open | We would suggest to keep this parameter optional and add a note to specify that this parameter shall be present, if the old and new ground stations have different System masks. Our preoccupation is to avoid duplicated information in, and increasing size of, the XID frames. |
| 44 | T3 Definition | Support |  |
| 45 | Make Public parameter Set ID, Procedure Class and HDLC Options mandatory on XID_CMD_HO and XID_RSP_HO | Open | Same commentary as WP 43. |
| 46 | Addressing type?? | Open | A rewording of this amendment will be presented. |
| 47 | Join and Leave events not reported to ATN Router | Open | Comments will be presented. |
| 48 | Add requirement for VME to generate a handoff event to IS-SME | Open | Comments will be presented. |
| 50 | Remove the word Minimum from the name of TG1 to name it “Frequency Dwell Timer” | Open | We have two understandings of this paragraph. Either TG1 is really the “minimum frequency dwell time” and the sentence “It shall be cancelled when a valid uplink is received.” and the recommendation that follows (6.5.4.3.1.1 in current sarps) shall be deleted. Or it is not a minimum time, so an aircraft shall connect as soon as it receives a valid uplink (or a valid uplink of its most prefered system), and in this case, the word minimum and the condition a) shall be deleted : because with this understanding, if TG1 expires, it means that no valid up link have been received, so we can not connect to a ground station. |
| 51 | Remove Call Request from the Ground | Support | Same commentary as WP 42 |
| 64 | VSDA definition | Open | Comments will be presented. |
| 53 | Subnetwork Entity Initialization | Reject | As it is not possible to initiate sub network connections from the ground, we disagree this amendment. Solution exposed in ARINC 631-3 section 9.4.1.1 is acceptable. |
| 65 | Subnetwork Connection Establishment and Maintenance | Open | Comments will be presented. |
| 66 | AOA | Support | We agree on updating the tables, but if some text is needed, it should be clarified. |
| 49 | Ground System definition | Reject |  |