Amendment Proposal

| Title: | Use of unique address |
| --- | --- |
| AP working paper number and date | WGM2/WP15, WGMM2/WP20 |
| Document(s) Affected: | Manual on VDL Mode 4 Technical Specifications |
| Document Version: | AMCP/7 Report WP/81 Appendix B, Agenda Item 2 |
| Sections of Documents Affected: | Table 1-55, Section 1.4.2.1.2 |
| Coordinator: | Nikos Fistas |
| Coordinator's Address: | Eurocontrol |
| Coordinator's Phone: | +32 2 7294777 |
| Coordinator's Fax: |  |
| Coordinator's E-mail Address: | nikolaos.fistas@eurocontrol.be |
| Category: | Clarification |
| Problem description: | This proposal requires the aircraft to use the unique 24-bit ICAO address when engaged in ATS communications. In addition a change is introduced to distinguish between addresses of aircraft and ground vehicles |
| Background: | [Validation Details] validated by inspection |
| Backwards compatibility: | Not applicable |
| Amendment Proposal: | See attached text for specific changes to TM. |
| WG-M Status: | PROPOSED 26/04/01 |

The following modifications are needed in the Manual on VDL Mode 4 Technical Specifications:

<start of text>

1.4.2.1.1		Address type

The address type field is described in Table 1-55.

Table 1-55. Address type field encoding

| Bit encoding | Description type | Bits 1 to 24 |
| --- | --- | --- |
| 27 | 26 | 25 |  |  |
| 0 | 0 | 0 | Mobile | Non-unique identity |
| 0 | 0 | 1 | aircraft | 24-bit ICAO address |
| 0 | 1 | 0 | ground vehicles | nationally administered address space |
| 0 | 1 | 1 | Reserved | Future use |
| 1 | 0 | 0 | Ground station | ICAO-administered address space |
| 1 | 0 | 1 | Ground station | ICAO-delegated address space |
| 1 | 1 | 0 | Reserved | Future use |
| 1 | 1 | 1 | All stations broadcast | All stations |

1.4.2.1.2		Non-unique identity address

A mobile station using the non-unique identity address shall randomly choose a 24-bit address. The non-unique identity address of all zeros shall not be used. The non-unique identity address of all ones shall be used for broadcast applications only. All radio units located at a station shall use the same non-unique identity address.

If the station detects that another station is using the same random address, it shall stop transmitting on the current address; it shall then randomly select a new address. It shall use this new address in subsequent transmissions.

Note 1.— Processing of ambiguous data resulting from use of the non-unique address is an end system issue.

When using VDL Mode 4 for ATS applications, aircraft shall use the unique 24-bit ICAO address.

Note 2.— In this case bits 25, 26, and 27 of the full 27-bit address will be 1, 0, and 0 respectively, as is defined in Table 1-55.

<end of text>