AMCP WG M2-WP.......

HFDL frequency planning software

Basic requirements:

The software should: run on a PC with Windows 98, with CD-ROM reading capabilities; contain the basic run-time elements to support management of the assignments database; take into account all assignments of the official ITU-IFL as well as any regionally co-ordinated assignments not yet in the ITU-IFL; be capable of importing/updating from a new(er) edition of the ITU-IFL CD-ROM, while keeping the regionally co-ordinated assignments; apply interference calculations as per ITU-RR Appendix 27 material; provide a screen plot of the relevant radio stations, showing the areas where potential interference is calculated based upon the above; provide for a printout of this screen plot, completed with the relevant station details; be applicable to RDARA, MWARA, VOLMET and World-wide allotment areas as per Appendix 27; function properly in a single user configuration; provide for a compatibility analysis of a radio station in conjunction with the existing radio environment on the relevant frequency as per ITU-IFL; present the results of the compatibility calculation in a way consistent with the App 27 method(s); provide for a printout of the screen information together with the necessary station details and corresponding legenda to it all.

Databases:

Allotment areas properties/tools: include all geografical information on MWARA, RDARA, VOLMET and World Wide Allotment Areas as given in ITU RR App 27; treat this geografical information as fixed, not to be changed by users; provide for additional modified areas corresponding to the (intended) actual operational coverage area of a new tentative radio station yet to be co-ordinated.

Assignable frequency database properties/tools: include all assignable channel/appropriate area combinations from RR App 27 treat all these channel/area combinations as fixed, not to be changed by users; provide for tentative channel/area combinations for purposes of analysing potential incompatibility with the existing radio environment;

Assignment database properties/tools: import data from new ITU-IFL CD-ROM while identifying regionally co-ordinated assignments as yes/no formally co-ordinated and registered in the new IFL; treat all ITU-IFL assignments as fixed, not to be changed by users. provide for the creation of a tentative new radio station on a chosen frequency for (in)compatibility calculations;

Calculation/plotting environment database: provide for extraction of all radio stations on a specified frequency as stations to be taken into account in any compatibility calculation; prepare and provide all data needed to enable the (separate) screen plotting software program to visualise the whole radio station environment together with the results of compatibility calculations;

Proposed order of development:

Define/set up and fill the Allotment areas database with APP 27 MWARA, RDARA, VOLMET and World-wide Allotment Areas; Define/set up and fill the Assignable frequency database with the relevant App 27 material; Define/set up the Assignment database; Develop the import routine(s) for updating the assignments database with new ITU-IFL CD-ROM material; Define/set up the calculation database Develop the compatibility analysis routine(s); Demonstrate the software developed so far to CNS and collect first comments: sept/oct 2001. After the separate plotting software with world maps has been made available: Expand the calculation/plotting database set up to accomodate the information needed for the plotting process; Adapt the compatibility routine(s) to deliver the required resultant plotting information; Provide the necessary legenda details for a print out of the resulting screen plot; Develop the necessary overall menu screen(s) to access the various functionalities of the software; Write some fundamental guide lines on how the software functions; Demonstrate the full package and documentation to CNS: jan 2002.