AMCP WG-M2 WP41

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

Addition of non 8208 service for VDL mode 2 system.

SUMMARY

This paper proposes a method for using the VDL mode 2 to transport non 8208 data over the Datalink layer (AVLC).

Prepared by

WG-M

| Title: Original: AMCP WGM/1 AP21 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 101 | AMCP WG-M2 WP41 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | technical manual addition |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | Addition |
| Problem description: |  |
| Background: | New service over the VDL network |
| Backwards compatibility: |  |
| Amendment Proposal: | Text attached |
| WG-M status: | RESOLVED |
|  | Approved |

This Table replaces Table 5-15.of current Technical Manual

AVLC Specific Options Parameter Format

| Parameter ID | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |
| Parameter value | 0 | 0 | 0 a | bs | bl | i | v | x |

This Table replaces Table 5-16.of current Technical Manual

AVLC Specific Options Parameter Values

| BIT | Name | Value | Description |
| --- | --- | --- | --- |
| 1 | x | x = 1 | Only VDL-specific DTE addresses |
|  |  | x = 0 | Ground network DTE address accepted |
| 2 | v | v = 0 | Expedited subnetwork connection not supported |
|  |  | v = 1 | Expedited subnetwork connection is supported |
| 3 | i | i = 0 | Does not support initiated handoff |
|  |  | i = 1 | Supports initiated handoff |
| 4 | bl | bl = 0 | Broadcast link handoff not supported |
|  |  | bl = 1 | Broadcast link handoff supported |
| 5 | bs | bs = 0 bs = 1 | Broadcast subnetwork connection not supported |
|  |  |  | Broadcast subnetwork connection supported |
| 6 | a | a = 0 | 8208 only service supported and/or requested |
|  |  | a = 1 | Non 8208 service supported1 and/or requested |
| 7 | Reserved | Set to 0 | Reserved for future use |
| 8 | Reserved | Set to 0 | Reserved for future use |

1Note : If  a=1 and VSDA is valid than both 8208 and non-8208 service are supported. To ensure the compatibility of mixed services, the Initial Protocol Identifer ISO-9577 shall be used in any packet header.