AMCP WG-M2 WP46

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

Restriction in allowed values for datalink service k-window parameter.

SUMMARY

This paper proposes to change the maximum value of the k "window size" parameter to 4 from the its current value.

Prepared by

WG-M

| Title: | VDL Mode 2 Technical Manual Amendments |
| --- | --- |

AP working paper number and date:

| AP 106 | AMCP WG-M/2 WP46 |
| --- | --- |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Table 5-5 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | BUG |
| Problem description: | Use of Multi-selective SREJ option implies a K-window maximum size of 4 |
| Background: |

When an out of sequence frame is received, AVLC layer shall check if it is an out of sequence error or a duplicated frame. In the former case, a SREJ frame shall be sent, and in the later, the frame shall be dropped and T2 timer restarted, if not currently running.

This is only possible if the k window is less or equal to frame numbering modulus / 2, where modulus is 8 in AVLC. This avoids overlap of possible duplicated frames window (that will be dropped) and next expected frames window (that will lead to SREJ if out of sequence).

| The SARPs allow values between 1 and 7 for the k parameter which is not compliant with the use of multi-selective reject option. |
| --- |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Reduce maximum value of k-window from 7 to 4 in Table 5-5. |
| WG-M status: | PROPOSED |
|  | pending |

Table 5-5.  Data link service system parameters for Mode 2

| Symbol | Parameter name |
| --- | --- |
| Minimum | Maximum |
| Mode 2 default | Increment |
|  | T1min | Delay before retransmission | Minimum | 0 s | 20 s |
| 1.0 s | 1 ms |
| T1max |
| Maximum | 1 s | 20 s |
| 15 s | 1 ms |
| T1mult |
| Multiplier | 1 | 2.5 |
| 1.45 | 0.01 |
| T1exp |
| Exponent | 1 | 2.5 |
| 1.7 | 0.01 |
| T2 | Delay before ACK |
| 25 ms | 10 s |
| 500 ms | 1 ms |
| T3min | Link initilization time | Minimum | 5 s | 25 s |
| 6 s | 1 ms |
| T3max |
| Maximum | 1 s | 20 s |
| 15 s | 1 ms |
| T3mult |
| Multiplier | 1 | 2.5 |
| 1.45 | 0.01 |
| T3exp |
| Exponent | 1 | 2.5 |
| 1.7 | 0.01 |
| T4 | Maximum delay between transmissions | aircraft | 10 min | 1440 min |
| 20 min | 1 min |
| ground | 12 min | 1442 min |
| 22 min | 1 min |
| N1 | Maximum number of bits in any frame |
| 1144 bits | 16504 bits |
| 8312 bits | 1 bit |
| N2 | Maximum number of transmissions |
| 1 | 15 |
| 6 | 1 |
| k | Window size |
| 1 frame | 74 frames |
| 4 frames | 1 frame |