AMCP WG-M2 WP47

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

Clarification of SREJ procedure.

SUMMARY

This paper proposes to clarify the format and use of SREJ frame.

Prepared by

WG-M

| Title: | VDL Mode 2 Technical Manual Amendments |
| --- | --- |

AP working paper number and date:

| AP 107 | AMCP WG-M/2 WP47 |
| --- | --- |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.3.11.2 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | CLARIFICATION |
| Problem description: | Modification of SREJ information field modifies HDLC procedures |
| Background: |

Modification of SREJ interpretation modifies the HDLC procedures in many ways:

It is not possible to have several SREJ conditions because each frame will contain every not received I frames,

ISO 4335 AMENDMENT 7 “Enhanced multi-selective reject option” shows a complex scenario that can not be applied: the second SREJ will acknowledge frame 0, although this frame has not been received,

HDLC does not support acknowledgement of non contiguous I frames.

| Paragraph 5.3.11.2 shall contain the complete SREJ procedure to be applied with AVLC protocol and all the special cases described in ISO/4335. |
| --- |
| Backwards compatibility: | Yes |
| Amendment Proposal: |

Add following text:

| “Any out of sequence received frame, that is not duplicated, shall be held for later delivery and trigger a new SREJ for retransmission of all the not received I frames: SREJ frame shall have Nr set to first not received I frame and information field contains all the others. ” |
| --- |
| WG-M status: | PROPOSED |
|  | pending |

5.3.11.2    SREJ frame. The multi-selective reject option in ISO 4335 shall be used to request the retransmission of more than one INFO frame. The SREJ (F=0) frame shall be generated only after receipt of an out-of-order INFO (P=0). The SREJ (F=1) shall be generated only after receipt of an INFO (P=1), RR (P=1) or SREJ (P=1). The SREJ (P=1) frame shall be generated only in accordance with the procedures of 5.3.4.4. A DLE shall acknowledge those frames which were received correctly but out of order by including in the SREJ information field an octet with bits 6-8 set to the INFO frame's sequence number and bit 1 set to 1. Although the F bit may be set to 0, the SREJ frame shall always acknowledge INFO frames up to N(r)-1 (where N(r) is the value in the control field). Any out-of-order received frame, that is not duplicated, shall be held for later delivery and trigger a new SREJ for retransmission of all the not received I frames, i.e. SREJ frame shall have Nr set to first not received I frame and information field contains all the others.

Note.— AVLC has extended the standard ISO 4335 SREJ functionality to selectively acknowledge frames. In ISO 4335, the octets in the information field which were requesting retransmission of frames had bit position 1 set by default to 0.