AMCP WG-M2 WP48

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M

Helsinki, Finland

April 2001

Inconsistency in N2 counter definition.

SUMMARY

This paper proposes to remove an inconsistency in the N2 counter definition.

Prepared by

WG-M

| Title: | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 108 | AMCP WG-M/2 WP48 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.3.4.6 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | CLARIFICATION |
| Problem description: | Inconsistency in T1 timer definition |
| Background: | This paragraph defines links this counter to the XID_CMD frames only in the first sentence. But the way this counter has to be used comprises the T1 timer that is not used for those frames. This is inconsistent with the definition above. STNA's understanding is that this counter applies to all the frames that need to be acknowledged, that is to say: XID_CMD frames but also INFO, RR(P=1), SREJ(P=1 and FRMR frames. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Replace "XID_CMD frame" by "AVLC frame that need to be acknowledged". |
| WG-M status: | PROPOSED |
|  | Pending |

5.3.4.6 Counter N2 (maximum number of transmissions). Counter N2 defines the maximum number

of transmissions that the DLS shall attempt to transmit any outstanding AVLC frame that need to be acknowledged. A Counter N2

shall be set to zero when a new frame is ready for transmission. Counter N2 shall be incremented after each

transmission of the frame. The counter shall be cleared after its associated frame is acknowledged. When

Timer T1 expires, a DLE shall invoke the retransmission procedures of 5.3.4.1 up to N2 - 1 times. When

Timer T3 expires, a DLE shall invoke the retransmission procedures of 5.3.4.3 up to N2 - 1 times. When

Counter N2 reaches the maximum number of attempts (value of parameter N2) the LME shall be informed

and the frame shall not be transmitted.