Appendix F

# Simulation of log-on rush at the event of satellite failure

The following information was presented by Mr. Shigeki Masuda from JCAB.

SUMMARY

When a satellite becomes disabled for some reason, all AESs that have operated with the satellite start a recovery procedure specified in the INMARSAT SDM or AMSS SARPs. That is, they begin a log on procedure to a GES operating to another satellite. Since the timing all AESs lose connection is simultaneous, they send a first log-on request to the GES almost simultaneously. Thus, the channels used for log-on are congested and it may lead to a large log-on delay or even a log-on failure for some AESs. This paper describes the simulation result about what happens when many AESs try to log on to a GES almost simultaneously. Although the simulation was conducted for a limited condition, it showed the possibility that many AESs may have to wait for a log-on completion for a long time or may fail to log on to a GES operating to an alternative satellite at the event of satellite failure. Considering it affects flight safety, it is important to find a way to avoid such possibility.

- Introduction

When a satellite becomes disabled for some reason, all AESs that have operated with the satellite start a recovery procedure specified in the INMARSAT SDM or AMSS SARPs. That is, they begin a log on procedure to a GES operating to another satellite. Since the timing all AESs lose connection is simultaneous, they send a log-on request to the GES almost simultaneously. Thus, the channels used for log-on are congested and it may lead to a large log-on delay or even a log-on failure for some AESs. This paper describes the simulation result about what happens when many AESs try to log on to a GES almost simultaneously.

2. Operation at the event of Satellite failure

Figure 1 shows a simulation concept. We consider the situation where a satellite becomes disabled suddenly while a certain number of AES logs on to a GES operating to the satellite. When it happens, each AES loses P channel signal and waits for its recovery. But, if it lasts for more than 10 seconds, each AES starts a log-on procedure to a GES operating to an alternative satellite (5.2.18, SDM). (To be more precise, each AES starts a log-on procedure to another GES operating to the same satellite first, but in vain because of the failure of the satellite. Then, each AES starts a log-on procedure to a GES operating to another satellite.) The problem is that this occurs almost simultaneously. That is, all AESs start to send a log-on request to the GES within a very short period. The channels used for log-on are congested and data transmission loss or delay occurs. It may lead to a large log-on delay or even a log-on failure.

- Simulation Condition

3.1 Simulation software

The ASET model developed by Mayflower Co. is used for the computer simulation. This ASET model works on the OPNET, a network simulation software. They are installed in an EWS. The simulation software was once used to validate the AMSS Draft SARPs.

3.2 Parameters for Simulation

Table 1 lists the parameters set for simulation. We focus on one GES operating to one alternative satellite. Ordinarily, a certain number of AES logs on to the GES and conduct ADS/CPDLC communications. But, we assume no AES logs on to the GES at the start of the simulation for simplicity. So, the result would be somewhat conservative. Figure 2 shows the log-on sequence described in SDM. Specified number of AES (that is assumed to have logged on to a GES operating to a disabled satellite) begins transmission of a log-on request to the GES operating to alternative satellite on R channel at random within 1minute from the start of simulation. The AES that has completed a log-on procedure restarts ADS report transmissions on T channel immediately and repeats them every 640 seconds (about 10 minutes).

One Psmc+d channel (600bps) is allocated to the GES for forward link. The number of Rsmc+d channel(600bps) is changed between 1 and 4 for each simulation. One T channel (10500bps) is allocated for transmission of ADS report. In the simulation, transactions of CPDLC are neglected assuming ADS report transmissions are dominant in the data link.

RGCSP has specified the requirement for ADS transmission interval for 30 NM lateral separation(RNP 4) is 21minutes 30 seconds. The ADS transmission interval is assumed to be about 10 minutes to meet the requirement by logging on to another GES within 10minutes even if one ADS report is lost due to satellite failure.

- Simulation Result

4.1 Percentage of Logged-on AES in 10 minutes

Figure 3 shows the percentage of AES that has completed a log on within 10 minutes after a satellite had failed. The curves are shown for various number of R channel between 1 and 4. The abscissa represents the total number of AES that tries to log on to the GES. When the number of R channel is 1(one), the percentage of logged-on AES is about 80% for 20 AESs. As the number of AES increases, the percentage of logged-on AES decreases. It is caused by congestion on R and P channels. Since a lot of log on request are transmitted within 1 minute, collision of transferred data occurs on R channel and those requests are lost. When a log on request is lost, it is retransmitted after a specified time (timeout). This process is repeated four times. Even on P channel, congestion on the channel causes transmission delay or loss due to queuing or buffer overflow. Therefore, as shown in Fig.3, the percentage of logged-on AES increases as the number of R channel increases. But, the case of 3 R channels is the same as that of 4 R channels. This is caused by congestion on P channel.

Figure 4 also shows the percentage of AES that has completed a log on within 10 minutes after a satellite had failed. In this case, the number of P channel is 2. Comparing this with Fig.3, it is found that the percentage of logged-on AES in Fig.4 is higher than that in Fig.3 for each number of R channel. Especially, the percentage for 4 R channels increases than that for 3 R channels by the decrease of congestion on P channel.

4.2 Change in Number of Logged-on AES with time

Figure 5 shows the number of logged-on AES with time for one P channel and one R channel. The curves are shown for various numbers of AES. For 10 AESs, all AES complete a log on within 10 minutes. But, for 20 AESs, it takes more than 10 minutes for all AES to complete a log on. For 40 AESs, it takes more than 50 minutes. For 50 AESs or more, all AES don’t complete a log on within 1 hour.

Figure 6 shows the number of logged-on AES with time for one P channel and 2 R channels. Since the number of R channel doubles, the number of logged-on AES is larger than the previous case. For 50 AESs, it takes about 30 minutes for all AESs to complete a log on. For 80 AESs, it takes 50 minutes. For 100 AESs, all AES don’t complete a log on within 1 hour.

Figures 7 and 8 show the number of logged-on AES with time for one P channel and 3 R channels, and for one P channel and 4 R channels, respectively.  For 80 AESs or more, it takes more than 50 minutes for most AESs to complete a log on.

- Discussion

From the simulation result, the followings are found.

  - For one P channel and one R channel, the number of AES that can log on to the GES in about 10 minutes is less than 20. By increasing the number of R channel up to 3, it comes to about 45. But, even if the number of R channel is increased further, there is no further improvement.

  - When the number of P channel is increased to 2, the number of AES that can log on to the GES in about 10 minutes comes to about 80 for 4 R channels.

  - The number of logged-on AES increases with time for all cases. The larger the number of AES that tries to log on to the GES is, the larger the log-on delay is and the larger the number of AES that fails to log on.

Considering that hundreds of AES will operate with a satellite in the near future, many AESs may fail to log on to an alternative GES when the satellite becomes disabled.

5. Conclusion

The simulation showed the possibility that many AESs may have to wait for a log-on completion for a long time or may fail to log on to a GES operating to an alternative satellite at the event of satellite failure. Although the possibility has not been considered so far, it is a serious problem to acquire flight safety. It is important to find a way to avoid such situation.

Table 1  Parameters for Simulation

| Parameters | Values, etc. |
| --- | --- |
| Satellite and GES | 1 Satellite 1 GES |
| Channel | 1 or 2 P channel(s) (600bps) 1 to 4 R channel(s) (600bps) 1 T channel (10500bps) |
| Application | ADS |
| ADS report length | 95 octet |
| ADS transmission interval | 640 seconds |
| Time for first log-on request transmission | Less than 1 minute |

Fig.1 Simulation Concept

Fig.2 Log-on Sequence

Fig.3 Percentage of Logged-on AES in 640 seconds after simulation start

(1 Psmc+d channel)

Fig.4 Percentage of Logged-on AES in 640 seconds after simulation start

(2 Psmc+d channels)

Fig.5 Number of Logged-on AES with Time

(1 Psmc+d cahnnel and 1 Rsmc+d channel)

Fig.6 Number of Logged-on AES with Time

(1 Psmc+d cahnnel and 2 Rsmc+d channels)

Fig.7 Number of Logged-on AES with Time

(1 Psmc+d cahnnel and 3 Rsmc+d channels)

Fig.8 Number of Logged-on AES with Time

(1 Psmc+d cahnnel and 4 Rsmc+d channels)