AMCP WG-M/3-WP06

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

WORKING GROUP M

Third Meeting

Tianjin, China, 10 – 18 December 2001

Agenda Item 3:  	HFDL Update, Concerns from Prof. Zhou Zhuoren

Additional Comments on

the Manual on Detailed Technical Specifications for the HFDL

( Doc 9741-AN/962, Part II )

Prepared by Zhou Zhuoren

Civil Aviation University of China

SUMMARY

This Working Paper provides some proposals to update the Doc 9741-AN/962.

Additional Comments on

the Manual on Detailed Technical Specifications for the HFDL

( Doc 9741-AN/962, Part II )

1 Chapter 2, Physical Layer

1.1 In both of the Table II-2-3 and Table II-2-4 (Doc 9741-AN/962, Part II, page II-2-3), the fourth column should be modified as follows :

|  | Code rate |  |
| --- | --- | --- |
|  | 36 1611/2 |  |
|  | 36 1611/2 |  |
|  | 36 1611/2 |  |
|  | 36 1631/4 |  |

2 Chapter 3, Link Layer

2.1 The eighth cell of the first column of the Table II-3-1 (Doc 9741-AN/962, Part II, page II-3-2) should be modified as follows :

|  | 271316-630 octets |  |
| --- | --- | --- |

3 Chapter 4, Subnetwork Layer Protocols and Services

3.1 Paragraph 4.3.7.2.6 (Doc 9741-AN/962, Part II, page II-4-4), the text in the parentheses should be modified as follows :

(see 4.3.8.32)

3.2 Paragraph 4.3.7.3.2 (Doc 9741-AN/962, Part II, page II-4-4), the eighth line, HFSNDPG should be modified as HFSNDPX .

3.3 Paragraph 4.3.7.3.2 (Doc 9741-AN/962, Part II, page II-4-4), the twelfth line, SNDPX should be modified as HFSNDPX .

3.4 Table II-4-1, HFNPDU type identifier encoding (Doc 9741-AN/962, Part II, page II-4-17)

a) The original sixth line is

| 000010 | CONNECTION REQUEST, NO CALLING NSAP ADD., NO CALLED NSAP ADD., WITH FACILITY FIELD, NO RESTRICTION ON RESPONSE |
| --- | --- |

It should be modified as follows :

| 000010 | CONNECTION REQUEST, NO CALLING NSAP ADD., WITH CALLED NSAP ADD., NO FACILITY FIELD, NO RESTRICTION ON RESPONSE |
| --- | --- |

b) The original seventh line is

| 000011 | CONNECTION REQUEST, NO CALLING NSAP ADD., NO CALLED NSAP ADD., WITH FACILITY FIELD, NO RESTRICTION ON RESPONSE |
| --- | --- |

It should be modified as follows :

| 000011 | CONNECTION REQUEST, NO CALLING NSAP ADD., WITH CALLED NSAP ADD., WITH FACILITY FIELD, NO RESTRICTION ON RESPONSE |
| --- | --- |

c) The original 25th line is

| 100000 | CONNECTION REQUEST, NO CALLING NSAP ADD., NO FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

It should be modified as follows :

| 100000 | CONNECTION REQUEST, NO CALLING NSAP ADD., NO CALLED NSAP ADD., NO FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

d) The original 26th line is

| 100001 | CONNECTION REQUEST, NO CALLING NSAP ADD., WITH FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

It should be modified as follows :

| 100001 | CONNECTION REQUEST, NO CALLING NSAP ADD., NO CALLED NSAP ADD., WITH FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

e) The original 27th line is

| 100010 | CONNECTION REQUEST, NO CALLING NSAP ADD., WITH FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

It should be modified as follows :

| 100010 | CONNECTION REQUEST, NO CALLING NSAP ADD., WITH CALLED NSAP ADD., NO FACILITY FIELD, WITH RESTRICTION ON RESPONSE |
| --- | --- |

3.5 Table II-4-3 (Doc 9741-AN/962, Part II, page II-4-18), the second line of the left column, there is no definition on HFNDP , perhaps it should be modified as HFSNDP .

3.6 Table II-4-8 (Doc 9741-AN/962, Part II, page II-4-21), the first cell of the left column should be modified as :

|  | HFSNDPXDU received from remote HFSNDPX |  |
| --- | --- | --- |

3.7 Table II-4-10 (Doc 9741-AN/962, Part II, page II-4-23), in the note 1 and note 2, HFND should be modified as HFSND .

3.8 Table II-4-13 (Doc 9741-AN/962, Part II, page II-4-25), the seventh line of the middle column should be modified as :

|  | DCE INCOMING CALL |  |
| --- | --- | --- |

3.9 Table II-4-14, DCE actions at reset, interrupt, and flow control states (Doc 9741-AN/962, Part II, page II-4-26)

a) The state definition of j1 should be modified as :

|  | DTCE INTERRUPT READY |  |
| --- | --- | --- |

b) The state definition of j2 should be modified as :

|  | DTCE INTERRUPT SENT |  |
| --- | --- | --- |

c) The state definition of f1 should be modified as :

|  | DTCE RECEIVE READY |  |
| --- | --- | --- |

d) The state definition of f2 should be modified as :

|  | DTCE RECEIVE NOT READY |  |
| --- | --- | --- |

3.10 Table II-4-16 (Doc 9741-AN/962, Part II, page II-4-27), note 6, second line, the text behind the comma should be modified as :

and discard indicates that the received packet is to be cleaned from the buffers.

3.11 Table II-4-17 (Doc 9741-AN/962, Part II, page II-4-28), note 5, the text “d = diagnostic code” should be modified as “D = diagnostic code”.

3.12 Table II-4-18, DTE effect on DCE reset states (Doc 9741-AN/962, Part II, page II-4-29)

a) When packet received from DTE is RESET REQUEST, the effect on DCE at FLOW CONTROL READY d1 state should be modified as :

A = NORMAL

(8.2)

DS = d2

(forward)

b) In the note 2, “AES” should be deleted.

3.13 Table II-4-20, DTE effect on DCE flow control transfer states (Doc 9741-AN/962, Part II, page II-4-31)

a) The cell about the state g1 should be modified as follows :

|  | DCTE RECEIVE READY g1 |  |
| --- | --- | --- |

b) The cell about the state g2 should be modified as follows :

|  | DCTE RECEIVE NOT READY g2 |  |
| --- | --- | --- |

c) In the note 6, for consistent, P(R) should be modified as PR; or contrariwise, all PS be changed to P(S), and all PR be changed to P(R).

d) Recommendation: It is better to provide the definitions for PS, PR, RR, and RNR.

3.14 Table II-4-22 (Doc 9741-AN/962, Part II, page II-4-32), the fourth line of the left column should be modified as follows :

CALLEAR INDICATION

3.15 Figure II-4-1, The HFSNL functions and the ATN subnetwork (Doc 9741-AN/962, Part II, page II-4-34)

The text in the left_top triangle cell of the HFDL aircraft station subsystem should be modified as :

HFSND

(HFSNDPGA)

3.16 Figure II-4-2, HFSNDPX entities (Doc 9741-AN/962, Part II, page II-4-35)

The text in the circle cells of the two HFDL aircraft station subsystems should be modified as :

HFSNDPGA

entity

3.17 Figure II-4-6, Connection released HFNPDU format (Doc 9741-AN/962, Part II, page II-4-37)

a) The original octet 1 is

|  | 0 | 0 | 0 | 0 | 1 | x | x | x |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

It should be modified as follows :

|  | 0 | 0 | 0 | 1 | 0 | 0 | x | 0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

b) The original octet 4 is

|  | Clearing cause* |  |
| --- | --- | --- |

It should be modified as follows :

|  | Clearing cause |  |
| --- | --- | --- |

i.e. the star should be deleted, because the clearing cause field is necessary, and there is no indicator bit for indicating the clearing cause field present.

3.18 The title of the Figure II-4-15 (Doc 9741-AN/962, Part II, page II-4-41) should be modified as :

Throughput class negotiation (TCN) facility field format

4 Attachment 2 to Part II, SIGNAL UNIT FIELD DESCRIPTIONS, CODING AND DESIGNATIONS

4.1 FIELD DESCRIPTIONS (Doc 9741-AN/962, Part II, page II-A2-1)

a) The description of item number 50 should be modified as follows :

UDR  UPLINK DATA ROUATE

b) The description of item number 53 should be modified as follows :

SPDU VERSION

4.2 Item 12, TDMA FRAME OFFSET (Doc 9741-AN/962, Part II, page II-A2-3)

Following original text

Code   Function

0	  Offset relative to a master TDMA

frame starting at exactly at 0000 UTC

should be modified as :

Code   Function

0 - 12  Offset relative to a master TDMA

frame starting exactly at 0000 UTC

4.3 Item 21, LONGITUDE (Doc 9741-AN/962, Part II, page II-A2-4)

The last sentence of the text of item 21 should be modified as :

Positive numbers represent eastern latitudes longitudes, and negative values represent western latitudes longitudes.

4.4 Item 24, HFNPDU TYPE (Doc 9741-AN/962, Part II, page II-A2-4)

The eighth line of the item 24 should be modified as follows :

FFh D5h    Frequency data downlink (optional)

4.5 Item 59, K (Doc 9741-AN/962, Part II, page II-A2-9)

The original text is as follows :

59. K

A 4-bit field indicating the transmit window size for outstanding packet acknowledgements. The value is cal-culated as the transmit window size +1. Therefore the value can range from 1 to 16. The value is only used in RLS transmissions.

This text implies somewhat confusion. Who’s value can range from 1 to 16? Is it the K’ s value? If so, then it means that: the value of K can range from 1 to 16; however, the value is calculated as the transmit window size +1, then the transmit window size can range from 0 to 15. Is this the original intention? What’s the meaning about “transmit window size = 0”?

On the other hand, when we refer to the octet 6 in Figure II-A1-8 (Doc 9741-AN/962, Part II, page II-A1-9), as follows :

|  | 0 | 0 | 0 | 0 | k (transmit window size) |  |
| --- | --- | --- | --- | --- | --- | --- |

The bits 4 to 1 indicate the k (transmit window size). It does mean that the k (transmit window size) can range from 0 to 15. Does the k in Figure II-A1-8 equal to the K in item 59 above?

In order to resolve these confusions, if the original intention is k = K , and the transmit window size should range from 1 to 16, then we can make following modifications:

a) The item 59 should be modified as follows :

59. k

This is the transmit window size specified by the HFDL ground station subsystem in the log-on confirm and log-on resume confirm LPDU for outstanding packet ack-nowledgements. The value of k can range from 1 to 16. It is only used in RLS transmissions. The four least significant bits of the octet 6 in the log-on confirm and log-on resume confirm LPDU is equal to k – 1. Such as, if all the four bits are set to 0, then k=1; if all the four bits are set to 1, then k=16.

b) The octet 6 in the log-on confirm and log-on resume confirm LPDU should be modified as follows :

|  | 0 | 0 | 0 | 0 | k(transmit window size) -1 |  |
| --- | --- | --- | --- | --- | --- | --- |

------------------------------------------------