AMCP WG-M/3 WP22

VDL 2 Frequency planning results

Bertrand Desperier bertrand.desperier@eurocontrol.int  (EUROCONTROL EEC/Bretigny)

Patrick Delhaise patrick.delhaise@eurocontrol.int (EUROCONTROL EATMP DIS/COM)

(version 1.2)

Abstract

Operating VDL Mode 2 requires the allocation of 25 kHz-channels inside the aeronautical VHF band.

With VDL 2, D8PSK modulation is inserted in this band for the first time. Considering the scarcity of VHF channels, EUROCONTROL developed a general interference measurement method in 1999 to cover operation of VDL Mode 2 adjacent to voice-ATC and OPC channels, ACARS or other VDL channels. Once granted by AMCP, the method has been extensively applied among others in EUROCONTROL labs (EEC/Bretigny); airborne and  ground-station radios of analogue and digital types including even General Aviation radios have been involved in tests. Finally frequency ‘protection criteria’ (the channels separation rules) have been proposed for review by ICAO for the interference cases involving VDL 2 and DSB-AM.

Those criteria were accepted  in  ICAO AMCP Sept. 2001 meeting and are considered by ICAO FMG EUR that currently undertakes VDL 2 deployment across Europe.

The present paper summarises the contributions to AMCP WGB since 1999, describing the general interference testing method and results; it introduces the frequency plan proposed to ICAO FMG EUR.

# Introduction

As proposed by Eurocontrol in reference [1], the test program presented in this paper consists of testing VDL2 vs. VDL2 or DSB-AM interferences. The test methods used at EEC are recalled in table 1.

| Vs. | Interference Source |
| --- | --- |
|  | DSB-AM | VDL 2 |
| Victim | DSB-AM | - | Method 2 |
|  | VDL 2 | Method 3 | Method 3 |

Table 1: Test methods used for VDL2 interference testing as defined at ICAO AMCP.

This paper is organised as follows:

- In § 2 an overview of the test procedures and frequency planning methodology is given.

- The main interferences scenarios are depicted in § 3

- Tests results and frequency planning are presented in § 4.

- Conclusions and implementation of results in ICAO EUR region are given in § 5

# Overview on the method

The general method, the relevant test parameters, and the different radio types involved are presented in this paragraph.

## The method in a nutshell

Test methods 2 and 3 are based on the measurement of the capability of a radio receiving a desired signal at a specified power level (i.e. minimum signal level at the receiver input) to reject an interfering signal present on a different adjacent channel. The interfering signal maximum power beyond which annoyance becomes unacceptable to the user [1], is noted for each adjacent channel. The adjacent channel rejection (ACR) capability of the victim radio for the current channel under test is then calculated.

The Adjacent Channel Rejection ratio is the ratio in dB between the maximum adjacent interfering signal level defined above, and the desired signal level.

The unacceptable interference thresholds are specific to the victim communication type:

- VDL2 to DSB-AM interference (method 2):

- Measurement of signal to pulse (S/P) ratio superior or equal to 6 dB

- Measurement of a degradation of the signal plus noise to noise (S+N/N) of 6 dB.

- Observation of squelch break without any victim signal.

- VDL2 or DSB-AM to VDL2 interference(method 3):

- Measurement of an uncorrected Bit Error Rate (BER before FEC) superior or equal to10-3.

## Signal characteristics in operational worst cases.

The parameters used during the tests for deriving frequency planning criteria have been fixed together with AMCP WG B to represent the considered operational worst case :

- Minimum victim signal at the antenna input :
 respectively (-82) dBm (airborne receiver)  and  (-93) dBm (Ground receiver)

- VDL2 closest interferer channel load : 2%.

- VDL2 Victim channel load : 20%.

These loads are simulated by frames of size and interval also fixed by AMCP.

## Radios tested

A set of 8 DSB-AM radios has been tested as victim of VDL 2 interference, consisting of :

-      3 airborne digital radios (Thales EVR 750, Thales EVR 716, RC 900B),

- 2 airborne analog radios (RC700, RC618M3),

- 1 ground digital radio (Telerad 9000)

- 2 general aviation radios (Dittel, Becker RT5202)

The test set also included 3 VDL2 radios with 2 airborne  (Thales EVR 750, RC920) and 1 ground radio set (Telerad 9000).

It was obviously impossible to test every combination of 3 radios to represent transmitter, receiver, and interferer roles, although many combinations have been covered in order to get a large base of results.

## Frequency planning methodology

As outlined in [5] the protection distance can be calculated for method 2 and 3 as follows when propagation occurs in free space:

Formula 1. Formula for protection distance calculation based on total power

This formula derives from the following figure describing the flow of desired and undesired signal in an interference scenario until the victim receiver input.

Figure 1. Reference interference scenario based on total power

It has to be noted that, due to the definition of the ACR given above, the D/U total power (Desired to undesired signal total power ratio) in formula 1 is equal to the opposite of the measured ACR.

The free space propagation model is applied since study revealed it represents the worst operational case relevant for developing the VDL 2 frequency planning criteria. Further explanations have been given in [6] and were granted by AMCP WGB.

# Frequency planning scenarios

In [1] the main critical interference scenarios impacting frequency planning criteria were defined by AMCP as:

##### Scenario 1: Aircraft on the Ground vs Aircraft on the Ground

Two aircraft located at adjacent gates communicating on different frequencies with an assumed physical separation of 50 meters (170ft) between antenna.

- Scenario 2: Aircraft on the Ground vs Ground Station

One aircraft on gate communicating on one frequency and a ground station communicating with another aircraft where it is assumed that the minimum physical separation between antenna is somewhere between 50 & 100 meters (170 – 340ft)

##### Scenario 4: Aircraft in Flight vs Aircraft in Flight

Two aircraft in flight flying parallel tracks communicating on two different frequencies with an assumed vertical physical separation of 600 meters (2,000ft) between the antenna.

However, as detailed in [3] there are several concurrent indications that in scenario 1 and 2 the assumed physical separation of only 50 m was too stringent to accommodate the protection of minimum signal power of –82 dBm and –93 dBm. In [3], it was then shown that the SARPs compliant protection distance for -82 dBm (resp. –93 dBm) was 210 m (resp. 750 m).

# Test results and development of separation criteria

## VDL Mode 2 interference to DSB-AM

### Comments on ACR results of VDL Mode 2 interference to DSB-AM

The main observations issued from the performed tests were as follows:

- The ACR obtained with the S/P criteria across the test campaign were at most in the range of these derived from the S+N/N criteria, and usually were smaller (i.e. worse). Due to this observation, S/P criteria was often the single criteria needed for tests.

- The squelch breaking has been checked for all the airborne radios involved in testing. On all radios, from the second adjacent channel on, the squelch break was only observed at a very high interfering power (e.g. over 0 dBm). Therefore it was concluded that squelch breaking was not the dimensioning criteria for VDL 2 / AM frequency planning design.

- In the case of the ground station, the ACR presented was the ACR of the receiver itself, not taking into account the drastic improvements in interference rejection which may be obtained through the addition in the ground station of a cavity filter and a quartz filter. Those were further discussed in [3].

### Discussion on protection distances for VDL Mode 2 interference to DSB-AM

#### Air frequency planning scenario (scenario 4)

The required protection distance in scenario 4 is 600 m. Results shows that this distance is reached at the 2nd adjacent channel for the test configurations involving airborne radios.

Therefore it was proposed to allocate a DSB-AM channel in the same service volume of a VDL mode 2 channel with 1 guard-band channel when scenario 4 was considered.

#### Ground frequency planning scenarios

The ground frequency planning scenario involves scenario 1 and 2.

Scenario 1 (Aircraft on the Ground vs Aircraft on the Ground)

- The problem of finding for the worst case a relevant pair of minimum protected field strength / distance of interference had been discussed in details in [3]. Experimental and operational evidence proved that protecting a minimum power of–82dBm with an interfering station at 50m was far too stringent and  not compatible with SARPS for DSB-AM radios even. It was concluded in [3] to use the reference distance of 210m which was derived from DSB-AM receiver SARPS.  Inspection of measurements results has shown that this distance is reached at the 5th adjacent channel for the tests involving airborne radios.

Therefore when scenario 1 was considered for VDL2 to DSB-AM interferences, 4 guard-band channels were recommended.

Scenario 2 (Aircraft on the Ground vs Ground station)

- It was first noted that the rejection capacity or ACR of the ground station measured at –93dBm was at least comparable to ACR of other radio types without additional cavity and/or quartz filter. But the 11 dB difference between victim signal levels (–93dBm requested for ground-station and –82dBm for airborne radio) directly translates into a drastic increase of protection distance, as may be seen in formula 1.

- Similarly to scenario 1 above, the problem of fixing the worse realistic combination of minimum protected field strength/distance from interference also appeared here. In line with scenario 1 argumentation and as discussed in [3], for the minimum field strength of  (-93dBm) to be protected, it was recommended to use the reference distance of 750 m derived from SARPS.

- Large improvements are possible for ground-stations, linked to the flexibility in their location choice, and to the higher sensitivity and rejection performance they present as they operate at a fixed frequency.

- Looking at their measurements results and especially filters capabilities, it appeared easily possible to  accommodate interference on a ground station within the first few channels in the range of proposed protection distance.

This meant that scenario 1 was finally more stringent than scenario 2 to fix frequency planning criteria in the ground interference scenario and the 4 guard-band channels protection proposed for scenario 1 were also sufficient for scenario 2.

- This proposal was in accordance with current frequency planning criteria for ACARS, since in Europe ACARS is fielded at the top of VHF band with a 4 to 5 channels guard-band to the first protected operational VHF channel. As the required protection distances for ACARS interference are much larger than for VDL mode 2, as also predicted by industry reports (e.g. [4]), such a configuration would further be safe for VDL mode 2.

In conclusion it was proposed to allocate a DSB-AM channel in the same service volume of a VDL mode 2 channel with a guard-band of 4 channels when the ground frequency planning scenario is considered.

## VDL 2 interference to VDL 2

### Comments on ACR results of VDL Mode 2 interference to VDL Mode 2

- As for DSB-AM ground receiver, in the case of the ground station the ACR measured is the ACR of the receiver not taking into account the interference rejection improvement available through addition of a cavity filter and of a quartz filter.

- The different combinations tested had shown a smaller dispersion of the measured ACR than in the case of VDL 2 to DSB-AM interference. This was due to the fact that the VDL 2 radios RF and signal processing unit design is more uniform.

- It was observed that the adjacent channel rejection of VDL mode 2 to VDL mode 2 is presenting a smaller variance and at same time higher values than VDL 2 to DSB-AM interference. Therefore frequency planning criteria for VDL 2 to VDL 2 interference revealed to be less constraining than VDL 2 to DSB-AM.

### Discussion on protection distances for VDL Mode 2 interference to VDL mode 2

#### Air frequency planning scenario

The ground frequency planning scenario is defined by scenario 4.

- The required protection distance in scenario 4 is 600 m. This distance is reached at the 2nd adjacent channel with a very large margin for the tests involving airborne radios.

Therefore it was proposed to allocate a VDL mode 2 channel in the same service volume as another VDL mode 2 channel with a single channel guard band when the air frequency planning scenario is considered.

#### Ground frequency planning scenarios

The ground frequency planning scenario involves scenario 1 and 2.

Scenario 1 (Aircraft on the Ground vs Aircraft on the Ground)

- The discussion of § 4.1.2.2 applies here as well. If the minimum field strength of –82dBm has to be protected, it is recommended as in [3] to use the reference distance of 210 m which may be derived from SARPs specifications. Observation of the results concluded that this distance was reached at the 2nd adjacent channel for the relevant test configurations.

Therefore 1 guard-band channel was recommended for scenario 1.

Scenario 2 (Aircraft on the Ground vs Ground station)

- The discussions of § 4.1.2.2 on the relevant pair of minimum power / interference distance and specific filtering techniques also applied here. It may be seen that the protection distance at the second adjacent channel, for the radio itself (without addition of cavity and/or quartz filters) is around 400 m, comfortably below the recommended 750 m reference distance; it would further get down to less than 100 m with the addition of dedicated filters.

- This meant that, for the same reason than in the case of DSB-AM ground station, scenario 1 became more stringent than scenario 2 to fix frequency planning criteria in the ground interference scenario and the 1 guard-band channel protection proposed for scenario 1 was also sufficient for scenario 2.

In conclusion it was proposed to allocate a VDL mode 2 channel in the same service volume of a VDL mode 2 channel with a guard-band of 1 channel when the ground frequency planning scenario was considered.

## DSB-AM interference to VDL 2

### Comments on ACR results and protection distance of DSB-AM interference to VDL 2

- Preliminary tests at EEC had already shown that interference of VDL 2 to DSB-AM would be more constraining in terms of frequency planning criteria than the reverse mechanism (DSB-AM to VDL2)

Therefore it had been proposed to adopt for this case the same frequency planning criteria as defined in § 4.1.2.2, concluding in 1 guard-band channel for air scenario and 4 guard-band channels for ground scenarios.

# Conclusions for VDL Mode 2 frequency planning and implementation case in EUR region.

This paper has presented the main results issued from EUROCONTROL study and experimental interference measurements  involving VDL Mode 2.

Those efforts were done in support of ICAO AMCP developing VDL 2 frequency protection criteria.

The results are summarised in the following table :

|  | Interference Source |
| --- | --- |
|  | DSB-AM | VDL 2 |
|  | Air | Gd | Air | Gd |
| Victim | DSB-AM | - | - | 1 | 1 |
|  | VDL 2 | 1 | 4 | 1 | 1 |

Table 4: 25 kHz guard-band channels required between different services.

Those criteria were accepted ²  in  ICAO AMCP WG B meeting in Sept. 2001.

ICAO FMG EUR was preparing for some years VDL deployment in EUR region; it is planned to stepwise deploy up to 4 VDL Mode 2 channels, and provide resource to continue evaluation of VDL Mode 4.

Therefore, EUROCONTROL presented in October 2001 a likely frequency plan as depicted in the following table (the picture presents only one of the interim steps):

| Highest aer. VHF Channels | Current (2001) | One interim possible step | Around 2010 |
| --- | --- | --- | --- |
| 136.625 | ATS | ATS | ATS |
| 136.650 | ATS | ATS | ATS |
| 136.675 | ATS | ATS | ATS |
| 136.700 | ATS | GB | GB |
| 136.725 | ATS | VDL4 | VDL4 |
| 136.750 | ATS | GB | GB |
| 136.775 | ATS | GB | VDL4 |
| 136.800 | OPC | GB | GB |
| 136.825 | OPC | ACARS a | VDL2 |
| 136.850 | OPC | GB | GB |
| 136.875 | OPC | GB | VDL2 |
| 136.900 | ACARS s | ACARS s | GB |
| 136.925 | ACARS a | GB | VDL2 |
| 136.950 | Exp VDL4 | GB | GB |
| 136.975 | VDL2 | VDL2 | VDL2 |

ATS :Protected Air traffic Services (voice)

ACARS s : SITA ACARS

ACARS a : ARINC ACARS

OPC : Operational Communications (Airlines voice channels)

GB : Guard Band channel

Around 2010, up to 4 VDL Mode 2 channels would be deployed with the required separations. Provision for two VDL Mode 4 channels is made, today assuming that deployment would be confirmed and that VDL 2 separation criteria would be applicable to VDL 4. ACARS resources are further maintained during the migration period to VDL Mode 2.

The first step towards 2010 proposes to protect from 2004 on the first VDL 2 channel, therefore re-allocating the two directly adjacent channels. (exper.VDL4 and ACARS).This goes along IATA plan carried out by EUROCONTROL on its behalf for regrouping its OPC channels in another OPC VHF sub-band.

Taking the proposal plan into account, ICAO FMG EUR decided to implement the first step with IATA involvement for OPC channels, requesting the Block Planning Meeting group to undertake a progressive clearing of all channels at 136.700 and beyond in view of the VDL deployment.

# Reference papers

[1] Meeting report of 9th working group B meeting of Aeronautical Mobile Communications Panel. Bretigny, France, 10th-13th July 2000.

[2] B. Roturier, Patrick Delhaise, Bertrand Desperier, “VDL Mode 2 test results and frequency planning criteria proposal” AMCP/WG-B, San Diego 15-23 January 2001

[3] Patrick Delhaise, Bertrand Desperier, B. Roturier “Proposed modifications to the ground-ground interference scenario” AMCP/WG-B, Montreal 29 Aug –07 Sept 2001.

[4] Stephen Leger, Jeff Kelly, David Scrivener, ARINC Inc., “VDL Mode 2 and ACARS Adjacent Channel Comparison”, RTCA SC-172, WG2/WP 298, 16 Nov. 1998.

[5] B. Roturier, Patrick Delhaise, “Some further explanations on EUROCONTROL proposed method to assess frequency planning criteria” AMCP/WG-B/IP 8-2; Rio de Janeiro, Jan. 2000.

[6] B. Roturier, Patrick Delhaise, Bertrand Desperier, “Ground-ground propagation attenuation applicability to VHF frequency planning criteria”, AMCP/WG-B, San Diego 15-23 January 2001.

- ² AMCP acceptation requires one final confirmation test : DFS delivered in last September audio samples of interference on one G.A. radio showing a discrepancy with other results. EUROCONTROL repeated the tests on the same radio but only results consequent with AMCP conclusions were observed. EUROCONTROL has invited DFS for running together a confirmation test and publishing the conclusions.

ANNEX  Measurements results

VDL2 to AM interference

VDL2 to VDL2 interference

DSB-AM to VDL2 interference