## AERONAUTICAL MOBILE COMMUNICATIONS PANEL

Working Group M

Brussels, Belgium

6th – 15th March 2002

## LIMITATION OF VDL MODE 4 OPERATIONS

## TO THE BAND 112-137 MHz

Prepared by:

Stephen Heppe, Steven Friedman and Prasad Nair

ADSI, Inc

- Issues to be accommodated

FM Compatibility.  Irrespective of current and future ITU-R allocation constraints for VDL Mode 4, assignments of frequencies below approximately 108.5 MHz should be avoided due to the potential for interference to low-cost FM receivers (ref AMCP/WG-M/4 WP03).

ILS Protection. The MOPS for ILS (RTCA/DO-195) provide guidance on interference immunity with regard to interfering VOR signals more than 98 kHz from the desired carrier, and interfering ILS signals more than 141 kHz from the desired carrier. The MOPS also provide guidance on spurious response for any signal in the band 108-137 MHz. Since guidance for all types of interfering signals is available at frequency separations larger than approximately 150 MHz from the ILS signal, but is unavailable at frequency separations less than approximately 150 kHz from the ILS signal, it may be necessary to provide a guard band of 150 kHz with respect to any ILS assignment in the local airspace. Given the limited number of possible ILS assignments, it may be infeasible to consider VDL Mode 4 assignments below 112.100 MHz.

Congestion In The Band Below 112 MHz. The band below 112 MHz is used for ILS and VOR, and is highly congested in many regions. Considering the impact of airborne transmissions in this band and the potential need for a large guard band around any VDL Mode 4 assignment in this band, it may be impractical to make any VDL Mode 4 assignments in the band below 112 MHz.

Lack of Operational Rationale for Assignments Below 112 MHz. The total number of required assignments for VDL Mode 4 in the VHF ARNS band is limited (at most two GSCs and several local channels), and these requirements can in principle be accommodated in the band above 112 MHz. There is no identified operational requirement for an assignment below 112 MHz.

Complexity of Design and Certification for Operation in the Band Below 112 MHz. The interaction between VDL Mode 4 and ILS has not been investigated. Certification issues below 112 MHz have not been investigated. New and unknown requirements may be identified, which may delay the introduction into service of VDL Mode 4.

- Recommendation

The members are urged to consider the foregoing information as a basis for adjustment of the lowest recommended operating frequency for VDL Mode 4 to 112 MHz (Annex 10, Volume 3, Paragraph 6.9.2.1.2).

# Footnotes

Spectrum planning criteria must be developed to verify the required guardband. These spectrum planning criteria may be developed in parallel with the international efforts leading to a modification of ITU-R Radio Regulations.

# Text boxes

# SUMMARY

VDL Mode 4 is currently specified to be capable of tuning to any of the 25 kHz channels from 117.975 MHz through 137 MHz, with a recommendation to support tuning from 108 MHz to 117.975 MHz. There are various constraints on possible assignments for VDL Mode 4 within the frequency bands 108-117.975 MHz. AMCP/WG-B has identified the general desirability of a limitation to the band above 112 MHz. This paper recommends that WG-M adopt this view and make a suitable adjustment to the recommendation in SARPs (Annex 10, Volume 3, Para. 6.9.2.1.2).