# Options to Modify SARPs Regarding VDL Mode 4 Operations

Either Above or Below 112 MHz

## Stephen Heppe/ADSI

OPTION 1: Modify Annex 10, Volume 3, Paragraph 6.9.2.1.2 defining recommendation on tuning range. In combination with the unmodified 6.3.5.1, this option looks forward to operation in the band 112-137 MHz and does not consider tuning below 112 MHz.

6.9.2.1.2	Recommendation.—A VDL Mode 4 transmitter/receiver should be capable of tuning to any of the 25 kHz channels from 112 MHz to 117.975 MHz.

OPTION 2: Modify Annex 10, Volume 3, Paragraph 6.3.5.1 defining specified error rate. In combination with the unmodified 6.9.2.1.2, this option recommends tuning down to 108 MHz but only recommends nominal performance down to 112 MHz.

6.3.5.1	Specified error rate. The specified error rate for Mode 2 operation shall be the maximum corrected Bit Error Rate (BER) of 1 in 104.  The specified error rate for Mode 3 operation shall be the maximum uncorrected BER of 1 in 103.  The specified error rate for Mode 4 operation shall be the maximum uncorrected BER of 1 in 104 on any assignable channel in the band 118 – 137 MHz.

6.3.5.1.1.	Recommendation.—A VDL Mode 4 receiver should achieve the specified error rate of 1 in 104 on any assignable channel in the band 112 – 117.975 MHz.

### OPTION 3: Modify Annex 10, Volume 3, para. 6.1.2, to include time-phased introduction of services in the band 108-117.975 MHz. Append the following new text:

6.1.2.4	Utilization of the band 108-117.975 MHz.  Channels in the band 112-117.975 MHz may be assigned immediately, subject to agreed spectrum planning criteria, following enabling changes in the Radio Regulations. Channels in the band 108-111.975 MHz may be assigned on the basis of a regional agreement, subject to agreed spectrum planning criteria, following a date prescribed by the Council giving a period of two years or more following approval of the regional agreement concerned.