AMCP WG M04  WP15

Proposed Changes to Annex 10, Volume V

(Presented by the Secretary)

4.1.2.2.3

Requirements for mandatory carriage of equipment specifically designed for VDL Mode 3 and VDL Mode 4 shall be made on the basis of regional air navigation agreements which specify the airspace of operation, frequency range in accordance with 4.2.7 when operating in the band 108-117.975 MHz and the implementation time-scales for the carriage of equipment, including the appropriate lead time

ADD 4.2.7

Frequencies for VDL Mode 4 facilities in the band 108-117.975 shall be selected in the following order:

a)	112-117.975 (137) MHz

b)	108-111.975 MHz in areas where requirements for VDL Mode 4 facilities can not be met in the frequency range 112-117.975 (137) MHz