AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

WORKING GROUP M

Fifth Meeting

Saint Petersburg, Russia, 19 - 23 August 2002

Proposed Updates to VDL Mode 3 Protocols to Harmonize with RTCA SC172

Presented by the U.S. Member

(Prepared by)

Rob Morgenstern

Center for Advanced Aviation System Development

The MITRE Corporation

SUMMARY

This Working Paper identifies a number of amendment proposals to align the VDL Mode 3 Technical Manual with work from manufacturers that has been documented in the RTCA VDL Mode 3 MASPS.

# Introduction

RTCA SC172 has recently forwarded revisions to the VDL Mode 3 MASPS and MOPS for considering by the Program Management Committee due to updates related to the evolvement of the U.S. Federal Aviation Administration's NEXCOM program.  This working paper proposes amendments to the Technical Manual to harmonize this document with the MASPS and MOPS.

# Proposed Amendments

2.1.	System Configurations 1V3D/1V2D

An operational scenario was raised with respect to surface operations for large airports, where there are large quantities of users with low traffic demands.  A similar need was potentially seen for super-high enroute sectors covering large areas.  As such, a concept was developed to provide a system configuration that could support at least 200 users within a User Group.  As such, the 1V3D/1V2D concept was devised whereby the user group uses the entire 25kHz channel for a single voice channel and a large data channel so that the entire 8-bit local identifier space could be utilized.  This provides up to 240 users for either system configuration.  This proposal has been simulated using a detailed OPNET protocol model (including ATN stack) to validate its performance.

Amendment Proposal

| Title: | 1V3D/1V2D System Configuration |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.2.5.1, 5.2.2.5.2, 5.2.4.1.1, 5.2.4.3.2, 5.4.2.1.1, 5.4.2.1.2 Tables 5-1, 5-3c, 5-3d, 5-3e, 5-4, 5-5, 5-6, 5-7b, B-2, B-6 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Need to support a voice and data capable system configuration that can support at least 200 simultaneous users that do not have a high data demand per user. |
| Background: | [Validation Details] Validated by inspection, analysis and simulation. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Implement a new 4-slot and 3-slot system configuration that supports a single voice channel with the remaining slots used for data. Utilize the entire 8-bit local address space for aircraft users to provide up to 240 users. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to implement the 1V3D and 1V2D system configurations and to harmonize with the VDL Mode 3 MASPS.

Modify Sections 5.2.2.5.1 and 5.2.2.5.2 as follows:

5.2.2.5.1 	Logical burst access channels. For configurations 4V, 2V2D, 3V, 3V1D, and 2V1D, VDL Mode 3 shall grant media access individually for each of up to 8 separate Logical Burst Access Channels (LBACs) numbered 1-8. A description of each LBAC for these cases is given by Table 5-5. For the 3T configuration, VDL Mode 3 shall grant media access individually for each of up to 18 separate LBACs numbered 1-18. A description for each LBAC for the 3T configuration is given by Table 5-2. For the 3S configuration, VDL Mode 3 shall grant media access individually for each of up to 10 separate LBACs numbered 1-10. A description for each LBAC for the 3S configuration is given by Table 5-3a). For the 2S1X configuration, VDL Mode 3 shall grant media access individually for each of up to 7 separate LBACs numbered 1-7. A description for each LBAC for the 2S1X configuration is given by Table 5-3b).  For the 1V3D configuration, VDL Mode 3 shall grant media access individually for each of up to 16 separate LBACs numbered 1-16. A description of each LBAC for the 1V3D configuration is given by Table 5-3d). For the 1V2D configuration, VDL Mode 3 shall grant media access individually for each of up to 12 separate LBACs numbered 1-12. A description of each LBAC for the 1V2D configuration is given by Table 5-3e).

Note.—  MAC cycles for each system configuration are shown labelled with each LBAC in the Implementation Aspects of this manual.

5.2.2.5.2	Burst access timing. The system configuration code provided in the M uplink burst (Appendix B, 2.1) shall be used by the aircraft stationin conjunction with the timing reference point to establish proper burst timing. For configurations 4V, 2V2D, 3V, 3V1D , and 2V1D, LBACs shall be established according to Table 5-1; for the 3T configuration, LBACs shall be established according to Table 5-2; for the 3S configuration, LBACs shall be established according to Table 5-3a); for the 2S1X configuration, LBACs shall be established according to Table 5-3b); for the 1V3D configuration, LBACs shall be established according to Table 5-3d); and for the 1V2D configuration, LBACs shall be established according to Table 5-3e). The timing reference point (TRP) shall be established per 5.2.4.1. The relative timings among the TRPs of different user groups for the various system configurations are shown in Table 5-3c).

Modify Section 5.2.4.1.1 as follows:

5.2.4.1.1	Primary timing reference. The aircraft station shall derive its primary timing from the received M uplink burst (LBAC 11 for 3T configuration, either LBAC 5, 7 or 9 for 3S configuration, either LBAC 4 or 6 for 2S1X, LBAC 9 for 1V3D, LBAC 7 for 1V2D, and LBAC 5 for other configurations) associated with its assigned user group and Ground Station Code. The timing reference point shall be established based on the centre of the first received symbol of the synchronization sequence at the antenna port of the M uplink burst associated with the user group assigned. VDL Mode 3 media access opportunities for transmitted bursts shall be set relative to this reference in terms of transmitted symbol periods as shown in Tables 5-1, 5-2 and 5-3.

Note 1.—  To remain in the normal timing state (TS1), an aircraft station should maintain its primary timing to within ± 1 symbol period of the correct time based on the position of the aircraft relative to the ground station. This timing tolerance is the basis for developing the timing state transition rules of  5.2.4.1.4 and 5.2.4.1.5. Refer to 5.2.3.1 for this timing accuracy requirement.

Note 2.—  The relative timings among the TRPs of the different user groups are as shown in Table 5-3c).

Modify Section 5.2.4.3.2 as follows:

5.2.4.3.2	Net entry request message. When directed by the LME (see Section 5.4), the aircraft MAC sub-layer shall transmit a Net Entry Request message. The MAC sub-layer shall attempt transmission in LBAC 1, 2, 3, 4, 5, 7, 9, 13, 15 or 17 for 3T configuration, LBAC 1, 3 or 7 for 2V2D configuration, LBAC 3, 5, 7, 11, 13, or 15 for 1V3D configuration, LBAC 3, 5, 9, or 11 for 1V2D configuration, and LBAC 1 for 4V, 3V, 3S, 2S1X, 3V1D and 2V1D configurations, when these LBAC channels are available for random access (RA) on a slotted aloha basis.

Modify Section 5.4.2.1.1 as follows:

5.4.2.1.1	Net Initialization. Before the link establishment procedure, the aircraft station shall initialize to initial timing state 0 (TS0) and set parameters CTC1, CTC2 and CTC3 to max(f-50, t). The aircraft station shall enter TS0 either at the end of the transmission of the Leaving Net message (for discrete-addressed operation) or upon receipt of a new tuning command at the radio (for non-discrete-addressed operation).  The first part of the link establishment procedure shall be the acquisition of the M uplink burst (LBAC 11 for 3T configuration, LBAC 5, 7 or 9 for 3S configuration, LBAC 4 or 6 for 2S1X, LBAC 9 for 1V3D configuration, LBAC 7 for 1V2D configuration, and LBAC 5 for other configurations) associated with the specified user group identifier. Upon receipt of two consecutive M uplink bursts containing the identical information (i.e. System Configuration, Squelch Window, Slot ID and Ground Station Code) in bits 5-8 of octet 2 and all of octet 3 of the uplink burst, the LME shall declare the net initialized and shall establish the net operating parameters based on the static information contained in bits 5-8 of octet 2 and all of octet 3. Configurations 3S and 2S1X shall be considered initialized when at least one of the wide area coverage slots provide two consecutive M uplink bursts containing the same information in bits 5-8 of octet 2 and all of octet 3. Upon net initialization, the aircraft VDL shall transition from TS0 to TS1.

Modify Section 5.4.2.1.2 as follows:

5.4.2.1.2	Net Entry. The net entry procedure shall begin with the aircraft station transmitting a Net Entry Request message following a successful net initialization. The transmission of the Net Entry Request message and the subsequent retransmission, if enabled, shall follow the procedures described in Appendix D. The Net Entry retransmission shall continue until a Net Entry Response message is received or the number of retransmissions reaches NL1. After NL1 retries (Table 5-10a)), the SN-SME shall be notified. If a Net Entry Response message is received, the aircraft station shall transmit a Poll Response message in the next MAC cycle. If the Net Entry Response message is of type “previous link preserved”, the aircraft TL3 timer (Table 5-10a)) shall be stopped.

Note.— All configurations that offer one or more data circuit(s) must support net entry (3V1D, 2V2D, 2V1D, 1V3D, 1V2D, and 3T). The voice only configurations (3V, 4V, 3S and 2S1X) may support net entry if discrete addressing is enabled by the ground user.

Modify Tables 5-3c, d, e, 5-4, 5-5, 5-6, 5-7b and B-2, as well as the title of Table 5-1 as follows:

Table 5-1.  LBAC timing offset values for configurations 4V, 2V2D, 3V, 3V1D and 2V1D

Table 5-3c).  Relative timing relationship for TRPsof different user groups for all system configurations

|  | Relative Timings Among TRPs of Different User Groups (Symbol Periods) |
| --- | --- |
| User Group ID | 4V | 3V1D | 2V2D | 3T* | 3V | 3S** | 2S1X*** | 2V1D | 1V3D**** | 1V2D**** |
| A | 0 | 0 | 0 | N/A | 0 | 0 | 0 | 0 | 0 | 0 |
| B | 315 | 315 | 315 | 0 | 420 | 420 | N/A | 420 | 0 | 0 |
| C | 630 | 630 | N/A | 0 | 840 | 840 | 840 | N/A | 0 | 0 |
| D | 945 | N/A | N/A | 0 | N/A | N/A | N/A | N/A | 0 | 0 |

*	For 3T configuration, Group IDs B, C and D are treated as one user group.

**	For 3S configuration, Group IDs A, B and C are treated as one user group.

***	For 2S1X configuration, Group ID’s A and C are treated as one user group.

****  For 1V3D and 1V2D configurations, Group IDs A, B, C, and D are treated as one user group.

Table 5-3d: LBAC Description and Timing for 1V3D Configuration

| LBAC # | Applicability | Description | Media Access Timing for Each LBAC Relative to Timing Reference Point (Symbol Periods) |
| --- | --- | --- | --- |
| 1 | Air only | M downlink poll response | -1260 |
| 2 | Air/Ground | V/D (voice) even frame | -1195 |
| 3 | Air only | M downlink ACK or RA | -945 |
| 4 | Air/Ground | V/D (data) even frame | -880 |
| 5 | Air only | M downlink ACK or RA | -630 |
| 6 | Air/Ground | V/D (data) even frame | -565 |
| 7 | Air only | M downlink ACK or RA | -315 |
| 8 | Air/Ground | V/D (data) even frame | -250 |
| 9 | Ground only | M uplink, Timing Reference Point | 0 |
| 10 | Air/Ground | V/D (voice) odd frame | 65 |
| 11 | Air only | M downlink ACK or RA | 315 |
| 12 | Air/Ground | V/D (data) odd frame | 380 |
| 13 | Air only | M downlink ACK or RA | 630 |
| 14 | Air/Ground | V/D (data) odd frame | 695 |
| 15 | Air only | M downlink ACK or RA | 945 |
| 16 | Air/Ground | V/D (data) odd frame | 1010 |

Table 5-3e: LBAC Description and Timing for 1V2D Configuration

| LBAC # | Applicability | Description | Media Access Timing for Each LBAC Relative to Timing Reference Point (Symbol Periods) |
| --- | --- | --- | --- |
| 1 | Air only | M downlink poll response | -1260 |
| 2 | Air/Ground | V/D (voice) even frame | -1142 |
| 3 | Air only | M downlink ACK or RA | -840 |
| 4 | Air/Ground | V/D (data) even frame | -722 |
| 5 | Air only | M downlink ACK or RA | -420 |
| 6 | Air/Ground | V/D (data) even frame | -302 |
| 7 | Ground only | M uplink, Timing Reference Point | 0 |
| 8 | Air/Ground | V/D (voice) even frame | 118 |
| 9 | Air only | M downlink ACK or RA | 420 |
| 10 | Air/Ground | V/D (data) odd frame | 538 |
| 11 | Air only | M downlink ACK or RA | 840 |
| 12 | Air/Ground | V/D (data) odd frame | 958 |

Table 5-4.  System configurations

|  | System Config. | User groups supported/ identifying time slots* | Services to each group | V/D slots assigned to each group |
| --- | --- | --- | --- | --- |
| Normal Range | 4V | 4/(A, B, C, D) | Dedicated voice circuit | A, B, C or D |
|  | 3V1D | 3/(A, B, C) | Dedicated voice circuit w/shared data circuit | A/D, B/D or C/D |
|  | 2V2D | 2/(A, B) | Dedicated voice circuit w/dedicated data circuit | A/C or B/D |
|  | 3T | 1/(A) | Demand assigned voice and data | B/C/D |
|  | 1V3D | 1/(A,B,C,D) | Dedicated voice circuit w/ dedicated data circuit | A/B/C/D |
| Long Range | 3V | 3/(A, B, C) | Dedicated voice circuit | A, B or C |
|  | 3S | 1/(A, B, C) | Dedicated voice circuit with 3 station diversity | A/B/C |
|  | 2S1X | 1/(A, C) | Dedicated voice circuit with 2 station diversity | A/C |
|  | 2V1D | 2/(A, B) | Dedicated voice circuit w/shared data circuit | A/C or B/C |
|  | 1V2D | 1/(A,B,C) | Dedicated voice circuit w/ dedicated data circuit | A/B/C |

*	The term “identifying time slots” is defined as the value in the Slot Number field in the Beacon2 word of the uplink M channel.

Table 5-5.  Logical Burst Access Channel (LBAC)descriptions for configurations 4V, 2V2D, 3V, 3V1D and 2V1D

| LBAC#* | Applicability | Description |
| --- | --- | --- |
| 1 | air only | M downlink burst used for poll response or Random Access (RA) |
| 2 | air, ground | V/D (voice) burst even TDMA frame |
| 3 | air only | M downlink burst used for ACK or RA even TDMA frame |
| 4 | air, ground | V/D (data) burst even TDMA frame |
| 5 | ground only | M uplink burst and timing reference point |
| 6 | air, ground | V/D (voice) burst odd TDMA frame |
| 7 | air only | M downlink burst used for ACK or RA odd TDMA frame |
| 8 | air, ground | V/D (data) burst odd TDMA frame |

* Used to identify burst opportunities in Table 5-1.

Note.—  For 4V and 3V only LBACs 1, 2, 5, and 6 apply, as shown in Table 5-1.

Table 5-6.  Access rules for M downlink

| Configu-ration | LBAC # | Utilization of LBAC |
| --- | --- | --- |
|  |  | RA | ACK |
| 4V, 2V2D, 3V, 3V1D and 2V1D | 1 | LBAC 5 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
|  | 3 | LBAC 4 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM* = 1 | LBAC 4 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 7 | LBAC 8 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 8 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
| 3T | 1 | Unconditional RA | No acknowledgement allowed |
|  | 2 | LBAC 11 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
|  | 3 | LBAC 11 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
|  | 4 | LBAC 11 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
|  | 5 | LBAC 6 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 6 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 7 | LBAC 8 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 8 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 9 | LBAC 10 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 10 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 13 | LBAC 14 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 14 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 15 | LBAC 16 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 16 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
|  | 17 | LBAC 18 in previous MAC cycle did not have an uplink V/D (data) burst Header segment with EOM = 1 | LBAC 18 in previous MAC cycle had an uplink V/D (data) burst Header segment with EOM = 1 |
| 3S | 1 | LBAC 5, 7 or 9 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
| 2S1X | 1 | LBAC 4 in previous MAC cycle did not request a poll response | No acknowledgement allowed |
| 1V3D | 1 | N/A (Poll Response only) | No acknowledgment allowed |
|  | 3 | LBAC 4 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 4 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 5 | LBAC 6 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 6 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 7 | LBAC 8 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 8 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 11 | LBAC 12 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 12 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 13 | LBAC 14 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 14 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 15 | LBAC 16 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 16 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
| 1V2D | 1 | N/A (Poll Response only) | No acknowledgment allowed |
|  | 3 | LBAC 4 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 4 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 5 | LBAC 6 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 6 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 9 | LBAC 10 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 10 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |
|  | 11 | LBAC 12 in previous MAC cycle did not have an uplink V/D (data) burst header with EOM=1 | LBAC 12 in previous MAC cycle had an uplink V/D (data) burst header with EOM=1 |

* Defined in 3.1.2 of Appendix B.

Table 5-7b).  Aircraft MAC service system parameters

|  |  | System Configuration |
| --- | --- | --- |
| Symbol | Parameter Name | 4V | 3V1D | 2V2D | 3T | 3V | 2V1D | 3S | 2S1X | 1V3D | 1V2D |
| RE | Net Entry Randomizer (Note 2) | 3 | 8 | 8 | 8 | 3 | 8 | 3 | 3 | 8 | 8 |
| RR | Reservation Request Randomizer (Note 2) | 3 | 8 | 8 | 8 | 3 | 8 | 3 | 3 | 8 | 8 |
| RL | Leaving Net Randomizer (Note 2) | 3 | 8 | 8 | 8 | 3 | 8 | 3 | 3 | 8 | 8 |
| WR | Reservation Request Delay (MAC cycle) | 1 | 2 | 2 | 2 | 1 | 2 | 1 | 1 | 2 | 2 |

Note 1.— RE, RR, RL and WR are system configuration dependent.

Note 2.— Units for RE, RR, RL are in number of available time slots.

Table B-2.  System configuration codes

| Code | System configuration |
| --- | --- |
| 0000 | 4V |
| 0001 | 3S |
| 0010 | 3V1D |
| 0011 | 2V2D |
| 0100 | 3T |
| 0101 | 3V |
| 0110 | 2V1D |
| 0111 | 2S1X |
| 1000 | 1V3D |
| 1001 | 1V2D |
| 1000-1111 | Spare |

Modify Table B-6 as follows:

Table B-6.  Reserved slot subfield encoding

| Code | Description |
| --- | --- |
| 0000 | No Reservation Information |
| 0001 | RACK |
| 0010 | Spare |
| 0011 | Spare |
| 0100 | Data Reservation (start in even B-slot) |
| 0101 | Data Reservation (start in odd B-slot) |
| 0110 | Data Reservation (start in even B-slot, skip D) |
| 0111 | Data Reservation (start in odd B-slot, skip D) |
| 1000 | Data Reservation (start in even C-slot) |
| 1001 | Data Reservation (start in odd C-slot) |
| 1010 | Data Reservation (start in even C-slot, skip D) |
| 1011 | Data Reservation (start in odd C-slot, skip D) |
| 1100 | Data Reservation (start in even D-slot) |
| 1101 | Data Reservation (start in odd D-slot) |
| 1110 | Voice Reservation (start in even D-slot) |
| 1111 | Voice Reservation (start in odd D-slot) |

Note:  	For non-3T configurations, use only the codes with the third bit set to 0.  For system configuration 2V2D, allowable values are 0000, 0001, 1000, 1001, 1100, and 1101.  For system configuration 3V1D, allowable values are 0000, 0001, 1100, and 1101.  For system configuration 2V1D, allowable values are 0000, 0001, 1000, and 10001. For configuration 1V3D the allowable values are 0000, 0001, 0100, 0101, 1000, 1001, 1100, and 1101. For configuration 1V2D the allowable values are 0000, 0001, 0100, 0101, 1000, and 1001.

2.2.	Minimum Polling Period

Concern was expressed by the aircraft integrators, based on experience certifying VDL Mode 2, about the duty cycle of emissions interfering with existing receivers on the aircraft.  Furthermore, for certification, the absolute worst case has to be tested, so it is desirable if implementations were planned to significantly exceed minimum requirements then specify the minimum requirements near the expected implementation.  This also affects the recommendation to coordination ground stations globally.  By elevated this to a requirement, the aircraft integrator does not have to worry about inter-slot interference from other ground stations, so the certification testing is eased.  This would allow the aircraft integrators to not have to test extreme circumstances that will never likely be implemented.

Amendment Proposal

| Title: | Minimum Polling Period |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.2.1.5, 5.4.2.4 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Concern was expressed by the aircraft integrators, based on experience certifying VDL Mode 2, about the duty cycle of emissions interfering with existing receivers on the aircraft. Furthermore, for certification, the absolute worst case has to be tested, so it was desirable to define minimum requirements that could provide some flexibility to aircraft integrators without unduly constraining their implementations. |
| Background: | [Validation Details] Validated by inspection, analysis and simulation. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Institute a minimum period for polling a particular aircraft to reduce an aircraft's transmission duty cycle and reduce co-site emissions. Also, the recommendation to coordinate ground stations is elevated to a requirement. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to implement a minimum polling period and to harmonize with the VDL Mode 3 MASPS.

5.2.2.1.5	External time reference interface. The VDL Mode 3 ground stations shall synchronize their station TDMA system timing clocks to a common absolute time standard. This external time source shall provide a timing strobe once per second on the second and a means to identify epoch boundaries. For purposes of providing epoch strobes, the external time source shall be aligned to universal coordinated time (UTC) on 6 January 1980 with no further leap second adjustments.

Note 1.— UTC is not easily usable as a time source for VDL Mode 3 because UTC requires leap second adjustments at irregular intervals.

Note 2.— GPS system time was aligned to UTC time on 6 January 1980, but now differs by an integral number of seconds. (A GPS receiver calculates GPS system time and provides conversion to UTC time by adding the appropriate number of leap seconds. This number is available as part of the GPS navigation message.) Any other absolute time source which is traceable to UTC without leap second adjustments is also suitable as an external time source for VDL Mode 3.

Note 3 — Synchronization of aircraft radios to a common external time source is not required for Mode 3 operation.

5.4.2.4	Link Maintenance. The ground LME shall periodically poll each aircraft participating in the net using the Poll Request message, no more frequently than once per 6 seconds. If the ground LME receives a Poll Response message it shall reset the Polling Reply Counter (NL2) to 0. Otherwise, the ground LME shall increment the Polling Reply Counter.

2.3.	Urgent Downlink Request

With the work of RTCA SC-198 looking at the operational context of the VDL Mode 3, some updates were deemed necessary to the Urgent Downlink Request feature to support human factors of the implementation.

Amendment Proposal

| Title: | Urgent Downlink Request |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.1.4.3.6, 5.4.2.1.2.1, 5.4.2.1.2.2, 5.4.2.1.2.3, 5.4.2.1.2.7, 8.2.4, 8.4.3.5, 8.4.3.5.1, Appendix B, 2.15 Table B-1, B-6, B-9; Figure B-12b |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Human factors issues related to Urgent Downlink Request operation require updates to the standard |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | No. |
| Amendment Proposal: | Require an explicit RACK for all UDRs so that the aircraft knows it has been received. Also, provide a means to indicate whether or not the ground system supports the optional capability. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following additions and modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix the implementation of urgent downlink request and to harmonize with the VDL Mode 3 MASPS.

Insert new section:

5.2.1.4.3.6	Supported Options Message.  The ground LME shall transmit the Supported Options message in response to the initial Poll Response of an aircraft entering the net.  The aircraft MAC sublayer shall provide the supported options information to the aircraft LME.

Note:   See Section 5.4.2.1.2.1 for LME actions and Table B-9 for options supported.

Modify the subsections of 5.4.2.1.2 as follows:

5.4.2.1.2.1	Upon receiving a Net Entry Request message, the ground shall check the aircraft ICAO address. If this address has been assigned a Local ID and the TL3 timer has not been started, the ground shall transmit the Net Entry Response message of type “previous link preserved.” When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response, contained within a Supported Options message, to the entering aircraft during the next MAC cycle. This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” indication if no data slots were requested.

5.4.2.1.2.2	If the aircraft ICAO address has not been assigned a Local ID, the ground shall assign the next available Local User ID to the requesting aircraft and the pending disconnect link table shall be examined. If the aircraft ICAO address is found in the table, the link status shall be reinstated, the TL3 timer shall be stopped, and the link port address shall be changed to the new radio station port address. The ground shall transmit the Net Entry Response message of type “previous link preserved”. When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response, contained within a Supported Options message, to the entering aircraft during the next MAC cycle. This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” indication if no data slots were requested.

5.4.2.1.2.3	If the aircraft ICAO address is not found in the table and a Local ID has been assigned, the ground shall transmit the Net Entry Response message of type “no previous link”. When the Poll Response message is received by the ground station, the ground station shall respond by sending a Reservation Response, contained within a Supported Options message, to the entering aircraft during the next MAC cycle. This message shall be either a reservation or a RACK if data slots were requested or a “no reservation” indication if no data slots were requested. If an aircraft receives a Net Entry Response message of type “no previous link”, it shall also form a join event message, as required by the supported network stack, and deliver it to the air router.

Insert new Section 5.4.2.1.2.7:

5.4.2.1.2.7	Supported Options. The final uplink in the net entry process includes the Supported Option message.  The aircraft LME shall enable or disable the options indicated in the message.  The options shall be as defined in Table B-9.

Insert New Section 8.2.4:

8.2.4	Urgent Downlink Request (UDR) Signaling.  The Voice Unit shall support signaling whereby the aircraft station can notify the ground station user of an urgent desire to access the voice channel, when the voice channel is otherwise occupied.

.

Insert new Sections 8.4.3.5 and 8.4.3.5.1

8.4.3.5	Urgent Downlink Request (UDR).  When the CTS indication is cleared and upon user command, the MAC sublayer shall formulate a Reservation Request M burst message (or Poll Response M burst message, as appropriate) setting the Voice Request field (Appendix B, Section 2.10.4) to 'Request Priority Access' and shall transmit the M burst message at the next available opportunity. The slots used for sending and retransmitting the urgent/priority message are chosen using the same rules that are used for making a data reservation request. The aircraft station will continue sending the message until it receives a RACK.

Note:  Sending of a Reservation Request with the Voice Signal field indicating ‘No Request’ is used to cancel pending Urgent Downlink Requests.

8.4.3.5.1	Urgent Downlink Request Not Supported.  If the Supported Options message or acknowledging RACK indicates Urgent Downlink Request is not supported, the aircraft radio shall provide an indicator for the user that the request has failed.  Further attempts to transmit Urgent Downlink Request shall be inhibited while the aircraft remains in that net.

Modify Table B-1 as follows:

Table B-1.  M burst messages

|  | Message ID | M bursts | Paragraph No. of this appendix |
| --- | --- | --- | --- |
|  | 0000 | Normal message | 2.2 |
|  | 0001 | Net entry response message (no previous link) | 2.3 |
| Uplink | 0010 | Net entry response message (previous link preserved) | 2.3 |
|  | 0011 | Next net command message | 2.4 |
|  | 0100 | Recovery message | 2.5 |
|  | 0101 | Handoff check message | 2.6 |
|  | 0110 | Spare |  |
|  | 0111 | Supported Options message | 2.15 |
|  | Identified by separate sync sequence | Net entry request message | 2.9 |
|  | 1000* | Reservation request message | 2.10 |
| Downlink | 1001* | Acknowledgement message | 2.11 |
|  | 1010* | Leaving net message | 2.12 |
|  | 1011-1111* | Spare |  |
|  | 1000** | 4-slot configuration poll response | 2.10 |
|  | 1001** | Spare |  |
|  | 1010** | 3-slot configuration poll response | 2.10 |
|  | 1011** | Spare |  |
|  | 1100** | 3T configuration poll response | 2.10 |
|  | 1101** | Spare |  |
|  | 1110** | Spare |  |
|  | 1111** | Next net ACK | 2.13 |

*	Identified by standard synchronization sequence defined in Annex 10 Volume III, Part I, Chapter 6.

**	Identified by special synchronization sequence for poll responses defined in Annex 10 Volume III, Part I, Chapter 6.

Modify Table B-6 as follows:

Table B-6.  Reserved slot subfield encoding

| Code | Description |
| --- | --- |
| 0000 | No Reservation Information |
| 0001 | RACK (UDR Supported) |
| 0010 | RACK (UDR Not Supported) |
| 0011 | Spare |
| 0100 | Data Reservation (start in even B-slot) |
| 0101 | Data Reservation (start in odd B-slot) |
| 0110 | Data Reservation (start in even B-slot, skip D) |
| 0111 | Data Reservation (start in odd B-slot, skip D) |
| 1000 | Data Reservation (start in even C-slot) |
| 1001 | Data Reservation (start in odd C-slot) |
| 1010 | Data Reservation (start in even C-slot, skip D) |
| 1011 | Data Reservation (start in odd C-slot, skip D) |
| 1100 | Data Reservation (start in even D-slot) |
| 1101 | Data Reservation (start in odd D-slot) |
| 1110 | Voice Reservation (start in even D-slot) |
| 1111 | Voice Reservation (start in odd D-slot) |

Note:  	For non-3T configurations, use only the codes with the third bit set to 0.  For system configuration 2V2D, allowable values are 0000, 0001, 1000, 1001, 1100, and 1101.  For system configuration 3V1D, allowable values are 0000, 0001, 1100, and 1101.  For system configuration 2V1D, allowable values are 0000, 0001, 1000, and 10001.

Insert a new Section 2.15 in Appendix B:

2.15 	Supported Options Message.  The Supported Options message shown in Figure B-12b), is used to indicate options that are supported by the current ground station. One Reservation Response field is included in this message, along with an Options field. Each Reservation Response field consists of 12 bits.  The Reservation Response field can signal the actual allocation of channel resources to the entering aircraft.  The Options field is a 12-bit field with each bit set to 1 to indicate a specific option is supported and 0 if not supported, as described in Table B-9.  Reserved bits are set to 0.

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID | Voice Signal | Aircraft ID (Poll) |
| 2 | Aircraft ID (Poll) (cont.) | System Configuration |
| 3 | Slot ID | Ground Station Code | Squelch Window |
| 4 | Reservation Response |
| 5 | Reservation Response (cont.) | Options |
| 6 | Options (cont.) |

Figure B-12b). M Uplink (Supported Options Message)

Table B-9. Options field

| Octet | Bit Number | Field |
| --- | --- | --- |
| 5 | 5 | Urgent Downlink Request |
| 5 | 6-8 | reserved |
| 6 | 1-8 | reserved |

2.4.	Timing Accuracy

There was confusion about the timing accuracies applicable during a particular timing state.

Amendment Proposal

| Title: | Timing Accuracy |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.2.1.2.1, 5.2.2.1.2.2 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | EDITORIAL |
| Problem description: | There was confusion about the timing accuracies applicable during a particular timing state. |
| Background: | [Validation Details] Validated by inspection, analysis, unit test and manufacturer data. |
| Backwards compatibility: | YES. |
| Amendment Proposal: | Clarify that TS1 can have one symbol error and TS2 and TS3 allow the 5ppm drift See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to loosen the frequency stability requirement and to harmonize with the VDL Mode 3 MASPS.

Insert new Sections 5.2.2.1.2.1 and 5.2.2.1.2.2:

5.2.2.1.2.1 Timing Accuracy (Timing State 1).  While in Timing State 1 (see Section 5.2.4.1.4) an aircraft radio’s slot timing error shall be less than 1 symbol period.

Note: The correct slot timing for an aircraft radio in TS1 is equal to that of its associated ground station plus an offset equal to the ground-to-air propagation time.

5.2.2.1.2.2 Timing Accuracy (Timing State 2 or 3).  While in Timing State 2 or 3 (see Section 5.2.4.1.4) an aircraft radio’s slot timing shall drift at a rate no greater than (5 ppm.

Note: This drift rate, in conjunction with an assumed maximum drift rate of (2 ppm for a ground station, provides the rationale for the timing rules specified in Section 5.2.4.1.

2.5.	Timing State operation

Clarification is provided to the Timing State operation to help explain how the various timing states function.  Particular attention is paid to TS3.

Amendment Proposal

| Title: | Timing State Operation |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.4.1.2, 5.2.4.1.5, 5.2.4.2, 5.2.4.2.2, 5.2.4.2.3, 5.2.4.3.4.1, 5.2.4.3.4.2, 5.4.2.1.1, 8.4.1.1 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | The timing state requirements were not well understood, so it is desirable to rework them for clarification. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | No. |
| Amendment Proposal: | Clarify alternate timing, timing state transition and voice operation in the various timing states. Also clarify TS3 operation. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix the timing state operation and to harmonize with the VDL Mode 3 MASPS.

Modify Section 5.2.4.1.2 as follows:

5.2.4.1.2	Alternate timing reference. When required by the procedures of 5.2.4.1.3 through 5.2.4.1.5, the aircraft station shall derive alternate timing in truncate timing state 2 (TS2) from alternate timing sources (ALTs). ALTs are poll responses (except in the 3T configuration) associated with the user group or another user group (if available) and M uplink bursts in slots other than the one controlling the aircraft radio’s user group received during that MAC cycle.

5.2.4.1.2.1  An aircraft radio in TS0 will accept ALT timing originating from a ground station, yet remain in TS0, if the ground station M uplink burst indicates the aircraft radio is tuned to a data slot of a voice and data system configuration.

5.2.4.1.2.2  An aircraft radio in TS0 shall accept ALT timing originating from a ground station.

5.2.4.1.2.3  This alternate timing shall be derived based on the first received symbol of the synchronization sequence of the received poll responses or uplink M bursts. The aircraft station shall accept timing from ALTs if they obey the following rule:

Tr < Ta + 0.04  CTC2  Ts

where Ta is the expected time of an ALT as determined by the aircraft radio’s clock, Tr is the actual time of arrival of the ALT with respect to the aircraft radio’s clock, Ts is the symbol period, and CTC2 is the current value of the CTC2 counter (defined in 5.2.4.1.3). If CTC2 is greater than 800, all ATS time updates shall be accepted. If the time is updated, CTC2 shall be reset to 0.

Modify 5.2.4.1.5 as follows:

5.2.4.1.5	Timing state transitions. When in TS1, an aircraft station in non-3T configurations shall transition through TS2 before entering TS3. An aircraft station in 3T configuration shall transition from TS1 through a non-transmit transition period before entering TS3. When in TS3, the aircraft station shall accept time from any ALT and enter TS2. Any aircraft station shall immediately revert to TS1 upon reception of a valid primary timing signal.

5.2.4.1.5.1	During a PTT event, no timing state transition (except for transition to TS0 in response to a new tuning command) shall occur until that PTT event is completed. For data transmissions, a timing state transition shall be delayed (except for transition to TS0 in response to a new tuning command) until the current message transmission is completed. In the event that an aircraft station is engaged in a PTT event and a data event (transmit or receive) simultaneously, the timing state transition shall be delayed until both events are completed.

Modify Section 5.2.4.2 and its subsections as follows:

5.2.4.2	Voice operation support. The aircraft station shall grant media access on a MAC cycle-by-MAC cycle basis based on the timing state and the voice signalling information received in the M uplink burst of the previous MAC cycle. The rules for media access shall be as described in Table 5-9. Furthermore, if Table 5-9 indicates 'Access', the MAC subnlayer shall determine if there was a V/D (voice) burst in the previous TDMA frame from another user.  If so, access shall be granted if the V/D (voice) header indicated an EOM; otherwise, the access shall be denied.

5.2.4.2.1	The MAC sublayer shall set the CTS flag for the Voice Unit (Section 8.4.3) when access is allowed; otherwise, the CTS flag is cleared.  The setting of the CTS flag for each TDMA frame shall coincide with the MAC timing associated with when the V/D (voice) burst is to be transmitted per Tables 5-, 5-, and 5- as appropriate.  The conditions of both the timing state and the signalling shall be met in order to be granted access in a given MAC cycle.  The aircraft station shall process received V/D (voice) bursts with correct Group ID while in timing states TS1 and TS2.

Note 1.—  Reception of voice in TS0 is not required.  Transmission of voice in TS0 is not permitted.

Note 2.—  Reception and transmission of voice in TS3 are specified separately in Section 5.2.4.2.2 TS3 Voice Operation.

5.2.4.2.2	The Voice Unit (Section 8 of these Technical Specifications) shall be notified of the timing state during each MAC cycle.

5.2.4.2.3	The maximum duration of an aircraft PTT event shall be limited to no more than 35 seconds (approximately 145 MAC cycles). Aircraft station shall automatically terminate the PTT event upon reaching this limit.

5.2.4.2.4	Any aircraft station transmitting a voice signal shall cease transmitting if it receives a valid uplink M channel signal with the Voice Signal code set to any value other than 012 (occupied). (See 2.1.4 of Appendix B.) This rule shall apply for the duration of the PTT event, starting two cycles after the first voice burst transmission.

Note 1.—  Currently, only the 3T system configuration supports voice reservation signalling.

Note 2.—  It is desirable for implementation simplicity to be able to remain in the same timing state for the duration of a PTT event. Putting an upper limit on the duration of an aircraft PTT event makes this practical. This limit does not apply to the ground station because of normal AT operating procedures.

Note 3.—  The 35 seconds limit on an aircraft PTT event is based on the Automatic Termination of transmission requirement in RTCA/DO-207, “Minimum operational performance standards for devices that prevent blocked channels used in two-way radio communication due to unintentional transmissions”, January 25, 1991.

5.2.4.2.5	Free Running Voice Operation.  While in TS3, the aircraft station shall process all V/D (voice) bursts without regard to Group ID.  Multiple V/D (voice) bursts with different Group ID shall be processed on a first-come-first-serve basis, regardless of Group ID.  Once a particular V/D (voice) burst is processed, the aircraft station shall continue to process only V/D (voice) bursts from the same user until EOM is indicated.

5.2.4.2.5.1	The aircraft station in TS3 timing state shall maintain system timing autonomously.  While in TS3, the aircraft station shall transmit V/D (voice) bursts in the assigned time slot based on the system timing maintained by the aircraft.

Note.—  Without beacons and ALT available to correct its time, an aircraft station in TS3 is expected to drift relative to UTC at a rate determined by the stability of its reference oscillator.

Insert new Section 5.2.4.3.4.1 and 5.2.4.3.4.2:

5.2.4.3.4.1	The aircraft station shall stop all transmitting and receiving activities on that net after the aircraft MAC sublayer sends the Leaving Net message.

5.2.4.3.4.2	Tuning to Next Net.  Upon completion of the Leaving Net message transmission, the aircraft LME shall automatically tune to the next net, provided that the aircraft LME has received the Next Net information.

Note.—  It is not necessary for the aircraft to acknowledge the Next Net message to  initiate Leaving Net message transmission.

Modify Section 5.4.2.1.1 as follows:

5.4.2.1.1	Net Initialization. Before the link establishment procedure, the aircraft station shall initialize to initial timing state 0 (TS0) and set parameters CTC1, CTC2 and CTC3 to max(f-50, t). The first part of the link establishment procedure shall be the acquisition of the M uplink burst (LBAC 11 for 3T configuration, LBAC 5, 7 or 9 for 3S configuration, LBAC 4 or 6 for 2S1X, and LBAC 5 for other configurations) associated with the specified user group identifier.

5.4.2.1.1.1	Upon receipt of two consecutive M uplink bursts containing the identical information (i.e. System Configuration, Squelch Window, Slot ID and Ground Station Code) in octets 1-3 of the uplink burst, the LME shall declare the net initialized and shall establish the net operating parameters based on the static information contained in octets 1-3. In configurations 3S and 2S1X the LME shall declare the net initialized when at least one of the wide area coverage slots provide two consecutive M uplink bursts containing the same information in octets 1-3. Upon net initialization, the aircraft station shall transition from TS0 to TS1.

5.4.2.1.1.2If the aircraft station is unable to enter TS1, it shall search for ALTs to determine the number of slots in its net and enter TS2. If CTC3 equals parameter f before the aircraft station enters TS2, it shall enter TS3. Prior to net initialization, voice access shall be inhibited.

5.4.2.1.1.3	Transition from TS0 to TS2 or TS3 shall be prohibited (see Section 5.2.4.1.2) if an ALT received from a ground station (i.e., an uplink beacon from a ground station operating in another time slot) contains system configuration information that indicates that the aircraft radio has incorrectly tuned to a data slot.

Note.— Net Initialization is a prerequisite for the next step of Net Entry, however with Net Initialization only, basic voice services can be supported.

Add Note to Section 8.4.1.1 as follows:

8.4.1.1	Link initialization.  Upon Net Initialization (see  5.4.2.1.1), the aircraft LME shall provide the Voice Unit with the net parameters as part of the LME’s net initialization procedure. These parameters shall be the Slot ID and Squelch window.

Note.—   For net initialization directly from TS0 to TS3, there will be no Slot ID information and the Squelch window will be wide open.

2.6.	Diversity Site Group operations

Upon further examination of transition for the U. S. FAA, it was determined that additional requirements were needed to support diversity site group operations.  A diversity site group is a group of 2-12 ground sites (up to 6 primary sites and up to 6 backup sites) that share a common operating frequency, where the ground controller selects which transmitter to use and all receivers are active with the voice switch arbitrating which one reaches the controller.    Diversity site groups are used similar to offset-carrier systems in Europe.  Considering the need for regular beacon transmissions for the VDL Mode 3 system to operate, new requirements are necessary to support this method of operation.

Amendment Proposal

| Title: | Diversity Site Group Operations |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.3.1.1, 5.2.3.1.2, 5.2.4.1.6, 5.2.4.1.6.1, 5.4.3.2.4 Tables 5-10a, 5-10b, 8-1, 8-2 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Upon further examination of transition for the U. S. FAA, it was determined that additional requirements were needed to support diversity site group operations. A diversity site group is a group of 2-12 ground sites (up to 6 primary sites and up to 6 backup sites) that share a common operating frequency, where the ground controller selects which transmitter to use and all receivers are active with the voice switch arbitrating which one reaches the controller. Diversity site groups are used similar to offset-carrier systems in Europe. Considering the need for regular beacon transmissions for the VDL Mode 3 system to operate, new requirements are necessary to support this method of operation |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | No. |
| Amendment Proposal: | Revert to a single validity window (the more open one). Require aircraft to track signaling information even if it isn't the ground station that is providing timing. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix diversity site group operations and to harmonize with the VDL Mode 3 MASPS.

Modify 5.2.3.1.1 and 5.2.3.1.2 as follows:

5.2.3.1.1	Validity window. A timing beacon (with appropriate Slot ID and Ground Station Code) shall be considered valid (i.e., acceptable for aircraft radio timing updates) if it is received within the validity window with respect to the previous beacon’s timing reference. The validity window shall be defined to extend from –K(n+1)+1 to +1 symbol periods, where K = 4 for 4-slot configurations and K = 8 for 3-slot configurations and n is the squelch window parameter. To allow an aircraft radio to adapt in a timely manner to an abrupt change in the location of a beacon transmitter, an aircraft radio shall extend its validity window to include all relative times whenever its counter CTC1 exceeds 24.

Note.— This definition takes into account the 1 symbol period accuracy assumed for the aircraft radio timing.  It is also designed to support site diversity and selective keying operation, where it is desirable that the aircraft radio should base its timing on the signal from the closest ground site.

5.2.3.1.2	Receipt of Beacon Information.  Aircraft radios shall decode and process information contained in any ground beacon signal with a Slot ID and Ground Station Code appropriate for the aircraft radio’s current net.

Note.— Although an aircraft radio must use the validity window to restrict which ground beacons it should use to update its timing, it should accept and react to any ground beacon associated with its net.  This allows an aircraft radio to have its timing based on the closest ground site, while getting system information in the most timely manner.

Modify 5.2.4.1.6 and subsections as follows:

5.2.4.1.6	Dummy poll responses. When an aircraft radio receives an uplink M channel message with value 61 (Appendix B, 2.1.5) in the Aircraft ID (Poll) field, indicating that the ground station does not support discrete addressing, an aircraft radio shall transmit dummy Poll Responses in downlink M slots reserved for Poll Response. The format of a dummy Poll Response shall be identical to a regular Poll Response. Dummy Poll Responses shall not be processed by the controlling ground station. The MAC cycle in which to transmit the dummy Poll Responses shall be chosen by the following algorithm:

5.2.4.1.6.1	Immediately after net initialization, after determining that the uplink Beacon contains Aircraft ID = 61, divide all further MAC cycles into groups of 25. Within each group, choose one MAC cycle at random from 1 to 25 in which to transmit a dummy Poll Response. Continue to transmit dummy Poll Responses for as long as the aircraft radio remains in timing state TS1.

Note 1.—  For the voice-only configurations: 4V, 3V, 3S and 2S1X, polling may not be implemented and a ground radio in one of these configurations may not support polling. In order to support the transmission of an Alternate Timing Reference in these configurations (see  5.2.4.1.2), aircraft radios must transmit “Dummy Poll Response” messages since they are never actually polled.

Note 2.—  Analysis and simulation have shown that, unless the number of aircraft radios is extremely large, the probability that at least one MAC cycle out of 25 contains one and only one dummy Poll Response is very close to 1.

Note 3.—  The LBACs available for dummy Poll Responses include LBAC 1 for configurations 4V, 3V, 3S and 2S1X, irrespective of which LBAC is associated with the time slot to which the aircraft radio is currently connected.

Modify Section 5.4.3.2.4 as follows:

5.4.3.2.4	Timer TL4 (polling interval). Timer TL4 shall represent the maximum number of elapsed MAC cycles between receipt of two consecutive polls. Timer TL4 shall be started upon receipt of a poll. Upon expiration of this timer, the LME shall notify the DLS, SNDCF and the Voice Unit and attempt to re-establish the link by sending a Net Entry message to the ground station.

Modify Section 8.4.4.1.1 as follows:

Table 5-10a).  LME system parameters

| Symbol | Parameter Name | Minimum | Maximum | Mode 3 Default | Increment |
| --- | --- | --- | --- | --- | --- |
| WE | Net Entry Request Delay (MAC cycle) | 1 | 256 | *See Table 5-10b) | 1 |
| NL1 (air) | Maximum net entry request retry | 1 | 128 | 20 | 1 |
| NL2 (gnd) | Polling reply counter | 1 | 255 | 3 | 1 |
| TL3 | Disconnect delay timer (seconds) | 5 | 30 | 10 | 1 |
| TL4 (air) | Polling interval (MAC_cycles) | 1 | 600 | *See Table 5-10b) | 1 |

*Table 5-10b).  WE and TL4 parameter default values

|  |  | System Configuration |
| --- | --- | --- |
| Symbol | Parameter Name | 4V | 3V1D | 2V2D | 3T | 3V | 2V1D | 3S | 2S1X | 1V3D | 1V2D |
| WE | Net Entry Request Delay (MAC cycles) | 1 | 2 | 2 | 2 | 1 | 2 | 1 | 1 | 4 | 4 |
| TL4 (air) | Polling Interval (MAC cycles) | 480 | 120 | 120 | 120 | 480 | 120 | 240 | 240 | 480 | 480 |

Note.— This table takes into account the possibility that the first six system configurations might be used in sectors with site diversity.

Modify Tables 8-1 and 8-2 as follows:

Table 8-1.  Source filtering squelch window matrix for 4-slot configurations

|  | Aircraft Receiver State Squelch Window (Note 1) | Ground Receiver State Squelch Window (Note 1) |
| --- | --- | --- |
| State Message Type | TS1 (Note 2) | TS2 (Note 2, Note 3) | TS3 (Note 5) | TS1 (Note 2) |
| Uplink voice | -1 to +1 | -33 to +1 | Wide Open | NA |
| Downlink voice: TS1 | -2 to +4(n+1) | -34 to +4(n+1) | Wide Open | -1 to +(4n+3) |
| Downlink voice: TS2 | -2 to +4(n+9) | -34 to +4(n+9) | Wide Open | -1 to +(4n+35) |
| Downlink voice: TS3 | Wide Open (Note 4) | Wide Open (Note 4) | Wide Open | Wide Open (Note 4) |
| Note 1.— Each squelch window is defined relative to the nominal burst time in symbols. Note 2.— n = squelch window parameter. Note 3.— If n is unknown, then the default value is 6. N=7 is not a valid Squelch Window parameter. Note 4.— Receive any such message with “correct” group ID if not already receiving a voice message. Note 5.— In this column, "Wide Open" implies that an aircraft radio will receive voice messages without regard to Group ID based on the rules defined in Section 5.2.4.2.5. |

Table 8-2.  Source filtering squelch window matrix for 3-Slot configurations

|  | Aircraft Receiver State Squelch Window (Note 1) | Ground Receiver State Squelch Window (Note 1) |
| --- | --- | --- |
| State Message Type | TS1 (Note 2) | TS2 (Note 2, Note 3) | TS3 (Note 5) | TS1 (Note 2) |
| Uplink voice | -1 to +1 | -33 to +1 | Wide Open | NA |
| Downlink voice: TS1 | -2 to +8(n+1) | -34 to +8(n+1) | Wide Open | -1 to +(8n+7) |
| Downlink voice: TS2 | -2 to +8(n+5) | -34 to +8(n+5) | Wide Open | -1 to +(8n+39) |
| Downlink voice: TS3 | Wide Open (Note 4) | Wide Open (Note 4) | Wide Open | Wide Open (Note 4) |
| Note 1.— Each squelch window is defined relative to the nominal burst time in symbols. Note 2.— n = squelch window parameter. Note 3.— If n is unknown, then the default value is 7. Note 4.— Receive any such message with “correct” group ID if not already receiving a voice message. Note 5.— In this column, "Wide Open" implies that an aircraft radio will receive voice messages without regard to Group ID based on the rules defined in Section 5.2.4.2.5. |

2.7.	User Notification

The requirements relating to notification to the user are currently scattered throughout the document, and sometimes stated in an obscure fashion.  For clarity, it is desirable to gather them together and highlight them.

Amendment Proposal

| Title: | User Notification |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.1.2, 5.2.1.3, 5.2.1.4, 5.2.4.2.6, 8.4.3, 8.4.4.1.3 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | EDITORIAL |
| Problem description: | The user notification requirements are obscure and spread throughout the document. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Gather all of the user notification requirements together for clarity. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to clarify the user notification and to harmonize with the VDL Mode 3 MASPS.

Modify Section 5.2.1.2, 5.2.1.3, and 5.2.1.4 as follows:

5.2.1.2	Channel occupancy. Channel occupancy is the amount of time spent on the channel per access event.

5.2.1.2.1	For data operation, an access event shall consist of no more than 15 consecutive V/D (data) burst opportunities. For downlink data transmission, an access event shall be the result of a single Reservation Request.

5.2.1.2.2	For aircraft voice operation, an access event shall be limited by the duration of the push-to-talk (PTT) assertion or 35 seconds, whichever is less. Voice access shall also honour the voice signalling information issued in the M_uplink burst. In case the access event is terminated due to the 35 second limit or because of M uplink burst information, an indication of the termination will be provided for the terminated user (see Section 5.2.4.2.6).

5.2.1.2.3	For ground voice operation, an access event shall be limited by the duration of the PTT assertion.

Insert new Section 5.2.4.2.6 as follows:

5.2.4.2.6	User Notification.  The aircraft station shall notify the users if any of the following events occurs:

- Voice transmission (including unintentional transmission) is stopped when received uplink M burst voice signal code is other than 01b,

- PTT event exceeds the 35-second limit,

- PTT is asserted while access is not allowed (see Table 5-9).

Note.— The methods used for user notification are beyond the scope of this document.  Notification to the user could, as an example, be implemented as signalling to the transceiver external interface or implemented as a short duration audible signal that is mixed with the received audio.

Modify Section 8.4.3 as follows:

8.4.3    Voice transmit function

Upon PTT activation, the voice unit shall set the Request-to-Send (RTS) flag to notify the MAC sub-layer that the voice unit would like to transmit. The voice unit shall also check the Cleared-to-Send (CTS) flag (set by the MAC sublayer, see Section 5.2.4.2) to determine if the channel is available. The timing of the CTS flag is described in Section 5.2.4.2. If the channel is available (i.e. CTS flag set), the voice unit shall transmit the V/D (voice) burst. If, upon PTT, the channel is occupied (CTS flag cleared), the user is notified. The final V/D (voice) burst transmitted as a result of release of PTT shall be indicated by setting the EOM flag in the Header Segment of the burst.

Modify Section 8.4.4.1.3 as follows:

8.4.4.1.3	Source identification. The Voice Unit shall indicate the source (ground user or aircraft user) of the received voice message based on the V/D (voice) burst header.

2.8.	Multiple Radio operation

Air carrier implementations operate multiple VHF communications radios in a simultaneous fashion.  This was not previously accounted for in VDL Mode 3 operation.  As such, some requirements are needed to ensure the radios do not interfere with each other and perturb system operation.

Amendment Proposal

| Title: | Multiple Radio Operations |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.4.3.7 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | CRITICAL |
| Problem description: | Air carrier implementations operate multiple VHF communications radios in a simultaneous fashion. Coordination is required to prevent them from interfering with each other. |
| Background: | [Validation Details] Validated by inspection, and analysis. Manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Require radios to coordinate if installed on a common airframe. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to allow a multiple radio installation and to harmonize with the VDL Mode 3 MASPS.

Insert a new Section 5.2.4.3.7 as follows:

5.2.4.3.7	Multiple Radio Installations.  If multiple radios are installed on an aircraft station and are operating on the same channel, the radio systems shall coordinate their MAC sublayers, as necessary, so that only one radio acknowledges to polls and next net messages, and that one radio acknowledges uplink V/D (data) uplink bursts.

Note.— This requirement is to resolve issues with multiple radios tuned to the same net, or for system configurations 3V1D/2V1D with multiple radios sharing the same data slot regardless of different local identifiers.  Arbitration of downlink messaging in these cases is already handled by the router.

2.9.	Data link termination/recovery (CTRL_RSP_LCR & Terminate Net)

It was pointed out that it wasn't necessarily desirable to terminate discrete addressing if the data link is terminated, as the user may still wish to use the voice-related functions of discrete addressing. Also, recovery had some issues that the fault may not allow the aircraft to send the CTRL_RSP_LCR frame, as the aircraft radio may have lost its assigned Local Identifier information.

Amendment Proposal

| Title: | Data link termination/recovery |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.4.3.5, 5.4.2.1.3.4.2, 5.4.2.5, B.2.14 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | It was pointed out that it wasn't necessarily desirable to terminate discrete addressing if the data link is terminated, as the user may still wish to use the voice-related functions of discrete addressing. Also, recovery had some issues that the fault may not allow the aircraft to send the CTRL_RSP_LCR frame. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | No. |
| Amendment Proposal: | Remove requirement that local ID cleared upon CTRL_RSP_LCR. Add Terminate Net message to provide ground a means to clear the Local ID association. Clarify aircraft recovery. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix the implementation of CTRL_RSP_LCR and to harmonize with the VDL Mode 3 MASPS.

Insert new Section 5.2.4.3.5:

5.2.4.3.5	Terminate Net Message.  Upon reception of the Terminate Net message, the aircraft MAC shall clear the Local ID association and revert to an aircraft ID of 61, and notify the LME of the loss of discrete-addressed services.  The Terminate Net message format shall be as defined in Appendix B, Section 2.14.  After the receipt of the Terminate Net message, the aircraft station shall begin the delayed net entry procedures described in Section 5.4.2.1.2.

Modify Section 5.4.2.1.3.4.2 as follows:

5.4.2.1.3.4.2	Unacceptable parameters. If the parameters in the CTRL_RSP_LE from the ground LME are not acceptable to the aircraft LME, then the aircraft LME shall send a CTRL_RSP_LCR frame and terminate the data link connection.

Note.— The CTRL_RSP_LCR frame will terminate the data link connection, but the aircraft radio will retain its Local ID number.  It will then be able to continue participating in Enhanced Voice functions. There is no point to the radio reattempting Net Entry to this ground station, as it will continue to fail to establish the connection.

Modify Section 5.4.2.5.1 and 5.4.2.5.2 as follows:

5.4.2.5    Recovery

5.4.2.5.1	The recovery procedure shall be initiated when either the ground or aircraft protocol stack has lost state information needed to communicate. If an aircraft loses protocol state information, it shall send a CTRL_RSP frame with LCR Cause XID indicating an appropriate code, when possible, followed by the aircraft attempting to do part or all of the Link Establishment procedures per 5.4.2.1, whatever is necessary to re-establish the link with the ground station.

Note 1.— An example of the VDL Mode 3 protocol states and state transitions is given in Section 13 of the ICAO VDL Mode 3 Implementation Manual.

Note 2.— Depending on the extent of the loss of the protocol state information, the aircraft station may or may not be capable of sending a CTRL_RSP frame.  For example, if only the DLS protocol state information is lost it may be necessary for the aircraft station to do only Link Negotiation, bypassing Net Initialization and Net Entry, in order to re-establish the link with the ground station.

5.4.2.5.2	After the ground begins recovery, it shall broadcast a Recovery message to instruct all aircraft to enter into the same condition. Both the ground and aircraft stations shall undertake recovery procedures until connections are re-established with all responding aircraft. While in the recovery procedure, the ground station shall attempt to sequentially contact each possible aircraft identifier to determine which identifiers are in use.

Note.— The recovery procedure allows the normal net entry process to be bypassed to re-establish contact with aircraft that are still in the ground station coverage area when the recovery procedure is invoked.

Modify Table B-1 as follows:

Table B-1:  M Burst Messages

|  | Message ID | M Bursts | Section # of this Appendix |
| --- | --- | --- | --- |
|  | 0000 | Normal Message | 2.2 |
|  | 0001 | Net Entry Response Message (no previous link) | 2.3 |
| Uplink | 0010 | Net Entry Response Message (previous link preserved) | 2.3 |
|  | 0011 | Next Net Command Message | 2.4 |
|  | 0100 | Recovery Message | 2.5 |
|  | 0101 | Handoff Check Message | 2.6 |
|  | 0110 | Terminate Net Message | 2.14 |
|  | 0111 | Spare |  |
|  | Identified by separate sync sequence | Net Entry Request Message | 2.9 |
|  | 1000* | Reservation Request Message | 2.10 |
| Downlink | 1001* | Acknowledgement Message | 2.11 |
|  | 1010* | Leaving Net Message | 2.12 |
|  | 1011-1111* | Spare |  |
|  | 1000** | 4-slot configuration Poll Response | 2.10 |
|  | 1001** | Spare |  |
|  | 1010** | 3-slot configuration Poll Response | 2.10 |
|  | 1011** | Spare |  |
|  | 1100** | 3T configuration Poll Response | 2.10 |
|  | 1101** | Spare |  |
|  | 1110** | Spare |  |
|  | 1111** | Next Net ACK | 2.13 |

*	Identified by standard synchronization sequence defined in Annex 10 Volume III, Part I, Chapter 6.

**	Identified by special synchronization sequence for poll responses defined in Annex 10 Volume III, Part I, Chapter 6.

Insert the following new section in Appendix B:

### 2.14	Terminate Net Message.  The terminate net message shown in Figure B-12a), is used to terminate an aircraft link at the MAC sublayer. The first Golay word after the beacon information contains the Local Identifier of the aircraft whose net is being terminated, and four spare bits.  One reservation response opportunity is also included in a terminate net message.  The Reservation Response field consists of 12 bits.  The Reservation Response field can signal the actual allocation of channel resources to a requesting aircraft.

|  | first bit transmitted | Bit Number |
| --- | --- | --- |
| Octet No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | Message ID | Voice Signal | Aircraft ID (Poll) |
| 2 | Aircraft ID (Poll) (cont.) | System Configuration |
| 3 | Slot ID | Ground Station Code | Squelch Window |
| 4 | Terminated Local ID |
| 5 | Spare | Reservation Response |
| 6 | Reservation Response (cont.) |

Figure B-12a).  M Uplink (Terminate Net Message)

2.10.	Delayed Net Entry

To expedite log-in for aircraft that were previously denied discrete-addressed services, a simple change allows the ground to just assign a local identifier to the aircraft rather than waiting for a new Net Entry Request.  This also helps hold down transmissions in the random access channel by preventing these Net Entry Requests.  The initial Poll Response is still around as an acknowledgement of the Net Entry Response, so even if the aircraft is no longer in coverage, the system will sort itself out.

Amendment Proposal

| Title: | Delayed Net Entry |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.4.2.1.2.4, 5.4.2.1.2.5, 5.4.2.1.2.6 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | To expedite log-in for aircraft that were previously denied discrete-addressed services, a simple change allows the ground to just assign a local identifier to the aircraft rather than waiting for a new Net Entry Request. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Provide a means whereby aircraft will recognize a Net Entry Response sent after a rejected Net Entry Request. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to implement Delayed Net Entry and to harmonize with the VDL Mode 3 MASPS.

Modify Sections 5.4.2.1.2.4 through 5.4.2.1.2.6 as follows:

5.4.2.1.2.4	If there are already 60 aircraft in the net when the Net Entry Request message is received, the ground LME shall respond with a Net Entry Response message with the local identifier field set to 0 indicating that the net is currently full. The aircraft radio shall then use an Aircraft ID of 61 when communicating with the ground station and other aircraft to indicate that it has not entered the net.  When an aircraft radio is in this state, it shall continue to monitor all Net Entry Response messages in order to detect a delayed Net Entry Response message addressed to it via its aircraft ICAO address.  Upon receipt of such a message, the aircraft radio shall change its Local ID to the value provided.

Note 1.— There is no limit on how many aircraft can use the aircraft ID of 61 simultaneously.

Note 2.— Aircraft radios receiving a “Net Full” indication in the Net Entry Response message cannot avail themselves of services requiring discrete addressing until a valid Local ID is provided via the delayed net entry process.  From that point forward the aircraft radio can participate in all discrete-addressed services it can support.  For example, data-capable radios can begin link negotiation via XIDs at this time.

Note 3.— In order to provide a delayed net entry capability, the ground station must maintain a time ordered list of potential net entrants. As they become available due to aircraft leaving the net, Local ID numbers should be distributed to waiting aircraft radios on a first-come-first-served basis.

5.4.2.1.2.5	If a duplicate Net Entry Request message is received it shall be discarded.

Note.— A Net Entry Request message is considered to be a duplicate if a ground station receives a retransmitted Net Entry Request while it is still processing a previously received Net Entry Request from the same aircraft.

5.4.2.1.2.6	If the requesting aircraft does not receive a Reservation message from the ground in the next MAC cycle after transmitting the Poll Response message, it shall restart the net entry procedure.

Note.— The GNI provides a connection management function across multiple ground stations such that the same subnetwork connections are maintained with aircraft served by those ground stations. A description of the GNI function is provided in the Implementation Aspects of this manual.

2.11.	Vocoder Bit Ordering clarification

One of the manufacturers expressed some uncertainty regarding the vocoder bit ordering.  As such, additional words are suggested to explicitly define the order in which the bits are transmitted in reference to the VC-20 ATC-10b implementation.

Amendment Proposal

| Title: | Vocoder Bit Ordering Clarification |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 8.2.3.1, 8.2.3.2 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | EDITORIAL |
| Problem description: | One of the manufacturers expressed some uncertainty regarding the vocoder bit ordering. |
| Background: | [Validation Details] Validated by inspection, Integration testing and flight testing. Manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Provide further clarification of the explicit bit ordering for the vocoder. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to clarify the vocoder bit ordering and to harmonize with the VDL Mode 3 MASPS.

Modify 8.2.3 and its subsections as follows:

8.2.3    Vocoder Frame Bit Ordering

8.2.3.1	The 96 bits of the vocoder frame shall be ordered as follows:

For the DVSI VC-20 ATC-10B implementation, the vocoder encoder frame shall consist of the concatenation of twenty-four 4-bit words output from the vocoder board.  For the 4-bit bus, the bit designated as TXD3 (DIN41612 connector pin C4) shall be designated as the msb of the 4-bit word.  The first 4-bit word output from the vocoder decoder board shall be transmitted first and in each 4-bit word the msb shall be transmitted first. The VC-20 ATC-10B vocoder decoder frame shall consist of the concatenation of twenty-four 4-bit words input to the vocoder board.  The first four bits in the 96-bit vocoder frame received shall be the first 4-bit word of that frame.  The first bit received in each 4-bit word is the msb and shall be input to RXD3 (DIN41612 connector pin C9) or its equivalent. For the VC-20 ATC-10B implementation, the 4-bit control words which precede each vocoder frame shall not be considered part of the 96-bit vocoder frame.

8.2.3.2	All other implementations shall conform to this bit ordering.

Note.— For other implementations, implementers are advised to contact Digital Voice Systems, Incorporated to ensure correct bit ordering to ensure interoperability with the VC-20 ATC-10B based bit ordering.

2.12.	Next Net Bit Ordering clarification

One of the manufacturers highlighted an ambiguity in the next net M burst formatting of one of the fields.  As such explicit requirements for the bit ordering are suggested.

Amendment Proposal

| Title: | Next Net Bit Ordering |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | Appendix B, Section 2.4.2 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | CRITICAL |
| Problem description: | It was pointed out there is an ambiguity of the bit ordering between the Next Group ID and Frequency subfields of the Next Net M burst message. |
| Background: | [Validation Details] Validated by inspection, Integration testing and flight testing. Manufacturer data forthcoming. |
| Backwards compatibility: | No. |
| Amendment Proposal: | Specify the relative bit ordering of the frequency field of the Next Net M burst message. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix the bit ordering of the Next Net M burst message and to harmonize with the VDL Mode 3 MASPS.

Modify Appendix B, Section 2.4.2 as follows:

2.4.2	Next net. The Next Net field is 12 bits. It contains two subfields: Next Group ID (2 bits) and Frequency (10 bits). The Next Group ID field is located in bits 1 and 2 of octet 4 and is encoded the same as defined in  2.2.3 of this Appendix when the Net Type field is set to 1 (TDMA). However, when the Net Type field is set to 0 (AM), the field shall be set as defined in Table B-7 below. For a frequency X in megahertz, the Frequency field is encoded as 40(X-112) with the most significant bit starting at bit 3 of octet 4.

Note.— For 8.33 kHz channels that are not a multiple of a 25 kHz channel, the value of X used for encoding shall be that of the next lowest 25 kHz channel. The frequencies of these 8.33 kHz channels are uniquely identified by use of the Next Group ID field.

2.13.	Preemption & Anti-blocking

During flight trials in preparation for an upcoming demonstration, a problem was identified with the operation of anti-blocking.  In the scenario, one aircraft correctly blocked another, but when the transmission ended, the other user immediately accessed the channel leading to potential confusion on the part of the listeners.  As such, it was deemed appropriate that the blocked aircraft should have its PTT locked out and require a release and rekey to access the channel.

Amendment Proposal

| Title: | Preemption and Anti-blocking |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 8.4.3.3, 8.4.3.4 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: |  |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | No |
| Amendment Proposal: | Add a section to allow aircraft to disable the anti-blocking feature when caused by a TS2 or TS3 transmission. Add information for a PTT lockout for anti-blocking. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to fix the implementation of anti-blocking and preemption and to harmonize with the VDL Mode 3 MASPS.

Modify Section 8.4.3.3 as follows:

8.4.3.3	Access pre-emption. If the CTS flag indication is lost during transmission (signalling a ground pre-emption), the voice unit shall cease transmitting and shall process any received V/D (voice) bursts. The ability to transmit voice after the CTS flag is cleared during a transmission shall be inhibited until PTT is reasserted by the user (after which the voice access rules of Table 5-9 need to be reapplied).

Note.— Since TS2 and TS3 users cannot hear the ground station, they cannot be overridden by the ground station.  This aircraft RF channel unblocking capability is intended to prevent one of these users from interfering with the proper voice operation of the sector.

Insert a new Section 8.4.3.4 as follows:

8.4.3.4 Anti-blocking.  If an aircraft radio has its PTT keyed and CTS is cleared (indicating the channel is busy), voice transmission shall be inhibited until PTT is reasserted by the user (after which the voice access rules of Table 5-9 need to be reapplied).  Upon user command, the aircraft station shall unblock the cleared CTS flag when the cleared flag is due to the channel being occupied by TS2 or TS3 voice activity.

Note 1.— The purpose of this requirement is to prevent a second user from transmitting a partial communication immediately following the end of transmission of another user, which could lead listeners to misunderstand the communications.

Note 2.— As for the ability to disable the transmission inhibit, Table 5-9 is still applicable to determine whether the transmitter is allowed to output to the voice channel.

2.14.	Assigned Altitude

During a handoff operation, the aircraft must confirm its assigned altitude with the controller as part of the conformance checking that the controller and pilot understand where the aircraft is supposed to be.  Currently, the Next Channel Uplink feature does not have a means to convey this information and would external assistance from CPDLC or the voice channel.

Amendment Proposal

| Title: | Assigned Altitude |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.4.3.3.4.1.8 Tables 5-15a, 5-15b, 5-28g |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | During a handoff operation, the aircraft must confirm its assigned altitude with the controller as part of the conformance checking that the controller and pilot understand where the aircraft is supposed to be. Currently, the Next Channel Uplink feature does not have a means to convey this information and would external assistance from CPDLC or the voice channel. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Add an XID to support the conveyance of Assigned Altitude information during a handoff, similar to the CPDLC application. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to allow for a voice-free handoff and to harmonize with the VDL Mode 3 MASPS.

Insert a new Section 5.4.3.3.4.1.8 as follows:

5.4.3.3.4.1.8		Assigned Altitude Parameter.  The Assigned Altitude parameter, used by the ground station, shall be encoded as an unsigned 16-bit integer in units of 1 foot relative to mean sea level per Table 5-28g).

Modify Tables 5-15a and 5-15b as follows:

Table 5-15a).  XID parameters

|  |  | Air-initiated link establishment | Link connection rejection |
| --- | --- | --- | --- |
|  | Source | Aircraft | New ground station | Any station |
|  | Destination | Proposed ground station | Aircraft | Any station |
| XID parameters | GI | PI | CTRL_CMD_LE | CTRL_RSP_LE | CTRL_RSP_LCRCTRL_CMD_LCR |
| Public parameters (8885:1993:Mode 3) |
| Parameter set ID | 80h | 01h | N/A | O | N/A |
| N1-downlink | 80h | 05h | N/A | O | N/A |
| N1-uplink | 80h | 06h | N/A | O | N/A |
| Counter N2 | 80h | 0Ah | N/A | O | N/A |
| Timer T1 | 80h | 09h | N/A | O | N/A |
| T-ack | 80h | 08h | N/A | O | N/A |
| Private parameters (V) |
| Parameter set ID | F0h | 00h | O | O | M |
| SQP | F0h | 02h | O | O | N/A |
| LCR cause | F0h | 06h | N/A | N/A | M |
| Modulation support | F0h | 81h | O | N/A | N/A |
| Private parameters (W) |
| Parameter set ID | F0h | 00h | M | M | O |
| Algorithm version number | F0h | 01h | O | O | O |
| Network initialization | F0h | 02h | M | M | N/A |
| Connection check | F0h | 03h | N/A | N/A | N/A |
| Version | F0h | 04h | O | O | O |
| Authentication | F0h | 05h | O | O | O |
| Subnetwork user data | F0h | 06h | O | O | O |
| Assigned Altitude | F0h | 07h | O | O | O |
| NM1 | F0h | 42h | N/A | O | N/A |
| RR | F0h | 43h | N/A | O | N/A |
| WR | F0h | 44h | N/A | O | N/A |
| RE | F0h | 46h | N/A | O | N/A |
| RL | F0h | 47h | N/A | O | N/A |
| Timer T3 | F0h | 48h | N/A | O | N/A |
| NL1 | F0h | 49h | N/A | O | N/A |
| Timer TL3 | F0h | 4Ah | N/A | O | N/A |
| Timer TL4 | F0h | 4Bh | N/A | O | N/A |
| WE | F0h | 4Ch | N/A | O | N/A |
| Operative_GNIp | F0h | 4Fh | O | O | N/A |
| Aircraft_TMbB | F0h | 50h | O | O | N/A |
| MbB_Operations_Permitted | F0h | 51h | O | O | N/A |
| Expedited recovery | F0h | 80h | O | N/A | N/A |
| t | F0h | 81h | O | N/A | N/A |
| f | F0h | 82h | O | N/A | N/A |
| Former_GNIp | F0h | 83h | O | O | N/A |
| Counter NL2 | F0h | C1h | N/A | O | N/A |

Key for Table 5-15a) above:

Abbreviations used:

GI	= ISO 8885 Group Identifier

PI	= ISO 8885 Parameter Identifier

M	= Mandatory

O	= Optional

N/A	= Not applicable

h	= hexadecimal

Table 5-15b).  XID parameters

|  | Addressed link parameter modification | Broadcast link parameter modification |
| --- | --- | --- |
|  | Source | Current ground station | Aircraft | Current ground station |
|  | Destination | Aircraft | Current ground station | Aircraft |
| XID parameters | GI | PI | CTRL_CMD_LPM | CTRL_RSP_LPM | CTRL_CMD_LPM(GSIF) |
| Public parameters (8885:1993:Mode3) |
| Parameter set ID | 80h | 01h | O | N/A | O |
| N1-downlink | 80h | 05h | O | N/A | O |
| N1-uplink | 80h | 06h | O | N/A | O |
| Counter N2 | 80h | 0Ah | O | N/A | O |
| Timer T1 | 80h | 09h | O | N/A | O |
| T-ack | 80h | 08h | N/A | 0 | N/A |
| Private parameters (V) |  |  |  |  |  |
| Parameter set ID | F0h | 00h | O | O | O |
| SQP | F0h | 02h | O | O | O |
| LCR cause | F0h | 06h | N/A | N/A | N/A |
| Modulation support | F0h | 81h | N/A | N/A | N/A |
| Private parameters (W) |
| Parameter set ID | F0h | 00h | O | O | O |
| Algorithm version number | F0h | 01h | O | N/A | O |
| Network initialization | F0h | 02h | O | O | O |
| Connection check | F0h | 03h | O | O | O |
| Version | F0h | 04h | N/A | N/A | O |
| Authentication | F0h | 05h | O | O | O |
| Subnetwork user data | F0h | 06h | O | O | O |
| Assigned Altitude | F0h | 07h | O | O | O |
| NM1 | F0h | 42h | O | N/A | O |
| RR | F0h | 43h | O | N/A | O |
| WR | F0h | 44h | O | N/A | O |
| RE | F0h | 46h | O | N/A | O |
| RL | F0h | 47h | O | N/A | O |
| Timer T3 | F0h | 48h | O | N/A | O |
| NL1 | F0h | 49h | O | N/A | O |
| Timer TL3 | F0h | 4Ah | O | N/A | O |
| Timer TL4 | F0h | 4Bh | O | N/A | O |
| WE | F0h | 4Ch | O | N/A | O |
| Operative_GNIp | F0h | 4Fh | O | O | O |
| Aircraft_TMbB | F0h | 50h | O | O | O |
| MbB_Operations_Permitted | F0h | 51h | O | O | O |
| Expedited recovery | F0h | 80h | N/A | N/A | N/A |
| t | F0h | 81h | O | N/A | O |
| f | F0h | 82h | O | N/A | O |
| Former_GNIp | F0h | 83h | O | O | O |
| Counter NL2 | F0h | C1h | O | N/A | O |

Key for Table 5-15b) above:

Abbreviations used:

GI	= ISO 8885 Group Identifier

PI	= ISO 8885 Parameter Identifier

M	= Mandatory

O	= Optional

N/A	= Not applicable

h	= hexadecimal

Insert a new Table 5-28g as follows:

Table 5-28g).  Assigned Altitude Parameter

| Parameter ID | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | Assigned Altitude |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  |
| Parameter value | v16 | v15 | v14 | v13 | v12 | v11 | v10 | v9 | Value |
|  | v8 | v7 | v6 | v5 | v4 | v3 | v2 | v1 |  |

2.15.	Optional System Configuration 3T

Due to certification requirements and the lack of an immediate operational need for system configuration 3T, which is significantly different from the other system configurations, the capability should be optional.

Amendment Proposal

| Title: | Optional 3T |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.2.4 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Due to certification requirements and the lack of an immediate operational need for system configuration 3T which is significantly different from the other system configurations, the capability should be optional. |
| Background: | [Validation Details] Validated by inspection, and analysis. Integration testing and manufacturer data forthcoming. |
| Backwards compatibility: | Yes. |
| Amendment Proposal: | Make system configuration 3T an optional capability. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to make System Configuration 3T an optional capability and to harmonize with the VDL Mode 3 MASPS.

Modify Section 5.2.2.4 as follows:

5.2.2.4	System configurations. VDL Mode 3 equipment shall recognize and support the set of system configurations identified in Table 5-4, with the exception of the optional 3T configuration.

Note 1.— All the configurations except 3T are called non-3T configurations.

Note 2.— See the Implementation Aspects of this manual for the applications and descriptions of each system configuration.

2.16.	Editorials

Some additional editorial changes to clarify requirements and testability of requirements.

Amendment Proposal

| Title: | Editorials |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on VDL Mode 3 Technical Specifications |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 5.2.4.4.3.4, 5.3.3.2, 5.4.3.3.1.1, 6.2.3.1.1, 8.4.3.2.4, 8.4.3.2.5, J.6.8.1 Table 5-18 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | Rmorgens@mitre.org |
| Category: | EDITORIAL |
| Problem description: | Miscellaneous fixes for readability and testability |
| Background: | [Validation Details] Validated by inspection. |
| Backwards compatibility: | YES. |
| Amendment Proposal: | Fix wording for clarity or testability. See attached for specific changes to TM. |
| WG-M Status: | PROPOSED 19/8/02 |

The following modifications are needed in the Manual on VDL Mode 3 Technical Specifications to improve clarity and to harmonize with the VDL Mode 3 MASPS.

Modify Section 5.2.4.4.3.4 as follows:

5.2.4.4.3.4	Reservation request retransmission. The aircraft radio shall select a downlink M-burst LBAC for random access Reservation Request Retransmission based on the process of Appendix D and the random number generator algorithm of Appendix C. The Reservation Request Retransmission shall be repeated until one of the following occurs: (1) a valid response is received, (2) a poll is received, or (3) the number of retransmissions exceeds NM1 (defined in Section 5.2.3.3). The value of NM1 is given in Table 5-7a).  When the number of reservation request retransmissions exceeds NM1, random access reservation request retransmission shall be terminated.  After the random access reservation request retransmissions have been terminated, the aircraft station shall continue to provide the data reservation in poll responses.

Modify Section 5.3.3.2 as follows:

5.3.3.2	Parameter N1 (Maximum frame group size). The N1 parameter shall indicate the maximum frame group size in octets. The value of parameter N1 includes all DLS frame headers of its component frames.

Modify Section 5.4.3.3.1.1 as follows:

5.4.3.3.1.1	General public parameters. The general public parameters’ XID information field shall be encoded as defined in ISO 8885, with the addition of private parameter data link layer subfields as defined in ISO 8885. The format identifier, hexadecimal 82, shall be used (per ISO 4335.2, Annex C) to identify the public parameter list identified in ISO 8885. The VDL Mode 3 shall use the public parameter group ID of hexadecimal 80 to indicate negotiation of the common parameters. The public parameter set ID shall be included in CTRL frames if other public parameters are included; the public parameter set ID shall not be included in the CTRL frame if other public parameters are not included. Only the public parameters Unique Identifier (also known as Parameter Set Identifier), Maximum information field length - transmit and receive (N1), Acknowledgment timer (T1), and Retransmission attempts (N2) shall apply to the VDL Mode 3 system.

Note.— A Control Frame example is contained in the Manual on the Implementation of the Very High Frequency (VHF) Digital Link Mode 3 (VDL Mode 3) of ICAO.

Modify title to Section 6.2.3.1.1 as follows, so the definition for the term GNIp-group can be found:

6.2.3.1.1	GNIp-Group Addressing. For the group of GNIs that are associated with the same ATN router, a primary GNI, represented as GNIp, shall be designated. Each GNIp shall be assigned a non-zero identifier that is unique with respect to the set of GNIps that an aircraft can contact at any one time. The identifier shall be 6 bits in length and is denoted the ground subnetwork address per 5.3.2.4.1. The group of GNIs associated with a GNIp is denoted the GNIp-group.

Modify Section 8.4.3.2.4 and 8.4.3.2.5 as follows:

8.4.3.2.3	Truncated mode formatting. The Voice Unit shall delay transmission of truncated bursts by 16 symbol periods relative to the nominal CTS signal.

Note.— This allows for 16 symbol periods of positive or negative timing drift.

8.4.3.2.4	The MID field of the V/D (voice) burst header shall be set to Downlink voice, TS2, to indicate to the receiver that the burst is truncated.

8.4.3.2.5	If the Voice Unit is notified that it is to operate in normal or free running mode, the voice unit shall transmit full length V/D (voice) bursts. In normal mode, the MID field of the V/D (voice) burst header shall be set to Uplink voice for the ground station and to Downlink voice, TS1, for the aircraft station. In free running mode, the MID field of the V/D (voice) burst header shall be set to Downlink voice, TS3. The Voice Unit shall transmit the bursts at the nominal CTS signal.

Modify Table 5-9 as follows:

Table 5-9.  Conditions for voice media access (Aircraft Station)

|  | Voice signal field* encoding |
| --- | --- |
| Timing state | Ground access | Occupied | Voice channel idle |
| Initial TS0** | No Access | No Access | No Access |
| Normal TS1 | No Access | Access permitted if access granted in previous MAC cycle | Access |
| Truncate TS2** (non-3T) | Access | Access | Access |
| Transition**(3T only) | No access | No access | No access |
| Free Running TS3** | Access | Access | Access |

*	Defined in Appendix B,  2.1.4.

**	The aircraft station does not receive Voice Signal Field Encoding information in these cases.

Modify Table 5-18 as follows:

Table 5-18.  Timer T_ack parameter

| Parameter ID | 0 | 0 | 0 | 0 |  | 1 | 0 | 1 | 1 | Timer T_ack (ground station) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter length | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 1 |  |
| Parameter value | v8 | v7 | v6 | v5 |  | v4 | v3 | v2 | v1 | Value |

Modify Appendix J, Section 6.8.1 as follows:

6.8.1    Incorrect format. When the XDCE receives from the peer XDCE a VDL Mode 3 DATA Packet with incorrect format or whose packet sequence number (PS) is not within the defined window, it shall discard the received packet and send a VDL Mode 3 REJECT Packet to the peer XDCE via the Internetworking Process.  Otherwise, the ISO 8208 subnetwork interface will never be capable of resequencing out of order packets.  The VDL Mode 3 Packet shall indicate a value of PR for which retransmission of the VDL Mode 3 DATA Packets is to begin. The XDCE shall discard subsequent out-of-sequence VDL Mode 3 DATA Packets whose receipt occurs while the VDL Mode 3 REJECT Packet response is still outstanding.

2.17.	System Configuration 1V3D/1V2D - Implementation Aspects

Amendment Proposal

| Title: | 1V3D/1V2D System Configuration Descriptions |
| --- | --- |
| AP working paper number and date | M5/WPx 19 Aug 2002 |
| Document(s) Affected: | Manual on the Implementation of the VDL Mode 3 |
| Document Version: | Pre-release ICAO Doc version |
| Sections of Documents Affected: | 1.3.2, 1.3.3 |
| Coordinator: | Robert Morgenstern |
| Coordinator's Address: | 7515 Colshire Drive, M/S N660 McLean, VA 22102 USA |
| Coordinator's Phone: | +1 703 883 7846 |
| Coordinator's Fax: | +1 703 883 1367 |
| Coordinator's E-mail Address: | rmorgens@mitre.org |
| Category: | ESSENTIAL |
| Problem description: | Need to support a voice and data capable system configuration that can support at least 200 simultaneous users that do not have a high data demand per user. |
| Background: | [Validation Details] Validated by inspection. |
| Backwards compatibility: | Yes. This is only affecting guidance material. |
| Amendment Proposal: | See attached for specific changes to IA to support system configurations 1V3D and 1V2D. |
| WG-M Status: | PROPOSED 19/8/02 |

Modify Sections 1.3.2 and 1.3.3 in the Manual on the Implementation of the VDL Mode 3 as follows:

1.3.2	The 4-slot configurations include the following:

a)	4V. Provides four voice channels (no data) in one 25 kilohertz (kHz) channel. This mode may, as an option, include downlink M channel transmissions and features such as urgent/priority access, semi-automatic frequency change and caller ID.

b)	2V2D. Provides two voice and two data channels in one 25 kHz channel. These are paired so that one user group uses one voice and data time slot pair and a second, independent, group uses the other voice and data pair.

c)	3V1D. Provides three voice and one data channel in one 25 kHz channel. The three voice channels are completely independent; however, the single data channel is shared by the three user groups.

d)	3T. Provides a trunked capability shared by all users in one 25 kHz channel in which one out of four time slots is available for voice or data and two out of four time slots are available exclusively for data. The fourth time slot is used exclusively for channel management functions.

e)	1V3D.  Provides independent voice and data using one time slot for voice and three time slots for data by a single user group. This is used to support sectors with more than 60 users that also require real-time voice service.  Can support up to 240 addressed aircraft in one (large) user group.

1.3.3	The 3-slot configurations include the following:

a)	3V. Provides three voice channels (no data) in one 25 kHz channel. This mode is analogous to 4V, but provides more propagation guard time.

b)	2V1D. Provides two voice and one data channel in one 25 kHz channel. This mode is analogous to 3V1D, but provides more propagation guard time.

c)	3S. Provides a single voice channel in one 25 kHz channel. The same digital voice bit-stream can be transported on each of three time slots used by three separate ground sites to provide coverage over an area larger than that which could be provided by a single ground site.

d)	2S1X. Provides one wide area voice channel for two separate ground stations and reserves another independent channel in one 25 kHz channel. The independent channel is defined separately in its own beacon.

e)	1V2D. Provides independent voice and data using one time slot for voice and two time slots for data by a single user group. This is used to support sectors with more than 60 users that also require real-time voice service. Can support up to 240 addressed aircraft in one (large) user group.

# Recommendation

WG-M is encouraged to consider these Amendment Proposals and their resolutions.