ATTACHMENT A

AMENDMENT PROPOSAL SUMMARY

| AP # | Problem | Needed Change | Sections Affected | WG-M Status | AEEC Requested Action |
| --- | --- | --- | --- | --- | --- |
| 106 | Out of sequence frames are duplicated | Reduce the maximum value of the k-window from 7 to 4. | Table 5-5 | Proposed | Approve |
| 108 | Inconsistency of T1 timer definition. T1 timer is linked to XID_CMD frame only | T1 timer needs to be linked to XID_CMD, INFO, RR(P=1), SREJ (P=1), and FRMR frames | 5.3.4.6 | Proposed | Approve |
| 12 | “Join” and “Leave” Events not reported to the ATN Router | “Join” and “Leave” events need to report the availability status of peer ATN routing. | 5.4.2.7.4 | Proposed | Disapprove (See AP-19) |
| 107 | Modification of SREJ information field modifies HDLC procedures. | Add clarifying text. | 5.3.11.2 | Proposed | Disapprove |
| 7 | Existing text supports call requests from the ground | Fix text to conform with section 6.6.3.2 | 6.3.2.4 | Proposed | Keep pending for further study |
| 13 | There is no requirement in the Tech Manual to generate a handoff event to IS-SME | A requirement needs to be added to generate a handoff event to the ATN IS-SME to artificially force a connection establishment without triggering the ES-IS and the IDRP routing protocols. | TBD | Proposed | Keep pending for further study |
| 15 &100 | The title of the TG1 timer specified in section 6.5.4.3.1 appears to be incorrect | Remove the word minimum from “minimum frequency dwell time”. Add a statement to indicate the action recommended upon receipt of an uplink from a preferred ground station. | 6.5.4.3.1 | Proposed | Keep pending for further study |
| TBD-J | There are redundant FRMR frames being sent. | Remove “Send a FRMR in the FRM mode. | 5.3.4.4 | Proposed | Keep pending for further study |
| TBD-K | When there is no Autotune, the aircraft does not follow normal retransmission procedures on the XID_CMD_HO(P=1) | Modify the last clause of the last sentence so that normal retransmissions are followed for XID_CMD_HO(P=1) | 5.4.4.9.3 | Proposed | Keep pending for further study |
| 19 | Definition of the router NET is ambiguous and does not agree with current implementation | Include the VDL Specific DTE addressing (VSDA) in the ground station GSIF. | 6.3.2.3, 5.4.2.7 | Proposed | Approve |
| 20 | The subnetwork connection establishment and maintenance sections are not very clear | Clarifying information was added to sections 6 6 3 2 1, 6.6.3.2.2, 6.6.3.3.1, and 6.6.3.3.2. | 6.6.3.2, 6.6.3.3 | Proposed | Approve |
| 102 | The means of passing the calling aircraft address to a called ATN Air/Ground Router is not identified | Add text in the guidance material that presents a standard way for a VDL Mode 2 RGS to provide the calling aircraft address. | 1.3.3 | Proposed | Approve |
| TBD-A | There is no fixed means of disconnecting a link in a multiple services environment. | Maintain the link for the duration of timer TG5 | 5.4.4.6.6 | Proposed | Approve |
| TBD-B | Timers T24 &T25 cause increased transmissions for verification of connection that was accomplished by other layers | Remove the timers T24 and T25 from Table 6-1. Add R27 to Table 6-1. | Table 6-1 | Proposed | Approve |
| TBD-C | The current addressing of DTE does not include he field length. | Change text to add field length | 6.3.2.1 6.3.2.1.1 | Proposed | Approve |
| TBD-D | Current text in the Tech Manual interprets aircraft initiated handoff capability as an optional feature. | Change the text to show aircraft initiated handoff as a requirement. | 5.4.4.6 | Proposed | Approve |
| TBD-E | Section 7.2.1 implies that ISH PDU is included in every Call packet. This causes unnecessary overhead. | Change the text to include ISH PDU only when Routing initiation is required | 7.2.1 | Proposed | Approve |
| TBD-F | The Tech manual implies that any bad packet would cause a reject to be generated. | Change text to reflect that only a data packet with an invalid P (s) field will cause the Reject to occur. | 6.2.3 | Proposed | Approve. |
| TBD-H | Current text has the aircraft DTE or ground DCE sending a Reject when it receives a packet with a bad sequence number. | Text should be changed to send a Reject when a DATA packet is received with a bad sequence number. | 6.6.4 | Proposed | Approve. |