AERONAUTICAL MOBILE COMMUNICATIONS PANEL

WORKING GROUP M

Fifth Meeting

St Petersburg, Russia

19 – 23 August 2002

VDL MODE 4

Amendment Proposal

| Title: | Editorial corrections involving vertex count and a/d flag definition |
| --- | --- |
| AP working paper number and date | AMCP WGM5 WPX |
| Document(s) Affected: | Manual on Detailed Technical Specifications for the VDL Mode 4 Digital Link |
| Document Version: | VM4 TM EC chm 03-04-02 |
| Sections of Documents Affected: | Table 1-2, Table 3-31, Section 1.3.2, Table 1-66 |
| Coordinator: | N. Fistas |
| Coordinator's Address: | Eurocontrol, Brussels |
| Coordinator's Phone: | +32 2 729 4777 |
| Coordinator's Fax: | +32 2 729 3511 |
| Coordinator's E-mail Address: | nikolaos.fistas@eurocontrol.int |
| Category: | MINOR |
| Problem description: | No encoding exists for ‘vertex count’. The definition of a/d flag has been lost. |
| Background: | The current version of the TM, which includes the changes agreed at the AMCP WG-M/2 meeting, includes a field ‘vertex count’ in Table 3-30. However there is no encoding specified for this field. The changes to the TM agreed at the AMCP WG-M/2 meeting interchanged the locations of the a/d flag and the TCP change flag between the general burst and the sync burst. In this process, the definition of the a/d flag appears to have been lost. |
| Backwards compatibility: |  |
| Amendment Proposal: | Include encoding for ‘vertex count’. Reintroduce the lost definition of the a/d flag.. |
| WG-M Status: | Open |

Insert new row at alphabetic order in Table 1-2

Table 1-2. Symbols and variables for link layer protocols and services

| Parameter | Name | Section or table defined in |
| --- | --- | --- |
| vc | vertex count | Table 3-31 |

Insert new row at the beginning of Table 3-31

# Table 3-31. Regional multicast block field encoding

| Subfield | Encoding | Notes |
| --- | --- | --- |
| vertex count (vc) | 0: vertex 1 1-15: vertex 2 to vertex 16 | vertex k corresponds to radial k and distance k |

Insert new text:

1.3.2.6	Autonomous/directed flag

The autonomous/directed (a/d) flag shall be encoded as defined in Table 1-66 if the message ID (see Table 1-6) indicates that the burst is synchronisation burst.  Otherwise it shall be reserved for future definition and set equal to 1.

Reinstate old text in new first row of Table 1-66 (keeping current rows):

Table 1-66. Synchronization burst field encoding(fixed data field)

| Subfield | Range | Encoding | Notes |
| --- | --- | --- | --- |
| autonomous/directed (a/d) | Boolean | 0 = autonomous slot selection (including directed rate), 1 = directed slot selection or ground station transmission | Identifies whether the synchronization burst is an autonomous or directed burst |