Amendment Proposal

Title:

| Original: AMCP WG M/WP 24 | Receiver Sensitivity |
| --- | --- |
| AP Working paper number and date: | Attachment to WGM/5 report 23 August 2002 |
| Document(s) affected: | AMSS SARPs Annex 10, Chapter 4 |
| Sections of document affected: | New section 4.2.3.4.6 |
| Coordinator: | Rohan Hiesler |
| Co-ordinator’s address: | 99 City Road, London, England EC1Y 1AX |
| Co-ordinator’s phone: | +44 (0) 207 728 1161 |
| Co-ordinator’s fax: | +44 (0) 207 728 1175 |
| Co-ordinator’s email: | Rohan_Hiesler@inmarsat.com |
| Category: | Critical |
| Problem Description: | Modern aircraft are now operating with many different transmitting equipment onboard, and in environments where there are many external transmitters. Determining the whether a piece of equipment can be certified to operate in the environment it is being placed in will be made easier if the receiver interference susceptibility is known by the certifying agency. To facilitate this, all SARPs should state this parameter |
| Background: | Since the last amendment to the AMSS SARPs were accepted by the AMCP/6 meeting in March 1999, there has been considerable activity within several international standardization bodies which has resulted in the adoption of requirements which are now at variance with the corresponding Requirements or Recommendations in the ICAO AMSS SARPs. The bodies which have been most active, and continue to be most active is the Radio Technical Committee for Aeronautics (RTCA), Special Committee 165, who have been responsible for developing the document DO210, which are the Minimum Operational Performance requirements for Geosynchronous Orbit Aeronautical Mobile Satellite Services (AMSS) Avionics. This Committee recently passed Change 1 and Change 2 to DO210D. |
| Backwards Compatibility: | All existing AESs do comply with requirements |
| Amendment Proposal: | Add a new section 4.2.3.4.6 |
| WG-M Status: | Resolved 22 August 2002 |
|  | Approved |

Proposed new section 4.2.3.4.6.

Receiver Interference Susceptibility. Receivers meeting the requirements of these SARPs shall operate satisfactorily in the presence of interference at RF levels at the receivers input port not exceeding the following tabulated levels.

Frequency Range		Maximum Interference Level

470 to 1450 MHz		+3 dBm

1450 to 1529 MHz		Decreases linearly in decibels from

+3 dBm at 1450 MHz to -72 dBm

at 1529 MHz

1529 to 1560 MHz		-163.3 dBm

1560 to 1626.5 MHz		Increases linearly in decibels from

-72 dBm at 1560 MHz to +3 dBm

at 1626.5 MHz.

1626.5 to 1660.5 MHz		+47.8 dBm

1660.5 to 18000 MHz		+3 dBm

Title:

| Original: AMCP WG M/WP 24 | Harmonics, Noise and Spurious Alignment |
| --- | --- |
| AP Working paper number and date: | Attachment to WGM/5 report 23 August 2002 |
| Document(s) affected: | AMSS SARPs Annex 10, Chapter 4 |
| Sections of document affected: | Table 4-3 |
| Coordinator: | Rohan Hiesler |
| Co-ordinator’s address: | 99 City Road, London, England EC1Y 1AX |
| Co-ordinator’s phone: | +44 (0) 207 728 1161 |
| Co-ordinator’s fax: | +44 (0) 207 728 1175 |
| Co-ordinator’s email: | Rohan_Hiesler@inmarsat.com |
| Category: | Critical |
| Problem Description: | In the months since AMCP/6, interference issues have been discussed in detail, and the table in section 2.2.1 reflects the latest values that have been adopted by the RTCA. However, discussions are still ongoing, particularly for the 1610.6 to 1613.8 MHz Radio Astronomy band. It would be expected that some of these values would change again in the future. |
| Background: |

Since the last amendment to the AMSS SARPs were accepted by the AMCP/6 meeting in March 1999, there has been considerable activity within several international standardization bodies which has resulted in the adoption of requirements which are now at variance with the corresponding Requirements or Recommendations in the ICAO AMSS SARPs. The bodies which have been most active, and continue to be most active are:

a)	European Technical Standards Institute (ETSI), who have been developing a standard for Aircraft Earth Stations entitled -  EN 301 473 - Aircraft Earth Stations (AES) operating under the Aeronautical Mobile Satellite Service (AMSS)/ Mobile Satellite Service (MSS) and/or the Aeronautical Mobile Satellite on Route Service (AMS(R)S)/ Mobile Satellite Service (MSS). This standard was recently adopted by the ETSI body Satellite Earth Stations (SES) – Technical Committee, at its forty sixth meeting 9th – 12th October 2000.

Radio Technical Committee for Aeronautics (RTCA), Special Committee 165, who have been responsible for developing the document DO210, which are the Minimum Operational Performance requirements for Geosynchronous Orbit Aeronautical Mobile Satellite Services (AMSS) Avionics. This Committee recently passed Change 1 to DO210.

| c) Committee European de Post et Telecommunications (CEPT) Spectrum Engineering group (SE) 28. This group has been the working group which is investigating the spurious emission requirements for AES, and specifically into the Radio Astronomy bands 1610.6 to 1613.8 MHz and 1660 to 1670 MHz. This work is still ongoing, and values, particularly in the 1610.6 to 1613.8 MHz band are likely to change in the future. |
| --- |
| Backwards Compatibility: | All existing AESs do comply with the proposed requirements |
| Amendment Proposal: | Replace Table 4-3. |
| WG-M Status: | Resolved 22 August 2002 |
|  | Approved |

New table 4-3:

Frequency (MHz)		Power Density

0.01 to 15251	-135	dBc/4 kHz

1525 to 1559	-203	dBc/ 4kHz

1559 to 1585	-155	dBc/MHz

1585 to 1605	-143	dBc/MHz

1605 to 1610	-117	dBc/MHz

1610 to 1610.6	  -95	dBc/MHz

1610.6 to 1613.8	  -80	dBW/MHz5,7

1613.8 to 1614	  -95	dBc/MHz

1614 to 1626.5	  -70	dBc/4 kHz

1626.5 to 1660	  -70	dBc/4 kHz2,3,4,5,6

1660 to 1660.5	-49.5	dBW/20 kHz2,3,4,5,6,7

1660.5 to 1670	-49.5	dBW/20 kHz4,5,7

1670 to 1735	  -60	dBc/4 kHz

1735 to 12000	-105	dBc/4 kHz

12000 to 18000	  -70	dBc/4 kHz

1.	AMSS operations are permitted in the MMS (maritime) band which has been extended to include 1525-1530 MHz.

2.	Within the transmit band, excluding the frequency band within (35 kHz of the carrier.

3.	The –55 dBc/4kHz spectrum level in this table is equivalent to –55 – 10 log10(4000/SR) dBe (relative to the maximum envelope) under the definitions in Section 2.2.4.2.16.

4.	For wide band spurious the limit is –39.5 dBW/MHz.

5.	This level is not applicable for intermodulation products

6.	The upper limit for the excess power for any narrow-band spurious emission (excluding intermodulation products) within a 30 kHz measurement bandwidth shall be 10 dB above the power limit in this table.

7.	Note that the power density is expressed in terms of absolute power (dBW) in some instances, and in terms relative to carrier power (dBc) in other instances.

Title:

| Original: AMCP WG M/WP 24 | Intermodulation requirement |
| --- | --- |
| AP Working paper number and date: | Attachment to WGM/5 report 23 August 2002 |
| Document(s) affected: | AMSS SARPs Annex 10, Chapter 4 |
| Sections of document affected: | New section of 4.2.3.5.7.4 and new table 4-3 bis. |
| Coordinator: | Rohan Hiesler |
| Co-ordinator’s address: | 99 City Road, London, England EC1Y 1AX |
| Co-ordinator’s phone: | +44 (0) 207 728 1161 |
| Co-ordinator’s fax: | +44 (0) 207 728 1175 |
| Co-ordinator’s email: | Rohan_Hiesler@inmarsat.com |
| Category: | Critical |
| Problem Description: | A Class 4 AES is capable of transmitting at least 1 C-channel through a common High Power Amplifier. This will result in intermodulation products being produced at the output of the HPA due to non-linearities within the HPA. These intermodulation products are a spurious emission, but need to be treated differently from other types of spurious emission. The level of the intermodulation product, when they fall outside the transmit pass band of the terminal, will be affected by the filtering employed in the diplexer. The values can be met by appropriate HPA design, and diplexer filter rejection. |
| Background: | Since the last amendment to the AMSS SARPs were accepted by the AMCP/6 meeting in March 1999, there has been considerable activity within several international standardization bodies which has resulted in the adoption of requirements which are now at variance with the corresponding Requirements or Recommendations in the ICAO AMSS SARPs. The bodies which have been most active, and continue to be most active is the Radio Technical Committee for Aeronautics (RTCA), Special Committee 165, who have been responsible for developing the document DO210, which are the Minimum Operational Performance requirements for Geosynchronous Orbit Aeronautical Mobile Satellite Services (AMSS) Avionics. This Committee recently passed Change 1 to DO210. |
| Backwards Compatibility: | All existing AESs do comply with requirements |
| Amendment Proposal: | New section and table |
| WG-M Status: | Resolved 22 August 2002 |
|  | Approved |

New section:

4.2.3.5.7.4	For multicarrier AES, when transmitting two equal carriers with a total power equal to the maximum allowable operating EIRP of the AES, the power level of each of the intermodulation products shall not exceed the levels specified in table 4-3 bis.

New table:

Table 4-3 bis Maximum Intermodulation Product levels.

Frequency MHz				IM Level

Below 1610				<-70 dBc

1610 to 1614				-64 dBc

1614 to 1671.25				-24 dBc

1671.25 to 1711				-29 dBc

1711 to 1735				-34 dBc

1735 to 18000				<-70 dBc

Title:

| Original: AMCP WG M/WP 24 | Table 4.30 Corrections |
| --- | --- |
| AP Working paper number and date: | Attachment to WGM/5 report 23 August 2002 |
| Document(s) affected: | AMSS SARPs Annex 10, Chapter 4 |
| Sections of document affected: | Table 4.30 |
| Coordinator: | Rohan Hiesler |
| Co-ordinator’s address: | 99 City Road, London, England EC1Y 1AX |
| Co-ordinator’s phone: | +44 (0) 207 728 1161 |
| Co-ordinator’s fax: | +44 (0) 207 728 1175 |
| Co-ordinator’s email: | Rohan_Hiesler@inmarsat.com |
| Category: | BUG |
| Problem Description: |

- For most ERROR conditions in the r2 DTE RESTART REQUEST states, the MOPS and SARPs  reference Note 3. The RTCA DO210D MOPS Note 3 actually states "The received packet is not forwarded to the SSNIW", which is consistent with 8208 and X.25. SARPs Note 3 actually states "No action is taken by the DCE." This is obviously incorrect, since a state transition occurs, a diagnostic code is declared, etc. SARPs Table 4.30 Note 3 needs to be corrected.

In Table 4-30, the row labelled “Restart request”, the r1 column should not reference “Note 1” but “(4.2)”. The r3 column should reference “(4.3)”, not “(4.2)”. This table contains parenthetical references to ISO 8208 for the Normal responses by the DCE. e.g., it has the correct reference to 8208 Section 4.4 for the r3 case of receipt of  Restart Confirmation packet (row 7). However, SARPs is lacking a reference to Section 4.2 for the r1 case of receipt of a Restart Request (back in row 6); where such a reference is expected, there is instead the unnecessary redundant reference to Note 1. For the r3 case in row 6, the SARPs incorrectly references 8208 Section 4.2. This is the "restart collision" case (the DCE and DTE both indicating/requesting a restart at the same time), which should reference 8208 Section 4.3 ("Restart collision") rather than 4.2 ("Receiving a restart indication").

- In table 4-30, last column, for the row starting “Restart request or restart confirmation packet with format error”, after the entry “A = ERROR D = 38, 39, 81 or 82”, add (see Note 3). Should such a packet be received with a format error, the DCE should not  forward it to the IWF. This is made clear by referencing Note 3.

- In Table 4-30, the last row, column r2 the reference to note 4 should be changed to Note 3. Note 4 applies to the entire column. In this cell, there should be a reference to Note 3, which is more explicit.

Table 4-30, Note 1 is basically correct, but could benefit from some clarification, and should be similar to the corresponding note in the MOPS. The proposed new note should be re written. What the SSNL in the DCE does in response to a RESTART REQUEST from the DTE is to execute a separate connection release procedure for each VC associated with the originating DTE (reference ARINC 741 Part 2 Section 4.3.4.2.1). Per MOPS Note 1, the received RESTART REQUEST packet is forwarded by the DCE to the SSNIW sublayer (known as the IWF in the SARPs). What is specified in the earlier referenced SDM material (in Module 1 Appendix 10 Sections 4.1.5.x) is that the SSNIW is to issue an SN-DISCONNECT request primitive for each VC. The SN-DISCONNECT primitives map to CONNECTION RELEASED SNPDUs, which are sent to the GES (reference SDM Section 7.3.2.1 and MOPS Figure 2-2). This in turn ultimately results in CLEAR INDICATION packets being delivered to the far-end DTE for each applicable VC. The DCE also sends a RESTART CONFIRMATION packet to the originating DTE, indicating that it effectively performed the RESTART REQUEST function. The SARPs version of Note 1 states "Receipt of a restart request packet causes the DCE to issue a clear request packet to the IWF for each VC associated with the DCE entity." It could be implemented this way, but the MOPS more logically states that the received RESTART REQUEST packet itself (not a series of CLEAR REQUEST packets) is forwarded to the SSNIW (or IWF) (which then performs the necessary interworking functions). The SARPs note would thus be corrected and clarified if it is replaced by the MOPS version (aligned to the SARPs style and usage peculiarities).

- Table 4-30 Note 4 should be rewritten. The text of the existing version of the SARPs Note 4 is incorrect ("The restart request packet is not forwarded to the IWF") -- in fact, the MOPS Table 2-4 Note 1 states just the opposite: "The RESTART REQUEST packet is forwarded to the SSNIW ...", which makes sense (since the received packet has to be processed internally on the SSNIW/SSND side as well as on the DTE side). Since and both documents reference Note 4 in their r2 state (3rd) column header, the SARPs should use the MOPS form of Note 4: "If the DCE enters the r3 state, then the RESTART CONFIRMATION is not sent." This note gives pertinent information regarding the r2 state, in which the DCE normally DOES send a RESTART CONFIRMATION, but not when it first enters the r3 state from the r2 state.

| - In the notes of table 4-30, Note 5 needs to be modified - see discussion above. |
| --- |
| Background: | Since the last amendment to the AMSS SARPs were accepted by the AMCP/6 meeting in March 1999, there has been considerable activity within the RTCA which has resulted in the adoption of requirements which are now at variance with the corresponding Requirements or Recommendations in the ICAO AMSS SARPs. The Radio Technical Committee for Aeronautics (RTCA), Special Committee 165, who have been responsible for developing the document DO210, which are the Minimum Operational Performance requirements for Geosynchronous Orbit Aeronautical Mobile Satellite Services (AMSS) Avionics. This Committee recently passed Change 1 and Change 2 to DO210. |
| Backwards Compatibility: | All existing AESs do comply with requirements |
| Amendment Proposal: | Modify table 4.30 as shown below. |
| WG-M Status: | Resolved 22 August 2002 |
|  | Approved |

Modified Table 4-30

Table 4-30. DTE effect on DCE restart state.

|  | DCE restart states (see Notes 6 and 7) |
| --- | --- |

Packet received from DTE

Packet Layer READY

(see Note 1) r1

DTE RESTART

REUEST

(see Note 4) r2

DCE RESTART

INDICATION

(see Note 5) r3

Packets having a packet type identifier shorter than

| 1 octet with assigned logical channel identifier <>0 | See Table 4-31 |
| --- | --- |

A = ERROR

S  = r3

D = 38

| (see Note 3) | A = DISCARD |
| --- | --- |
| Packet supported by DCE other than restart with a logical channel identifier of 0 |

A= DIAG

D = 36

A = DIAG

D = 36

A = DIAG

| D = 36 |
| --- |
| Packet with a packet type identifier which is undefined or not supported by DCE and with assigned logical channel identifier <>0 | See Table 4-31 |

A = ERROR

S = r3

D = 33

| (see Note 3) | A = DISCARD |
| --- | --- |
| Restart request, or reset confirmation with an assigned logical channel identifier <>0 | See Table 4 –31 |

A = ERROR

S = r3

D = 41

| (see Note 3) | A = DISCARD |
| --- | --- |
| Restart request |

A = NORMAL

(see Note 1 4.2)

| S = r2 | A = DISCARD |
| --- | --- |

A = NORMAL (4.32)

S = p1 or d1 (see Note 2)

Request confirmation

A = ERROR

S = r3

D = 17

(see Note 8)

A = ERROR

S = r3

D = 18

(see Note 3)

A = NORMAL (4.4)

S = p1 or d1 (see Note 2)

Restart request or restart confirmation with format error

A = DIAG

| D = 38, 39, 81, or 82 | A = DISCARD |
| --- | --- |

A = ERROR

D=38, 39, 81, or 82

| (see Note 3) |
| --- |
| Call setup, call clearing, data interrupt, flow control, or reset packet | See Table 4-31 |

A = ERROR

S = r3

D = 18

| (see Note 3) | A= DISCARD |
| --- | --- |
| Packets having a packet type identifier shorter than 1 byte and logical channel identifier to 0 |

A = DIAG

D = 38

A = ERROR

S = r3

D = 38

| (see Note 3) | A=DISCARD |
| --- | --- |
| Packet with a packet type identifier which is undefined or not supported by DCE and a logical channel identifier equal to 0 |

A = DIAG

D = 33

A = ERROR

S = r3

D = 33

| (see Note 3 4) | A= DISCARD |
| --- | --- |

Notes:

Receipt of a restart request packet causes the DCE to issue a clear request packet to the IWF for each VC associated with the DCE entity The AES subnetwork has no restart states. Receipt of  restart request causes the DCE to respopnd with a restart confirmation. This restart request packet is forwarded to the IWF, which responds by executing a connection release procedure for each VC associated with the DTE/DCE interface. This is equivalent to the originating DTE separately issuing a clear request for each VC, i.e. the equivalent of a restart request.

The VC channels are returned to the state p1, the PVC are returned to state D1

No action is taken by the DCE The received packet is not forwarded to the IWF

The restart request packet is not forwarded to the IWF If the DCE enters the r3 state, then the restart confirmation is not sent.

The DCE upon entering the r3 state checks for the completion of r2 processing and issues an ISO 8208 restart indication packet to the DTE, when the r3 state is entered via the r2 stat. If the r3 state is not entered via the r state, the DCE performs all the actions normally performed when entering r2, and issues an ISO 8208 restart indication packet to the DTE, and send a clear request packet to the IWF for each VC associated with the DCE entity. The DCE upon entering the r3 state, checks for the completion of the r2 processing. If the r3 state is entered via the r2 state, the DCE discards the received packet and indicates a restart by transmitting to the DTE a restart indication packet with the cause ‘local procedure error’ and the appropriate diagnostic code. If the r3 state is not entered via the r2 state, the DCE performs all the actions normally performed when entering  r2 and issues an ISO 8208 restart indication packet to the DTE, and sends a restart request packet to the IWF (the equivalent of a clear request packet for each VC associated with the DCE entity).

Table entries are defined as follows: A=action to be taken, S=state to be entered, D=diagnostic code to be entered in packets to be generated as a result of this action, and discard indicates that the received packet is to be cleared from the buffers.

The number in the parentheses below an “A=normal” table entry is the paragraph in ISO 8208, second edition. The DCE shall take the same action as the one taken by the DTE, acting as a DCE, to perform nominal processing on the received packet. If no paragraph number is referenced, the normal processing is defined in the table entry.

The error procedure consists of entering the r3 state and sending a restart indication packet to the DTE

Title:

| Original: AMCP WG M/WP 24 | Table 4.34 corrections |
| --- | --- |
| AP Working paper number and date: | Attachment to WGM/5 report 23 August 2002 |
| Document(s) affected: | AMSS SARPs Annex 10, Chapter 4 |
| Sections of document affected: | Table 4.34 |
| Coordinator: | Rohan Hiesler |
| Co-ordinator’s address: | 99 City Road, London, England EC1Y 1AX |
| Co-ordinator’s phone: | +44 (0) 207 728 1161 |
| Co-ordinator’s fax: | +44 (0) 207 728 1175 |
| Co-ordinator’s email: | Rohan_Hiesler@inmarsat.com |
| Category: | BUG |
| Problem Description: |

- The reference to REJECT Packets in Note 6 should be removed since the Packet Retransmission facility is not supported, the REJECT packet will never be received, so all the Reject Packet references should be removed from the SARPs.

- There are no references to note 1 in the table. This is corrected by amending the text in the heading of the second part of the table.

| - The 4 occurrences of references to the ISO8208 document sections 7.1.5 and 7.1.6, in the last two rows of Table 4-34, are incorrectly prefixed with a “4”. This “4” should be deleted in the 4 instances. |
| --- |
| Background: | Since the last amendment to the AMSS SARPs were accepted by the AMCP/6 meeting in March 1999, there has been considerable activity within the RTCA which has resulted in the adoption of requirements which are now at variance with the corresponding Requirements or Recommendations in the ICAO AMSS SARPs. The Radio Technical Committee for Aeronautics (RTCA), Special Committee 165, who have been responsible for developing the document DO210, which are the Minimum Operational Performance requirements for Geosynchronous Orbit Aeronautical Mobile Satellite Services (AMSS) Avionics. This Committee recently passed Change 1 and Change 2 to DO210D. |
| Backwards Compatibility: | All existing DCEs and DTEs do comply with requirements |
| Amendment Proposal: | Modify table 4-34 as shown below. |
| WG-M Status: | Resolved 22 August 2002 |
|  | Approved |

Modified Table 4-34.

Table 4-34. DTE effect on DCE flow control transfer states

|  | DCE flow control transfer states (see Note 2) |
| --- | --- |
| Packet received from DTE |

DCE RECEIVE READY

f1

DCE RECEIVE NOT READY

f2

DATA packet with invalid PR

A = ERROR

S = d3

D = 2

(see Note 4)

A =ERROR

S = d3

D = 2

(see Note 4)

DATA packet with valid PR but invalid PS or user data field with improper format

A = ERROR

S  = d3

D = (see Note 5)

(see Note 4)

A = DEICARD

(process PR data)

DATA packet with valid PR with M-bit set to 1 when the user data field is partially full, or the D-bit is set to 1 (when not supported)

A = ERROR

S = d3

D = 165 or 166

(see Note 4)

A = DISCARD

(process PR data)

DATA packet with valid PR, PS and user data field with proper format

A = NORMAL

(forward)

A = DISCARD

(process PR data)

| (see Note 7) |
| --- |
|  | DCE flow control transfer states (see Notes1, 2 and 3) |
| Packet received from DTE |

DTE RECEIVE

READY

g1

DTE RECEIVE

NOT READY

g2

RR, or RNR packet with a valid PR (see Note 6) invalid PR

A = ERROR

S = d3

D = 2

(see Note 4)

A = ERROR

S = d3

D = 2

(see Note 4)

RR Packet with a valid PR (see note 6)

A = NORMAL

(4.7.1.5)

A = NORMAL

(4.7.1.5)

S = g1

RNR packet with a valid PR (see Note 6)

A = NORMAL

(4.7.1.6)

S = g2

A = NORMAL

(4.7.1.6)

Notes:

The RR and RNR procedures are a local DTE/DCE matter and the corresponding packets are not forwarded to the IWF.

Table entries are defined as follows: A = action to be taken, S=the state to be entered, D=diagnostic code to be used in packets generated as a result of this action, and discard indicates that the received packets are to be cleared from the buffers.

The number in parentheses below an “A=normal” table entry is the paragraph number in ISO 8208, second edition. The DCE shall take the same action as those taken by the DTE to perform normal processing on the received packet. If no paragraph is referenced, the normal processing is defined in the table entry.

The error procedure consists of performing the specified actions when entering the d3 state (which includes forwarding a reset indication packet to the DTE) and sending a reset request packet to the IWF.

The diagnostic codes are as flows: D=1 for invalid PS; D=39 for a user data field greater than 128 octets; D = 82 for a user data field not octet aligned.

For RR, and RNR, or REJECT, packets, the presence of one or more octets beyond the third octet is considered an error. Although a valid P(R) may be accepted to update the status of outstanding data packets, the DCE shall invoke the error procedure defined in Note 4 (with D=39).

If possible, the DCE should process these packets normally. On the other hand, the DCE may define an internal mechanism to indicate that valid data packets have been discarded during a receive-not-ready condition. In this case when the receive-not-ready condition clears, the DCE should reset the logical channel, forwarding both the reset indication packet to the DTE (D=0, no additional information) and a reset request packet to the IWF.