VDL Mode 2 Technical Manual Amendments

WGM output to the VDL Mode 2 Technical Manual

SUMMARY

This paper is the summary of the review of the VDL Mode 2 Technical Manual by the WGM.  The review took into consideration all the open amendment proposals within the ICAO/AMCP WGM and other proposals based on the current implementation and systems interoperability.

# Recommendation

The WGM VDLM2 subgroup evaluated all amendments proposals and agreed on the following :

- Reject AP7, AP12, AP13, AP16, AP18, AP107.

- Keep pending AP100, AP204, AP208, AP209, AP211, AP212, AP213, AP214, AP215.

- Accept AP19, AP20, AP102, AP106, AP108, AP200, AP201, AP202, AP203, AP205, AP206, AP207, AP210.

The current document sections are organized by the type of recommendation.

Section 1

Reject

This AP was rejected due to the existence of AP 19.  It was agreed that AP19 resolves the same issue, and have a more comprehensive text.

| Title: Original: AMCP WGM/1 WP47 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#12 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Specific Requirements should be added to the VHF Management Entity (VME) section of the VDL SARPs or technical manual to support this capability. |
| Coordinator: | Damien Marce |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | Update |
| Problem description: | “Join” and “Leave” events not reported to ATN Router |
| Background: | The ATN routing process requires that the underlying sub-networks (e.g., VDL Mode 2) should report the availability status of peer ATN routing via the “join” and “leave” events. Currently, the VDL SARPs do not have this provision. The VHF ground stations broadcast the air/ground router availability information in the GSIF. Each GSIF contains ADM and optionally the ARS fields of the air/ground router NET that is reachable via that ground station. These NETs and the ground service provider ID’s should be forwarded to the ATN router IS-SME. The IS-SME is responsible for the selection of specific air/ground route based on owner preference and initiating subnetwork connection establishment. The GSIF needs to include a unique identification of each AGR to the airborne system. The a/c needs to be able to determine when handoff to a particular ground station within the domain of the same DSP will require transitioning to a different AGR. Thus simplifying the decision process and minimizing the possibility that the system will go NOCOMM. ARINC recommends the replacement of the components of the ATN NETs to include: Three Octets of the ADM Three Octets to be DSP defined to uniquely identify an AGR The new NETs should be used in the GSIF and other appropriate XID exchanges such a alternate ground station lists. Paragraph 5.4.2.7.4 and Figure 5-40 show a proposed ATN Router NET Parameter that includes the proposed fields. |
| Backwards compatibility: | Yes. This is the exact current implementation |
| Amendment Proposal: | See Attachment (Extract of WP-23, section 1.1 ARINC Response) |
| WG-M status: | REJECT |

5.4.2.7.4 ATN router NETs parameter. This parameter defines a list of ATN air-ground routers identified by the “administration identifier” (ADM) and a Three Octet User Defined subfields of their network entity titles (NETs). It shall be encoded as per Table 5-40.

Table 5-40. ATN router NETs parameter

| Parameter ID | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | ATN router NETs |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameter Length | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1 |  |
| Parameter value | a24 | a23 | a22 | a21 | a20 | a19 | a18 | a17 | ADM subfield |
|  | a16 | a15 | a14 | a13 | a12 | a11 | a10 | a9 |  |
|  | a8 | a7 | a6 | a5 | a4 | a3 | a2 | a1 |  |
|  | u24 | u23 | u22 | u21 | u20 | u19 | u18 | u17 | User Defined subfield |
|  | u16 | u15 | u14 | u13 | u12 | u11 | u10 | u9 |  |
|  | u8 | u7 | u6 | u5 | u4 | u3 | u2 | u1 |  |

This AP is rejected because it is equivalent to AP7.

| Title: Original: AMCP WGM/1 WP51 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#16 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.3.2.4 VDL SARPs |
| Coordinator: | Damien Marce |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | MINOR |
| Problem description: | The last sentence of section 6.6.3.2.4 states the “All CALL REQUESTs from the ground shall use, as the calling address, the ground DTE X.121 address”.. |
| Background: | Mixed support for this proposal. Ground DTE call establishment is required for expedited ground-initiated handoffs. |
| Backwards compatibility: |  |
| Amendment Proposal: | A proposal was delivered to prohibit VDL Mode 2 from allowing an initiation of a call establishment by the ground DTE. |
| WG-M status: | REJECT |

It is decided to reject this AP as far as the issue is embedded in AP215.

| Title: Original: AMCP WGM/1 WP53 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#18 | AMCP WG-M, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.6.3.1 VDL SARPs |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | TBD |
| Problem description: |  |
| Background: | In order to support Expedited Ground-Initiated Handoffs, the aircraft DTE will have to be initialized upon receipt of an XID_CMD_HO containing an Expedited Subnetwork Connection Parameter (which contains the 8208 Call Request packet(s)). |
| Backwards compatibility: |  |
| Amendment Proposal: | TBD |
| WG-M status: | REJECT |

6.6.3.1 Subnetwork entity initialization.  The ground DCE shall be initialized on receipt of a valid XID_CMD_LE.  The aircraft DTE shall be initialized on receipt of a valid XID_CMD_HO containing an Expedited Subnetwork Connection Parameter in the 8208 Call Request packet(s).

This AP does not do a comprehensive coverage of the SREJ cases. A more detailed text has to be submitted to reconsider the change to section 5.3.11.2.

| Title: Modification of SREJ interpretation | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 107 | AMCP WG-M/2 WP47 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.3.11.2 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | CLARIFICATION |
| Problem description: | Modification of SREJ information field modifies HDLC procedures |
| Background: | Modification of SREJ interpretation modifies the HDLC procedures in many ways: It is not possible to have several SREJ conditions because each frame will contain every not received I frames, ISO 4335 AMENDMENT 7 “Enhanced multi-selective reject option” shows a complex scenario that can not be applied: the second SREJ will acknowledge frame 0, although this frame has not been received, HDLC does not support acknowledgement of non contiguous I frames. Paragraph 5.3.11.2 shall contain the complete SREJ procedure to be applied with AVLC protocol and all the special cases described in ISO/4335. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Add following text: “Any out of sequence received frame, that is not duplicated, shall be held for later delivery and trigger a new SREJ for retransmission of all the not received I frames: SREJ frame shall have Nr set to first not received I frame and information field contains all the others. ” |
| WG-M status: | REJECT |

5.3.11.2    SREJ frame. The multi-selective reject option in ISO 4335 shall be used to request the retransmission of more than one INFO frame. The SREJ (F=0) frame shall be generated only after receipt of an out-of-order INFO (P=0). The SREJ (F=1) shall be generated only after receipt of an INFO (P=1), RR (P=1) or SREJ (P=1). The SREJ (P=1) frame shall be generated only in accordance with the procedures of 5.3.4.4. A DLE shall acknowledge those frames which were received correctly but out of order by including in the SREJ information field an octet with bits 6-8 set to the INFO frame's sequence number and bit 1 set to 1. Although the F bit may be set to 0, the SREJ frame shall always acknowledge INFO frames up to N(r)-1 (where N(r) is the value in the control field). Any out-of-order received frame, that is not duplicated, shall be held for later delivery and trigger a new SREJ for retransmission of all the not received I frames, i.e. SREJ frame shall have Nr set to first not received I frame and information field contains all the others.

Note.— AVLC has extended the standard ISO 4335 SREJ functionality to selectively acknowledge frames. In ISO 4335, the octets in the information field which were requesting retransmission of frames had bit position 1 set by default to 0.

It is decided to reject this AP as far as the issue is embedded in AP215.

| Title: Original: AMCP WGM/1 WP42 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP#7 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.3.2.4, (Section 6.3.2.4 in Technical Manual) |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: |  |
| Problem description: | Existing Text supports “Call Requests from the Ground”. |
| Background: | There are no Call requests from the ground. Refer to SARPs Section 6.6.6.3.2 (section 6.6.3.2 in Technical Manual) that ground can not initiate subnetwork connections. Also for resolution regarding expedited Ground Initiated Handoff, refer to ARINC 631-3 section 9.4.1.1 that modified this process to conform to the above Technical Manual explicit statement. |
| Backwards compatibility: |  |
| Amendment Proposal: | Delete references to “Call requests from the ground”. |
| WG-M status: | REJECTED |

6.3.2.4 Ground network DTE addresses. If the ground LME indicates support of ground network DTE addresses during link establishment, it shall accept and process addresses which follow the format used in the ground network. All CALL REQUESTs from the ground shall use, as the Calling Address, the ground DTEs X.121 address.

This AP has been rejected because no suggested text has been submitted since it has been proposed at WG-M/1.

| Title: Original: AMCP WGM/1 WP48 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#13 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | General Modifications to Technical Manual |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | TBD |
| Problem description: | Add requirement for VME to generate a handoff event to IS-SME |
| Background: | Although VDL Mode 2 subnetwork is based on ISO 8208 standard, it has unique requirements to address aircraft mobility. An enroute aircraft typically transitions through the line-of-sight coverage region of a VHF ground station within 10 to 15 minutes. This requires the VDL to reestablish air/ground connectivity seamlessly to reduce the RF overhead associated with the ATN route initiation. |
| Backwards compatibility: |  |
| Amendment Proposal: | As such the VME should generate a handoff event to the ATN IS-SME to artificially force a connection establishment without triggering the ES-IS and the IDRP routing protocols. Requirement should be added to provide this capability. |
| WG-M status: | REJECT |

Section 2

Keep Pending

Title:

| Original: AMCP WGM/1 WP50 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#15 and 100 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.5.4.3.1 of the VDL SARPs |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | MINOR |
| Problem description: | The title of the TG1 timer specified in section 6.5.4.3.1 of the VDL SARPs appears to be incorrect. |
| Background: | TG1 is the minimum time an aircraft should dwell on a frequency to detect valid uplinks if it has no link established (condition (c) in section 6.5.4.3.1). If the aircraft has already received an uplink on that frequency, it may establish a new connection or continue searching (condition (a) or condition (b) in section 6.5.4.3.1). |
| Backwards compatibility: |  |
| Amendment Proposal: | The title “minimum frequency dwell time” is not appropriate for TG1. It is recommended that the word “minimum” be deleted. Also, a statement to indicate the action recommended upon reception of an uplink from preferred ground system. |
| WG-M status: | PENDING |

# Current Text

5.4.3.1 Timer TG1 (minimum frequency dwell time). Timer TG1 shall be set to the minimum time (TG1) an aircraft LME dwells on a frequency while attempting to establish a link (in order to receive a valid uplink from at least one ground station). This timer shall be set by an aircraft LME (if it is not already running) when an aircraft tunes to a new frequency during a frequency search. It shall be cancelled when a valid uplink is received. On expiry of the timer the aircraft station shall:

a) establish a link with one of the ground-based systems from which it has received a valid uplink;

b) continue searching; or

c) if an aircraft does not detect any uplink traffic within TG1 seconds, it shall tune to the next

frequency in the search table.

Note 1.— The duration of TG1 should be chosen to ensure a valid uplink is received from at least one ground-based system before the timer expires

Note 2.— There is one Timer TG1 per LME.

5.4.3.1.1 Recommendation.— In order to allow an aircraft station an opportunity to link to its most preferred ground-based system, Timer TG1 should not be cancelled unless a

Valid uplink is received from its most preferred ground-based system.

# Proposed Text

Option 1

5.4.3.1 Timer TG1 (frequency dwell time).

Timer TG1 shall be set to the minimum time (TG1) an aircraft VME dwells on a frequency while attempting to establish a link (in order to receive a valid uplink from at least one ground station).

This timer shall be set by an aircraft VME when an aircraft tunes to a new frequency during a frequency search.

Timer TG1 shall be cancelled when a link is established.

On expiry of the timer TG1 the aircraft station shall tune another frequency, if another frequency is known.

Note 1.— The duration of TG1 should be chosen to ensure a valid uplink is received from at least one ground-based system before the timer expires.

Note 2.— There is one Timer TG1 per VME.

Option 2

5.4.3.1 Timer TG1 (frequency dwell time).

Timer TG1 shall be set to the minimum time (TG1) an aircraft LME dwells on a frequency while attempting to establish a link (in order to receive a valid uplink from at least one ground station).

This timer shall be set by an aircraft LME (if it is not already running) when an aircraft tunes to a new frequency during a frequency search.

Timer TG1 shall be cancelled when a valid uplink is received.

If timer TG1 expires and no uplinks were received and another frequency is known then the aircraft station shall tune another frequency.

If timer TG1 expires and one or more valid uplinks were received then the avionics should either attempt link establishment of continue searching. This decision is made based on the airline preferences and the ground systems identified by the uplink(s) received. If the decision is to continue searching then that may occur on the present frequency or a different frequency base on direction from the SN-SME.

Note 1.- The duration of TG1 should be chosen to ensure a valid uplink is received from at least one ground-based system before the timer expires.

Note 2.- There is one Timer TG1 per LME.

| Title: | ISH PDU Not in Every Call |
| --- | --- |
| AP working paper number and date: AP# 204 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 7.2.1 ISH PDU |
| Co-ordinator: | Bassam Farroha |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | 7.2.1 implies ISH PDU is included in every Call packet. This adds unnecessary overhead during Handoff events when the air-ground router stays the same. |
| Background: | The ISH PDU exchange is only needed in route initiation. The ISH PDU should only be sent in the Call packets when the air-ground router is new, which occurs in every Join Event and only in Handoff Events that involve a change in air-ground router. It should not be included in Calls in Handoff Events when the router does not change. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section 6.7.3.1 to qualify the inclusion of ISH PDU in Call packets only when route initiation is required. See redlined changes below. |
| WG-M status: | PENDING |

Suggested Redlines of text:

7.2.1 ISH PDU. The ISH PDU shall be included in both the CALL REQUEST and CALL CONFIRMATION packets, only when route initiation is needed.

| Title: | T4 Timeout Procedure in FRM Mode |
| --- | --- |
| AP working paper number and date: AP 208 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.3.4.4 Timer T4 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | Minor |
| Problem description: | Presentation This working paper deals with redundancy procedure, transmission of an FRMR frame on T4 expiration in FRM mode and retransmission of FRMR frame on T1 time-out. |
| Background: | Description The AVLC layer enters FRM mode only on reception of an invalid frame, by sending a FRMR frame to reset the link. This procedure is very similar to the procedure in SRM mode, that leads to the transmission of an SREJ frame. However, the SREJ is a response frame, and will not be retransmitted. The FRMR is a command frame and will be retransmitted (using the T1/N2 procedure) and the T1 timer will be started. In both cases, timer T4 will be reset. If the AVLC layer has been configured so that T4 timer value is below T1 timer value, in the FRM case, a second FRMR frame will be generated on T4 expiration. This second frame is redundant as it would be the 2nd response to the same received frame. Conclusion When T4 expires and the link is in FRM mode, a FRMR frame has already been sent and T1 timer is running. So it would be redundant to try to send a new FRMR frame. In consequence, each tentative to send a FRMR frame will be dropped by applying the redundancy procedure. |
| Backwards compatibility: |  |
| Amendment Proposal: | Modify section as shown; Suggestion We suggest to remove the reference: “Send a FRMR in FRM mode” in the T4 timer procedure. |
| WG-M status: | PENDING |

5.3.4.4	Timer T4 (maximum delay between transmissions). Timer T4 shall be set to the maximum delay between transmissions (T4). Timer T4 shall be started or restarted on en-queuing a frame for transmission. Timer T4 shall never be cancelled. If a DLE does not receive a frame before timer T4 expires, it shall send a command frame (P=1) to ensure a response from the peer DLE. When in the ABM, the DLE shall send a RR; when in the SRM, the DLE shall send an SREJ; when in the FRM, the DLE shall send a FRMR. The value of Timer T4 shall be at last two minutes longer for a ground DLE than for the peer aircraft DLE. The command frame shall be transmitted using normal Timer T1 procedures up to N2 times. If no response is received, the DLE shall assume that the link is disconnected and that site recovery procedures shall be invoked.

| Title: | Ground-based Requested Air-initiated Handoff Exceptional Cases Change |
| --- | --- |
| AP working paper number and date: AP 209 | AMCP WG-M/#, <date> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.4.4.9.3 Exceptional cases |
| Co-ordinator: | Bassam Farroha |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | Minor |
| Problem description: | In the current section 5.4.4.9.3, Exceptional cases, when there is no autotune, the aircraft does not follow the normal retransmission procedures on the XID_CMD_HO (P=1). Instead, the XID_CMD_HO (P=1) is only transmitted once per received XID_CMD_HO (P=0). |
| Background: | SARPs specifies a retransmission procedure to be followed for transmission of XIDs with P=1. This procedure should be followed consistently for all XIDs (P=1), but section 5.4.4.9.3 deviates from this procedure as given above in Problem Description. |
| Backwards compatibility: | N/A |
| Amendment Proposal: | Modify section 5.4.4.9.3 by removing the last clause of the last sentence so that normal retransmissions are followed for XID_CMD_HO (P=1). See redlined changes below. |
| WG-M status: | PENDING |

Suggested Redlines of text:

Paragraph 5.4.4.9.3 Exceptional Cases.

5.4.4.9.3 Exceptional cases. If the aircraft LME cannot initiate the handoff, it shall send an XID_CMD_LCR (P=0); the current link shall not be affected. If the Autotune parameter is included in the XID_CMD_HO (P=0), the aircraft LME shall retransmit on the new frequency the XID_CMD_HO (P=1) using the normal retransmission procedures.

| Title: | Introduction of a new ground expedited handoff variant |
| --- | --- |
| AP working paper number and date: AP 211 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: |  |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Major |
| Problem description: | If the aircraft does not support expedited subnetwork connection, it needs 2 INFO frames for each subnetwork connection to be maintained. Industry standards have introduced a hybrid variant of the expedited ground initiated handoff that allows to include the CALL REQUESTs in the RSP_HO is more efficient. This solution allow some saving in RF bandwidth by embedding all the CALL REQUESTs in the same AVLC frame. |
| Background: | This hybrid variant has not been implemented yet and is, at this time, only a provision. |
| Backwards compatibility: | TBD |
| Amendment Proposal: | In the case of a ground initiated handoff, allow the aircraft LME to include CALL REQUESTs in the RSP_HO by adding the subnetwork connection parameter. |
| WG-M status: | PENDING (the rejection of this amendment could lead to some interoperability problems and inconsistencies if industry standards are not modified) |

| Title: | Ground reject of a ground initiated handoff |
| --- | --- |
| AP working paper number and date: AP 212 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.3.6.2.1 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Clarification |
| Problem description: | When the ground station rejects the establishment of the link after a ground initiated hand-off by sending a DISC, the behavior of the airborne station remains unclear. The previous link can't be re-used as it is considered by both sides as an old link to be closed within TG5 seconds, but no new link has been successfully established. The result of such situation is that the airborne station will lose all links with the ground. |
| Background: | Yes |
| Backwards compatibility: |  |
| Amendment Proposal: | Add a requirement to initiate a link handoff and that will reset TG5 timer when a DISC frame is received while TG5 timer is running. In the same time, add a requirement to not start TG5 if the response handoff is refused. |
| WG-M status: | PENDING |

5.3.6.2.1 DISC frame. If a DLE is unable to continue to receive, it shall transmit a DISC to terminate the current link. The P bit shall be set to 0 in DISC commands. A DLE shall treat all received DISCs (regardless of the P bit) as a DISC (P=0). An aircraft receiving a DISC frame in response of a RSP_HO shall initiate a new link handoff and restart the TG5 timer.

| Title: | System Mask and Ground System ID |
| --- | --- |
| AP working paper number and date: AP 213 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.4.2.7.5 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Clarification |
| Problem description: | Different interpretations of the system mask are possible: The system mask value identifies by itself the ground system to which it belongs. In other words, two ground stations belonging to the same ground system shall provide the same system mask value. The system mask value provides a bit pattern value that should be applied to the ground station address value in order to find the ground system identifier to which the station belongs. In other words, in order to belong to the same ground system, two stations shall have the same resulting value when applying a logical AND on their VDL address and system mask value. The tech manual does not clearly define the way to compute the system Id value associated with a ground station. |
| Background: |  |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Add the usage of the system mask. |
| WG-M status: | PENDING |

5.4.2.7.5 Ground-based system mask parameter. This parameter defines the ground-based system mask that shall be bit-wise ANDed to the DLS address to obtain a ground system identifier. It shall be encoded as a 27-bit mask in a 32-bit field as per Table 5-41.

| Title: | Editorial on TG4 timer values |
| --- | --- |
| AP working paper number and date: AP 214 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Tables 5-45 |
| Co-ordinator: | Damien Marce |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | Editorial |
| Problem description: | Editorial corrections |
| Background: | Editorial corrections |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section as shown |
| WG-M status: | PENDING |

Table 5-45. VDL management entity system parameters

| Symbol | Parameter name | Minimum | Maximum | Mode 2 Default | Increment |
| --- | --- | --- | --- | --- | --- |
| TG4 (ground only) | Maximum time between GSIFs | 100 s | None | N/A100 s | 1 s |

| Title: Original: AMCP WGM/5 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date:AP215 | AMCP WG-M/5 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 6.3.2.4 and related sections and tables |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | Consistency |
| Problem description: | Existing Text supports “Call Requests from the Ground”. |
| Background: | The CALL REQUESTs from the ground is required for expedited ground initiated handoff. The CALL REQUEST from the ground function is allowed in certain section and prohibited in other sections. This amendment proposal will make the technical manual self consistence by selecting either option. |
| Backwards compatibility: | TBD |
| Amendment Proposal: | Either delete references to “Call requests from the ground” or add reference in section 6.6.3.1. |
| WG-M status: | PENDING |

# Option 1: Delete the CALL REQUEST from the ground

Expedited subnetwork connection maintenance. The process by which an aircraft or ground DTE maintains a subnetwork connection with a DTE with which it has a subnetwork connection during link handoff by inserting the CALL REQUEST packet and its response in the link handoff frame and its response.

5.4.4.12 EXPEDITED SUBNETWORK CONNECTION MANAGEMENT

If a LME implements this section, then it shall set the “v” bit in both the AVLC Specific Options and in the Connection Management parameters to 1; otherwise it shall set them to 0. This section shall only be applicable for the link establishment, and air initiated handoff, and ground initiated handoff processes.

6.3.2.4 Ground network DTE addresses. If the ground LME indicates support of ground network DTE addresses during link establishment, it shall accept and process addresses which follow the format used in the ground network. All CALL REQUESTs from the ground shall use, as the Calling Address, the ground DTEs X.121 address.

6.6.3.3.2 Expedited subnetwork connection maintenance.

Note.— The CLEAR CONFIRMATION, if required, will be transferred in an INFO frame. How the ground LME obtains the CALL REQUEST packet(s) (in ground-initiated handoffs) is outside the scope of this document.

Table 5-46b Change expedited subnetwork parameter to N/A in the ground initiated CMD and RSP HO frames.

Private parameters

Parameter set ID	F0h	00h	M	M	M	M

Connection management	F0h	01h	M	M	M	M

SQP	F0h	02h	O	O	O	O

XID sequencing	F0h	03h	M	M	M	M

AVLC specific options	F0h	04h	O	O	O	O

Expedited SN connection	F0h	05h	ON/A	ON/A	O	O

Option 2: Make Tech Manual consistent and add CALL REQUEST from the ground where it is missing

6.6.3.1 Subnetwork entity initialization.  The ground DCE shall be initialized on receipt of a valid XID_CMD_LE.  The aircraft DTE shall be initialized on receipt of a valid XID_CMD_HO containing an Expedited Subnetwork Connection Parameter in the 8208 Call Request packet(s).

Section 3

Accept

| Title: Window size | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 106 | AMCP WG-M/2 WP46 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Table 5-5 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | damien.marce@aviation-civile.gouv.fr |
| Category: | BUG |
| Problem description: | Use of Multi-selective SREJ option implies a K-window maximum size of 4 |
| Background: | When an out of sequence frame is received, AVLC layer shall check if it is an out of sequence error or a duplicated frame. In the former case, a SREJ frame shall be sent, and in the later, the frame shall be dropped and T2 timer restarted, if not currently running. This is only possible if the k window is less or equal to frame numbering modulus / 2, where modulus is 8 in AVLC. This avoids overlap of possible duplicated frames window (that will be dropped) and next expected frames window (that will lead to SREJ if out of sequence). The use of P/F bit also need the maximum window size to be equals to 4. The SARPs allow values between 1 and 7 for the k parameter which is not compliant with the use of multi-selective reject option. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Reduce maximum value of k-window from 7 to 4 in Table 5-5. |
| WG-M status: | ACCEPTED |

Table 5-5.  Data link service system parameters for Mode 2

| Symbol | Parameter name | Minimum | Maximum |  | Mode 2 default | Increment |
| --- | --- | --- | --- | --- | --- | --- |
| T1min | Delay before retransmission | Minimum | 0 s | 20 s |  | 1.0 s | 1 ms |
| T1max |  | Maximum | 1 s | 20 s |  | 15 s | 1 ms |
| T1mult |  | Multiplier | 1 | 2.5 |  | 1.45 | 0.01 |
| T1exp |  | Exponent | 1 | 2.5 |  | 1.7 | 0.01 |
| T2 | Delay before ACK | 25 ms | 10 s |  | 500 ms | 1 ms |
| T3min | Link initilization time | Minimum | 5 s | 25 s |  | 6 s | 1 ms |
| T3max |  | Maximum | 1 s | 20 s |  | 15 s | 1 ms |
| T3mult |  | Multiplier | 1 | 2.5 |  | 1.45 | 0.01 |
| T3exp |  | Exponent | 1 | 2.5 |  | 1.7 | 0.01 |
| T4 | Maximum delay between transmissions | aircraft | 10 min | 1440 min |  | 20 min | 1 min |
|  |  | ground | 12 min | 1442 min |  | 22 min | 1 min |
| N1 | Maximum number of bits in any frame | 1144 bits | 16504 bits |  | 8312 bits | 1 bit |
| N2 | Maximum number of transmissions | 1 | 15 |  | 6 | 1 |
| k | Window size | 1 frame | 4 frames |  | 4 frames | 1 frame |

| Title: | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 108 | AMCP WG-M/2 WP48 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.3.4.6 |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | CLARIFICATION |
| Problem description: | Inconsistency in T1 timer definition |
| Background: | This paragraph defines links this counter to the XID_CMD frames only in the first sentence. But the way this counter has to be used comprises the T1 timer that is not used for those frames. This is inconsistent with the definition above. STNA's understanding is that this counter applies to all the frames that need to be acknowledged, that is to say: XID_CMD frames but also INFO, RR(P=1), SREJ(P=1 and FRMR frames. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Replace "XID_CMD frame" by "AVLC frame that need to be acknowledged". |
| WG-M status: | ACCEPTED |

5.3.4.6 Counter N2 (maximum number of transmissions). Counter N2 defines the maximum number of transmissions that the DLS shall attempt to transmit any outstanding AVLC frame that requires acknowledgement. A Counter N2 shall be set to zero when a new frame is ready for transmission. Counter N2 shall be incremented after each transmission of the frame. The counter shall be cleared after its associated frame is acknowledged. When Timer T1 expires, a DLE shall invoke the retransmission procedures of 5.3.4.1 up to N2 - 1 times. When Timer T3 expires, a DLE shall invoke the retransmission procedures of 5.3.4.3 up to N2 - 1 times. When Counter N2 reaches the maximum number of attempts (value of parameter N2) the LME shall be informed and the frame shall not be transmitted.

| Title: Original: AMCP WGM/1 WP64 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#19 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.3.2.3 of technical manual |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | Clarification |
| Problem description: |  |
| Background: | Definition of the Router NET is ambiguous and does not agree with current implementation. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Text attached |
| WG-M status: | ACCEPTED |

Current Proposal

6.3.2.3 Ground DTE address. The VDL subnetwork-specific ground DTE addresses shall be the BCD encoding of the ADM, and optionally the ARS field (from the NET, as defined in the ATN Manual). It shall be sent in the Called Address Extension facility. Bit 8 of the first octet after the facility code shall be set to 1 and bit 7 shall be set to 0. The Called Address shall not be included when using VDL subnetwork-specific ground DTE addresses.

6.3.2.3.1 Since the VDL SARPs supports two addressing options at the subnetwork layer.  The default addressing is called VDL Specific DTE Addressing (VSDA) and should be supported by all VDL entities.  Optionally, VDL SARPs supports X.121 addressing.  The VSDA consists of six octets.  The first three octets of VSDA should be the same as the ATN Administration Domain Identifier (ADM) field as defined in the ATN SARPs.  The service provider assigns the second three octets of VSDA.  The service provider may use these three octets to uniquely address an air/ground router or may use them as a routing area identifier (same as the ATN ARS field specified in the ATN SARPs).  If the VSDA assigned by the DSP does not uniquely identify a specific air /ground router, then the ground system should support X.121 addressing option.

Newly Proposed Text

6.3.2.3  Ground DTE Address: The VDL subnetwork specific ground DTE address shall be the binary representation of the NET (the facility is to convey the called address that was received from the ground station GSIF) . This default addressing is called VDL Specific DTE Addressing (VSDA). The VSDA consists of six octets. The first three octets of VSDA should be the same as the ATN Administration Domain Identifier (ADM) field as defined in the ATN SARPs. The air/ground router is assigned the second three octets of VSDA. The ground system may use these three octets to uniquely address an air/ground router or may use them as a routing area identifier (same as the ATN ARS field specified in the ATN SARPs ICAO Doc 9705). If the VSDA assigned to a router does not uniquely identify a specific air/ground router, then the ground system should support X.121addressing option. The VSDA shall be sent in the Called Address Extension facility.  Bit 8 of the first octet after the facility code shall set to 1 and bit 7 shall be set to 0.  The Called Address shall not be included when using VDL subnetwork-specific ground DTE address.

5.4.2.7.4 ATN router NETs parameter. This parameter defines a list of ATN air-ground routers identified by the “administration identifier” (ADM) and a Three Octet User Defined subfields of their network entity titles (NETs). It shall be encoded as per Table 5-40.

Table 5-40. ATN router NETs parameter

Parameter ID 		1         1        0       0       0       1       0        0 	    ATN router NETs

Parameter length	 n8      n7      n6     n5     n4     n3     n2      n1

Parameter value 	a24     a23    a22    a21   a20   a19   a18     a17 	ADM subfield

a16     a15    a14    a13   a12   a11   a10     a9

a8       a7      a6      a5     a4     a3     a2       a1

u24     u23    u22   u21   u20   u19   u18     u17 	User Defined subfield

u16     u15    u14   u13   u12   u11   u10     u9

u8       u7      u6     u5     u4    u3      u2       u1

| Title: Original: AMCP WGM/1 WP65 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP#20 | AMCP WG-M,WP22 , WP19, 12 DEC 00 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Section 6.6.3.2 & 6.6.3.3 of technical manual |
| Coordinator: | Bassam Farroha |
| Coordinators address: | 2551 Riva Road, Annapolis Maryland, USA, 21401 |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | Bfarroha@arinc.com |
| Category: | Clarification |
| Problem description: | The subnetwork connection establishment and maintenance sections (6.6.3.2, 6.6.3.3) are not very clear. |
| Background: | The current text wording does not place any requirements on VSDA type addressing. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Text attached |
| WG-M status: | ACCEPTED |

6.6.3.2 Subnetwork connection establishment. Only aircraft DTEs shall request subnetwork Connection establishment in the VDL subnetwork.

6.6.3.2.1 Explicit subnetwork connection establishment. Immediately after link establishment, the aircraft DTE shall attempt to establish a subnetwork connection to at least one ground DTE. The aircraft DTE shall request a single subnetwork connection per ground DTE by the transmission of a

CALL REQUEST packet specifying the ground DTE address. On receipt of the CALL REQUEST, the ground DCE shall attempt to establish a subnetwork connection to the aircraft DTE by responding with a CALL CONFIRMATION packet; otherwise the ground DCE shall send a CLEAR REQUEST packet including the clearing cause and diagnostic code of the failure If Ground Network X.121DTE addressing is implemented then the ground DCE shall use the Called Line Address Modification Notification facility to inform the aircraft DTE of the ground DTE's X.121 address. Else, if the default Ground DTE addressing is implemented the ground DCE shall use the Called Address Extension facility to inform the aircraft of the ground DTE’s VSDA address that was delivered in the CALL REQUEST.

6.6.3.2.2 Expedited subnetwork connection establishment. An aircraft LME initiating expedited subnetwork connection establishment shall implement this section. The aircraft LME shall invoke the procedures described in 5.4.4.12 when connecting to a ground LME indicating support for expedited subnetwork connection procedures. The aircraft DTE shall reissue CALL REQUESTs for those logical channels for which responses (i.e. either a CALL CONFIRMATION or a CLEAR REQUEST) were not included in the XID_RSP_LE. If Ground Network X.121 DTE addressing is implemented then the ground DCE shall use the Called Line Address Modification Notification facility to inform the aircraft DTE of the ground DTE's X.121 address. Else, if the default Ground DTE addressing is implemented then the ground DCE shall use the Called Address Extension facility to inform the aircraft of the ground’s VSDA address that was delivered in the CALL REQUEST.

Note .— The CLEAR CONFIRMATION, if required, will be transferred in an INFO frame.

6.6.3.3 Subnetwork connection maintenance. During link establishment a ground DCE shall indicate its available routers in the ATN Router NETs parameter and the aircraft LME shall then attempt to maintain all subnetwork connections.

Note.— For subnetwork connections to be maintained across ground station changes, the LME gives preference in choosing a new ground station to ground stations indicating accessibility to the DTEs to which subnetwork connections already exist.

6.6.3.3.1 Explicit subnetwork connection maintenance. To explicitly request subnetwork connection maintenance to a ground DTE, an aircraft DTE shall send a CALL REQUEST packet to the ground DTE with the fast select facility set containing a VDL mobile SNDCF Call User Data Field indicating a request to maintain SNDCF context. If the ground DTE can accept the call, it shall respond with a CALL CONFIRMATION packet with the fast select facility set containing a VDL mobile SNDCF Call User Data field indicating whether the SNDCF context was maintained. If the Ground DTE or a DCE is unable to accept the call, it shall send a CLEAR REQUEST packet to the aircraft DTE including the clearing cause and diagnostic code of failure. If Ground Network X.121 DTE addressing is implemented then the ground DTE shall use the Called Line Address Modification Notification facility to inform the aircraft DTE of the ground DTE's X.121 address. Else if the default Ground DTE addressing is implemented then the ground DCE shall use the Called Address Extension facility to inform the aircraft of the ground’s VSDA address that was delivered in the CALL REQUEST.

6.6.3.3.2 Expedited subnetwork connection maintenance. An LME initiating expedited subnetwork connection maintenance shall implement this section. If both the aircraft and ground LMEs support expedited subnetwork procedures, then the procedures described in 5.4.4.12 shall be invoked. The initiating DTE shall reissue CALL REQUESTs for those logical channels for which responses (i.e. a CALL CONFIRMATION or a CLEAR REQUEST) were not included in the XID_RSP_HO. A ground DTE shall include its Calling Address in the appropriate field. If Ground Network DTE addressing is implemented then the ground DTE shall use the Called Line Address Modification Notification facility to inform the aircraft DTE of the ground DTE's X.121 address. Else, if the default Ground DTE addressing is implemented then the ground DCE shall use the Called Address Extension facility to inform the aircraft of the ground’s VSDA address that was delivered in the CALL REQUEST.

Note.— The CLEAR CONFIRMATION, if required, will be transferred in an INFO frame. How the ground LME obtains the CALL REQUEST packet(s) (in ground-initiated handoffs) is outside the scope of this document.

| Title: Original: AMCP WGM/1 AP#11 | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 102 | AMCP WG-M/2 WP42 |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications, |
| Sections of Documents affected: | Proposed new paragraph of Section “VDL Principles” of the Guidance material in the “Manual on VDL Mode 2 Technical Specifications”. |
| Coordinator: | Damien Marcé |
| Coordinators address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Coordinators Phone: | (33) 562 14 59 24 |
| Coordinators Fax: | (33) 562 14 58 53 |
| Coordinators e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | CLARIFICATION |
| Problem description: | For the proper behavior of an ATN air ground router, the VDL must send the aircraft address to the air ground router. If the RGS and air-ground router are connected to and ISO 8208 ground-ground subnetwork, the current documents do not specify the way the calling Aircraft address is passed to a called ATN Air/Ground router. |
| Background: | In the course of its ATN/VDL SARPs validation activities, the STNA has encountered problems when interconnecting VDL RGS (Remote Ground Station) to an ATN Air-Ground router. The VDL subnetwork ground station manufacturers are offering different specific interfaces that may not be supported by the ATN Air-Ground router. When a difference exists between the interface offered on one side and the interface supported on the other side, interconnection of the systems is not possible without upgrading the systems. The STNA has experienced this problem several times, and was forced to redevelop or adapt the mobile SNDCF of its ATN air-ground router every time a new mobile subnetwork from a different manufacturer had to be connected. The adaptations relates in particular to the way the mobile subnetwork address of the airborne router is communicated to the air/ground router. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Add the following text in the guidance material that present a standard way for a VDL Mode 2 RGS to provide the calling aircraft address to a called ATN Air/Ground router. Remark 1 : the specification for the call from the ground router to the aircraft (paragraph 1.3.3.2.2 in following text) should be deleted if the amendment (AP#7) presented in WGM1 WP 42 is accepted (no call from the ground to the plane clearly specify inside the VDL SARPs). Remark 2 : this specification has no links with the facilities tables present inside the VDL SARPs. The facilities tables of the VDL SARPs deals with the facilities allowed or forbidden on the air segment. This specification deals with the ground segment, from the VDL Ground Station towards the air-ground router. |
| WG-M status: | ACCEPTED |

The following text is proposed to be inserted in the Manual on VDL Mode 2 Technical Specifications, as a new paragraph of section “VDL Principles” of the guidance material :

1.3.3 : Addressing for use with Air Ground router

1.3.3.1 For the proper behavior of an ATN Air Ground router, the VDL must send the aircraft address to the air Ground Router. If the RGS and air-ground router are connected to an ISO 8208 ground-ground subnetwork the interface described in the following may be used.

Note : the RGS and the ATN router are assumed to have a priori knowledge of the aircraft address encoding supported by the peer remote DTE.

1.3.3.2 Interface  : Address encoding using ISO 8208 call address extension

1.3.3.2.1 Call from the aircraft to the router :

The RGS will encode its own X121 address in the calling address field of the ISO 8208 call request packet and the aircraft address in the ISO 8208 calling address extension facility as follow :

| Octet | Representation | Value |
| --- | --- | --- |
| 1 | Facility parameter | 0xcb |
| 2 | First octet of the facility parameter field | 0x88 (Address not assigned following ISO 8348 – 8 digits length) |
| 3-6 | BCD encoding of the octal representation of the 24 bits aircraft address | BBBBBBBB |

1.3.3.2.2 Call from the router to the aircraft (case of handoff):

The ATN router will encode the RGS X121 address in the called address field of the ISO 8208 call request packet and the aircraft address in the ISO 8208 called address extension facility as follow :

| Octet | Representation | Value |
| --- | --- | --- |
| 1 | Facility parameter | 0xc9 |
| 2 | First octet of the facility parameter field | 0x88 (Address not assigned following ISO 8348 – 8 digits length) |
| 3-6 | BCD encoding of the octal representation of the 24 bits aircraft address | BBBBBBBB |

| Title: Disconnecting old links | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 200 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.4.4.6.6 |
| Coordinator: | Bassam Farroha |
| Coordinators address: | Bassam Farroha ARINC Aviation and Air Traffic Services Advanced Communications 2551 Riva Road Columbia, MD 21401 USA |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | When to use the New Link |
| Background: | The use of multiple services over the same link makes the decision of using the new link dependent on the capabilities of the Ground System. The peers will determine the best link, for the duration. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Remove the text dealing with a communication path is viable. The link does not reflect the status of all the services that are using it. The link might be established but the AOA, ATN, etc. ... services might not be ready yet. It is understood that the new link should be used as soon as the air and ground have established the link and the corresponding service is set up. |
| WG-M status: | ACCEPTED |

# Current Text

5.4.4.6.6 Disconnecting old link. If the new and old ground stations are associated with different systems, the procedures of 5.4.4.6.4 shall be followed. Otherwise, the aircraft LME shall set Timer TG5 when it receives the XID_RSP_HO. The ground LME shall set Timer TG5 after it transmits the XID_RSP_HO. Once the new communication path is viable, downlinks should only be sent over the newly established link. Both stations shall continue to maintain  the old link until their respective Timer TG5 expires, after which each will consider the link disconnected without sending or receiving a DISC.

# New Text

5.4.4.6.6 Disconnecting old link. If the new and old ground stations are associated with different systems, the procedures of 5.4.4.6.4 shall be followed. Otherwise, the aircraft LME shall set Timer TG5 when it receives the XID_RSP_HO. The ground LME shall set Timer TG5 after it transmits the XID_RSP_HO. Both stations shall continue to maintain the old link until their respective Timer TG5 expires, after which each will consider the link disconnected without sending or receiving a DISC.

| Title: Remove T24 and T25 from the subnetwork protocol | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 201 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Table 6-1 |
| Coordinator: | Bassam Farroha |
| Coordinators address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | bfarroha@arinc.com |
| Category: | Performance Enhancement |
| Problem description: | We need to update Table 6-1 in the VDL Technical manual by removing T24 and T25. Rational: Removing timers T24 and T25 is highly recommended for the VDL Mode 2 performance enhancement in the V8208 subnetwork, based on the PETAL II trials. The adoption of these timers causes increased transmissions for verification of connection and message delivery, where it is done by other layers. The initial proposal to the SARPs was to make them optional, but when they were added, the wording of making them optional were omitted. This makes these timers mandatory on all systems which was not the intend of the proposal nor the ICAO/AMCP group. The best solution at this time is to remove them from the table. |
| Background: | These timers (T24_Window Status Transmission Timer) and (T25_ Window Rotation Timer) were added to the SARPs as optional timers for special implementations which was supposed to simplify the 8202 Subnetwork implementation. After through testing of systems that implement them, they proved to add additional overhead on the RF without. A survey of the air and ground developers showed that a unanimous agreement on removing these timers from the Technical Manual will ensure a better performance. . |
| Backwards compatibility: | Yes, with all known implementations. |
| Amendment Proposal: | Disallow the use of timers T24 &T25 |
| WG-M status: | ACCEPTED |

Table 6-1. Subnetwork layer service system parameters for VDL Mode 2

Symbol 	Name 					Minimum 	Maximum	Mode2

T20 	RESTART REQUEST response timer 		1 s 		300 s 		180 s

T21 	CALL REQUEST response timer 		1 s 		300 s 		200 s

T22 	RESET REQUEST response timer 		1 s 		300 s 		180 s

T23 	CLEAR REQUEST response timer 		1 s 		300 s 		180 s

T24	Window Status Transmission Timer		1 s		300 s		180 s

T25	Window Rotation Timer			1 s		300 s		180 s

T27	Reject Response Timer				1 s		300 s		180 s

R20 	RESTART REQUEST retransmission count	0 		7 		1

R22 	RESET REQUEST retransmission count 	0 		7 		1

R23 	CLEAR REQUEST retransmission count 	0 		7 		1

R27	Reject Retransmission Counter			0		7		1

P 	Packet size 					128 octets 	2048 octets 	1024 octets

W 	Transmit window size 				1 packet 	7 packets	7 packets

A 	Acknowledgment window size 		1 packet 	4 packets 	4 packets

LTC 	Lowest two-way channel 			0 		4095 		1024

HTC 	Highest two-way channel 			0 		4095 		3071

Note.— P, W, A values define defaults. Other parameter values are preset and not negotiated. The

packet size (P) and window sizes (W, A) define defaults, and may be negotiated during call setup.

| Title: Add length to field | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 202 | AMCP WG-M/5 ,<2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 6.3.2.1 |
| Coordinator: | Bassam Farroha |
| Coordinators address: | Bassam Farroha ARINC Aviation and Air Traffic Services Advanced Communications 2551 Riva Road Columbia, MD 21401 USA |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | The current addressing of DTE currently does not include the length field in the title and paragraphs. |
| Background: | Since this section deals with addressing, it is useful to include the DTE length criteria |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Add the length field to the title and paragraphs.. |
| WG-M status: | ACCEPTED |

Section 6.3.2.1 Encoding.

Current Text: “Octet 5 and consecutive octets shall consist of the following addresses, in order:

- called DTE address; and

- calling DTE address.”

Updated Suggested Text: “Octet 4 shall consist of the address lengths, encoded as follow

- 4 least significant bits : called DTE address length; and

- 4 most significant bits : calling DTE address length

Octet 5 and consecutive octets shall consist of the following address fields, in order

- called DTE address field

- calling DTE address field”.

The A-bit in the General Format Identifier shall be set to 0 to indicate the use of this Address Block format.

Section 6.3.2.1.1 Address field

Current Text: “ 6.3.2.1.1 Address Field.  This variable length field is known informally as the address field.  The address field shall be encoded in BCD form.  When appropriate, the address field shall be rounded up to an integer number of octets.”

Suggested Text: “6.3.2.1.1 Address Length and Address Field.  The address length shall indicate the field length for the calling and called DTE addresses.  The variable length field is known informally as the address field.  The address field shall be encoded in BCD form.  When appropriate, the address field shall be rounded up to an integer number of octets.”

| Title: Air Initiated handoff capability | VDL Mode 2 Technical Manual Amendments |
| --- | --- |
| AP working paper number and date: AP 203 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 5.4.4.6 |
| Coordinator: | Bassam Farroha |
| Coordinators address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Coordinators Phone: | 410-266-2160 |
| Coordinators Fax: | 410-266-4040 |
| Coordinators e-mail address: | bfarroha@arinc.com |
| Category: | Performance Enhancement |
| Problem description: | The current technical Manual is interpreted as Aircraft initiated handoff capability an optional feature. |
| Background: | This no-implementation of “Aircraft initiated handoff” is not the optimal method of designing reliable mobile systems. |
| Backwards compatibility: | Yes, feature is implemented in all known avionics and ground systems. |
| Amendment Proposal: | This Amendment proposal affects section 5.4.4.6 (6.5.4.4.6 in the old SARPs. The current text indicated that Aircraft-Initiated Handoff is an optional feature. All known avionics and ground systems today implement this feature due to the favorable system interaction and efficiency it provides. We had conversations to reword the text to indicate that this feature is required. I am forwarding the text for the rewording of the Technical Manual |
| WG-M status: | ACCEPTED |

Old Text:

5.4.4.6

Aircraft-Initiated Handoff.  If an aircraft LME implements this section, then it shall set the "i" bit in the AVLC Specific Options to 1; otherwise, it shall set the "i" bit to 0.

New Text:

5.4.4.6

Aircraft-Initiated Handoff.  The aircraft LME shall implement Aircraft-Initiated Handoff.  The aircraft LME shall always set the "i" bit in the AVLC Specific Options to 1.

| Title: | Error Recovery-reject packet |
| --- | --- |
| AP working paper number and date: AP 205 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 6.2.3 Error Recovery |
| Co-ordinator: | Bassam Farroha |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | Rationale: The original text implies that any bad packet would cause a REJECT to be generated. The new text makes it clear that only a DATA packet with an invalid P(s) field will cause the REJECT to occur. |
| Background: | The original text implies that any bad packet would cause a REJECT to be generated. The new text makes it clear that only a DATA packet with an invalid P(s) field will cause the REJECT to occur. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section as shown |
| WG-M status: | ACCEPTED |

Current Text: “REJECT packet types shall be used for subnetwork-level error recovery.  These packets shall be sent between subnetwork entities to cause retransmission of invalid packets and to recover……….”

Suggested Text: “REJECT packet types shall be used for subnetwork-level error recovery.  These packets shall be sent between subnetwork entities to cause retransmission of DATA packets, and to recover……….”

| Title: | Error Handling-request |
| --- | --- |
| AP working paper number and date: AP 206 | AMCP WG-M/#, <date> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 6.6.4 Error Handling |
| Co-ordinator: |  |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | Rationale: Makes the association of sequence numbers with the DATA packet. |
| Background: | Rationale: Makes the association of sequence numbers with the DATA packet. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section as shown |
| WG-M status: | ACCEPTED |

Current Text: “An aircraft DTE or ground DCE shall send a CLEAR REQUEST, RESET REQUEST, or RESTART REQUEST packet only for recovery from a DTE failure. When an aircraft DTE or ground DCE receives a packet with a bad sequence number, it shall transmit a REJECT, as specified in ISO 8208, Section 13.4.”

Suggested Text: An aircraft DTE or ground DCE shall send a CLEAR REQUEST, RESET REQUEST, or RESTART REQUEST packet only for recovery from a DTE failure. When an aircraft DTE or ground DCE receives a DATA packet with a bad sequence number, it shall transmit a REJECT, as specified in ISO 8208, Section 13.4.”

| Title: | Acknowledgement |
| --- | --- |
| AP working paper number and date: AP 207 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 6.6.5 Acknowledgements. |
| Co-ordinator: | Bassam Farroha |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | Rationale: The role of the DATA packet is more clear. |
| Background: | Rationale: The role of the DATA packet is more clear. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section as shown |
| WG-M status: | ACCEPTED |

Current Text: “An RR packet shall be generated only when a valid DATA packet is received with a P(s), which closes the acknowledgment window. The aircraft DTE or ground DCE shall transmit an RR packet acknowledging the outstanding packets as soon as it is able.”

| Suggested Text: “An RR packet shall be generated only when a DATA packet with a valid P(s) and P(r) is received, which closes the acknowledgment window. The aircraft DTE or ground DCE shall transmit an RR packet acknowledging the outstanding packets as soon as it is able.” |  |
| --- | --- |

| Title: | Various Editorials |
| --- | --- |
| AP working paper number and date: AP 210 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | Section 3.3.3.1.3.1 Tables 5-1, 5-7, 5-36, 5-42 and 5-45 |
| Co-ordinator: | Damien Marce |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | Editorial |
| Problem description: | Editorial corrections |
| Background: | Editorial corrections |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section as shown |
| WG-M status: | ACCEPTED |

3.3.3.1.3.1 N1 computation. The N1 parameter (i.e. maximum number of bits in any frame) is computed as follows:

Mode 1 (min): N1 = [11 (link layer) + 4 (packet layer) + 128] x 8 = 1 144

Mode 1 (default): N1 = [11 (link layer) + 4 (packet layer) + 256] x 8 = 2 168

##### Table 5-1. MAC service system parameters

| Symbol | Parameter name | Minimum | Maximum | Mode 2 Default | Increment |
| --- | --- | --- | --- | --- | --- |
| TM1 | Inter-access delay | 0.5 ms | 125 ms | 4.5 ms | 0.5 ms |
| TM2 | Channel busy | 6 s | 120 s | 60 s | 1 s |
| p | Persistence | 01/256 | 1 | 013/256 | 01/256 |
| M1 | Maximum number of access attempts | 1 | 65 535 | 135 | 1 |

##### Table 5-7. Timer T1 parameter

Parameter value	l16l16	l15l15	l14l14	l13l13	l12l12	l11l11	110l10	19l9	(T1min )

18l8	17l7	16l6	15l5	14l4	13l3	12l2	11l1

##### Table 5-36. Broadcast connection (link and subnetwork) parameter

0	0	0	m	112l12	111l11	110l10	19l9	an M/I bit and an LCI

18l8	17l7	16l6	15l5	14l4	13l3	12l2	11l1

##### Table 5-42. Timer TG3 parameter

Parameter value	116l16	115l15	114l14	113l13	112l12	111l11	110l10	19l9	(lower bound)

18l8	17l7	16l6	15l5	14l4	13l3	12l2	11l1

# Comments

Missing a space?

Don't leave blank

Don't leave blank

Extra table row

Don't leave blank

Extra table row