AMCP WG-M/6-WP/6

AERONAUTICAL MOBILE COMMUNICATIONS PANEL (AMCP)

Working Group M Meeting

Montreal, Canada

12-18 December, 2002

Concerns with Consideration for VDL Mode-4 to Support ATC Communications

Presented by the Brent Phillips

(Prepared by)

Brent Phillips

Federal Aviation Administration

SUMMARY

This Working Paper identifies a number of existing issues which should be addressed before further consideration and work are expended by the AMCP to investigate the use of VDL Mode-4 to support ATC Communications.

- Introduction

The AMCP WG-M has been performing work to investigate the possible use of the VDL Mode-4 System to support ATC data communications.  This paper identifies a number of concerns with the continuation of these activities under the work of this ICAO Panel.   Concerns, which are similar if not identical, have recently been expressed by AMCP participants from several States, particularly Sweden, in reference to the standardization of another data link system, the Universal Access Transceiver (UAT). UAT has approved  implementation standards (RTCA MASPS and MOPS) and is presently being used operationally for ADS-B. VDL Mode 4 SARPs were approved for the surveillance application. VDL Mode 4 SARPs were not approved for ATC data communications.

- Background

At the Communications/Meteorology/Operations Divisional Meeting (1990), Recommendation 2/4 called for “States and an appropriate ICAO body to urgently conduct the necessary studies on the possibilities, advantages, consequences and conditions for improving communications in the 117.975 – 137 MHz VHF band, including channel spacing of 12.5 kHz and other alternatives, taking into account all technical, operational, planning and economic aspects of the problem, including compatibility with other equipment using 25 kHz  channel spacing”.  The AMCP was tasked by the ANC to study this matter and the panel reported its work in this subject in 1994.  Based on this information, the Special Communications/Operations Divisional Meeting (1995) agreed that SARPs for a new system, which should satisfy identified technical and operational requirements and is based on TDMA technology, should be completed as early as possible.  Recommendation 6/2 (Development of the future VHF air-ground voice and data link system) as identified in the COM/OPS/95 Report states that ICAO should expedite work on the 25 kHz TDMA integrated voice and data link system with identified draft standards to be finalized.

The same COM/OPS/95 meeting identified an additional  Recommendation 6/3 to develop data links to support navigation and surveillance application. They did not request additional data links to support Communications. Further the meeting report did not identify VDL Mode 4 or its predecessor name of STDMA. The VDL Mode 4 link is in development in the AMCP under this Recommendation.

- Issues/Concerns

The AMCP has followed this direction and as a result, there are now approved SARPs available for the VDL Mode-3 technology, which is based on TDMA technology and supports both voice and data as identified by the COM/OPS/95.  Given the fact that an agreed-upon international standard exists, and in light of the concerns identified below, the AMCP should carefully consider next steps in its work on consideration of VDL Mode-4 as a communications system, presuming consistency of approach with that articulated in the recent Working Group of the Whole meeting for UAT, until these issues have been resolved.  Unless carefully framed, further work on the use of VDL Mode 4 for ATC data communications might end up being a waste of limited AMCP resources and might jeopardize global interoperability.  For example, what benefits does VDL Mode 4 offer that are not offered by VDL Mode 3?

| Issue | Rationale |
| --- | --- |
| Unavailability of VHF Spectrum to support VDL-4 for ATC data communications | Spectrum availability has to be assessed. The number of channels required to support data communications is uncertain; however, as many as 25 channels have been suggested. This is likely to be unacceptable for regions with limited VHF Spectrum. |
| VDL-4 System does not support a simple Voice and Data Communication installation | The COM/OPS/95 decision required a TDMA system which supports voice and data to take advantage of efficiency gains from requiring a single antenna and receiver. |
| There is no comparative assessment to support additional benefits over existing SARPed systems | The existing analysis presented in a paper titled “VHF Datalinks for point to point Communications” concludes that VDL Mode-4 does not provide any additional benefits over the existing SARPed system. |
| Certification, Safety and availability concerns with placing CN&S functionality on the same box. | Even with redundant equipment, there are serious concerns about certifying an architecture which has CN&S functions all dependant on the same single system. |
| Introduction of a new Communications system will introduce International interoperability problems | Compliance with the ICAO 1995 decision will lead to International Interoperability. |
| COM/OPS/95 did not request this work. No direction has been provided by ANC to conduct work on this effort and none is provided in the AMCP Work Program | AMCP should not perform any further work before directives to do so have been given by the ANC |

A further reason for caution is the fact that a number of air carriers are now provisioning for implementation of VDL Mode 2 for VHF data communications.  VDL Mode 2 is also an internationally standardized system.  In addition, it has not been made clear what benefits may be achieved by VDL Mode 4 that are not already provided by either or both of both VDL Mode 2 or VDL Mode 3, We note with concern that the same participants in the AMCP who prominently voice concerns over progressing UAT to SARPs, have not seemed to consider that the same concerns exist for the application of VDL Mode 4 for ATC data communications.

- Recommendations:

The AMCP WG-M/5 meeting is invited to:

  - note the information presented in this paper;

  - Consider the implications of proliferating additional communications data links in light of previous directions from ANC.

  - consider the risk of jeopardizing the opportunity to achieve international interoperability by introducing another communications system that has not yet been shown to provide any benefits above and beyond those of the currently SARPed systems.

  - recommend to AMCP/8 a consistent position on progressing VDL Mode 4 (for ATC data communications) to include resolving all existing open issues prior to additional recommendations for approval for ATC data communications.