# WG-M/7 WP9

Some Editorial Issues in the VDL Mode 4 Technical Manual

(Sent as an e-mail by Steve Friedman, ADSI)

In preparation for replacing the existing link layer protocol with the new

protocol, I have been reviewing the text.  I have discovered the following

editorial issues.  I am not sure to whom these should be directed.

These comments are based on the 11OCT02 doc from WG/M-5

(VDL4_TM_WGM5_v11_ChangesAccepted.pdf), with a quick review to ensure that

they weren't mentioned in any subsequent documents:

- rename ND2 as "max length of a short DLS transmission" for clarification

- section 1.5.7.3 says send GSIF with CTRL_CMD (re=0) as a cut-paste

anachronism from VDL/2.  s/CTRL_CMD (re=0)/UCTRL (ucid=0)/.

- sect 1.5.7.5.1 item (c) has the 'or' which should be on item (d)

- note 3 to sect 1.5.4.1 s.b. updated to include the effects of TL3.  Also

in 1.5.4.1 s/TL3seconds/TL3 seconds/

- parameter 4C (broadcast connection) missing from second and third

sub-tables of Table 1-97.

- sect 1.5.3.6.6 and 3.2.7.1 these sections talk about eliminating the

parameter ID but don't mention eliminating the length byte.  Per the

previous version of the text, the parameter length byte should be

eliminated as well.

- table 3-25, sect 3.7.2.6 and sub-paras, table 3-43 (and possibly others).

s/SARPs/technical manual/

- table 3-30, octet 1, bit 8 s.b. a 1

- sect 3.7.2.6.1 s/XID/CTRL/

- also ai bit 3 calls out "application subfield" rather than "application

field". s/subfield/field/ for consistency of terminology as the rest of

the paragraph calls it an "application field".

Steve Friedman