ACP WG-M8 WP/2

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WGM

November 20-28, 2003

Review of the VDL Mode 2 Technical Manual Open Amendment Proposals

SUMMARY

The recommendations reflected in this paper will bring harmonization between the VDL Mode 2 Technical Manual and ARINC Specification 631.  The AEEC DLK Systems Subcommittee at the September 2003 meeting reviewed the outstanding Amendment Proposals (AP) and found it was not necessary to implement the proposed changes.  It is therefore recommended that all APs in the Pending category are rejected.

Presented by

Victor J. Nagowski

ARINC

2551 Riva Road

Annapolis, MD 21401 USA

(410) 266-4229

vjn@arinc.com

# Recommendation

The AEEC DLK Systems Subcommittee met in Annapolis, Maryland in September 2003 and studied the remaining open APs.  Five APs were in the Pending category.  After careful analysis and review of the outstanding APs and noting that reliable system operation has been attained, it was decided that there was no need to implement any of the outstanding APs.  It is therefore recommended that that the following APs are rejected:

- AP204, AP208, AP211, AP212, and AP213

With the rejection of the above APs, there will be harmonization between the VDL Mode 2 Technical Manual and ARINC Specification 631.

The above APs are attached for reference.

| AP working paper number and date: AP# 204 | AMCP WG-M/5, <2002> |
| --- | --- |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 7.2.1 ISH PDU |
| Co-ordinator: | Bassam Farroha |
| Co-ordinator’s address: | Bassam Farroha ARINC Incorporated Aviation and Air Traffic Services Advanced Communication 2551 Riva Road Annapolis, MD 21401 USA |
| Co-ordinator’s Phone: | 410-266-2160 |
| Co-ordinator’s Fax: | 410-266-4040 |
| Co-ordinator’s e-mail address: | bfarroha@arinc.com |
| Category: | CLARIFICATION |
| Problem description: | 7.2.1 implies ISH PDU is included in every Call packet. This adds unnecessary overhead during Handoff events when the air-ground router stays the same. |
| Background: | The ISH PDU exchange is only needed in route initiation. The ISH PDU should only be sent in the Call packets when the air-ground router is new, which occurs in every Join Event and only in Handoff Events that involve a change in air-ground router. It should not be included in Calls in Handoff Events when the router does not change. |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Modify section 6.7.3.1 to qualify the inclusion of ISH PDU in Call packets only when route initiation is required. See redlined changes below. |
| WG-M status: | REJECT |

Suggested Redlines of text:

7.2.1 ISH PDU. The ISH PDU shall be included in both the CALL REQUEST and CALL CONFIRMATION packets, only when route initiation is needed.

| Title: | T4 Timeout Procedure in FRM Mode |
| --- | --- |
| AP working paper number and date: AP 208 | AMCP WG-M/5, <2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.3.4.4 Timer T4 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Marce_damien@stna.dgac.fr |
| Category: | Minor |
| Problem description: | Presentation This working paper deals with redundancy procedure, transmission of an FRMR frame on T4 expiration in FRM mode and retransmission of FRMR frame on T1 time-out. |
| Background: | Description The AVLC layer enters FRM mode only on reception of an invalid frame, by sending a FRMR frame to reset the link. This procedure is very similar to the procedure in SRM mode, that leads to the transmission of an SREJ frame. However, the SREJ is a response frame, and will not be retransmitted. The FRMR is a command frame and will be retransmitted (using the T1/N2 procedure) and the T1 timer will be started. In both cases, timer T4 will be reset. If the AVLC layer has been configured so that T4 timer value is below T1 timer value, in the FRM case, a second FRMR frame will be generated on T4 expiration. This second frame is redundant as it would be the 2nd response to the same received frame. Conclusion When T4 expires and the link is in FRM mode, a FRMR frame has already been sent and T1 timer is running. So it would be redundant to try to send a new FRMR frame. In consequence, each tentative to send a FRMR frame will be dropped by applying the redundancy procedure. |
| Backwards compatibility: |  |
| Amendment Proposal: | Modify section as shown; Suggestion We suggest to remove the reference: “Send a FRMR in FRM mode” in the T4 timer procedure. |
| WG-M status: | REJECT |

5.3.4.4	Timer T4 (maximum delay between transmissions). Timer T4 shall be set to the maximum delay between transmissions (T4). Timer T4 shall be started or restarted on en-queuing a frame for transmission. Timer T4 shall never be cancelled. If a DLE does not receive a frame before timer T4 expires, it shall send a command frame (P=1) to ensure a response from the peer DLE. When in the ABM, the DLE shall send a RR; when in the SRM, the DLE shall send an SREJ; when in the FRM, the DLE shall send a FRMR. The value of Timer T4 shall be at last two minutes longer for a ground DLE than for the peer aircraft DLE. The command frame shall be transmitted using normal Timer T1 procedures up to N2 times. If no response is received, the DLE shall assume that the link is disconnected and that site recovery procedures shall be invoked.

| Title: | Introduction of a new ground expedited handoff variant |
| --- | --- |
| AP working paper number and date: AP 211 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: |  |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Major |
| Problem description: | If the aircraft does not support expedited subnetwork connection, it needs 2 INFO frames for each subnetwork connection to be maintained. Industry standards have introduced a hybrid variant of the expedited ground initiated handoff that allows to include the CALL REQUESTs in the RSP_HO is more efficient. This solution allow some saving in RF bandwidth by embedding all the CALL REQUESTs in the same AVLC frame. |
| Background: | This hybrid variant has not been implemented yet and is, at this time, only a provision. |
| Backwards compatibility: | TBD |
| Amendment Proposal: | In the case of a ground initiated handoff, allow the aircraft LME to include CALL REQUESTs in the RSP_HO by adding the subnetwork connection parameter. |
| WG-M status: | REJECT |

| Title: | Ground reject of a ground initiated handoff |
| --- | --- |
| AP working paper number and date: AP 212 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.3.6.2.1 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Clarification |
| Problem description: | When the ground station rejects the establishment of the link after a ground initiated hand-off by sending a DISC, the behavior of the airborne station remains unclear. The previous link can't be re-used as it is considered by both sides as an old link to be closed within TG5 seconds, but no new link has been successfully established. The result of such situation is that the airborne station will lose all links with the ground. |
| Background: | Yes |
| Backwards compatibility: |  |
| Amendment Proposal: | Add a requirement to initiate a link handoff and that will reset TG5 timer when a DISC frame is received while TG5 timer is running. In the same time, add a requirement to not start TG5 if the response handoff is refused. |
| WG-M status: | REJECT |

5.3.6.2.1 DISC frame. If a DLE is unable to continue to receive, it shall transmit a DISC to terminate the current link. The P bit shall be set to 0 in DISC commands. A DLE shall treat all received DISCs (regardless of the P bit) as a DISC (P=0). An aircraft receiving a DISC frame in response of a RSP_HO shall initiate a new link handoff and restart the TG5 timer.

| Title: | System Mask and Ground System ID |
| --- | --- |
| AP working paper number and date: AP 213 | AMCP WG-M/5, <08/2002> |
| Document(s) affected: | Manual on VDL Mode 2 Technical Specifications |
| Sections of Documents affected: | 5.4.2.7.5 |
| Co-ordinator: | Damien Marcé |
| Co-ordinator’s address: | Service Technique De La Navigation Aerienne, 1 AV. Du DR Maurice Grynfogel, BP1084-31035, Toulouse Cedex, France |
| Co-ordinator’s Phone: | (33) 562 14 59 24 |
| Co-ordinator’s Fax: | (33) 562 14 58 53 |
| Co-ordinator’s e-mail address: | Damien.marce@aviation-civile.gouv.fr |
| Category: | Clarification |
| Problem description: | Different interpretations of the system mask are possible: The system mask value identifies by itself the ground system to which it belongs. In other words, two ground stations belonging to the same ground system shall provide the same system mask value. The system mask value provides a bit pattern value that should be applied to the ground station address value in order to find the ground system identifier to which the station belongs. In other words, in order to belong to the same ground system, two stations shall have the same resulting value when applying a logical AND on their VDL address and system mask value. The tech manual does not clearly define the way to compute the system Id value associated with a ground station. |
| Background: |  |
| Backwards compatibility: | Yes |
| Amendment Proposal: | Add the usage of the system mask. |
| WG-M status: | REJECT |

5.4.2.7.5 Ground-based system mask parameter. This parameter defines the ground-based system mask that shall be bit-wise ANDed to the DLS address to obtain a ground system identifier. It shall be encoded as a 27-bit mask in a 32-bit field as per Table 5-41.

# Comments

Don't leave blank