ACP WG M8/ WP20

Information Paper

21rst  November 2003

Assessment of VDL 2 airborne co-site impact 
on ATS data-link

Since Spring 2003, EUROCONTROL is progressing a task on the present subject.

The intention is to evaluate the impacts of airborne co-site interference and identify the possible constraints on ATS data-link applications. It will be verified that Link2000+ applications are compatible with the co-site impact in all operational and relevant conditions, and if possible it will be derived which further application profiles would also be possible.

In this analysis,

- Recent information about VDL 2 interference to AM-DSB voice will be assembled, as far as possible and depending on industry support.
It will be based for a part on certification tests achieved by industry.

However the interference from data-link to AM-DSB had already been documented in ICAO AMCP papers; in particular the impact of VDL 2 interference had been shown to be less severe than the ACARS impact on AM-DSB.
Therefore the focus will mainly be put on the reverse interference (voice on data-link), so far not much documented in ICAO ACP.

- The airborne co-site interference from AM-DSB voice transmission possibly on VDL 2 up-link data reception, or on down-link VDL 2 data transmission attempts will be assessed. In view of this:

- a laboratory aircraft is being used to document and quantify the co-site interference phenomena. Depending on the mutual antenna isolation and depending on the frequency separations, several representative cases will be documented. 
For each case it will be observed if a voice transmission coincident with the data transmission results in data loss or in transmission delay.

- This information will be combined with AM-DSB traffic statistics, to derive the portion (%) of message loss and compare it with the required quality-of-service criteria for Link2000+ applications.

- The statistics about voice AM-DSB transmissions onboard an aircraft are being gathered with the support of a major airline in Europe. Statistics on short-haul and long-haul aircraft will be available, and the distinction of AM-DSB traffic for ATC and non-ATC communications will be made.

- The results of this task will be documented and reported among others to ICAO ACP WG M.

P. Delhaise

Eurocontrol DAS/CSM