ACP WGC09/WP16

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

WORKING GROUP C

MEETING 9

Montreal, Canada

April 4-8, 2005

Agenda Item 5: New Technologies

An introduction in AOC

Presented by Kors van den Boogaard

Prepared by

Kors van den Boogaard.

# Introduction

The present ACARS traffic is for the largest part being conducted in the VHF band supported by VHF radios also being used for ATC services.  In order that the Airline Operational Communication traffic can be maintained within the next generation communication radios in support of ATC, it is needed to provide an inventory of its present and its future usage.

This paper provides a first assessment resulting from an IATA questionnaire send to its member airlines on the use of AOC.  It has to be noted due to differences in operation, different geographic conditions, airline size and type of aircraft and in particular different regulatory requirements the figures provided have to been seen as an attribute.

Airline Operational Communication

AOC is defined in ICAO as Communication required for the exercise of authority over the initiation, continuation, diversion or termination of flight for safety, regularity and efficiency reasons.  As such it conforms to the definition in ITU radio communication spectrum for safety and regularity of flight conform ITU Art 1.33 and 1.36. It comprises of a voice and data communication service.  While there is not much expected growth in the voice communication traffic per aircraft, the data service was introduced (the OOOI message) in 1976 and still hasn’t reached its mature status considering the yearly exponential growth.

# The AOC applications

Before satellite communication was introduced AOC air ground voice and data communications were conducted solely in the HF and VHF bands, allocated by ITU for safety and regularity services only.  With the introduction of satellite communication, also intended to support non-safety communication traffic, the classifications of various Airline Operational Communication (AOC) applications have been a topic of discussion within the aviation community and the ITU without being adequately resolved.

Preparing for the ITU WRC 2007 conference and deciding on the technology for a future aeronautical communication system, the question arises again as there is an increasing interest to provide passenger communication and administrative services being a non-safety service.  The market mechanism will having prospective communication providers shifting the gray line between safety and non-safety communication in their preferred direction, including the communication service to support some of the Electronic Flight Bag applications.

Through the IATA Regional offices we have conducted a survey with our members to obtain a better insight of the classification of AOC versus AAC and the present situation is presented in the following drawing.  It should be noted that with the changing operating environment and the aircraft systems design, the applications for the future are likely to increase and change.

# AOC traffic volume

IATA circulated a questionnaire to its member requesting to provide information on their present ACARS usage and the anticipated yearly percentage in traffic growth.  Replies were received from 12 airlines, representing around 25 % of the “IATA fleet”.  Taking into account the differences in size and operations and the maturity of ACARS usages the figures can only be seen as an indication.

# Recommendation

The WG –C is invited to note the information contained in this paper and request it be used in the consideration of the next generation communication system.

| Airline |  | Aircraft Number | Number of messages entire fleet | Message per aircraft per month | Annual Growth percentage | 2010 Message per aircraft | 2020 Message per aircraft |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  | 73 | 125000 | 1712 | 0.15 | 3961 | 16023 |
| 2 |  | 31 | 125000 | 4032 | 0.10 | 7143 | 18528 |
| 3 |  | 7 | 50000 | 7143 | 0.10 | 12654 | 32821 |
| 4 |  | 23 | 225000 | 9783 | 0.20 | 29211 | 180865 |
| 5 |  | 145 | 450000 | 3103 | 0.15 | 7178 | 29041 |
| 6 |  | 800 | 3000000 | 3750 | 0.20 | 11197 | 69332 |
| 7 |  | 14 | 75000 | 5357 | 0.05 | 7179 | 11694 |
| 8 |  | 7 | 22500 | 3214 | 0.15 | 7435 | 30078 |
| 9 |  | 12 | 40000 | 3333 | 0.05 | 4467 | 7276 |
| 10 |  | 94 | 325000 | 3457 | 0.10 | 6125 | 15887 |
| 11 |  | 564 | 1511000 | 2679 | 0.25 | 10220 | 95180 |
| 12 |  | 30 | 125000 | 4167 | 0.05 | 5584 | 9095 |
| 13 |  | 202 | 1250000 | 6188 | 0.10 | 10963 | 28434 |
| 14 |  | 60 | 175000 | 2917 | 0.20 | 8709 | 53925 |
| 15 |  | 150 | 325000 | 2167 | 0.10 | 3838 | 9956 |
| 16 |  | 93 | 775000 | 8333 | 0.10 | 14763 | 38291 |
| 17 |  | 30 | 175000 | 5833 | 0.05 | 7817 | 12733 |
| 18 |  | 30 | 125000 | 4167 | 0.05 | 5584 | 9095 |
| 19 |  | 84 | 325000 | 3869 | 0.20 | 11553 | 71533 |
| 20 |  | 4 | 12500 | 3125 | 0.20 | 9331 | 57776 |
| 21 |  | 101 | 125000 | 1238 | 0.05 | 1659 | 2702 |
| 22 |  | 500 | 325000 | 650 | 0.20 | 1941 | 12017 |
|  |  | 3054 | 9686000 | 3172 | 0.13 | 8569 | 36922 |
| Average flight time | 4 |  |  |  |  |  |  |
|  |  |  |  | 26 |  | 71 | 308 |
| Average message | 500 |  | bph | 13215 |  | 35703 | 153842 |
| Size |  |  |  |  |  |  |  |

# Text boxes

Customer

Segment

Channel

Media

A

P

P

L

I

C

A

T

I

O

N

Decreasing Regulatory-Safety Requirements & Constraints

/Increasing Sensitivity Traffic	 Volume Communication Cost

Passengers

Airlines

Air Traffic Service Provider

Sat (AMSS-MSS)/Cellular(MS)

Sat (AMS(R)S/HF-VHF (AM(R)S

- Telephone

- Internet service

- Message service

- Flight Crew schedule

- Passengers List

- Payroll

- Transfer information

- W&B

- Engine/AC 
monitoring

- Pilot reports

- Fuel uploading

- Pilot/Dispatcher
 com

- OOOI

- TWIP

- Delay Report

- Gate
 Assignments

- Weather reports

- ATC

- FIS

- TIS

- ADS

- Ground to Air

-LAAS

-WAAS

-FIS

- Air to Ground/Air

-ADS-B

Addressed

Broadcast

AAC

AOC

Voice

Data

Link

SUMMARY

In this working paper, a first assessment is provided on the AOC traffic based on a questionnaire send to IATA member airlines.  It provides a tentative result of the type and volume of AOC traffic to assist in the selection of a future communication system.