|  | International Civil Aviation Organization WORKING PAPER | ACP/1-WP/4 3/5/07 English only |
| --- | --- | --- |

AERONAUTICAL COMMUNICATIONS PANEL (ACP)

FIRST MEETING

Montréal, 10 to 18 May 2007

| Agenda Item | 3: | Review of ATN SARPs and guidance material, including: |
| --- | --- | --- |
|  | 3.1: | Draft ATN/IPS SARPs |

SARPs FOR IPS IN ANNEX 10

(Presented by Rapporteur of Working Group N)

SUMMARY

This paper contains the amendments to Annex 10, Volume III as presented in WP/3 in a format where all proposed amendments have been incorporated.

INTRODUCTION

Working Paper 3 contains proposals for amending the aeronautical telecommunication network (ATN) Standards and Recommended Practices (SARPs) in Annex 10 — Aeronautical Telecommunications, Volume III — Communication Systems and Part I — Digital Data Communication Systems, Chapters 1 and 3. Considering the numerous amendments and to facilitate their review of the by ACP/1, this paper has all the proposed amendments incorporated to the Appendix.

— — — — — — — —

ACP/1-WP/4 Appendix

APPENDIX

INTERNATIONAL STANDARDS

AND RECOMMENDED PRACTICES

# AERONAUTICAL TELECOMMUNICATIONS

# ANNEX 10

TO THE CONVENTION ON INTERNATIONAL CIVIL AVIATION

# VOLUME III

(COMMUNICATION SYSTEMS)

PART I — DIGITAL DATA COMMUNICATION SYSTEMS

CHAPTER 1.    DEFINITIONS

Note 1.— All references to “Radio Regulations” are to the Radio Regulations published by the International Telecom-munication Union (ITU). Radio Regulations are amended from time to time by the decisions embodied in the Final Acts of World Radiocommunication Conferences held normally every two to three years. Further information on the ITU processes as they relate to aeronautical radio system frequency use is contained in the Handbook on Radio Frequency Spectrum Requirements for Civil Aviation including statement of approved ICAO policies (Doc 9718).

Note 2.— This Part of Annex 10 includes Standards and Recommended Practices for certain forms of equipment for communication systems. While the Contracting State will determine the necessity for specific installations in accordance with the conditions prescribed in the relevant Standard or Recommended Practice, review of the need for specific installation and the formulation of ICAO opinion and recommendations to Contracting States concerned, is carried out periodically by Council, ordinarily on the basis of recommendations of Regional Air Navigation Meetings (Doc 8144, Directives to Regional Air Navigation Meetings and Rules of Procedure for their Conduct).

Note 3.— This chapter contains general definitions relevant to communication systems. Definitions specific to each of the systems included in this volume are contained in the relevant chapters.

Note 4.— Material on secondary power supply and guidance material concerning reliability and availability for communication systems is contained in Annex 10, Volume I, 2.9 and Volume I, Attachment F, respectively.

Aeronautical telecommunication network (ATN). A global internetwork architecture that allows ground, air-ground and avionic data subnetworks to exchange digital data for the safety of air navigation and for the regular, efficient and economic operation of air traffice services.

Aeronautical administrative communications (AAC). Communications necessary for the exchange of aeronautical administrative messages (Re. Annex 10, Volume II, paragraph 4.4.1.1.7).

Aeronautical operational control (AOC). Communication required for the exercise of authority over the initiation, continuation, diversion or termination of flight for safety, regularity and efficiency reasons (Re. Annex 6, Part I, Chapter 1 – Definitions).

Aircraft address. A unique combination of twenty-four bits available for assignment to an aircraft for the purpose of air-ground communications, navigation and surveillance.

Air traffic service.  A generic term meaning variously, flight information service, alerting service, air traffic advisory service, air traffic control service (area control service, approach control service or aerodrome control service) (Re. Annex 11, Chapter 1 – Definitions).

Aircraft earth station (AES). A mobile earth station in the aeronautical mobile-satellite service located on board an aircraft (see also “GES”).

Automatic Dependent Surveillance- Contract (ADS-C). A means by which the terms of an ADS agreement will be exchanged between the ground system and the aircraft, via a data link, specifying under what condition ADS-C reports would be initiated and what data would be contained in the report. (Re. Annex 11, Chapter 1 – Definitions).

Automatic terminal information service (ATIS).  The automatic provision of current, routine information to arriving and departing aircraft throughout 24 hours or a specified portion thereof. (Re. Annex 11, Chapter 1 – Definitions).

Data link-automatic terminal information service (D-ATIS).  The provision of ATIS via data link. (Re. Annex 11, Chapter 1 – Definitions).

Bit error rate (BER). The number of bit errors in a sample divided by the total number of bits in the sample, generally averaged over many such samples.

Carrier-to-multipath ratio (C/M). The ratio of the carrier power received directly, i.e. without reflection, to the multipath power, i.e. carrier power received via reflection.

Carrier-to-noise density ratio (C/No). The ratio of the total carrier power to the average noise power in a 1 Hz bandwidth, usually expressed in dBHz.

Channel rate. The rate at which bits are transmitted over the RF channel. These bits include those bits used for framing and error correction, as well as the information bits. For burst transmission, the channel rate refers to the instantaneous burst rate over the period of the burst.

Channel rate accuracy. This is relative accuracy of the clock to which the transmitted channel bits are synchronized. For example, at a channel rate of 1.2 kbits/s, maximum error of one part in 106 implies the maximum allowed error in the clock is ±1.2 ( 10-3 Hz.

Circuit mode. A configuration of the communications network which gives the appearance to the application of a dedicated transmission path.

Controller pilot data link communication (CPDLC).  A means of communication between controller and pilot, using data link for ATC communications. (Re. Annex 11, Chapter 1 – Definitions).

Data link flight information service (D-FIS).  The provision of FIS via data link(Re. Annex 11, Chapter 1 – Definitions).

Doppler shift. The frequency shift observed at a receiver due to any relative motion between transmitter and receiver.

End-to-end. Pertaining or relating to an entire communication path, typically from (1) the interface between the information source and the communication system at the transmitting end to (2) the interface between the communication system and the information user or processor or application at the receiving end.

End-user. An ultimate source and/or consumer of information.

Energy per symbol to noise density ratio (Es/No). The ratio of the average energy transmitted per channel symbol to the average noise power in a 1 Hz bandwidth, usually expressed in dB. For A-BPSK and A-QPSK, one channel symbol refers to one channel bit.

Equivalent isotropically radiated power (e.i.r.p). The product of the power supplied to the antenna and the antenna gain in a given direction relative to an isotropic antenna (absolute or isotropic gain).

Flight information service (FIS).  A service provided for the purpose of giving advice and information useful for the safe and efficient conduct of flights. (Re. Annex 11, Chapter 1 – Definitions).

Forward error correction (FEC). The process of adding redundant information to the transmitted signal in a manner which allows correction, at the receiver, of errors incurred in the transmission.

Gain-to-noise temperature ratio. The ratio, usually expressed in dB/K, of the antenna gain to the noise at the receiver output of the antenna subsystem. The noise is expressed as the temperature that a 1 ohm resistor must be raised to produce the same noise power density.

Ground earth station (GES). An earth station in the fixed satellite service, or, in some cases, in the aeronautical mobile-satellite service, located at a specified fixed point on land to provide a feeder link for the aeronautical mobile-satellite service.

Note.— This definition is used in the ITU’s Radio Regulations under the term “aeronautical earth station.” The definition herein as “GES” for use in the SARPs is to clearly distinguish it from an aircraft earth station (AES), which is a mobile station on an aircraft.

Mode S subnetwork. A means of performing an interchange of digital data through the use of secondary surveillance radar (SSR) Mode S interrogators and transponders in accordance with defined protocols.

Point-to-point. Pertaining or relating to the interconnection of two devices, particularly end-user instruments. A communication path of service intended to connect two discrete end-users; as distinguished from broadcast or multipoint service.

Slotted aloha. A random access strategy whereby multiple users access the same communications channel independently, but each communication must be confined to a fixed time slot. The same timing slot structure is known to all users, but there is no other co-ordination between the users.

Time division multiplex (TDM). A channel sharing strategy in which packets of information from the same source but with different destinations are sequenced in time on the same channel.

Time division multiple access (TDMA). A multiple access scheme based on time-shared use of an RF channel employing: (1) discrete contiguous time slots as the fundamental shared resource; and (2) a set of operating protocols that allows users to interact with a master control station to mediate access to the channel.

Transit delay. In packet data systems, the elapsed time between a request to transmit an assembled data packet and an indication at the receiving end that the corresponding packet has been received and is ready to be used or forwarded.

VHF digital link (VDL). A constituent mobile subnetwork of the aeronautical telecommunication network (ATN), operating in the aeronautical mobile VHF frequency band. In addition, the VDL may provide non-ATN functions such as, for instance, digitized voice.

Voice-automatic terminal information service (Voice-ATIS). The provision of ATIS by means of continuous and repetitive voice broadcasts. (Re. Annex 11, Chapter 1 – Definitions).

CHAPTER 3.    AERONAUTICAL

TELECOMMUNICATION NETWORK

Note 1.— Detailed technical specifications for ATN/OSI applications are contained in the “Manual of Detailed Technical Specifications for the ATN using ISO/OSI standards and protocols” (Doc 9880).

Note 2.— Detailed technical specifications for ATN/IPS applications are contained in the “Manual of Detailed Technical Specifications for the ATN using IPS standards and protocols” (Doc xxxx) [in preparation].

3.1    DEFINITIONS

Application entity (AE). An AE represents a set of OSI communication capabilities of a particular application process. (Re. ISO Doc. 9545 for further details)

ATN security services. A set of information security provisions allowing the receiving end system or intermediate system to unambiguously identify (i.e. authenticate) the source of the received information and to verify the integrity of that information.

Required communication performance (RCP). A statement of the performance requirements for operational communication in support of specific ATM functions. Re. Manual on Required Communication Performance (RCP) (Doc. 9869).

ATS interfacility data communication (AIDC). Automated data exchange between air traffic services units in support of flight notification, flight coordination, transfer of control and transfer of communication.  ATS message handling service (ATSMHS). An ATN application consisting of procedures used to exchange ATS messages in store-and-forward mode over the ATN such that the conveyance of an ATS message is in general not correlated with the conveyance of another ATS message by the service provider.

ATS message handling system(AMHS). The set of computing and communication resources implemented by ATS organizations to provide the ATS message handling service.

Authorized path. A communication path that the administrator(s) of the routing domain(s) has pre-defined as suitable for a given traffic type and category.

Data link initiation capability (DLIC). A data link application that provides the ability to exchange addresses, names and version numbers necessary to initiate data link applications. (Re. Doc. 4444).

3.2    INTRODUCTION

The ATN is specifically and exclusively intended to provide digital data communications services to air traffic service provider organizations and aircraft operating agencies in support of :

1)	air traffic services communication (ATSC) with aircraft;

2) air traffic services communications between ATS units;

3)	aeronautical operational control communications (AOC); and

4)	aeronautical administrative communication (AAC).

3.3    GENERAL

Note — The Standards and Recommended Practices in sections 3.4 – 3.8 below define the minimum required protocols and services that will enable the global implementation of the ICAO Aeronautical Telecommunication Network (ATN).

3.3.1    ATN communication services shall support ATN applications.

3.3.2    Requirements for implementation  of the ATN shall be made on the basis of regional air navigation agreements. These agreements shall specify the area in which the communication standards for the ATN/OSI or the ATN/IPS are applicable.

3.4    GENERAL REQUIREMENTS

3.4.1    The ATN shall either use International Organization for Standardization (ISO) communication standards for open systems interconnection (OSI) or use the Internet Society (ISOC) communications standards for the Internet Protocol Suite (IPS)

Note.— Interoperability between interconnecting OSI/IPS networks shall be arranged prior to implementation.

3.4.2    The AFTN/AMHS gateway shall ensure the interoperability of AFTN and CIDIN stations and networks with the ATN.

3.4.3    The ATN shall accommodate routing based on a pre-defined routing policy.

3.4.4    The ATN shall transmit, relay and (or) deliver messages in accordance with the priority classifications and without discrimination or undue delay.

3.4.5    The ATN shall provide means to define data communications that can be carried only over authorized paths for the traffic type and category specified by the user.

3.4.6    The ATN shall provide communication in accordance with the prescribed required communication performance (RCP) (Manual on Required Communication Performance (Doc. 9896) refers)

3.4.7    The ATN shall operate in accordance with the communication priorities defined in (Table 3-1 and Table 3-2.

3.4.8    The ATN shall enable exchange of application information when one or more authorized paths exist.

3.4.9    The ATN shall notify the appropriate application processes when no authorized path exists.

3.4.10    The ATN shall make provisions for the efficient use of limited bandwidth subnetworks.

3.4.11    Recommendation. The ATN should enable an aircraft intermediate system (router) to  connect to a ground intermediate system (router) via different  subnetworks.

3.4.12    Recommendation. The ATN shoud  enable an aircraft intermediate system (router) to  connect to different  ground intermediate systems (routers).

3.4.13    The ATN shall enable the exchange of address information between applications.

3.4.14    Where the absolute time of day is used within the ATN, it shall be accurate to within 1 second of coordinated universal time (UTC).

Note.— The  time accuracy value  results in synchronization errors of up to two seconds.

3.5    ATN APPLICATIONS REQUIREMENTS

3.5.1    System applications

Note.— System applications provide services that are necessary for operation of the ATN.

3.5.1.1    The ATN shall support the Data Link Initiation Capability (DLIC)  applications as contained in Doc. 9694 (Manual on ATS Data link applications Part I) when air-ground data links are implemented.

3.5.1.2    The ATN/OSI end system shall support the following DIR application functions when AMHS and/or security protocols are implemented (Re. ITU-T X.500 series):

a)	directory information retrieval; and

b)	directory information modification .

3.5.2    Air-ground applications

3.5.2.1    The ATN shall be capable of supporting on or more of the following  applications, in accordance with the provisions of Doc 9694:

a)	ADS-C;

b)	CPDLC; and

c)	FIS (including ATIS and METAR).

3.5.3    Ground-ground applications

3.5.3.1    The ATN shall be capable of supporting: AIDC applications as contained in Doc. 9694 and ATS message handling services application (ATSMHS).

3.6    ATN COMMUNICATION SERVICE REQUIREMENT

3.6.1    ATN/IPS upper layer communication service.

3.6.1.1    An ATN host shall be capable of supporting the ATN/IPS upper layers  including an application layer.

3.6.2    ATN/OSI upper layer communications service.

3.6.2.1    An ATN/OSI end system (ES) shall be capable of supporting the OSI upper layer communications service (ULCS) including session, presentation and application layers.

Note.— The detailed technical specifications for OSI ULCS are defined in Doc. 9705.

3.6.3    ATN/IPS Internet Communication Service.

3.6.3.1    An ATN host shall be capable of supporting the ATN/IPS Internet including the:

a)	transport layer in accordance with RFC 793 (TCP) and RFC 768 (UDP); and

b)	network layer in accordance with RFC 2460 (IPv6).

3.6.3.2    An IPS Router shall support the ATN network layer in accordance with RFC 2460 (IPv6) and RFC 4271 (BGP), and RFC 2858 (BGP multiprotocol extensions).

3.6.4    ATN/OSI Internet communications service.

3.6.4.1    An ATN/OSI end system  shall be capable of supporting the ATN Internet including the:

a)	transport layer in accordance with ISO/IEC 8073 (TP4) and ISO/IEC 8602 (CLTP); and

b)	network layer in accordance with ISO/IEC 8473 (CLNP).

3.6.4.2    An ATN intermediate system (IS) shall support the ATN network layer in accordance with ISO/IEC 8473 (CLNP) and ISO/IEC 10747 (IDRP).

3.7    ATN NAMING AND ADDRESSING REQUIREMENTS

Note.— The ATN naming and addressing scheme supports the principles of unambiguous identification of intermediate systems (routers) and end systems (hosts)  and provides global address standardization.

3.7.1    The ATN shall provide provisions for unambiguous application identification.

3.7.2    The ATN shall provide provisions for unambiguous  addressing.

3.7.3    The ATN shall provide means to unambiguously address al ATN end systems (hosts) and intermediate systems (routers).

3.7.4    The ATN addressing and naming plans shall allow States and organizations to assign addresses and names within their own administrative domains.

3.8    ATN SECURITY REQUIREMENTS

3.8.1    The ATN shall make provisions whereby only the controlling ATS unit may provide ATC instructions to aircraft operating in its airspace.

Note — This is achieved through the current and next data authority aspects of the controller-pilot data link communications (CPDLC) application.

3.8.2    The ATN shall enable the recipient of a message to identify the originator of that message.

3.8.3    ATN end systems supporting ATN security services shall be capable of authenticating the identity of peer end systems, authenticating the source of messages and ensuring the data integrity of the messages.

Note.— A request for non-use of protection may be honoured. This means that the use of security is the default and negotiation to non-use is based on local policy.

3.8.4    The ATN services shall be protected against service attacks to a level consistent with the application service requirements.

Table 3-1.    Mapping of ATN communication priorities

|  |  | Corresponding protocol priority |
| --- | --- | --- |
| Message categories | ATN application | Transport layer priority | Network layer priority |
| Network/systems management | SM | 0 | 14 |
| Distress communications |  | 1 | 13 |
| Urgent communications |  | 2 | 12 |
| High-priority flight safety messages | CPDLC, ADS | 3 | 11 |
| Normal-priority flight safety messages | AIDC, ATIS | 4 | 10 |
| Meteorological communications | METAR | 5 | 9 |
| Flight regularity communications | CM, ATSMHS | 6 | 8 |
| Aeronautical information service messages |  | 7 | 7 |
| Network/systems administration | SM, DIR | 8 | 6 |
| Aeronautical administrative messages |  | 9 | 5 |
| <unassigned> |  | 10 | 4 |
| Urgent-priority administrative and U.N. Charter communications |  | 11 | 3 |
| High-priority administrative and State/Government communications |  | 12 | 2 |
| Normalpriority administrative communications |  | 13 | 1 |
| Lowpriority administrative communications and aeronautical passenger communications |  | 14 | 0 |
| Note. The network layer priorities shown in the table apply only to connectionless network priority and do not apply to subnetwork priority. |

Table 3-2.    Mapping of ATN network priority to mobile subnetwork priority

| Message categories | ATN network layer priority | Corresponding mobile subnetwork priority (see Note 4) |
| --- | --- | --- |
|  |  | AMSS | VDL Mode 2 | VDL Mode 3 | VDL Mode 4 (see Note 5) | SSR Mode S | HFDL |
| Network/systems management | 14 | 14 | see Note 1 | 3 | high | high | 14 |
| Distress communications | 13 | 14 | see Note 1 | 2 | high | high | 14 |
| Urgent communications | 12 | 14 | see Note 1 | 2 | high | high | 14 |
| High-priority flight safety messages | 11 | 11 | see Note 1 | 2 | high | high | 11 |
| Normal-priority flight safety messages | 10 | 11 | see Note 1 | 2 | high | high | 11 |
| Meteorological communications | 9 | 8 | see Note 1 | 1 | medium | low | 8 |
| Flight regularity communications | 8 | 7 | see Note 1 | 1 | medium | low | 7 |
| Aeronautical information service messages | 7 | 6 | see Note 1 | 0 | medium | low | 6 |
| Network/systems administration | 6 | 5 | see Note 1 | 0 | medium | low | 5 |
| Aeronautical administrative messages | 5 | 5 | not allowed | not allowed | not allowed | not allowed | not allowed |
| <unassigned> | 4 | unassigned | unassigned | unassigned | unassigned | unassigned | unassigned |
| Urgent-priority administrative and U.N. Charter communications | 3 | 3 | not allowed | not allowed | not allowed | not allowed | not allowed |
| High-priority administrative and State/Government communications | 2 | 2 | not allowed | not allowed | not allowed | not allowed | not allowed |
| Normal-priority administrative communications | 1 | 1 | not allowed | not allowed | not allowed | not allowed | not allowed |
| Low-priority administrative communications and aeronautical passenger communications | 0 | 0 | not allowed | not allowed | not allowed | not allowed | not allowed |
| Note 1.— VDL Mode 2 has no specific subnetwork priority mechanisms. Note 2.— The AMSS SARPs specify mapping of message categories to subnetwork priority without explicitly referencing ATN network layer priority. Note 3.— The term “not allowed” means that only communications related to safety and regularity of flight are authorized to pass over this subnetwork as defined in the subnetwork SARPs. Note 4.— Only those mobile subnetworks are listed for which subnetwork SARPs exist and for which explicit support is provided by the ATN boundary intermediate system (BIS) technical provisions. Note 5.— The VDL Mode 4 subnetwork provides support for surveillance applications (e.g. ADS). |

— END —

# Footnotes

( Tables 3-1 and 3-2 are located at the end of this chapter.