## Slide 1: Session 1: The Nature of the Problem
ICAO Environmental Colloquium
April 2001
Presented by Mr. T. Connor

## Slide 2: Session 1: The Nature of the Problem
ICAO Environmental Colloquium
April 2001
Presented by Mr. T. Connor

## Slide 3: Session 1: The Nature of the Problem
ICAO Environmental Colloquium
April 2001
Presented by Mr. T. Connor

## Slide 4
noise
sound, especially when it is unwanted, unpleasant or loud
sound sensory perception as a result of periodic vibrations that are propagated
through a medium,
such as air, as
pressure waves,
so that the medium
is displaced from its
equilibrium state

## Slide 5: Adverse Effects of Noise
Noise-induced hearing impairment
Cardiovascular and physiological effects
  Hypertension, heart disease
Mental health disorders
  Anxiety, emotional stress
Performance deficiency
  Ability of children to learn
Interference with speech communications
Sleep disturbance
Annoyance
Degradation of quality of life

## Slide 6
annoyance a feeling of displeasure associated with any agent or condition, known or believed by an individual or group, to adversely affect them

## Slide 7: Noise (Sound) Properties
Pressure: Source vibration causes compressions and rarefactions of the air particles; pressure wave
Frequency: Number of compressions/rarefactions per second
Amplitude: Height of the pressure (sound) wave

## Slide 8: Noise (Sound) Properties
Pressure: Source vibration causes compressions and rarefactions of the air particles; pressure wave
Frequency: Number of compressions/rarefactions per second
Amplitude: Height of the pressure (sound) wave

## Slide 9: Frequency and Audibility
Sound
Spectra

## Slide 10: Frequency and Pitch
Source
Sound Spectra at Peak Level

## Slide 11: Frequency and Pitch
Source
Sound Spectra at Peak Level

## Slide 12: Frequency and Pitch
Source
Sound Spectra at Peak Level

## Slide 13: Frequency and Pitch
Source
Sound Spectra at Peak Level

## Slide 14: Noise Measurement
Decibel (dB)
A unit for measuring the loudness of sound. The logarithm of the ratio of acoustic power
(sound) intensities.

## Slide 15: Noise Measurement
Decibel (dB)
A unit for measuring the loudness of sound. The logarithm of the ratio of acoustic power
(sound) intensities.
A-weighting
Weighting of the sound
spectra to approximate
the human ear’s
response to sound.

## Slide 16: Noise Measurement Comparison of Noise Levels in dB(A)
Threshold of hearing
Threshold of pain

## Slide 17: Noise Measurement
Sound Exposure Level (SEL)
A measure of the physical energy of the noise event taking into account intensity and duration.

## Slide 18: Noise Measurement

## Slide 19
Noise Measurement
Sound Exposure Level (SEL)
Integration of A-weighted levels (AL)
Human ear’s response to sound
Assess community noise
Effective Perceived Noise Level (EPNL)
Tone-corrected PNL
Noisiness of discreet frequencies
Aircraft noise certification

## Slide 20
Aircraft Noise Assessment
Concerns to address
  health and welfare
  land use compatibility
  environmental degradation
Desired characteristics
  applicable to above concerns
  simple to understand and use
  relates to community/environmental noise
  ‘figure of merit’
  accounts for magnitude, frequency of occurrence, and time of day

## Slide 21
Aircraft Noise Assessment
Metrics
Method | Basic Noise Measure
Community Noise Equivalent Level (CNEL) | Sound Exposure Level (SEL)
Day Night Evening Noise Level (DNEL) | SEL
Day Night Sound Level (DNL) | SEL
Equivalent (Continuous) Sound Level (Leq) | SEL
KOSTEN | A-weighted Sound Pressure Level (AL)
Noise and Number Index (NNI) | Perceived Noise Level (PNL)
Noise Exposure Forecast (NEF) | Effective Perceived Noise Level (EPNL)
Psophic Index (IP) | PNL
Weighted Effective Continuous Perceived Noise Level (WECPNL) | EPNL or AL

## Slide 22
Aircraft Noise Assessment
Metrics
CAEP/5 chose DNL to assess the benefits of new aircraft noise standards and transition strategies with ‘significant’ exposure defined as DNL 55 dB or higher and ‘high’ exposure defined as DNL 65 dB or higher.

## Slide 23
Aircraft Noise Assessment
Metrics
Day Night Level (DNL) is the energy-averaged sound level measured over a 24-hour period with a 10 dB penalty applied to nighttime events (2200 to 0700 hr) to account for increased annoyance of sound during night hours.
10 dB
Penalty
10 dB
Penalty

## Slide 24
Aircraft Noise Assessment
DNL and Annoyance

## Slide 25
Attributes
aircraft noise and performance database
sound propagation and attenuation algorithms
runway orientation
flight track definitions
operations distribution
GIS tie-in (population centroids, geographic features, political boundaries)
Aircraft Noise Assessment
Use of Computer Models

## Slide 26
Aircraft Noise Assessment
Use of Computer Models
CAEP/5 decided to:
Initiate the effort to adopt FAA’s Integrated Noise Model (INM) as the noise engine to drive strategic assessments
Develop an ICAO database for noise modeling, building on the principle of the INM database

## Slide 27
Aircraft Noise Assessment
Integrated Noise Model
Capable of producing noise contours for a variety of noise metrics
Extensive aircraft noise and performance database
Wide distribution
Available in Windows 95, 98 or Windows NT
User’s Guide and Technical Manual
Web page for information and model updates
  http://www.aee.faa.gov/aee-100/inm
Technical support provided
Commercial training courses available

## Slide 28
Aircraft Noise Assessment
Integrated Noise Model
Integrated Noise Model (INM) produces the noise exposure maps used for land use planning.

## Slide 29
Premise
Aircraft noise exposure around an airport depends principally on the volume and mix of aircraft traffic, departure and arrival flight routings, operational practices, and the number and distribution of people living nearby.
CAEP experience
Before CAEP/3, an “average” airport had been used to assess stringency proposals.
At CAEP/3, a small sample (13) of airports was used in the assessment.
CAEP/4 agreed to evaluate a global model which became the Model for Assessing Global Exposure to the Noise of Transport Aircraft (MAGENTA).
Aircraft Noise Assessment
Regional and Global Evaluations

## Slide 30: Aircraft Noise Control and Mitigation
Source reduction
Noise abatement procedures/routes
Noise mitigation at the receiver
Land use compatibility management
Operating restrictions

## Slide 31: Aircraft Noise Control and Mitigation Source Reduction
Advancements in technology
Industry/government partnerships
Criteria for new noise standard:
  technologically practicable
  economically reasonable
  appropriate to type
  environmentally beneficial
  maintains highest degree of safety

## Slide 32: Aircraft Noise Control and Mitigation Noise Abatement Procedures/Routes
Departure
  Engine power cutback
Arrival
  Continuous descent
Flight tracks
  Geographic feature (bodies of water)
  Other compatible ‘pathways’ (major roads, railways)
Preferential runway usage

## Slide 33: Aircraft Noise Control and Mitigation Noise Abatement Procedures/Routes
Departure
  Engine power cutback
Arrival
  Continuous descent
Flight tracks
  Geographic feature (bodies of water)
  Other compatible ‘pathways’ (major roads, railways)
Preferential runway usage

## Slide 34: Aircraft Noise Control and Mitigation Noise Abatement Procedures/Routes
Departure
  Engine power cutback
Arrival
  Continuous descent
Flight tracks
  Geographic feature (bodies of water)
  Other compatible ‘pathways’ (major roads, railways)
Preferential runway usage

## Slide 35: Aircraft Noise Control and Mitigation Noise Abatement Procedures/Routes
Departure
  Engine power cutback
Arrival
  Continuous descent
Flight tracks
  Geographic feature (bodies of water)
  Other compatible ‘pathways’ (major roads, railways)
Preferential runway usage

## Slide 36: Aircraft Noise Control and Mitigation Mitigation at the Receiver
Residential noise insulation
Sound barriers

## Slide 37: Aircraft Noise Control and Mitigation Mitigation at the Receiver
Residential noise insulation
Sound barriers

## Slide 38: Aircraft Noise Control and Mitigation Mitigation at the Receiver
Residential noise insulation
Sound barriers
Noise berm at Chicago O’Hare International

## Slide 39: Aircraft Noise Control and Mitigation Land Use Compatibility Management
Local zoning
Buy-out
Relocation
Disclosure

## Slide 40: Aircraft Noise Control and Mitigation Operating Restrictions
Curfew
Noise surcharge
Quotas
Noise budgets
Phaseout

## Slide 41: Implications of Unresolved Aircraft Noise Problems
Organized opposition to airport expansion
Proliferation of local use restrictions
  119 in 1980 to 600 as of March 2001
Imposition of energy inefficient flight routing
Government outlays for local noise mitigation
Pressure to execute marginally safe flight procedures, i.e., “beat the box

## Slide 42
Organized Opposition to Airport Expansion
Individual groups established locally to express concerns over airport noise and expansion.
Trend for these groups to coordinate their activities internationally and share information through the internet.
Opposition to new runway addition will result in traffic shifts to reliever airports where incremental growth will lead to large increases in noise contours.
Opposition to new runway addition in the US is contributing to airport congestion.

## Slide 43
Organized Opposition to Airport Expansion
International Anti-Noise Groups
Friends of the Earth Europe (Austria, Belgium, Cyprus, Denmark, England, Finland, France, Germany, Greece, Ireland, Italy, Luxembourg, Macedonia, the Netherlands, Norway, Poland, Slovenia, Spain, Switzerland).
European Union Against Aircraft Nuisances (UECNA), England (Members of the UECNA are the national umbrella organizations against aviation noise)
Europe
Net-Sky Coalition against expansion of Liege- Airport (Belgium)
French National Association Against Aircraft Noise and Pollution, UFCNA (France)
Federal Organization Against Airport and Aircraft Noise (Germany)
Environmental Organization of Copenhagen (Denmark)
Heathrow Association for the Control of Aircraft Noise, HACAN (England)
Coalition Against Runway 2, CAR2 (England)
Mileudefensie (the Netherlands)
Australia
Bankstown & Environs Airport Resistance
Coalition of Airport Groups
Save Our Skies
Third runway Protest Page
United States
Citizens Against Airport Pollution, CAAP (CA)
Citizens Concerned About Jet Noise, CCAJN (VA)
AReCO Alliance of Residents concerning O’Hare (IL)
Sane Aviation For Everyone, SAFE (NY)
Boulder County Citizens Against Aviation Noise, BCCAAN (CO)
Airport Coordinating Team, ACT (MD)
Citizens against Sea-Tac Expansion, CASE (WA)
Westside Civic Federation, WCF (LAX)
South Metro Airport Action Council, SMAAC (MN)
Airport Neighbors Decide, AND (OH)
Colorado Citizens Against Noise, COLCAN (CO)
Airport Area Residents Alliance, AARA (TN)
Alaska Quiet Rights Coalition, AQRC

## Slide 44: Model for Assessing Global Exposure to the Noise of Transport Aircraft (MAGENTA)
Presented by Mr. Ben Sharp

## Slide 45: Purpose of MAGENTA
Determine aggregate world population impacted by aircraft noise for baseline year (1998).
Include significant noise impact contribution from all world airports with jet operations.
Base estimates on actual aircraft operations and demographic data.
Estimate the change in population impacted by aircraft noise worldwide for the following noise mitigation measures:
    Aircraft phase-out
    Reduced aircraft noise levels
    Air traffic control procedures
    Land-use planning

## Slide 46: The History of MAGENTA
Initiated as an FAA project in late 1996
Briefings given to:
  ICCAIA, Seattle, Oct 96
  CAEP FESG, Brussels, Nov 96
  ANCAT, Paris, Jan 1997
  CAEP Steering Committee, Canberra, Jan 98
  CAEP Working Group 2, Ottawa, April 1998
  Adopted by ICAO at CAEP 4, April 98
  Briefing on capabilities, CAEP Steering Group, Madrid, June 99
  Briefing on initial results, CAEP Steering Group, Singapore, May 2000
  Briefing on intermediate results, CAEP Steering Group, Seattle, Sept 2000
CAEP Magenta Task Group established in April 98

## Slide 47: MAGENTA Task Group
Chairman - Dr. John Ollerhead, UK CAA
Task Group members:
  FAA
  IATA
  ICCAIA
  ACI Europe
  ICAO/CAEP FESG/JET9
  CAEP representatives from France, Netherlands, Japan
Attendees:
  Boeing, Airbus
  PW,GE
  Airlines
  Eurocontrol
  NASA

## Slide 48: Basic Components of MAGENTA
Airport data
Airport operations for baseline year (1998)
Forecasted operations through 2020
Noise engine to develop noise contours
Aircraft noise data – current and future
Population data

## Slide 49: Airport Data
Airports classified into categories:
  Shell 1: Airports with INM data files containing runway usage and flight tracks, allowing noise contours to be developed and combined with digital population data to determine population exposed.
  Shell 1B: Airports with manufactured INM files allowing noise contours to be developed.
  Shell 2: Airports with no INM files. Noise contour size (not shape) calculated by generalized model (GCAM) developed from Shell 1 airport data.

## Slide 50: Study Regions and Airport Samples

## Slide 51: Airport Operations
Aircraft operations classified into seat class/stage length categories for each of 21 world Route Groups, i.e. North Atlantic, TransPacific, Europe-Africa, Intra-US, etc. , at each Shell 1 airport.
Baseline year (1998) mix of operations by seat class/stage length category at each airport determined by processing 1998 IOAG data for scheduled passenger, cargo and charter operations.
Baseline and future year total aircraft operations by seat class/stage length category and Route Group based on traffic projections provided by CAEP/FESG.

## Slide 52: Single Route Aircraft Matrix (Single airport, 1996)

## Slide 53: Fleet Mix Forecast Processor
Fleet forecast processor operates on 1998 baseline fleet at each airport and takes account of:
  Growth
  Retirement based on survivor curve
  Replacement
  Phase-out
  Stringency
Replacement aircraft selected from CAEP Jet-9 Best Practice database.

## Slide 54: Aircraft Operations Forecasts
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Noise Engine - INM
Shell 1 airports use INM to calculate contour area and shape - selected because of its comprehensive aircraft noise data base and widespread use in many countries.
INM run time is determined by number of aircraft/stage lengths - for 185 airports, run time is measured in weeks.
Equivalent aircraft concept developed by which aircraft are replaced by combinations of four standard aircraft.
This concept reduces run time per airport to minutes - total run time for 185 airports is about eight hours.

## Slide 56: Population Databases
MAGENTA population databases include:
  US Census Bureau 1990 population database for the US.
  Joint Resources Assessment Database System (JRADS) - a worldwide population database that includes population estimates for all major cities in 130 countries.
  Digital files for selected airports - LHR, SYD, CDG.
JRADS data in the form of circles for population centers and grids for distributed population.
Adjustments made using local land-use maps to increase accuracy.

## Slide 57: Key MAGENTA Assumptions
No change in airport configuration or routes with time.
Population distributions remain constant with time.
All aircraft use INM default departure procedure – ICAO B
All new production aircraft taken from CAEP Jet-9 database, and have unchanging noise/performance characteristics.
Within any aircraft range/size cell all new production aircraft are distributed evenly between a) manufacturers, and then b) eligible types/versions.

## Slide 58: MAGENTA Outputs
MAGENTA estimates the number of people living within the DNL 55 (impacted) and DNL 65 (significantly impacted) contours by region:
  Region 1 - North America (US, Canada)
  Region 2 - ECAC countries
  Region 3 – Japan, Australia, New Zealand
  Region 4 – Rest of the world, excluding CIS countries

## Slide 59: What are the trends?
Aviation growth
Source reduction technology
Airport restrictions/operational control
Number of people exposed to aircraft noise

## Slide 60: What are the trends? Aviation Growth

## Slide 61: What are the trends? Aviation Growth
Airports in Non-Exempt Countries Theoretically Reaching Capacity without Runway Additions

## Slide 62: What are the trends? Source Reduction Technology
Date of Entry into Service
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
2005
10 dB
Chapter 2
Chapter 3
Increase in
weight or range
Low-bypass-ratio Turbofans
First-generation high-bypass-ratio Turbofans
Second-generation high-bypass-ratio Turbofans
Turbojets
CONCORDE

## Slide 63: What are the trends? Airport Restrictions

## Slide 64: What are the trends? Number of People Exposed to Aircraft Noise