## Slide 1
International Civil Aviation Organization Colloquium on Environmental Aspects of Aviation Aircraft Noise - The Way Forward Willard Dodds, Chairman ICCAIA Noise and Emissions Committee Montreal, 9-11 April 2001

## Slide 2
Progress in Source Noise Reduction
Entry Into Service Date
Sideline Take-off Noise Level
Corrected for Aircraft Thrust
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
2nd Generation Turbofans
Turbojets
1st Generation Turbofans
20 dB
Technology has delivered major reductions in noise over past 40 years, but cannot be expected to deliver such dramatic reductions going forward - Elements of the balanced approach will be needed

## Slide 3
Balancing Aircraft Design Requirements
Reliability Fuel Cost Life-cycle Cost
Timing Cost Market
Noise Emissions
Fuel Burn
Payload
Range
Environmental requirements
Aircraft performance
Business case
Operating costs

## Slide 4
Aircraft size and seat capacity must match a wide range of operators’ market and efficiency requirements; aircraft families provide increased flexibility for the operators to optimise their fleets according to their specific needs
Aircraft families are very cost-efficient for operators (commonality in crew training, parts, support, etc.), and a plus for safety
Aircraft families enable manufacturers to offer timely and economically-efficient models, in response to a fast-evolving market demand, despite the long product design & production cycle and the considerable development costs. The largest growth version in a family is particularly productive
Market Completeness and Product Growth
Aircraft and Engines Incorporate Growth Potential at Product Launch by Building Noise Margins Into the Initial Design

## Slide 5
Aircraft Family Growth
Average MTOW growth ~ 2 % per year based on B737, B757, B767, B777, A300, A310, A320, A340 families
Aircraft Families Are Developed to Include Larger, More Productive Aircraft

## Slide 6
Market Completeness and Product Growth
737-100
1967
99 Passengers
2160 Statute miles range
110,000 lbs. MTOW
737-300
1984
149 Passengers
2595 Statute miles range
138,500 lbs. MTOW
737-900
2000
189 Passengers (91%)
3159 Statute miles range(46%)
174,200 lbs. MTOW (58%)

## Slide 7
Design & Test Margins
  To Ensure That New Aircraft Meet the Proposed Chapter 4 Standard, Manufacturers Will Have to Target An Extra Margin
A significant margin between noise targets and certification requirements is needed to guarantee compliance - Noise prediction inaccuracies - Design changes during development - Certification test variability
Thus, two components contribute to the need for a margin - The design and test margin covers technical risks associated with the aircraft development and with the noise level demonstration - A growth margin allows manufacturer to protect further development of the aircraft family

## Slide 8
Aircraft MTOW
Cumulative noise level
Design and test margin
Growth margin
Baseline
Final growth
Average
demonstrated
Guaranteed
80% confidence
80% confidence
ICAO standard limit
Design & Test Margins and Growth Margins
Required at Aircraft Launch

## Slide 9
Aggressive International Noise Research Programs
EU FANPAC
EU X-NOISE
EU SILENCE(R)
US NASA AST
US NASA QAT
1994
1995
1996
1997
1998
1999
2000
2001
2002
2003
2004
2005
Japanese ESPR
Japanese HYPR

## Slide 10
ICCAIA Support for Balanced Approach
Reduction of noise at source
Improved land use planning and control around airports and noise mitigation measures
Improved noise abatement operational procedures
CAEP examination of the role of operating restrictions …and further work on an ICAO framework for implementation

## Slide 11
Summary- Noise Stringency
Dramatic progress in source noise reduction has been achieved with the introduction of new technology
Environmental and design tradeoffs must always be balanced in aircraft and engine design, and considered in noise reduction measures
New aircraft will be designed with a margin below certification requirements to allow for design/test and growth needs
Research programs to further improve noise technology are active, but going beyond currently available technology becomes an increasingly difficult challenge, and relies on substantial and sustained funding
Nevertheless, noise reduction at source is only part of the solution. To protect and maximize the benefits, all the factors of the balanced approach should be addressed

## Slide 12
Concluding Remarks
ICCAIA believes that ICAO and the CAEP are the correct forums for developing international environmental standards and recommended practices. The administrative structure and work processes developed are crucial to the continued progress for improving the capacity of the international aviation sector. If the benefits of such standards and practices are to be maximized, they need to be implemented in a consistent manner by the international community.
In light of the difficult technical issues involved, we recognize the achievements of CAEP/5 in recommending
  a new Chapter 4 noise certification standard
  development of a recertification process
  balanced approach with no global phaseout
We accept the additional burden caused by the CAEP/5 stringency recommendation, and are taking appropriate actions on new and existing products

## Slide 13
Concluding Remarks
We appreciate the willingness by the CAEP to allow ICCAIA to contribute basic noise, cost and technical data to the Working Groups, MAGENTA and the FESG during the process of developing appropriate new noise standards
We are willing to take every opportunity of our involvement to continue supporting as efficiently as we can the efforts of ICAO/CAEP