## Slide 1: EMISSIONS OPERATIONAL-MEASURES WORKING GROUP CAEP WG-4 REDUCING FUEL BURN THROUGH IMPROVED OPERATIONAL MEASURES
Colloquium on Environmental Aspects of Aviation
Montreal, 9 to 11 April 2001
Alfredo Iglesias- Rapporteur WG4

## Slide 2: BACKGROUND
“IPCC Special Report on Aviation and the Global Atmosphera” identified the operational measures as a way to reduce emissions.
CAEP Action Plan incorporate the operational measures as one of the key issues in the strategy for accomplish Kioto objetives from aviation.

## Slide 3: Introduction
WG 4 was created in the CAEP-4, in 1998
Between CAEP 4 and CAEP 5 , WG activities was focused on two key task:
  Environmental beneficts of CNS/ATM implementation
  Circular on operational oportunities to minimize fuel consumption

## Slide 4: Summary of results
Draft ICAO Circular on Operational Opprtunities to Minimize Fuel Use
Quantification of fuel reduction via the implementation of CNS/ATM-(Europe/US airpace)
Parametric model for expand the model to the rest of the world

## Slide 5: ICAO CIRCULAR ON OPERATIONAL OPPORTUNITIES TO MINIMISE FUEL USE AND REDUCE EMISSIONS

## Slide 6: Circular Objectives
Document the environmental benefits resulting from the use of current aircraft and infrastructure, and the related benefits of infrastructure improvements; and
Demonstrate that the more efficient use of infrastructure and equipment is an effective means to reduce aviation emissions

## Slide 7: Background
CAEP/4 Agreed WG4 Work program
Task was specified to identify, disseminate, and to the extent practicable, ensure use of the industry’s fuel conservation/emissions reduction protection.
Focus on operational measures that achieve near term reductions in aircraft emissions including in-flight and ground level operation

## Slide 8: Principles of Fuel Savings
  Fly the most fuel efficient aircraft type for the sector
  Taxi the most fuel efficient route
  Fly the most fuel efficient route
  Fly at the most fuel-efficient speed
  Operate at the most economical altitude
  Maximise the aircraft’s load factor
  Minimise the empty weight of the aircraft
  Load the minimum fuel to safely complete the flight
  Minimise the number of non-revenue flights
  Maintain a clean and efficient airframe and engines

## Slide 9: Circular Structure
EXECUTIVE SUMMARY
ABOUT THIS CIRCULAR
INTRODUCTION
AIRPORT OPERATIONS
AIRCRAFT ENVIRONMENTAL PERFORMANCE
MAINTENANCE
WEIGHT REDUCTION
AIR TRAFFIC MANAGEMENT (ATM)
NON-REVENUE FLYING
FLIGHT/ROUTE PLANNING & OTHER OPERATIONAL ISSUES
TAKEOFF & CLIMB
CRUISE
DESCENT & LANDING
LOAD FACTOR IMPROVEMENT
IMPLEMENTATION

## Slide 10: Circular Findings
At airports,
Aircraft are only responsible for about half of the emissions produced, on average.
Other main emissions sources and fuel consumers are ground transportation and ground support equipment (GSE).
Airports vary greatly in terms of their current situation and their potential for appropriate improvements.

## Slide 11: Circular Findings
Good maintenance processes and procedures essential to assure optimum fuel consumption.
Operational measures
  Weight reduction
  Reduce Non Revenue Flying
  Flight procedures (T.O, Landing, approach)
  Flight Planning
Infrastructure
  CNS/ATM Implementation

## Slide 12: Stakeholders
Need for cooperation among multiple Stakeholders
  Manufactures
  Airports
  Operators
  Air Traffic Services provider
  Government Regulators
  Others (eg Handling companies, land use policymakers,etc.)

## Slide 13: Recommendations
CAEP was requested to endorse the Circular presented and recommend
  Publication as Guidance Material
  Distribution to Contracting States

## Slide 14: ENVIRONMENTAL BENEFITS ASSOCIATED WITH CNS/ATM INITIATIVES

## Slide 15: Background - History
Terms of Reference for Working Group 4: “quantify and ensure that relevant environmental impacts of aviation emissions are taken into account in the global and regional planning of CNS/ATM and incorporated into airport planning.”
In response to TOR, CAEP directed WG4 to “evaluate the potential impact of CNS/ATM systems enhancements and recommended actions to facilitate implementation on a regional and global basis.”

## Slide 16: Background - History (cont.)
Working Group 4 embarked on a task to develop an initial methodology to assess the environmental benefits of proposed CNS/ATM initiatives and to provide the CAEP with an initial global assessment of those benefits.
Notes: In response to that

## Slide 17: Background - MOA
FAA and EUROCONTROL signed MOA, “Development of a Preliminary Common Methodology to Quantify Environmental Benefits Arising From CNS/ATM Systems,” Oct 1999.
  Develop preliminary estimates of fuel savings and resulting emission reductions from CNS/ATM initiatives in the U.S and Europe*.
  Estimate global fuel burn and emissions for the baseline case. (No CNS/ATM initiatives considered)
*Note that the U.S. and Europe chosen for the initial development due
to availability of the required CNS/ATM initiative data.

## Slide 18: Background - MOA Scope of Work
Coordinate the development of a parametric model.
Estimate U.S. and Europe fuel burn and emissions for 1999-2015.
  CONUS and ECAC en route and terminal airspace
  Surface operations in CONUS and Europe (ECAC area)
  Oceanic airspace
Estimate potential reductions in fuel use for U.S. and Europe based on CNS/ATM modernization plans.
  Use NAS Architecture V4.0 for U.S. and the EUROCONTROL ATM 2000+ strategy document

## Slide 19: Background - MOA Tasks
Update and enhance U.S. emissions model presented at ICAO Worldwide CNS/ATM system implementation conference, 1998.
Gather relevant information, such as planned CNS/ATM initiatives and aircraft fleet mix for Europe.
Estimate European environmental benefits using the parametric model and a full simulation approach.
Estimate global aircraft emissions using simplified approach.

## Slide 20: U.S. CNS/ATM Initiatives
Initiatives considered in 1998 study:

## Slide 21: U.S./EUROPE CNS/ATM Initiatives
Current version of U.S. architecture differs from previous study
  Implementation of some key technologies delayed until 2007.
  30/30 oceanic separations eliminated.
Europe initiatives include
  Supports free flight in general.
  Reduced vertical separations (RVSM) and Reduced horizontal spacing.
  Automated conflict detection and resolution.
  Automated controller/pilot communications.
  ATC sector organization: Additional sectors, adapt sector to airspace.

## Slide 22: Optimized Flights
FL240(2007)
FL150(10/15)
SUA
Flight
Profile
Ground
Track
RVSM (2007/10)
Cruise Climb (2015)
Descents:
2005: procedural
2010+: optimal
Baseline Trajectory
Optimized Trajectory
>1000nmi - minimum fuel to meet schedule.
<1000nmi - shortest distance around active SUA.

## Slide 23: Phases of Flight
Surface (Taxi-In)
Take Off
Approach
Cruise
Climb Out
Surface (Taxi-Out)
915m/3000ft
915m/3000ft
305m/1000ft
Direct Routing above
24,000 ft in 2007
RVSM above 29,000 ft
for 2007 and 2010
Cruise
Direct Routing above
15,000 ft for 2010 and 2015
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Model Description
Developed a parametric model using U.S. CNS/ATM Emissions Study and new information including:
  Fleet mix, traffic growth, route distances, travel times, delays, and CNS/ATM initiatives
  Airport capacities, surface weather conditions, runways, taxi-times
Developed a simulation of the European airspace.
CNS/ATM improvements may have effects in three areas:
  Increase airport capacities, thereby reducing delays at congested airports.
  Shorten cruise times due to direct routes and sector delay reductions.
  Reduce unimpeded taxi-times.
Notes: These two efforts complimented each other and provided a more robust analysis

## Slide 25: Model Description (cont.)
Variables that directly influence fuel consumption:
  Phase of flights
  Current and forecast demands
  Rate of improvement in aircraft performance and fleet mix changes
  CNS/ATM initiatives
  Aircraft/Engine characteristics
  Delays
Calibrate some of the
variables to better
represent Europe.

## Slide 26: Summary Inputs
Base Demand (1999) for all Regions
Growth Rate FESG regional, (U.S., Europe and the rest of the globe) annual growth rates.
Current (1999) unimpeded taxi times for the airports.
Ground and arrival delays for 1999, the baseline year.
Airport Capacities with both CNS/ATM and non-CNS/ATM impacts
Aircraft Performance Parameters (e.g., ICAO engine database)
Performance Statistics (e.g., High, Low,Fuel Usage, Emissions,..)
Notes: Had information for 100+ US and European airports. Used an average for the rest.

## Slide 27: Primary Assumptions
CNS/ATM planned capabilities and efficiency benefits claimed in this study will be realized.
All similar Aircraft have the same performance parameters for LTO and initial climb (e.g., Fuel burn rate)
CNS/ATM improvements may reduce the cruise times but not fuel consumption rates.
Unconstrained airports have no delays
ECAC cruise fuel burn rate (both baseline and optimal) is based on US flights of less than 500 miles
Similar to the U.S., en route delay for Europe is negligible.
FESG Based aircraft performance improvement (1%/year)
Notes: This goes back to the original FAA simulation: for altitudes above24,00 and 15,000 feet for 2010 and 2015
Flights less than 1000 nmi had their distance reduced as much as possible
Some flights more than 1000nm where optimized for fuel while still meeting the same time or shorter time en-route. If the flight could fly faster and reduce the consumed fuel further it was assumed to do so. If the flight sould not meet the desired time due to constraints, it was assumed to fly in a minimum time.

## Slide 28: Parametric Model’s Initial Results (Tons/day)
Daily savings for 2015 in Metric Tons (CONUS)

## Slide 29: Parametric Model’s Initial Results (Tons/Day)
Daily Savings for 2015 in Metric Tonnes (ECAC)

## Slide 30: Parametric Models Initial Results(Tons/Day)
Global Remainder - 2015 Baseline Range of Results (Tons/Days)
  Excludes Oceanic, CONUS and ECAC airspaces

## Slide 31: European Simulation Results (Tonnes/Day)
European Simulation (Metric Tonnes/Day)
  Baseline scenario (without CNS/ATM improvements)

## Slide 32: Potential Future Activities
Continue cross-validation process.
Refine U.S., European estimates.
  Revise Aircraft mapping
  Refine emission calculation, especially for NOx
Expand CNS/ATM initiatives in Europe, U.S. and their impacts on total fuel burn.
  Perform additional simulations to better estimate impacts of specific technology enhancements on flight efficiency.

## Slide 33: Potential Future Activities(cont.)
Gather relevant data for other regions of the globe.
Add CNS/ATM initiatives for other regions.
Enhance the parametric model.
  Use FESG forecast with greater detail.
  Add more parameters such as “load factor” or “cruise altitude.”

## Slide 34: WG 4- Future work
Information of the environmental advantages of CNS/ATM implementation
Expand the parametric model to the rest of the world
Dissemination of of the ICAO Circular on operational opportunities
  Three regional seminars for dissemination: Europe, Asia, America, involving stakeholders.
  Additional analysis about the new opportunities