## Slide 1
EUROCONTROL
European Organisation for the Safety of Air Navigation
Notes: The key objective of EUROCONTROL, the European Organisation for the Safety of Air Navigation, is to harmonise and integrate air navigation services in Europe, aiming at the creation of a uniform European Air Traffic Management System, in order to achieve the safe, orderly, expeditious and economic flow of air traffic. The Organisation is made up of thirty Member States, an Agency of permanent staff and two independent Units for Safety Regulation and Performance Review. EUROCONTROL manages a range of activities on behalf of the thirty-eight States of the European Civil Aviation Conference (ECAC). Iceland, which is an ECAC State, does not participate in the harmonisation and integration process of the European Air Traffic Management Programme (EATMP).
EUROCONTROL’s core business covers:
Operation of a Central Flow Management Unit (CFMU), covering 33 European States and 7 States outside ECAC;
Management of the European Air Traffic Management Programme (EATMP) on behalf of the ECAC States (except Iceland);
Collection of all en-route and some airport route charges on behalf of its 30 Member States and a further five States through bilateral agreements;
Research and Development aimed at increasing ATC capacity and safety in Europe;
Management of an international air traffic control centre at Maastricht;
Development of a new international air traffic control centre at Vienna ;
Provision of education, training and transfer of knowledge in air navigation services throughout ECAC and beyond.

## Slide 2: Integrating Environmental Issues into Air Traffic Management (ATM) Operations
George Paulson Director Safety, Airspace, Airports & Information Services
Colloquium on Environmental Aspects of Aviation
Montreal, Canada
9 - 11 April 2001
Notes: This presentation to ICAO’s Colloquium on Environmental Aspects of Aviation, held in Montréal on 9-11 April 2001, outlines some of the practical measures that aviation can take to minimise its impact on the environment and thereby sustain its continued growth into the 21st Century. EUROCONTROL has contributed to ICAO’s environmental initiatives in recent years, in particular its Committee on Aviation Environmental Protection (CAEP) and the ECAC Group of Experts on Abatement of Nuisances Caused by Air Transport (ANCAT). Currently, EUROCONTROL is in the process of finalising a policy and strategy on the environment in order to ensure that environmental issues are taken fully into account in air traffic management’s decision making. EUROCONTROL will work with all its stakeholders, including ICAO, to ensure that the environmental objective of the EUROCONTROL ATM 2000+ Strategy is fulfilled, that aviation’s environmental impact is kept to a minimum and that aviation’s growth can be sustained well into the 21st Century.

## Slide 4: The EUROCONTROL ATM 2000+ Strategy
Safety
Economics
Capacity
Environment
National security and defence requirements
Uniformity
Quality
Human factors
Notes: The EUROCONTROL ATM 2000+ Strategy was approved by the ECAC Ministers of Transport in January 2000, at their sixth meeting on the Air Traffic System in Europe (MATSE/6). It has a number of strategic objectives, covering safety, economy, capacity, national security and defence requirements, uniformity, quality and human factors.
The reduction of air traffic-related effects of aviation on the environment is also one of the major strategic objectives of ATM 2000+, as stated below:
“To work with ICAO and its Member States to obtain improvements in ATM, in particular the accelerated implementation of CNS/ATM concepts, procedures and systems which help to mitigate the impact of aviation on the environment.”
Furthermore, at that meeting the ECAC Ministers:
“reaffirmed [their] commitment to develop air traffic services so as to maintain safe, cost-effective and environmentally sustainable air transport, which will benefit European economic development and, in particular, airports, airlines, the travelling public and other users of Europe’s airspace.”

## Slide 5: EUROCONTROL Environmental Policy and Strategy
Working within international framework
Joint commitment of EUROCONTROL States
Environmental considerations integral to ATM decision making
Objectives
  minimum impact at and around airports
  compliance with international standards and regulations
  mitigate aviation noise and emissions
Notes: To respond to the environmental commitment of the ATM 2000+ Strategy, EUROCONTROL has submitted an Environmental Policy and Strategy to its thirty Member States. Its adoption will lead to increased co-operation on environmental issues with ICAO, ECAC, the European Commission and other relevant international and national bodies.
In this context, EUROCONTROL will assess all ATM activities to determine their environmental impact. Furthermore, it will ensure that environmental considerations are an essential part of the ATM decision-making process.
This policy and strategy are intended to fulfil the spirit of the ATM2000+ Strategy where environment issues are concerned. The overall objective is threefold:-
(i) to permit daily aircraft operations with a minimum environmental impact;
(ii) to comply with international standards and regulations and
(iii) to support actions contributing to the mitigation of aviation noise and emissions.

## Slide 6: Reducing Emissions - ATM has role to play
Additional potential fuel saving from CNS/ATM
5% ICAO-CAEP WG/4, 2000
6 - 12% IPCC, 1999
7 % EUROCONTROL study, 1997
Potential savings from CNS/ATM
Estimate for ECAC area
Notes: ATM has a role to play in reducing the amount of fuel burnt by aircraft. EUROCONTROL has been working with ICAO, in particular in support of CAEP Working Group 4 whose remit is “development of a preliminary common methodology to quantify environmental benefits arising from CNS/ATM systems”.
EUROCONTROL has estimated that, for the period 1999-2015, air traffic movements in the ECAC area are expected to increase by around 84%. However, fuel burn and Carbon Dioxide (CO2) emissions are expected to increase by only 57%. This lesser growth rate can be explained because of the introduction of more efficient engine technology, the retirement of older less fuel-efficient aircraft, and the introduction of modern aircraft as the airline fleets expand.
The graph highlights the growing divergence in the traffic growth and fuel burn trends over time. It is expected that the increase in fuel burn can be further contained through the introduction of appropriate CNS/ATM measures, some of which are described in more detail in the following slides. Various estimates would suggest that CNS/ATM will further reduce the increase in fuel burn by approximately 6%.

## Slide 7: EUROCONTROL Environmental Assessment Tools
Advanced Emission Model (AEM)
European Harmonised Aircraft Noise Contour Modelling Environment (ENHANCE)
Simulation tools
Air traffic movement database
  38 ECAC States
  updated daily
Aircraft Performance Models
Notes: In order to assess a number of environmental factors EUROCONTROL
has developed several assessment tools.
The European Harmonised Aircraft Noise Contour Modelling Environment (ENHANCE) allows the four-dimensional trajectories of individual aircraft to be taken into account in the calculation of noise contours. The graphic shows the results of one such study at Toulouse airport, in south-west France.
Other models include the Advance Emission model (AEM) and two aircraft performance models
    BADA (base de données d’ávions; based on a thrust/drag model); and
    GAME (General Aircraft Model Environment), covering all phases of flight, e.g. rate of descent/climb, rate of acceleration/deceleration.
EUROCONTROL also has at its disposal simulation tools, such as SAAM and a comprehensive database on air traffic movements. This database is probably unique in that air traffic information throughout all ECAC States is updated on a daily basis.

## Slide 8: ATM - Delivering Environmental Benefits
Air Traffic Flow Management (ATFM)
European Route Network Developments
Flexible Use of Airspace (FUA)
Reduced Vertical Separation Minimum (RVSM)
Area Navigation (RNAV)
Continuous Descent Approaches (CDA)
Notes: This slide sets out a number of ways in which Air Traffic Management will deliver environmental benefits. These are described in more detail in the following slides.
    Air Traffic Flow Management
    Flexible Use of Airspace (FUA)
    European Route Network Developments
    Reduced Vertical Separation Minimum (RVSM)
    Area Navigation (RNAV)
    Continuous Descent Approaches (CDA)

## Slide 9: Air Traffic Flow Management (ATFM)
Balance demand with capacity
Protect ATC systems from overload
Re-routings
  avoid congested areas
Aircraft held at airports
  engines shut down
  avoid en-route and approach holding
  avoid taxi queuing
Notes: Air Traffic Flow Management (ATFM) plays a vital role in mitigating the impact of air traffic on the European environment. It is organised through EUROCONTROL’s Central Flow Management Unit (CFMU) that was set up to provide a flow management facility on behalf of all ECAC Member States, with whom the CFMU works very closely. Its primary task is to protect ATC, in particular the controller, from overload, thereby ensuring that safety is maintained. To do this, it balances demand with available capacity. When demand exceeds declared capacity levels there are two options that are available.
Firstly, the CFMU will offer airspace users alternative routings avoiding congested areas. If this cannot be achieved, then the CFMU system will ensure that the relevant aircraft will be held at airports with their engines shut down, waiting for their assigned air traffic flow management (ATFM) slots. These procedures avoid aircraft holdings either en-route, on approach or during taxi-ing on the airport and, although primarily safety measures, they do reduce the amount of fuel that is burnt by aircraft.
However, it is acknowledged that certain airports are obliged to maintain a reserve of holding aircraft in order to optimise runway capacity.

## Slide 10: ATS Route Network Developments
SPR
PAS
FRI
KINES
SRN
GEN
TOP
WIL
MOU
LSA
TDP
LARVI
ZUE
TRA
TGO
KRH
DIJ
RLP
EPL
HR
CTL
TGO
KPT
ZUE
KRH
RUWER
DIK
CTL
BRY
RLP
DIJ
MOU
ATN
LSA
HOC
TOVEL
LARVI
TOP
NIZ
DGN
MTG
SRN
SAPRI
PAMOU
LUL
WIL
KINES
TRA
Notes: This slide illustrates the re-organisation of air traffic routes to ease congestion in the important area around Geneva. Several East-West and North-South traffic streams converge on this area making it an extremely complex environment from the air traffic control perspective. EUROCONTROL, in conjunction with the relevant Member States, proposed a re-organisation of the airspace that led to the introduction of additional sectors and the separation of opposite-direction traffic flows. This has greatly improved the airspace capacity in question and it is estimated that the capacity gain is in the order of 30%. Although this may not appear at first sight to be of any environmental significance, there are a number of spin-off benefits such as more direct routes, optimum, or better, flight profiles and reduced flight times. Together, these reduce average fuel burn. In addition, the tools that EUROCONTROL has at its disposal to analyse such problems would be of benefit in assessing certain aspects of environmental impact.
.

## Slide 11: ATS Route Network Developments
European ATS Route Network developments
  shorten average route lengths
  increase capacity
Example - Sweden
  new route network 1998
  net flight distance annual reduction of 3,2 million NM
  annual flight time saving of 565,000 hours
Notes: EUROCONTROL, working closely with its stakeholders, has implemented a number of improvements to the air traffic services route network throughout ECAC. These have progressively reduced the complexity of the route structure and provided for more direct routings. Some improvements have been ECAC-wide, as will happen for RVSM in 2002, whereas others have been on a regional basis, such as for the Geneva area.
These changes share the common goals of shortening average route lengths and increasing airspace capacity. This leads to direct economic benefits to the airlines that are also indirectly beneficial to the environment.
For example, a new route network was introduced in Swedish airspace in 1998 and a cost-benefit analysis indicated that the implementation led to a reduction of 3.2 million nautical miles in the net flight distance flown and a saving in flight times of 565,000 hours. Clearly, this has an impact on the fuel burnt by aircraft and the subsequent emissions. (reference: cost-benefit airspace ES98).

## Slide 12: Flexible Use of Airspace (FUA)
Airspace available to all user groups
Security and Military needs satisfied
Shorter routings
More optimum flight profiles
Less fuel burn
Notes: The Flexible Use of Airspace (FUA) concept considers airspace as a continuum that is allocated according to user requirements. It is an excellent example of effective civil/military co-operation. FUA is one of the major programmes facilitating a progressive move towards a pan-European airspace no longer constrained by national boundaries or exclusive use by a particular user group. This concept was developed by EUROCONTROL as one means of coping with the rapid growth in air transport from the late 1980s onwards, easing the pressure on civil air traffic route structures that were then near capacity. Its adoption led to airspace hitherto reserved for military use being made available for joint military and civil needs.
The FUA Concept was formally endorsed by the ECAC Transport Ministers on 10th June 1994, at their fourth meeting on air traffic matters (MATSE/4). Any necessary airspace segregation is temporary, based on real-time needs in a specific time period. This means that artificial barriers to the free passage of civil aircraft have been removed. Although military requirements for designated airspace can be met, volumes of airspace are not blocked to other potential users when they are not required for military activity. Whilst the application of this concept within the ECAC States has already led to a significant increase in airspace availability for commercial activity, its application does vary depending on national requirements.
FUA affords more direct routings, more optimum flight profiles and reduced flight times, thereby saving fuel and reducing total emissions.

## Slide 13
Pre RVSM
RVSM
FL 430
FL 410
FL 390
FL 370
FL 350
FL 330
FL 310
FL 300
FL 290
FL 280
FL 430
FL 410
FL 400
FL 390
FL 380
FL 370
FL 360
FL 350
FL 340
FL 330
FL 320
FL 310
FL 300
FL 290
FL 280
1000 ft
2000 ft
1000 ft
1000 ft
2000 ft
24 Jan 02
Notes: The next two slides deal with Reduced Vertical Separation Minimum (RVSM), the EUROCONTROL-led programme to provide an additional six flight levels in ECAC airspace. This will be achieved between flight levels FL290 and FL410 (29,000 and 41,000 feet respectively), where the intermediate flight levels (FL 310, FL330, FL350, FL370, FL390) are currently separated by 2,000 feet.
This separation will be reduced to 1,000 feet on 24th January 2002 thus adding a further six flight levels (FL300, FL320, FL340, FL360, FL380, FL400).
These new flight levels are represented by the orange lines on the chart. The principle of aircraft flowing in opposite flight directions at successive flight levels has been maintained. However, the introduction of a further six levels has led to a switch in the traffic direction on some flight levels.
In summary, therefore, RVSM will be a major re-organisation of European airspace. Not only does it involve the forty participating RVSM States; its successful implementation relies upon close co-operation with the ICAO Atlantic and North European Office, the Russian Federation and a number of States on the periphery of ECAC in Africa and the Middle East.

## Slide 14: Reduced Vertical Separation Minimum (RVSM) on 24 January 2002
6 additional flight levels
Increase in airspace capacity
More optimum flight profiles
  reduction in fuel carriage and fuel burn
Principal benefits
  reduced delays
   200,000 tonnes fuel saved annually
Notes: The aim of introducing a further six flight levels as a result of RVSM is to increase capacity in the upper airspace. It is predicted that this will reduce delays, provide more optimum flight profiles and reduce both fuel carriage and fuel burn.
A cost-benefit analysis indicated that, of the total benefits produced by RVSM, 93% would be through reducing delays, whereas the remaining 7% of benefits would come from improved fuel efficiency.
RVSM is, therefore, an example of an ECAC-wide programme whose environmental benefits will be delivered throughout the area of interest.

## Slide 15: Area Navigation (RNAV) Procedures
Improved flight management
  more consistent track-keeping
    concentration of tracks
  shorter direct routes
    increased fuel efficiency
  highly flexible
    avoid noise sensitive areas
Key to continuous descent approaches
  consistent
  repeatable
Notes: Area Navigation (RNAV) allows aircraft to fly through navigating with respect to waypoints rather than to and from them on a fixed route network. It therefore offers ATC the potential to adopt a more flexible approach to the management of traffic flows. The introduction of RNAV will improve flight management mainly through more consistent track-keeping and providing aircraft with the capability to fly shorter, more direct routes. Through RNAV, aircraft will be able to fly the same track repeatedly, whether it be a Standard Instrument Departure (SID), en-route, or during a Standard Arrival Route (STAR). In particular, this repeatability will allow ATC planners to confine arrivals to and departures from airports along strict trajectories, minimising the effect of noise in particular.
En-route, RNAV offers the possibility of spreading traffic flows over wider areas, rather than concentrating them in areas where there may be bottlenecks. From the environmental perspective, this should reduce the concentration of aircraft emissions in particular areas.
Area Navigation is also a key element of Continuous Descent Approaches, which will become an important operational measure to reduce the impact of noise around airports.

## Slide 16: Use of Conventional STARs
RNAV
procedures
RNAV
Conventional
Source: Courtesy DFS
Notes: This slide shows the result of introducing RNAV procedures at Frankfurt Airport in Germany, and has been provided courtesy of Deutsche Flugsicherung (DFS). It shows how RNAV can be used to ensure that aircraft maintain track-keeping when following a particular approach procedure. The upper-left and lower-right graphs clearly show the difference between traditional and RNAV approaches, in particular the repeatability that comes through RNAV, leading to the concentration of flight paths over a very limited area.
This concentration of flight paths will limit the area affected by aircraft noise, thereby reducing the total number of people whose lives may be affected. Nevertheless it is clear that, in order to reduce the impact of noise even further, additional measures may have to be taken, such as providing improved noise insulation in the worst affected areas. It should also be noted that the combination of RNAV operations with improvements to engine and airframe technology together can limit the vulnerability of civil aviation to any actions seeking compensation for the nuisance caused.

## Slide 17: RNAV trial Nice Airport
RNAV - avoiding noise sensitive areas
Trial RNAV procedure
Co-operation between
  DGAC France
  EUROCONTROL
  European Space Agency
GNSS technology
Notes: This slide illustrates how CNS/ATM technology can be harnessed to reduce aviation’s environmental impact. In 2000, EUROCONTROL, the French Direction Générale de l’Aviation Civile (DGCA) and the European Space Agency (ESA) completed a series of flight simulator tests for a new approach procedure into Nice-Côte d’Azur airport. A full-motion A340-type aircraft simulator was used to assess the procedure that was designed to avoid noise-sensitive areas on the coast, under one of the approach paths. The Mediterranean Sea to the South of Nice airport clearly prevents the installation of any conventional ground-based navigation facilities; this degrades the geometry of the traditional navigation solution and limits the potential for designing procedures around sensitive areas.
Global Navigation Satellite Systems (GNSS) provide consistent performance world-wide, irrespective of whether an aircraft is navigating over land or sea. It is therefore ideal for delivering position information for manoeuvres that require increased accuracy, better integrity and greater availability from the navigation system. In this case, ESA provided information from the European Satellite Test-Bed (ESTB – which has been operational since early 2000) that emulates the performance of the European Geostationary Navigation Overlay Service.
EGNOS is Europe’s contribution to the world-wide implementation of Satellite-based Augmentation Systems (SBAS), for which ICAO Standards and Recommended Practices (SARPs) will be applicable from late 2001. The SBAS-type position information was provided to the simulator so that the trial procedure could be successfully flown. As well as highlighting the potential of GNSS to provide the basis for RNAV in and around airports, the study highlighted a number of issues that also had to be taken into account, such as human factors and pilot and controller training. Nevertheless, this work illustrates what can be achieved. If current planning is successful, the study should move to the flight trials stage by the end of 2001.
.

## Slide 18: Continuous Descent Approaches (CDA)
Concept description
  lower power settings
  from higher altitude
  no level-off segment
CDA
Conventional approach
Notes: The next four slides illustrate the concept of Continuous Descent Approach. A CDA is a flight operation whereby an aircraft descends using a more-or-less continuous engine power setting, maintaining that setting from an altitude that is higher than when that setting would usually be attained. Traditionally, variations in engine thrust have been a feature of flight descents, most of which are characterised by segments where the aircraft has to level-off (maintain the same altitude). This is not particularly fuel efficient and maintains a relatively large noise footprint.
A CDA substantially reduces both the noise footprint on the ground and the amount of fuel burnt during the last 40-50km of an approach. It is estimated that the fuel saving is in the order of 30%.
CDA’s are operational at some airports, for example Amsterdam Schiphol. These have confirmed the reduction in noise and fuel burn, but highlighted some operational limitations that actually led to a reduction in capacity. It is thought that capacity can be increased to pre-CDA levels through the introduction of controller tools (such as arrivals managers). A EUROCONTROL project, ARETA (Future ATM with RNAV in Extended Terminal Area Operations), is aiming at optimising safety, capacity, cost and environmental objectives, and covers CDA’s.

## Slide 19: B747 Approach Radar Vector to ILS
-5
0
5
10
15
20
25
30
35
40
45
50
55
60
Track distance [km]
0
1000
2000
3000
4000
5000
6000
7000
8000
Altitude [ft]
Study performed by NLR (Sourdine project)
Altitude profile
Thrust profile
Corrected net Thrust
[lbs,all engines]
-2000
0
2000
4000
6000
8000
Notes: This slide illustrates the altitude profile and consequent engine thrust settings of a conventional approach, in this case for a Boeing B747 with radar vector to an ILS. The results come from a study performed by the Dutch Aerospace Research institute (NLR) in the Sourdine project.
The typical segmented altitude profile can be seen, as can the substantial variation in thrust settings. The graph should be read from right to left. The variation in thrust generates high fuel burn and noise.

## Slide 20: B747 Approach CDAs with RNAV procedures
-5
0
5
10
15
20
25
30
35
40
45
50
55
60
Track distance [km]
0
1000
2000
3000
4000
5000
6000
7000
8000
Altitude [ft]
Study performed by NLR (Sourdine project)
Altitude profile
Thrust profile
Corrected net Thrust
[lbs,all engines]
-2000
0
2000
4000
6000
8000
~ 30% fuel saving
Reduced noise impact
Notes: This slide should again be read from right to left. In this case, the Boeing B747 carries out the approach using a mix of CDA and RNAV procedures. The altitude profile is smooth, showing a continuous descent with no level-off segments. Engine thrust is maintained near to flight idle throughout the approach, and only increased immediately prior to and during the landing itself. It is estimated that the fuel saved is approximately 30% compared to a typical approach.

## Slide 21: Noise Reduction Benefits using RNAV CDAs
-10
-5
0
5
10
Y (km)
X (km)
45
40
35
30
25
20
15
10
5
0
65.0 dB(A): Decrease of 25 km²
75.0 dB(A): Decrease of 0.3 km²
55.0 dB(A): Decrease of 24 km²
Notes: This final slide on the issue of CDA’s illustrates the reduction in noise to be gained from RNAV CDA’s. The graph contains three important areas within the 55, 65 and 75 decibel (dB) noise contours. Compared to a traditional approach, an RNAV CDA can deliver a reduction in the noise-affected areas of approximately 24, 25 and 0.3 km² respectively.
(The calculations of the NLR study (Sourdine project) showed decreases in the area of the noise contours as follows:
55 dB(A): 23.96 km²;
65 dB(A): 25.01 km²;
75 dB(A): 0.297 km².)

## Slide 22: Summary
Environmental Policy and Strategy in place
Working to establish ATM environmental objectives
Integrating environmental considerations into ATM implementation programmes and operations
Delivering operational ATM environmental benefits
ATM contributing to sustainable aviation growth
Notes: This presentation has illustrated some of the practical measures that can be taken operationally to reduce aviation’s impact on the environment. This is particularly appropriate given that environmental concern about climate change, gaseous emissions and noise is becoming an increasingly important political, economic and social issue for aviation. As aviation activity in Europe increases, the pressure on aircraft operators, airports and ATM to increase capacity will intensify the debate on the environmental impact of aviation. In particular, it must be determined whether it is possible to achieve an environmentally sustainable air traffic system throughout ECAC and simultaneously meet demand.
ECAC Member States have concentrated their efforts in tackling environmental problems at and around airports through either regulatory methods or policy frameworks for operational measures. The European Union is itself proposing strong action to address environmental concerns and problems faced by European civil aviation. The airlines’ fleet renewals take into account the need for quieter aircraft that also have lower emission levels. States, aircraft operators and airports have exerted pressure on the aircraft manufacturing industry to ensure that future aircraft will be as environmentally friendly as possible.
EUROCONTROL is now in the process of putting its environmental policy and strategy in place. It has already contributed significantly to ICAO efforts through its support for the CAEP as well as ECAC-ANCAT. The approval of the policy and strategy confirms EUROCONTROL’s joint commitment with its stakeholders to ensuring that environmental concerns are built into the ATM decision making process.