## Slide 1: IPCC / Special Report on Aviation & Global Atmosphere 10 Apr 01 Joyce Penner Professor of Atmospheric, Oceanic and Space Sciences University of Michigan
Summary of recent assessment of climate change (IPCC Third Assessment Report)
How do aircraft affect climate and ozone?

## Slide 4
Special Report on Aviation and the Global Atmosphere
Produced following a request from the International Civil Aviation Authority
Produced following a request from the International Civil Aviation Authority

## Slide 5
Overall effects considered in the IPCC report:
Stratosphere
Tropopause
Troposphere
Emissions:
CO2, H2O, NOx, SOx
Sulfur, soot particles
Effects:
Ozone depletion
Surface UV-B
Radiation
Ozone production
CH4 decrease
Contrail formation
Cloud formation?
Climate
Change

## Slide 6: Subsonic aircraft fly near the tropopause -- where emissions may have a disproportionate impact compared to the same gases emitted at the surface

## Slide 7
Topics considered in IPCC Report
What are the overall and individual effects of aircraft emissions: CO2, H2O, NOx, soot, sulfur?
Will future growth in aviation increase its effect on climate and ozone?
Can technology or changes in operations help reduce the impact?

## Slide 8: Emissions of CO2, H2O, NOx, soot, and sulfur were estimated for current and future fleets

## Slide 9: CO2 is the primary greenhouse gas and aircraft CO2 emissions are an increasing proportion of total emissions

## Slide 10: NOx emissions produce ozone, a greenhouse gas, but the predicted increase differs between models:

## Slide 11: Nevertheless, there is a substantial increase in O3 as emissions of NOx increase

## Slide 12: Changes in the concentration of O3 cause increases in OH which decrease methane, a greenhouse gas:

## Slide 13: Water vapor emissions cause contrails when emitted into a region that is nearly saturated.

## Slide 14: Contrail occurrence is correlated with aviation fuel use:

## Slide 15: This correlation has been used to estimate contrail cover based on modeled temperature and humidity in the upper troposphere:

## Slide 16
Cirrus cloudiness seems to increase near areas where contrails form:

## Slide 17
Cirrus cloudiness increases as aviation fuel consumption increases:

## Slide 18: We use radiative forcing to guage the effects of aviation on climate change
Radiative forcing expresses the perturbation or change to the energy balance of the Earth-atmosphere system in watts per square meter (Wm-2).
Positive values of radiative forcing imply a net warming, while negative values imply cooling.

## Slide 19: Radiative Forcing from Aircraft in 1992:

## Slide 20
Q: Aviation NOx increases O3 and reduces CH4, do these RF cancel?
The radiative imbalance from
O3 & contrails is primarily in
the NH; that from CO2 & CH4,
global.
The global mean RF, O3+CH4, may cancel in terms of global mean surface temperature, but the latitudinal imbalance may cause regional climate change.

## Slide 21: Q: How much will Aviation’s use of fossil fuel grow?
Civil Aviation has grown rapidly to date, in 1990s reaching about 2.5% of all fossil fuel.
By 2050, projections give Aviation an equal or greater share of a growing economy.
No substitute for jet fuel (fossil C) is obvious.

## Slide 22: Q: How much is Aviation increasing CO2? Q: How big is this compared to other sectors or countries?
CO2 is projected to increase from fossil fuels & deforestation by +150 ppm from 1990 to 2050.
Aviation’s part of this increase is about +6 ppm (range: 4-12).
All of the Transportation sector would be about +50 ppm.
California, ~10% of U.S., is comparable to Aviation.

## Slide 23: Q: How much global warming could be due to Aviation?
The effect of Aviation on global warming (+0.05oC from 1990 to 2050)
is superimposed on the overall anthropogenic greenhouse warming
(+1oC) plus natural variability.
It has not been (nor is likely) possible
to attribute specific climate change
to aircraft, although Aviation is a
significant component.

## Slide 24
Q: What are the mechanisms that cause radiative forcing in 2050?
The major RF components shift (e.g., CO2 becomes more important than O3), but still remain the major contributors to climate change.

## Slide 25
Total radiative forcing in 2050
CO2 +.074 W/m2
O3 +.060
CH4 –.045
contrails +.100
strat H2O +.004
sulfur –.009
soot +.009
Compare with overall RF:
Greenhouse gases +5.8
Aerosols –1.9

## Slide 26: IPCC Special Report on Aviation & Global Atmosphere
Aviation’s share of ‘greenhouse gas warming’ will remain a significant fraction of the world total, when compared to other sub-sectors and to many nations.
Confidence intervals in some of the “atmospheric effects” are not adequate to quantify climate costs
Yet significant - Kyoto scale - reductions in Aviation’s climate impacts, could be achieved with any of several technologies:
  Further improve fuel efficiency per passenger–km
  Adopt low-NOx engines
  Avoid meteorological conditions favoring contrails