## Slide 1: CAEP Working Group 3 Emissions Technical Issues
Robert J. Shuter
Rapporteur WG 3

## Slide 2: WG 3 Responsibilities
develop standards for aircraft engine emissions
review the methodology for these standards
review measurement procedures
recommend changes to Annex 16,Volume II to the Convention on International Aviation, Aircraft Engine Emissions

## Slide 3: New Standards
Three ICAO principles for new standards are:
Environmental need
Technically achievable
Cost effective

## Slide 4: Environmental Problems
Ground level pollution
Global climate change (Kyoto Protocol)
Growth of aviation

## Slide 5: Determining the Environmental Need
Research Focal Points
Focal Point on Liaison
Airport Air Quality Studies
IPCC Report
Kyoto Accord

## Slide 6: Aviation Technology
Manufacturer’s briefings
20% improvement in aircraft efficiency between 1997 and 2015
NOx reductions 30-50% below CAEP/2 limits by 2020
Emissions reductions from advanced engine technology are not sufficient to counteract the projected growth of aviation

## Slide 7: Long Term Emissions Technology Goals
a task group has initiated work towards longer term framework of technology goals to reduce emissions
questioning the relationship between ICAO standards and technology development
believe that the development of emissions forecasting tools for aviation is ICAO’s responsibility

## Slide 8: Regulated Emissions
Smoke
Gaseous emissions:
  Unburned hydrocarbons (HC)
  Carbon monoxide (CO)
  Oxides of nitrogen (NOx)

## Slide 9: Carbon Dioxide (CO2)Standard
WG3 was asked to consider a CO2 standard
CO2 emissions are directly related to fuel burn
Fuel efficiency is already high as a result of market economic pressures
Point certification for CO2 could drive manufacturers to meet compliance for this point at the expense of the overall missions efficiency

## Slide 10: The LTO Cycle
The landing, take-off cycle includes four phases of flight:
mode time thrust
  take-off 0.7 minutes 100%
  climb 2.2 minutes 85%
  approach 4.0 minutes 30%
  taxi/ground idle 26.0 minutes 7%

## Slide 11: Alternative Emissions Methodology
address requirements for calculating emissions for cruise and climb phases of flight
use performance based procedures
need to define “worst case” certification points
develop method to estimate actual emissions

## Slide 12: Noise Stringency
WG3 was asked to examine the impact of noise stringency on emissions from aircraft
Generally more modern aircraft are more efficient (High bypass ratio)
Aggressive noise reduction could lead to increased emissions

## Slide 13: Conclusions Presented to CAEP
Need to review the validity of the existing LTO emissions certification regime
Good progress has been made on alternate emissions methodology and long term goals
No CO2 standard
No changes to Annex 16

## Slide 14: WG3 Future Work Program
Review current LTO cycle
Complete AEM task
Develop long term technology goals
Asses technology advances
Monitor atmospheric research
Investigate new NOx standard
Propose production cut-off for CAEP/4 std