## Slide 1
  RUNWAY INCURSION PREVENTION MEASURES
  AT PARIS-CHARLES DE GAULLE AIRPORT
  -------------------------
  ICAO NAM/CAR/SAM Runway Safety / Runway Incursion Conference
  (Mexico City, 22 to 25 October 2002)
  ------------------------------------------
  Mr Gerard BATISTELLA, studies and development Air Traffic Operations
  Mr Jean JEZEQUEL, Air Traffic Manager for Towers and TRACON, Charles de Gaulle Airport

## Slide 2: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT
OUTLINE OF THIS PRESENTATION
CDG Airport Traffic (2001 data)
CDG Airport Layout (Runways/taxi-ways/terminals – Air Traffic Control Towers)
CDG Airport Basic Operations
Runway Incursion Prevention Measures before opening south pair of RWYS (before 1999)
Additional Runway Incursion Prevention Measures, since 2000
Runway Incursions statistics
Further Runway Incursion Prevention Measures for 2003/2004…

## Slide 3: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT
AIRPORT TRAFFIC CONDITIONS (2001 data)
525,000 ops/year 2001
WORLD RANK for ops : 6 th
PEAKS
  peak day : 1,689 ops
  Peak hour : 125 ops (3 RWYS)
MAJOR HUB FOR AIR-FRANCE
over 150 foreign airlines operating at CDG
WEATHER CONDITIONS
  Low visibility Procedures :  5 % of time
  A few snowy days

## Slide 4: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT
AIRPORT LAYOUT
3200 Ha
4 PARALLEL RUNWAYS
  South pair of runways in use since March 1999
  A mixed-mode runway on the north side of the airport (north pair of RWYS will go into operating spring 2003)
TAXIWAYS ≈ 70Kms in all
2 AIR TRAFFIC CONTROL TOWERS
  South ATCT close to south pair of RWYS (including an apron tower)
  Central ATCT
  New north ATCT (2004) close to north pair of RWYS (including an apron tower)

## Slide 5: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 6: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 7: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 8: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 9: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 10: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
NEW FACILITIES
SOUTH AIR TRAFFIC CONTROL TOWER (cost : 15 millions Euros)
  good visibility on arrivals, holdings and crossings (in westerly and easterly flows)
  good visibility on departures sequences (in westerly and easterly flows)
APRON TOWER LOCATED IN SOUTH TOWER (able to manage traffic around all CDG2 terminals)
  to alleviate traffic load of ground control positions
AIR TRAFFIC CONTROL TOWER SIMULATOR ( cost : 4 millions Euros)
  To provide training of all controllers working the south pair of RWYS from south ATCT before opening
Note : This simulator is now adapted for north pair of RWYS, central and north ATCTs.

## Slide 11: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 12: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 13: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
NEW EQUIPMENT
2ND ASDE LOCATED ON SOUTH ATCT :
  better ground radar coverage of south side of airport
LABELS (data blocks) ON GROUND AND LOCAL CONTROL POSITIONS
  easier management of traffic
  better discrimination for LOCAL and GROUND controllers, of the different positions of airplanes (more specially inbounds holding between the two RWYS…)
VEHICLES RADIO LOCATION MONITORING SYSTEM
  to prevent drivers of incursions on RWYS

## Slide 14: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
TAXIWAY DESIGN
SPACE PROVIDED to decelerate AFTER VACATING RWY, hold BEFORE CROSSING, CROSS AND TAXI QUICKLY away from departure RWY
384m between rwy center lines, 4 exits (West and East rwy configurations)
CENTRAL PARALLEL TWY between rwys to collect several arrivals, hold and prepare sequences
4 TWYs PERPENDICULAR (West and East rwy configurations) to departure RWY for HOLDING AND CROSSING :
  good surveillance of departing traffic (West and East configurations)
  rapid and non confusing crossing of inner RWY
Lighting system strictly ICAO ANNEX 14 compliant

## Slide 15: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 16: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
PROCEDURES
ARRIVALS ON OUTER RWY/DEPARTURES ON INNER RWY
  Ground crossings
  ILS and Approach lighting on inner RWY to be OFF (to prevent landings on the inner RWY)
FOCUS ON READ BACK procedures (clearances and documentations) specially for ARRIVALS (ie: “HOLD SHORT OF RUNWAY 26R on taxiway SIERRA TWO” )
ONE LOCAL FREQUENCY FOR ARRIVALS AND DEPARTURES
  arrivals change to Ground Control frequency only after the crossing of departure RWY permitting to the LOCAL controller to call them if necessary. Pilots can monitor the sequence.
ALL VEHICLES
  All vehicles having to operate on RWYS are equipped with Local Control frequencies and drivers are in contact with Local Control position
AIRPORT DIAGRAMS
  in Westerly and Easterly flows, arrivals can see how to taxi immediately after departure RWY crossing if no immediate contact with ground control

## Slide 17: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
CONTROL POSITIONS
TWO GROUND CONTROL POSITIONS working on south side of airport
  One working mostly arrivals (GSW in West flow, GSE in East flow), available to speak immediately to the arrivals after the crossing, and to give taxi-clearances
   arrivals exit quickly the departure RWY area
  One working mostly departures (GSE in West flow, GSW in East flow) to prepare the departure sequence
TWO APRON TOWER POSITIONS (with a possible extension to three) to alleviate Ground Control traffic load on south side of airport

## Slide 18: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 19: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (BEFORE OPENING SOUTH PAIR OF RUNWAYS)
PRE-OPERATIONAL MEASURES
AIRPORT SIMULATOR « SIMULOC » in operation two months before opening the pair of RWYS, to train all the controllers
MEETINGS with airlines to explain the new procedures
VERY LARGE DISTRIBUTION OF A VIDEO demonstrating the new procedures of the south pair of RWYS, highlighting specificities, namely holding before crossing and crossing of departure RWY
ORGANIZATION OF TWO MEETINGS to allow pilots / controllers to acquire and mutually understand new procedures
PUBLICATION IN CONJUNCTION WITH IATA, of a leaflet named HIRO and subsequent large distribution
CAUTION MESSAGE on the ATIS, during the first month of operations (March 1999), for the arrivals vacating the outer RWY of the pair of RWYS ("After vacating RWY 26L hold short of runway 26R")

## Slide 20: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (AFTER OPENING SOUTH PAIR OF RUNWAYS)
FIRST DEBRIEFING AND CORRECTIONS (1999)
TASK FORCE TO MONITOR OPERATIONS AND ANALYZE INCIDENTS (one meeting per month)
MODIFICATIONS of procedures and documentation:
  GROUND CONTROL TAXI PROCEDURES : to give PRIORITY to arriving traffic over taxiing traffic on parallel TWY (to expedite crossing of inner RWY and avoid a holding of second arrival for a ground clearance close to (or on) the departure RWY).
  AIRPORT DOCUMENTATION DIAGRAMS : to integrate taxiing PRIORITIES
ADDITIONAL GROUND MARKING ON THE HOLDING POINTS to REINFORCE their meaning (STOP)
SIMULTANEOUS CAMPAIGN WITH AIR FRANCE for heightening pilot and controller awareness OF PHRASEOLOGY AND READ BACK SENSITIVITY

## Slide 21: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 22: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT ( SINCE 2000 )
INFORMATION AND DOCUMENTATION
PERMANENT (since 11/28/00) CAUTION MESSAGE on the ATIS, for inbounds vacating the OUTER RWY
MEETING WITH AIRLINES (12/15/00) for discussion and awareness
PUBLICATION (Feb 2001) OF AN AIC pertaining to this problem with special distribution to airlines operating on airport
UPDATING (2001) OF HIRO LEAFLET with special focus on this problem, promotion and large distribution
MEETING WITH AIRLINES (1/18/02)
REINFORCEMENT OF THE JEPPESEN caution box

## Slide 23: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (SINCE 2000)
ENHANCED CAT 1 HOLDING POINT AND OTHER ACTIONS
IMPLEMENTATION OF TWIN WIG-WAG: 4 orange flashing lights on each side of 90m holding points, differentiating those at 150m (single Wig-Wag).
REINFORCING HOLDING POINT : painting of ground with "RWY AHEAD" ground inscription
DUPLICATION OF HOLDING POINT SIGNS (90m) : on either side of the taxiway & erection of additional CAT1 sign.
H24 WIG – WAG at 90m holding point commuted with 150m WIG – WAG in LVP ops
REINFORCING SIGNS, MARKINGS AND RED LIGHTS on TWY with only one way : “NO ENTRY / RWY AHEAD ” painting of ground and specific signs for drivers, located at 90m from the runway centerline.

## Slide 24: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 25: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 26: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 27: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT ( SINCE 2000 )
NEW EQUIPMENT
3rd and 4th GROUND RADARS (ASDEs)
  3rd ASDE, located South/East of airport, in service since early 2001
  4th ASDE, located North/West of airport, in service since spring 2002
MODE "S" multi-lateration (installation finished October 2002, on test end of 2002)
GROUND SHORT TERM CONFLICT ALERT SYSTEM (on test autumn 2002)

## Slide 28: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT

## Slide 29: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT ( SINCE 2000 )
PROCEDURES / HUMAN ERROR PREVENTION
NEW PHRASEOLOGY (January 2001) for arrivals holding short of the inner runway of the pair, "DUPLICATING HOLDING INSTRUCTION"
  "…, Hold short of runway 26R, holding point SIERRA TWO"
  (instead of "…, Hold short of runway 26R, on taxi way SIERRA TWO)
SPECIFICALLY FAMILIARIZE PILOTS with CDG airport complex layout and read back procedures
  Distribution of a specific CD-Rom
IMPLEMENTATION of a Safety Management System (early July 2002)

## Slide 30: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT ( SINCE 2000 )
« In case of any doubt HOLD SHORT OF the inner RWY »
The basic principle is the arrival traffic must HOLD SHORT OF the inner RWY and wait for a crossing clearance and acknowledge it.
Arrival traffic on outer RWY must stop and wait on holding points.
DEPARTURES
ARRIVALS

## Slide 31: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT (STATISTICS 2000 & 2001)
Traffic 2000: 518,000
Incursions: 13 (0 in LVP conditions )
Traffic 2001: 525,000
Incursions: 3 (0 in LVP conditions)
Note: for 2001 and 2002 (up to august) 0 arrival crossing incursion, compare to 7 incursions in 2000.

## Slide 32: RUNWAY INCURSION PREVENTION MEASURES AT PARIS-CHARLES DE GAULLE AIRPORT ( FOR 2003 – 2004)
MODE S MULTI-LATERATION to be integrated in ground radar displays (early 2003)
GROUND SHORT TERM CONFLICT ALERT SYSTEM to be integrated in ground radar displays (Runway Incursion Monitoring and Conflict Alert System) (early 2003)
  A-SMGCS = 4 ASDEs, mode S multi-lateration, GSTCAS, alternated WIG-WAG
  90m /150m, stop bars 150m …
LARGE DISTRIBUTION OF A NEW VIDEO demonstrating procedures for north pair of RWYS (first quarter of 2003)
TRAINING ON TOWER SIMULATOR of the controllers for the north pair of rwys procedures (first quarter of 2003)
NEW NORTH AIR TRAFFIC CONTROL TOWER close to north pair of rwys (spring 2004)
PROVISION OF ASSISTANT LOCAL CONTROLLERS to help monitoring operations (scanning the runways)