## Slide 1: Runway Incursions in the CAR/SAM Regions and Prevention Measures at Aerodromes
ICAO NAM/CAR/SAM Runway Safety/Incursion Conference
22 – 25 October 2002
Michiel Vreedenburgh
Regional Officer, Aerodromes
International Civil Aviation Organization
North American, Central American and Caribbean Office

## Slide 2: Outline
Regional activities and developments on runway incursions
Regional runway incursion types, causes and contributory factors
Runway incursion prevention measures at aerodromes

## Slide 3: Introduction
Recent runway Incursions in the CAR/SAM Regions
  (CAR/SAM = Latin America & the Caribbean)
    Accidents – None
    Incidents – Many
Concern with runway incursions highlighted at regional air navigation meetings of States

## Slide 4: Air Navigation System Components Involved
Aerodrome Operators – Management & Personnel
Aircraft Operators – Airlines and Flight Crew
Air Traffic Services Providers – Air Traffic Controllers
All regulated by State Civil Aviation Authorities

## Slide 5: CAR/SAM Regions Air Navigation Planning and Implementation Mechanism
GREPECAS – ICAO, States & International Organisations – Providers & Users
AGA/AOP/SG – forum with participation of all Stakeholders
  CAAs – ICAO
  Airports – ACI
  Airlines – IATA
  Pilots – IFALPA
  Air Traffic Controllers – IFATCA

## Slide 6: AGA/AOP/SG Runway Incursion Activities to date
Collection of runway incursion incident data from States
Review of data collected
Identification of runway incursion types, causes and prevention measures
Developed runway incursion definition reflecting regional characteristics of runway incursions for regional application until ICAO adopts an internationally approved definition for global application

## Slide 7: AGA/AOP/SG Runway Incursion Activities to date
Primary action – reduce and eliminate aerodrome deficiencies through compliance with Annex 14 Volume I SARPs
  provision and maintenance of facilities and services at aerodromes
  implementation of safety management systems at aerodromes
  State safety oversight through certification of aerodromes
  ICAO aerodromes audits (USOAP)
Developed Annex 14 Volume I Aerodrome Runway Incursion Prevention Measures Checklist

## Slide 8: Future AGA/AOP/SG Runway Incursion Activities
Continue to collect and review runway incursion data
Monitor worldwide developments on runway incursion prevention programmes, measures, techniques, methodology, technology, training, education and awareness
Identify and promote regional application of runway incursion prevention measures

## Slide 9: Relevant GREPECAS AGA/AOP/SG Conclusions
DRAFT
CONCLUSION 2/15 RUNWAY INCURSIONS
That,
a) States adopt the definition of a runway incursion as “An unauthorised or unintended presence of an aircraft, vehicle, person, wildlife or object on a runway, within the graded portion of a runway strip or infringing on the obstacle free zone and in the area controlled on the ground by runway-holding and road-holding positions”;
b) States continuously collect and compile runway incursion incident reports from aerodrome operators, air traffic services providers and aircraft operators and periodically submit these to the ICAO Regional Offices; and
c) the information referred to in b) above be presented and reviewed at the AGA/AOP/SG/3 Meeting.

## Slide 10: Relevant GREPECAS AGA/AOP/SG Conclusions
DRAFT
CONCLUSION 2/16 AIRFIELD MAINTENANCE PROGRAMMES
That:
a) States ensure that aerodrome operators implement and maintain adequate airfield maintenance programmes to eliminate and prevent the future existence of urgent deficiencies in existing runway markings, lighting, signs and pavement surface conditions, and perimeter barriers which have a direct impact on the safety of aircraft runway operations; and
b) the AGA/AOP/SG review implementation of this conclusion at its third Meeting in September 2003 by reviewing the list of shortcomings and deficiencies.

## Slide 11: Relevant GREPECAS AGA/AOP/SG Conclusions
DRAFT
CONCLUSION 2/18 AERODROME CERTIFICATION IMPLEMENTATION
That States,
a) should urgently implement the aerodrome certification process in order to be compliant with the new standard by 27 November 2003; and
b) provide an implementation status report to the AGA/AOP/SG/3 Meeting in September 2003.

## Slide 12: Runway Incursion Data Collected and Reviewed
Data requested twice – 2001 and 2002
Received from 12 of 36 CAR/SAM States (33%)
227 Incident reports
Period 1996 – mid-2002

## Slide 13: Summary of Types of Runway Incursions in CAR/SAM Regions
Wildlife – animals and birds (65%)
Public – pedestrians, bicycles, horses, vehicles (16%)
Aerodrome vehicles and personnel (13%)
Aircraft (6%)

## Slide 15
Runway
Aircraft Parked within the Runway Strip
Dog
Notes: SLIDE 28
At this airport serving a tourist destination, commercial passenger aircraft are allowed to park alongside the runway which is used by aircraft up to 50-passenger turboprop in size.
This is another example of failing to attend to obstacles, and allowing a hazard to flight operations to exist.

## Slide 17
Children watching the aeroplanes land
No Graded Area or Strip Protection
Notes: SLIDE 23
The next 15 slides illustrate some runway excursion hazards.
This first slide shows a typical regional airport in Asia.
At this airport, the runway was extended for 737 and A300 jets, but none of the other safety features were provided as the runway moved from one ICAO Runway Code up into the next category.
As may be seen, there is no graded area at all to support an aircraft running off the runway, and no proper safety strip either.
There is no fencing to prevent unauthorised access by people, or animals, and it is clear that an aircraft leaving the runway would suffer damage by travelling down the side slope into the padi fields.
There are clearly airport-related hazards at this airport, and they are also in contravention of the airport safety standards.

## Slide 19
Public Vehicles
Runway Centreline
Notes: SLIDE 20
Intrusion on active runways is not by aircraft alone.
In some countries, it is quite common for people, vehicles and animals to be found on the runway.
This is a considerable hazard, over which the airport does have full control, but often fails to enforce the sanctity of the runway.

## Slide 20: Summary of Deficiencies which Cause Runway Incursions in CAR/SAM Regions
Wildlife
  Perimeter barriers
  Wildlife and bird control and management
Public
  Perimeter barriers
  AVSEC control

## Slide 21: Summary of Deficiencies which Cause Runway Incursions in CAR/SAM Regions
Aerodrome vehicles and personnel
  Runway and Road holding positions
  Aerodrome data and charts – AIS
  Airfield Visual Aids – markings, lights, signs
  Aerodrome Procedures & Personnel Training
  Ground Control – Procedures, Training, Communications, Phraseology, Language Proficiency, SMGCS, SMR, tower visibility

## Slide 22: Summary of Deficiencies which Cause Runway Incursions in CAR/SAM Regions
Aircraft
  Runway holding position on taxiway
  Aerodrome data and charts – AIS
  Airfield Visual Aids – markings, lights, signs
  Aerodrome Procedures & Personnel Training
  Ground Control – Procedures, Training, Communications, Phraseology, Language Proficiency, SMGCS, SMR, tower visibility
  Pilots – Procedures, Training, Communications, Phraseology, Language Proficiency

## Slide 24
Notes: SLIDE 37
At another international airport, another feature is evident.
The runway slopes down from either end and could result in an aircraft being high on approach, landing long, and therefore possibly overrunning the end of the runway.
Slopes on runways can mislead pilots, when transitioning to a visual approach, and can result in a pilot approaching a down-sloping runway at a high altitude, and an up-sloping runway at a lower altitude that is normal.
In this case, the runway slopes down and as seen in the photo, aircraft are high on the approach.
But this airport has no runway end safety protection, and at both ends there are steep slopes, down into residential areas beyond.

## Slide 26: Contributory Factors if deficiencies exist but not direct causes of Runway Incursions
High traffic volume – aircraft and vehicles
Low visibility conditions
Poorly designed, confusing and/or complex airfield configuration, routings and procedures
Traffic mix range
Language mix in ATC communications

## Slide 28: Runway Incursion Prevention Measures at Aerodromes
Compliance with Annex 14 Volume I SARPs
  provision and maintenance of facilities and services at aerodromes
    Perimeter barriers
    Runway and Road holding positions
    Airfield Visual Aids – markings, lights, signs
    Aerodrome control – Wildlife, AVSEC, Ground movement
    Aerodrome data and charts
    Aerodrome Procedures & Personnel Training

## Slide 29: Runway Incursion Prevention Measures at Aerodromes
Compliance with Annex 14 Volume I SARPs (cont’d)
  Aerodrome data – aeronautical information
  Safety management systems at aerodromes
  State safety oversight through certification of aerodromes
Training
Human Factors – situational awareness, errors
Institutional Factors – Organisation and Personnel

## Slide 38: FINAL THOUGHT
Runway Incursions
Serious safety situation with simple solutions
THANK YOU
www.icao.int
mvreedenburgh@mexico.icao.int