## Slide 1: Miami International Airport Runway Incursion Action Team Recommendations for Incursion Mitigation
Presented to:
ICAO NAM/CAR/SAM Runway Safety/Runway Incursion Conference
Friday, October 25th 2002, Mexico City
By: Sunil Harman
Chief of Airport Panning,
Miami International Airport

## Slide 2: An International Connecting Hub and Gateway to the US
Serving 45 US and foreign scheduled passenger carriers
Destination for 35 foreign scheduled passenger and cargo carriers, 8 scheduled foreign all-cargo carriers, 2 foreign passenger/cargo charter carriers and 3 foreign all cargo charters
Regularly served by 16 US scheduled passenger/cargo carriers including commuters (air-taxi), 4 US passenger/cargo charter carriers and 5 US all-cargo carriers

## Slide 3: EXISTING EAST VFR FLOW
Aircraft Departure Operation
Aircraft Arrival Operation

## Slide 4: Regional Runway Safety Integration Ream (RRSIT) Objectives
Zero Incursion Events as opposed to the three incursions experienced in FY 2001.
One Pilot deviation
One Operational Error
One Vehicle/Pedestrian Deviation
No surface incidents occurred

## Slide 5: Primary Contributing Factors
Pilot/ground vehicle operator/controller communications
Airport familiarity
Loss of Situational Awareness
A failure in any one or a combination of these could contribute to a potentially dangerous situation.

## Slide 6: Initiatives Currently in Place to Minimize RWY Incursions
Use of the Automated Surveillance Detection Equipment – Model 3
(ASDE-3)
Illuminated RWY hold/stop bars
RWY Hold/Stop Bar Guard (Wig-Wag) Lights installed at all “confusing” intersections
Increased utilization of Perimeter Interior Service Road and Mid-field tunnel

## Slide 7: New Technology & Runway/Airfield Configuration Design Initiatives to Reduce Incursions
Proposed use of AMASS - Airport Movement Area Safety System an enhancement to the Airport Surface Detection Equipment (ASDE-3) radar. The system provides automatic conflict alerts (both aural and text) to assist tower controllers in reducing runway accidents. The system issues alerts involving possible conflicts of aircraft on the runway and on the close approach path with other aircraft/vehicles/obstacles on or near the runway.
Airfield Geometry redesign and modifications.

## Slide 8: MIDFIELD HARDSTAND ANIMATION

## Slide 9: RUNWAY CAPACITY ANIMATION

## Slide 10: Airfield Pavement Marking and Signage Improvements
Widening RWY hold/stop bar striping from 6 inches to 12 inches and enhancing conspicuity by applying the yellow paint containing reflective beading to pavement painted black.
Increasing the frequency of pavement marking repainting and painting large islands which do not contain sod dark green.
Replacing faded mandatory signs and enhancing informational signs to advise of operational restrictions.

## Slide 11
Pavement Striping and Marking

## Slide 12: Painted Islands

## Slide 13: Enhanced Signs

## Slide 14: Enhanced Signs

## Slide 15: Procedural & Operational Improvements
Restricted offer, acceptance and use of Land and Hold Short Operations (LAHSO) for Simultaneous Operations on Intersecting Runways (SOIR) 9R and 12.
Limited to Dry and VFR Conditions
Limited to US carrier pilots at their procedures manuals contain LAHSO
Precludes offer to and acceptance by International Air Crews as their procedures manuals do not include such operations
Illumination of LAHSO hold bars during day and night operations

## Slide 16: Surface Incident Prevention Plan for MIA is a Coordinated Effort
Between FAA’s Airports, Air Traffic, Airway Facilities Divisions and Airport Operations and Carriers.
It involves:
Bi-Monthly meetings with tenants and carriers
Improved movement area training for tug drivers who tow airplanes on the AOA.
And an enduring pursuit of solutions to improve safety.