## Slide 1
Notes: NAV CANADA AT A GLANCE
NAV CANADA is the non-share capital, private corporation which owns and operates Canada’s civil air navigation service (ANS). It purchased the system from the Canadian government, on November 1, 1996, for $1.5 billion.
NAV CANADA is a private company and not a federal agency. However, the company’s safety performance is regulated by Transport Canada.
The company is responsible for the safety and efficiency of the ANS. Some 5,500 employees work at NAV CANADA, including air traffic controllers, flight service specialists, electronic technologists, operational support specialists, engineers, managers, and administrative staff.

## Slide 2
<number>
In 1999, the Government of Canada and NAV CANADA declared the runway incursion problem to be one of the most important safety issues in Canada
Background
Notes: As indicated in the Transport Canada presentation, a number of safety reports identified a growing concern with the incidents related to runway incursions. Both Transport Canada and NAV CANADA declared incursions to be one of the top safety issues in Canada and pledged to seek a solution.

## Slide 3
<number>
Transport Canada formed a
sub-committee to study runway incursions
NAV CANADA commissioned
a parallel study at 20 sites
with ATS facilities
Background (cont)
Notes: As part of this study, NAV CANADA officials invited local airport personnel involved with runway operations to attend each of the twenty site meetings.
The invitees included: air traffic controllers, flight service specialists, electronic technicians, airport security personnel, fire-fighters, runway maintenance crews, local flight instructors, private and commercial pilots.
Transport Canada attended many of these meetings as observers.

## Slide 4
NAV CANADA Methodology
Conduct WWW and literature review
Determine sites for visits and discussions
with local stakeholders
Interview company staff, review local
procedures, etc.
Conduct safety round-tables at each site and
compile summary reports
Convene panel of aviation experts to review
data (June 2000)
Submit report with recommendations of
expert panel
Notes: The philosophy taken to solve the issue of incursions was based on the application of best-practices and proven strategies.
Original steps involved:
a thorough Internet search
a review of existing literature
on-site visits to 20 NAV CANADA ATC and FSS installations
interviews with company staff and a review of existing equipment and incursion prevention procedures
discussions with focus groups such as pilots, runway maintenance crews and airport security personnel
A panel of Canadian aviation experts was convened for the purpose of reviewing the results of the NAV CANADA data collected during an Internet search and site visits in June of 2000. As a result of the discussions of this panel, a series of recommendations were made to NAV CANADA.

## Slide 5
NAV CANADA runway incursion final report accepted in March/01
Report published internally April 01
Report made public April 26/01
<number>
NAV CANADA REPORT
Notes: NAV CANADA personnel compiled the recommendations into a report on Runway Incursions and presented the report to NAV CANADA management in early 2001.
The NAV CANADA report on Runway Incursions can be found on the Internet at http://www.navcanada.ca, click on English or French, then click on Newsroom, Corporate Documents, Other Documents.
At the same time NAV CANADA conducted its own study, Transport Canada, through its own Sub-Committee on runway Incursions (SCRI), published the government report on runway incursions.

## Slide 6
<number>
NO EARLY SOLUTION
x
Neither Transport Canada or NAV CANADA study teams were able to find any single factor or combination of factors that have changed so radically as to account for such an increase in incursions since 1996
Notes: It became evident that action was required on a National scale to counter this increase.

## Slide 7
STUDY
RECOMMENDATIONS
<number>
23 recommendations by Transport Canada
27 recommendations by NAV CANADA
Some recommendations are similar
Notes: The SCRI published its report on September 20, 2000 and produced 23 recommendations for action by different branches within Transport Canada such as Aerodrome Safety, System Safety, General Aviation, Commercial and Business Aviation, Air Navigation Services and Airspace as well as Enforcement.
The NAV CANADA report contained 27 recommendations. Some of the recommendations were similar to those produced by the SCRI and would require extensive communication and co-ordination with a number of different government agencies.

## Slide 8: NAV CANADA STUDY:
Action Plan created to address 10 areas of concern: Policy, Procedures, Training, Awareness, Communication & Co-ordination, Monitoring, Database, Equipment, Diagrams and Other
Many areas required joint implementation with Transport Canada
<number>
Notes: The incursion study recommendations were divided into the ten groups mentioned above.
Some sort of arrangement was required in order to ensure a common approach to solving the common problems.

## Slide 9: POLICY
Adopt a common definition
“Any occurrence at an airport involving the unauthorized or unplanned presence of an aircraft, vehicle, or person on the protected area of a surface designated for aircraft landings and departures”
Apply a common risk severity factor to each reported occurrence:
  Negligible, Low, Medium, High and Extreme
<number>
Notes: The Risk definitions are broad in nature and as a result, difficulties have been incurred with the classification of risk.
Canadian Risk definitions:
Negligible - the occurrence would not have caused a collision between aircraft or vehicles. No intervention required to keep the runway clear. (Example: An aircraft or vehicle was near (within 200 feet) but not on a serviceable runway and stopped short of the runway surface without intervention).
Low - the occurrence was unlikely to result in a collision between aircraft or vehicles. ATC or pilot intervention was required to keep the runway clear. (Example: A vehicle or aircraft was near (within 200 feet) but not on a serviceable runway and stopped short of the runway surface when contacted by ATC).
Medium - the occurrence could have resulted in a collision between aircraft or vehicles. A vehicle or aircraft was on a serviceable runway without authorization or was cleared onto (or across) a serviceable runway by mistake. (Example: An aircraft crosses a serviceable runway without clearance).
High - the occurrence could have resulted in a collision between aircraft or vehicles. A vehicle or aircraft was on a serviceable runway without authorization or cleared by mistake and a clear risk of collision existed. Normally requires ATC intervention to correct. (Example: Two aircraft take off from the same runway at the same time).
Extreme - the occurrence would have resulted in a collision between vehicles and/or aircraft and was prevented only by last minute evasive action by the aircrew and/or vehicle operator(s). (Example: A pilot rejects a take-off to avoid a collision with a vehicle or another aircraft.)
Through the joint Transport Canada and NAV CANADA Incursion Prevention Action Team (IPAT) , NAV CANADA agreed to adopt the FAA severity scale in January 2003.

## Slide 10
<number>
Installation of NOVA 9000 Airport Surface Detection Equipment (ASDE) with RIMCAS at airports such as Toronto and Halifax
Engineering study into National Runway Use Indicator Systems
Technology
Notes: Arrivals
The Runway Incursion Monitoring and Collision Alert System (RIMCAS) monitors runway full width (200 feet) x full length in good visibility, and runway plus 100 feet on each side in poor visibility. When an a/c is detected on approach to that runway in good visibility, an amber (stage 1) alert is generated if a target (an a/c or vehicle tracked by ASDE) is on the runway when an arrival is within 30 seconds of conflict. A stage 2 alert (red, along with aural alarm) is generated when a target is on the runway and an arrival is within 9 seconds of conflict. In poor visibility, a stage 1 alert is generated when a target is detected in the protected area of the runway (full length x full width plus 100 feet on each side) and an arriving a/c is detected on approach and within 35 seconds of conflict. A stage 2 alert is generated when arrival is detected and within 20 seconds of conflict.
Departures
In the departure phase, RIMCAS monitors full length and width of runway in good visibility, and full length and full width plus 100 feet on each side in poor visibility. When a departing a/c accelerates to 60 knots, RIMCAS recognizes it as a departure (as opposed to a taxiing a/c). If there is another target on runway (other than in the button area), RIMCAS generates an immediate stage 2 alert. There is no stage 1 alert in this situation, for obvious reasons (situation requires immediate intervention)

## Slide 11
Notes: This is a simulated ASDE presentation of a RIMCAS picture.
This ASDE presentation of runway 24 R at Toronto International airport shows targets highlighted in yellow at either end of the runway in the bottom right-hand part of the picture. Neither of the targets has been tracked doing more than 60 knots. This yellow tag represents a Stage 1 alert to the controller.

## Slide 12
Notes: This is a simulated ASDE presentation of a RIMCAS picture.
This ASDE presentation of runway 24 R at Toronto International airport shows targets highlighted in RED at either end of the runway in the bottom right-hand part of the picture. One of the targets has been tracked doing more than 60 knots with another target on the runway. This RED tag, along with an aural signal, represents a Stage 2 alert to the controller.

## Slide 13
Awareness and Education
Safety articles in National aviation safety newsletter
Safety articles in company newsletters
Internal safety bulletins distributed
Tele-conference with managers and operations specialists at 117 sites
Incursion prevention Video & Posters (IPAT)
Notes: Runway incursion prevention safety articles were published in the Canadian Aviation Safety Newsletter and distributed to all licensed pilots in Canada.
NAV CANADA has published numerous incursion prevention articles in its own company newsletter. This newsletter is distributed to the company’s 5,500 employees.
NAV CANADA participated in the development of a runway incursion video and six incursion-prevention posters. NAV CANADA distributed the video and posters to all its sites and Transport Canada to all airport operators and flying clubs.
NAV CANADA provides all of its operational air traffic controllers and flight service specialists with incursion prevention training. Since October 2000, each controller and specialist has received yearly classroom training on incursion prevention initiatives and statistics.
Each of NAV CANADA’s site managers and their operations specialists or team leaders were contacted and briefed on Incursion prevention initiatives and company direction in this area in September of 2001.

## Slide 14
Poster # 1
Poster # 2
Notes: Poster # 1 on the left was developed with vehicle operators as the target audience.
Poster # 2 on the right was developed with General Aviation pilots as the target audience.

## Slide 15
Poster # 3
Poster # 4
Notes: Poster # 3 on the left was developed with air traffic controllers and flight service specialists as the target audience. There is also an incursion prevention message to the commercial operator seen through the tower window. Notice the jetliner on the runway and the light twin that passed the hold line.
Poster # 4 on the right was developed with the commercial pilot as the target audience.

## Slide 16
<number>
ATC PROCEDURES
ATC procedures changed:
Taxi to position procedures
Intersection departures
Cross-runway authorizations
Blanket clearances
Readback of “Hold Short”
No ATC clearance in position
Notes: On October 18, 2001, NAV CANADA introduced procedural changes in its battle against runway incursions. These changes included:
. Taxi to Position procedures. Controllers cannot taxi aircraft to position on an arrival runway at night, in IMC or if the aircraft is not visible, unless a take-off clearance can be issued within three minutes from the time the aircraft is in position.
. Intersection departures. Controllers must identify, in the clearance, the intersection at which the aircraft must align itself.Example: Taxi to position at Delta. Controllers must also identify the intersection in the Take-off clearance. Example: From Delta, cleared for take-off runway 3-2.
. Cross-Runway authorization. Controllers must issue an explicit instruction to either Cross or Hold Short of any runway an aircraft or vehicle may cross while on the manoeuvring area.
. Blanket clearances. While not strictly prohibited, controllers and specialists have been discouraged from issuing « blanket » clearances. Example; Proceed on the field .
. Controllers must obtain a readback from the pilot when issuing an instruction to Hold Short.
. A recent change to ATC procedures discourages controllers from issuing IFR route clearances to aircraft while in position for take-off.

## Slide 17: TRAINING
Annual recurrent training on:
Professional Communications
Position hand-over procedures
Runway scanning techniques
Controllers and flight service specialists given a complete review of the Incursion study during the 2001/2002 recurrent training year
<number>
Notes: The importance of professional communications was emphasized during the 2001 and 2002 recurrent training sessions for controllers and flight service specialists.
Position hand-over techniques were reviewed with emphasis given to the importance of identifying aircraft and vehicles on or near the runways, and on the use of checklists.
Runway scanning techniques were reviewed as well during the 2001 recurrent training session.

## Slide 18
COMMUNICATIONS/ COORDINATION
<number>
  Professional communications part of
  annual recurrent training for
  controllers and specialists
  Training on Hearback/Readback errors
  in 2002
Notes: This Fall, controllers and specialists will receive an in-depth briefing on the problems associated with hearback/readback problems. Emphasis will be placed on recognition of first-order mistakes by pilots and preventing second-order mistakes with the hearback by controllers and specialists.

## Slide 19
<number>
SYSTEM
MONITORING
Development and application of an Incursion monitoring program by NAV CANADA
Ensure that NAV CANADA authorities conduct a more vigorous monitoring of ATS communications
Notes: Abnormal aviation occurences and regulatory infractions are reported electronically by ATS personnel on the NAV CANADA Aviation Occurrence Reporting system(AOR).
The monitoring of runway incursion activities includes a daily review of all reported aviation incidents in Canada. Runway incursion data is taken from the AOR database and maintained on a separate database.
NAV CANADA Head Office authorities conduct a vigorous monitoring of ATS communications with the goal of ensuring a consistent use of standardised phraseologies.

## Slide 20
Install inductive loop systems
at high-risk sites
National standard for incursion warning system
RIMCAS software
<number>
EQUIPMENT
Notes: Inductive loop technology is well known to airport operators. The Canadian panel of aviation experts recommended loop technology at runway edge to activate guard lights of other lighting systems to alert pilots of proximity to a runway.
NAV CANADA engineers have been tasked with creating a « runway use indicator system » that could be used in towers as a tool to assist controllers and specialists in better identifying runway occupancy by aircraft and vehicles. Work is on-going with this project.

## Slide 21
<number>
AIRPORT DIAGRAMS
Diagrams of controlled airports
to be made available at low or no cost
OTHER
Develop standard taxi routes
On test in Vancouver
Notes: It has been suggested that identifying incursion areas on airport diagrams may assist pilots in their flight planning activities and facilitate ground movements in Canada. These diagrams could be available on the NAV CANADA web site.
The panel of aviation experts also rcommended that standard taxi routes be implemented at major Canadian airports. These pre-established routes would be advertised in aviation documents and provide ground routings to and from active runways. The first of these routes has been published for the Vancouver airport.

## Slide 22: RUNWAY INCURSION STATISTICS 1998-2001
<number>
*MORE DILIGENT REPORTING BY FSS & ATC since 2000
Notes: In 2001, data representing incursions by vehicle at aerodromes serviced by a Flight Service Station was added to the figures that were previously only representative of ATC-serviced airports.
Recent figures therefore provide a more accurate total of runway incursions.
Definitions
O.I.Operating Irregularity: situation that occurs when air traffic services are being provided and when a preliminary investigation indicates that safety may have been jeopardized, less than minimum separation may have existed, or both.
P.D Pilot Deviation:action of a pilot that results in non-compliance with an ATC instruction/clearance or a violation of a Canadian Aviation Regulation.
VPD Vehicle or Pedestrian Deviation: a situation that occurs when a vehicle operator, a non-pilot operator of an aircraft, or a pedestrian proceeds without authorization onto the protected area of a surface designated for landing or taking-off. This classification includes security breaches but excludes animals.

## Slide 23
PD
56%
VPD
32%
OI
12%
INCURSIONS 2001- 2002
INCURSION ALL TYPES
2001
2002
Notes: These percentages have remained relatively consistent throughout the past few years.

## Slide 24: Risk Level Graphs
<number>
Notes: The comparison in Risk levels is worthy of mention. The following table will show a dramatic reduction in Extreme and High risk incursions in 2002.

## Slide 25
<number>
Risk levels -Table
Notes: The reduction in Extreme-risk ATS irregularities is 3.41%. The reduction in High-risk ATS irregularities is 14.78%. The increase in Medium, Low and Neglible-risk events has increased by an amount equivalent to the total reduction.
We attribute this reduction to the hightened awareness of control personnel to the possibility of incursions and to the incursion-prevention strategies we have in place.

## Slide 26: ATS OPERATING IRREGULARITIES(OI) 2000-2002
34 ATC OIs in 2000
32 ATC OIs in 2001 and 10 FSS
20 ATC OIs in 2002 and 15 FSS
No seasonal tendency
Most occur between 8:00 and 18:00
24% occur at shift change/meal hours
(in 2001)
Most involve ATC clearances with an aircraft or vehicle on the active runway
Most reasons include forgetfulness, distractions or failure to scan the runway
<number>
Notes:   During the past two years, approximately 60% of runway incursion OIs occurred as the result of an ATC clearance to land or take off.
  Commercial a/c are implicated in 24% or these incursion OIs, Business type a/c 6%, General Aviation a/c represent 27% , and vehicles, 43%.
  There wasn’t an April runway incursion OI in 2000 or 2001 and only 1 in 2002.
  In 2000 and 2001, the number of incursion OIs between January and March was the same as the number of incursion OIs between May and September.
  There were half as many incursion OIs between October and December 2000 as there were in each of the periods above.
  Between 70% and 80% of runway incursion OIs occurred between 08:00 and 18:00 hrs. This number was anticipated as it reflects the normal period of work activity on an airport.
  Between 25% and 35% of runway incursion OIs occurred during periods of traditional meal periods or shift change.
  In 2000, 4 OI related incursions occurred after a “Hold short” instruction was not given or the readback was missed.

## Slide 27
What is the next step?
Continued monitoring of runway incursions
Enhanced collection/analysis of incursion data with emphasis on Human Factors
Investigate all incursions
Develop preventive measures based on analysis
Notes: The collection of incursion statistics and close monitoring will continue.
The next phase of incursion prevention will focus on the HF aspect. Human Factors experts at Transport Canada and NAV CANADA are intensifying their efforts at trying to better understand the reasons for incursion related mistakes by pilots, controllers and vehicle operators.
We recognise that airport activities will continue to pose challenges to all who operate on them. NAV CANADA remains committed to reducing the risk associated with runway incursions at Canadian airports.

## Slide 28
<number>
Next step (cont.)
Continue:
  education of controllers
  and flight service specialists
  incursion prevention articles
  annual recurrent training
  cooperation with government
  Safety inspectors
Notes: Our co-operative efforts with Transport Canada safety inspectors will continue. The education and awareness program for controllers and specialists will also continue for foreseeable future.

## Slide 29
For more information, please visit our Website at:
www.navcanada.ca.
or contact
cotedj@navcanada.ca
<number>
CANADA -2002