## Slide 1: Human Factors in Runway Incursion Incidents
Patrick Hudson
Centre for Safety Studies
Leiden University
The Netherlands

## Slide 2: Structure
The major factor in runway incursion - Human Error
Case studies
Superficial causes - How incidents happen
Underlying causes - Why incidents happen
Where to look, what to do
Conclusion

## Slide 3: The Human Factor
Runway incursions are usually failures to understand
  Where the plane is
  Where the runway is
  Where a vehicle is
Classically failures of Situation Awareness
Failures involve three different organisations
  Airlines - Pilots
  ATC providers -Air traffic controllers (arrivals, departures and ground)
  Airports - Airside vehicle staff etc.
The individual pilots/ATCOs are seen as the problem
The real causes are at the organisational level

## Slide 4: Why do Accidents Happen?
Equipment
  Breaks
  Doesn’t work
  Not fit for purpose
People
  Incompetence
  Distracted
  Careless
  Reckless
Organisation
  Organisations allow (known) failure to propagate
  Accidents waiting to happen have been accepted

## Slide 5: Latent Conditions = Underlying Causes
Latent Conditions represent accidents waiting to happen
Many problems are to be found. E.g.:
  Poor procedures (Incorrect, unknown, out of date)
  Bad design accepted
  Commercial pressures not well balanced
  Organisation incapable of supporting operation
  Maintenance poorly scheduled
Latent conditions make errors more likely or the consequences worse
Individuals are the recipients of somebody else’s problems

## Slide 6: Reason’s Swiss cheese model of accident causation
Some holes due
to active failures
Other holes due to
latent conditions
Successive layers of defences, barriers, & safeguards
Hazards
Losses

## Slide 7: Classic solutions
Technical solutions to ensure nothing goes wrong
  Better ground radars, especially for poor visibility
  Extra aircraft systems
    Cameras to prevent excursions
    GPS-based navigation aids
More attention to those causing the problems
  More rigid procedures
    In the cockpit
    In the tower
  More training and supervision of ATCo’s
More data collection
More analysis of existing incidents

## Slide 8: Improved SA on ND: Airport navigation for taxi
A380 cockpit proposal
To display the airport map and the aircraft’s position
To insert the prescribed taxi track
To display other traffic

## Slide 9: Problems with this approach
Analysis implies having a framework to understand what is happening
Analysis and investigation lead to paralysis
  Paralysis by analysis
  Action can be delayed until effectiveness is proven
The solutions are still aimed primarily at the ‘sharp end’
Understanding major incidents highlights where the real problems may be found
Major incidents can help us understand the causes
  SQ 006 at CKS, Taipei
  DAL 39 at Schiphol, Amsterdam
  SAS at Linate, Milan

## Slide 10: SQ 006
Departure 747-400 TPE -LAX
  31 October 2000 at 22.55 local time
Fresh crew (had flown previous sector the day before)
  3 pilots, 17 cabin crew 159 passengers
Imminent arrival Typhoon Xangsane next morning
Captain requested 05L because of weather conditions
  05L is Cat II, longer runway with lower minima
Aircraft crashed into barriers and construction equipment while taking off from 05R
83 people died

## Slide 11: What happened?
Aircraft hit obstructions after V1
The PVD (Parallel Visual Display) had failed to lock on to 05L localiser
The PFD (Primary Flight Display) and the ND (Navigation Display) were both showing information inconsistent with 05L
Pilot Error?

## Slide 12: Taipei Chiang Kai Shek Airport

## Slide 13: Some extra information
The weather was bad and there was no ground radar for ATC
The requested taxi route was altered by ATC
  Original route was along 05R in opposite direction
No hold was required on taxiway NP
The runway sign 05R-N1 was set up for departures from the domestic terminal
The pilot turned continuously from N1 onto 05R
Pilots discussed the PVD failure and decided to ignore it once they had a firm sight of an active runway
Pilot error?

## Slide 14: So - how did it happen?
The pilots saw the centre line lights onto 05R
They followed those lights - the only lights they could see!
  The other taxiway lights were invisible at 90o to line of sight
There were insufficient taxiway lights (ICAO standard) on N1
  One light was defective, one was dim 116 m to the first light and only 4 lights in total to 05L
The designation sign for 05R was parallel to NP
There were no flashing lights (wig-wags) at NP Holding Position for 05R
ATC gave take-off clearance to SQ 006 as they reached the 05R holding position on NP and did not require them to hold
There were no stop-bar lights or wigwags on N1
There were no ICAO required barriers on 05R

## Slide 15
First visible taxiway light on N1
2nd light

## Slide 16: Pilot Error or System Failure?
The pilots failed to look at all their instruments (ND) and actively ignored inconsistent information (PVD)
They taxied far too short a distance to have gone from NP to 05L
Therefore pilot error - BUT
The airport lighting and defences did not meet ICAO standards
05R was probably lit as if it were functional and the taxiway lights on N1 were totally inadequate to form a line (gestalt)
They were given T/O clearance one runway too early
The visual picture was therefore compelling - one last runway, therefore the right one
A typical example of an accident waiting to happen?

## Slide 17: An accident waiting to happen extra information
On 23rd October a freighter nearly started to take off from 05R
On 30th October another freight aircraft repeated that near miss, having known about the 23rd October incident - and having recognised it as such after having nearly started on 05R as well
There was no system for effective incident reporting (e.g. CHIRP)
CKS did not have a Safety Management System
  There is no evidence that the hazards of the work program were identified, assessed or actively managed
  There is no evidence of an audit program

## Slide 18: Who should have prevented the accident?
Everybody
Pilots should have stopped and asked the way
  But they had to trust
    Boeing instrumentation - and mistrust CKS
    CKS - and mistrust Boeing instrumentation
Airport should never have allowed such a situation to arise
  Having discovered problems, should have corrected them (accidents usually have ‘hidden’ precursors)

## Slide 19: The SQ 006 event scenario
Airport decides
to change
Runway structure
Holding positions not
marked clearly
Taxiway lights
And runway signage
do not meet ICAO
standards
Pilots decide to
take off on
the ‘only’ runway
No ICAO
standard barriers erected

## Slide 20: DAL 39
A Delta 76 aborted take-off at Amsterdam Schiphol on discovering 747 being towed across the runway
Reduced visibility conditions (Phase - B)
The tower controller was in training, under the tower supervisor
There was another trainee and of the 11 people in the tower five were changing out to rest
The incident happened between the inbound and outbound morning peaks

## Slide 21: DAL 39 continued
The marshalling vehicle called in unexpectedly as Charlie-8 with a towed KLM 747 from a parking apron
Radio communications were unclear and C-8 did not state exactly where he was
C-8 was given clearance
The stopbar light control box confused everyone in the tower (it was a new addition)
The controller, thinking that the tow had crossed successfully, gave DAL 39 clearance
The DAL pilots saw the 747 and stopped in time

## Slide 22: DAL 39 Initial Analysis
Tow failed to report exact position or destination
Tow not announced in advance (as per procedures for phase B)
Assistant ATCo believed tow from right to left (did not know that a tunnel was in use)
Controllers completely unfamiliar with new control box
Ground radar pictures set up to cover different arrival and departure runways meant tow not visible on one screen
Controller was meshing the tow between both take-offs and landings
The tow, given clearance 1m 40 sec earlier, started off once the stopbars went out

## Slide 23: Why did all this happen - 1?
Tow was in violation, but this appears to be routine
No clear protocols for ground vehicles and no hazard analysis
Different language for aircraft (English) and ground vehicles (Dutch)
Poor quality of ground radio
Clearances appeared to be unlimited once given
Tower supervisor was also OTJ trainer in the middle of the rush hour
Altered control box not introduced to ATC staff

## Slide 24: Why did all this happen - 2?
No briefings about alterations at Schiphol (It has been a building site for years)
Too many trainees in the tower in rush hour under low visibility conditions
Differences in definition of low visibility between aerodrome and ATC
No management apparent of the change in use of the S-Apron
No operational audits by LVNL or Schiphol, of practice as opposed to paper
Schiphol designed requiring crossing and the use of multiple runways for noise abatement reasons

## Slide 25: The DAL 39 event scenario
Airport decides
to change
airport structure
Tunnel brought into use
without briefings
Tower combining training
and operations
during difficult periods
Pilots see 747
and abort
take-off
Controller gives clearance without assurance of tow position
Routine violation
of tow
procedures
Airport structure

## Slide 26: SK 686 D-IEVX Linate
A SAS MD-87 collided with a Cessna 525A business jet while taking off from 36R
Visibility at 08.10 (local) was 50 -100 m (Fog)
All 114 occupants and 4 ground staff died
The Cessna was on the wrong taxiway crossing 36R
The pilots of the Cessna were confused
They thought they were on a different taxiway (R5, to the North)
The MD-87 did nothing wrong
There was no ground radar

## Slide 27: The details - the Cessna
“Delta Victor Xray taxi north via Romeo 5 QNH …, call me back at the stop bar of the … main runway extension”
“Roger via Romeo 5 and … [QNH], and call you back before reaching main runway”
The Cessna started off from the GA Apron in dense fog, turned left and then was faced with a split
They should have gone left (R5) but went right (R6)
If they had used their compass they would have noticed
The only taxiway lights visible at that point led to R6
The markings were worn and not ICAO compliant
The pilot went through a STOP line, a stop bar and a final yellow line on the taxiway

## Slide 28: ATC
ATC was using non-standard terms
Read-back confirmation did not check the details
SK 686 and D-IEVX were on different frequencies
The next aircraft on ground frequency was spoken to in Italian (as were many transmissions)
D-IEVX reported “approaching the runway … Sierra 4”
S4 is on R6 and the equivalent on R5 would have taken much more than 2 1/2 minutes
The controller appears to have believed they were on R5 and gave permission to taxi after stop-bar to proceed and “call me back entering the main taxiway”

## Slide 29: Problems with T/O Clearances
Both Taipei and Amsterdam had long-standing clearances
D-IEVX had an apparent clearance to continue taxi-ing
A 747 at Anchorage was given immediate clearance with 6 minutes taxi time and one runway crossing
Should clearances be valid for more than 15 seconds?

## Slide 30: ICAO SARPs
ICAO sets standards for runway signage
  Runway signs
  Stopbars and Holding Points
  Taxiway lighting
Problems with ICAO compliance at all airfields
  Taipei - lights, barriers, stopbars
  Amsterdam - traffic lights instead of stopbars
  Linate - markings on taxiways, lighting
If these had been complied with fully would there have been any problems?

## Slide 31: Visibility and Taxiway lighting
All these incidents occurred under poor visibility conditions
Pilots were forced to look out at where they were going
Taxiways were visually compelling and there was no visible alternative at CKS or Linate
Are airfields sufficiently well marked to be unambiguous under conditions of poor visibility?

## Slide 32: ATC Language
Two incidents involve the use of more than one Language - not best practice
Many incidents are associated with failures to use aviation English
ATC usage is nearly, but not quite, accurate enough to prevent most incidents
Calls and read-backs are prone to confirmation bias
Would strict adherence to established protocols have prevented these incidents?

## Slide 33: Considerations for runway safety
Initial analyses show both pilots and controllers to have been at fault - situation awareness failures
The problem was that the situation was the problem, expecting awareness is expecting too much
Deeper investigation begins to show that all cases were accidents waiting to happen
The individuals were victims of systemic failures
In no case was there any effective safety management as expected in other high hazard industries
Few (if any) extra technical solutions would have been necessary if what should have been done was done

## Slide 34: Conclusion
Runway incursions appear to be due to individual errors
Those individual errors are caused by system weaknesses
Most major incidents have minor precursors
Technical improvements may reduce low potential incidents - but these incidents would have been easily prevented by doing what already should have been done
Most problems can be avoided by application of safety management principles (c.f. ICAO Annexes 11 & 14)
  Risk assessment
  Audit programs
  Reporting systems
  Continuous improvement learning from errors