## Slide 1: Retrospective Human Factors Analysis of US Runway Incursions (Focus: Air Traffic Control)
Julia Pounds, Ph.D.
Alfretia Scarborough, M.P.H.
US Federal Aviation Administration
Civil Aerospace Medical Institute
ICAO NAM/CAR/SAM Runway Safety / Incursion Conference
Mexico City, 22 to 25 October 2002

## Slide 2: Background
FAA has aggressively developed strategies to increase runway safety
General decline from 2000-2001
Some airports continue to increase
Global Concern
Similar activities in Europe are also addressing human factors in incident investigation.
Notes: Reducing runway incursions (RIs) is a top priority for the FAA and RIs have been a top safety priority and on the "Most Wanted" list for the NTSB since the list’s beginning in 1990 and in calendar year 2001 (CY01), the number of runway incursions showed an 11% decline from the previous year (FAA Runway Safety Report. Cy1998 – CY2001. Runway Incursion Trends at Towered Airports in the United States, June 2002).
Runway incursion—a surface incident when a collision hazard or loss of separation occurs. (ASY CY2001 Annual Report)
However, although air traffic briefly declined after the terrorist attacks of September 11, 2001, overall there were only 3% fewer operations in CY01 than in CY00 (FAA Runway Safety Report. Cy1998 – CY2001. Runway Incursion Trends at Towered Airports in the United States, June 2002). This suggests that mitigation strategies implemented to reduce RIs have had an impact.
Nevertheless, statistics from the FAA’s 32 benchmark airports (the reference airports used by the FAA to monitor national capacity and safety trends) showed that the rate of runway incursions for these airports increased from 5.6 to 6.9 incursions per million operations from Cy2000 to CY2001.
Activities in EUROCONTROL – AP12 etc.

## Slide 3
VPD: vehicle or pedestrian
OE/D: operational error or deviation
PD: pilot deviation
CY: calendar year
Notes: Not all runway incursions are attributed to the air traffic control system as a causal factor. For example, Figure 1 shows that the distribution of US runway incursions for CY2001-2002. Pilot Deviations (PDs) accounted for 60 percent of all incidents in CY2000 and 56 percent of all incidents in CY2001. In 2000, 20% of the runway incursions were ATC Operational Errors and Deviations (OE/Ds) and Vehicle/Pedestrian Deviations (V/PDs) each accounted for 20%. In 2001, 23% of the runway incursions were OE/Ds, and 21% were V/PDs. Although several projects have been undertaken by the FAA’s Office of Runway Safety since its inception to address these areas and to develop mitigation strategies,
This paper focused specifically on gaining a better understanding of the air traffic controller’s performance. Other parallel projects are being conducted to identify factors in PDs and VPDs.

## Slide 4: Previous Research
1981 Bellatoni & Kodis
  ATC conflicting clearances
  Need better reporting process
1986 National Transportation Safety Board
  Memory errors
  Coordination errors
  Lack of supervision
Notes: An overview of some recent research will frame the problem.
In 1981 Bellatoni and Kodis reported that the most prominent type of human error associated with runway incursions was the controller’s issuance of a conflicting clearance, basing their conclusions on the voluntary ASRS reports, NTSB accident reports, OE reports, and interviews with ATC tower personnel.. They also identified problems of under reporting, recommending improvements to the reporting process to reduce time and effort and to the data to enable the incidents to be understood in terms which would permit mitigation strategies to be developed.
In 1986, the NTSB investigated 26 RIs (NTSB/SIR-86/01) and found that controller involvement could largely be categorized as memory errors (e.g., forgetting about aircraft or about previous coordination with other controllers) and coordination errors (incomplete or misunderstood coordination between controllers). In addition, the benefit of supervisory redundancy to ‘back up’ the controller was often missing. Recommendations were to develop effective memory aids and associated controller training.

## Slide 5: Previous Research
1990 Human Factors Work Group on Controller & Pilot Errors
  Pilot-controller communication
2000 Runway Safety Joint Analysis Team
  Loss of situational awareness
  ATC procedures
  Poor communications
  Improved data collection techniques
Notes: In 1990 a meeting of a Work Group on Human Factors Relating to Controller and Pilot Errors was held to develop recommendations for near term actions. The group recommended research in ways to improve pilot-controller communication techniques in phraseology, acknowledgement of transmissions, timing of clearance issuance, and English as second language for pilots.
In 2000, the Runway Incursion Joint Safety Analysis Team (JSAT) examined 49 OE RIs from 1997 and 1998, finding that factors contributing to RI occurrences included loss of situational awareness, ATC procedures, and poor communications. The authors recommended controller training, improved procedures, improved technology to increase situational awareness, communications, and surveillance. The authors also recommended improved data collection techniques.

## Slide 6: Previous Research
2001 Cardosi & Yost
  Poor observation of aircraft
  Poor coordination between controllers
  Communication misunderstandings between pilots and controllers
  Improved data collection techniques
Notes: Cardosi and Yost (2001) used 256 OE and operational deviations (ODs) reports to list the three most common categories of causal factors reported by the facility investigations: actual observation of aircraft, poor communication between pilots and controllers due to misunderstanding, and poor coordination between controllers.
Information from their direct observations of operations was reportedly misused by controllers in effecting aircraft landing, take off, and taxiing operations. The authors identified some remedies for these vulnerabilities which may mitigate occurrence of such incidents. These were better memory aids for controllers, better surveillance and monitoring equipment, reducing miscommunications between pilots and controllers, improving coordination processes between controllers, and maintaining sufficient staffing. In addition, the authors pointed out the need for revising the method for investigating operational errors so that the information is more useful regarding the contributing factors.

## Slide 7: Previous Research
2001 Kelley, Krantz, & Spelman
  Lack of situational awareness
  Inadequate scanning
  No use of memory aids
  Poor planning/prioritizing
  Revise investigation forms
Notes: Kelley, Krantz, and Spelman (2001) reported that that human factors were found most frequently as a causal factor for both pilots and controllers, followed by operational and environmental factors. Three subject matter experts with experience as pilots, ATC, and accident investigation examined 151 “major” runway incursions (based on judged collision risk). Of these, 86 were OEs and 80 contained sufficient data for analysis. Principal causal factors were tower controllers who “lacked adequate situational awareness, did not visually scan adequately, failed to maintain awareness of an aircraft’s or vehicle’s identity or location on the airport, did not use a memory aid, and did not plan or prioritize actions correctly” (pg. 3-7). Lack of situational awareness and misapplied methods were noted, for example, when reports noted controllers’ inattention, memory lapses, inattention to detail, lack of effective scanning, and not validating assumptions prior to acting. Other associated factors identified as significant were ATC procedures that remove redundancies from the operational sequence, lack of direct supervision, and traffic complexity as average or below in 73% of the incidents. The authors’ recommendations focused on training, teamwork, supervision, and technologies to aid human performance, noting the need for a revision in the investigative forms to collect the type of information which would enable identification, monitoring, and measuring the impact of initiatives to reduce RIs.

## Slide 8: Previous Research
2002 Khatwa
  Poor procedures/deviations from procedures
  Poor decision making and failure to anticipate
  Poor communications--Incorrect instructions and clearances
  Visual monitoring and awareness of traffic
Notes: Khatwa (2002) analyzed RIs from 1990 to 2002 from various aviation data sources, such as the FAA, the United Kingdom’s Civil Aviation Authority (CAA), International Civil Aviation Organization (ICAO), US National Transportation Safety Board (NTSB), etc. The report identified ATC causal factors of poor procedures, deviations from procedures, poor decision making, poor communications, inadequate visual monitoring, inadequate awareness of traffic, incorrect instructions and clearances, and failure to provide or anticipate separation. The author observed that frequencies were underreported because of missing data. The analyses excluded vehicle and pedestrian RIs. Recommendations for ATC included developing, training, and implementing standard operating procedures (e.g., coordination of crossing clearances, traffic advisories to flight crews on crossing runways with progressive taxi as appropriate, and use of “line up and wait” procedures in low visibility), emphasis on communications (e.g., standard ICAO phraseology, verification of ambiguous communications, clarification of pilot readbacks), effective use of visual scanning and memory aids, management of distractions, and training for low visibility conditions.

## Slide 9: Previous Research
2002 Fisher
“While traffic volume, capacity-enhancing procedures and aerodrome layout may increase the potential for a runway incursion, human error is the mechanism that translates this potential into an actual occurrence.”
Notes:   Fisher, B. (2002). Study looking at runway incursions identifies contributing factors and recommends solutions. ICAO Journal v57(1).
  Human factors include: complexity, familiarity, communications, and distractions (my italics).

## Slide 10
Person(s)
Task
Environment
Equipment
Person x Task x Equipment x Environment Interaction
THE “HUMAN” FACTOR IN CONTEXT
Notes: In 2000, Knott, Gannon, and Rench delivered a report to the FAA’s Office of the Chief Scientific and Technical Advisor for Human Factors summarizing domestic and international literatures and databases concerning research relating to human factors risks, problem identification, and risk mitigation of runway incursions. The authors found that, at the time, the US was more focused on reporting runway incursions compared to other countries and that, although RIs occurred in other countries, they were not considered an international problem, despite reports of US incursions which involve international flight crews. The authors categorized the information according to training, procedures, signage, and technology insertion, however, the relevant information for the present purpose was the discussion of training. “Certain perspectives found in the literature on runway incursions deem the issue to be a ‘people problem,’ and suggest that this problem is caused by those involved, and will persist until people stop making mistakes. While there is some basis to this perspective, it only serves as a valid basis to describe the problem and not to solve the problem. Treating the problem – as a people problem – with additional procedures, training and legislation may help in reducing incursions in the short term, but may also serve to burden the end users (i.e., pilots, and controllers) with additional workload. Procedures and training targeted at the end user should, in the long term, be only a part of a larger incursion treatment package that analyzes, identifies, and removes the sources of error” (pg. 3).
What was needed was a “human factors approach” defined broadly to include not only the individual but the task the individual is engaged in at the moment (for example, inter-facility coordination or radio communication), the equipment and materials the individual has available to work with (e.g., memory aids), and the environment in which the individual has to work.

## Slide 11: Common Themes
Improve communication between controller and pilot
Improve controller’s thinking processes
  Memory
  Situational Awareness
  Scanning
  Planning
Improve procedures, etc.
Data more informative about human factors
Notes: These studies are remarkable for their redundancy. They identify much the same factors as candidates for intervention strategies. Most also recommend a better method for investigation of operational errors so that better (more informative) data can be collected for analysis.

## Slide 12: This Study
Replicate
Extend
Revise
Notes: Replicated
  The study replicated previous findings.
Extended
  Identified specific mental processes and situational factors to be addressed.
Revise
  The payoff for taxonomic analysis of incidents will come when quality data to better identify causal and contributory factors.
  Needed: Change the investigation and reporting system
Enabling higher order analyses
  So the analyst can begin to look at more specific information and the complex associations between constellations of factors. This approach would be particularly helpful in domains as complex and dynamic as ATC.

## Slide 13: This Study
Test the classification method to replicate other findings
Examine results for added value
Develop a human factors technique for analyzing incidents so that better information will be available.
Notes: This project used archival data from operational errors (OEs) classified as RIs by the air traffic control (ATC) incident investigation process from a human factors perspective. Not all RIs are classified as OEs, meaning that the occurrence was attributable to an element of the ATC system.
This study was conducted as part of the larger project to develop a more robust method to capture the complexity of causal factors surrounding OEs. This particular study used a more comprehensive human factors perspective, determine whether this approach replicated previous findings and whether it would add any insight beyond previous research findings.
This data was obtained from the same FAA OE data archive from which several of the previous reports were developed. Narratives from three hundred forty-seven (347) OE reports were extracted from the FAA OE database based on its flag as an RI in the database. CY1996 through June 2000
Four ATC subject matter experts (SMEs) were selected to do the analysis based on their experience in terminal operations. Each had over 25 years of ATC experience with terminal operations.

## Slide 14: Method
Taxonomy used: HFACS-ATC
  Based on Human Factors Analysis and Classification System (Shappell & Wiegmann, 2001).
  Adapted for ATC
Narratives from 347 FAA OE reports were used: CY1996 through June 2000
Analysis by ATC subject matter experts with experience in terminal operations.
Notes: The error analysis method for air traffic (HFACS-ATC) was used for the classifications--a method generated by combining categories from an existing human factors technique: the Human Factors Analysis and Classification System (Shappell & Wiegmann, 2002), originally developed for retrospective analysis of aviation mishaps, and elements from the Taxonomy for Human Error Reduction originally developed for retrospective analysis of air traffic management incidents (EATMP, 2000).

## Slide 15: HFACS
Organizational Influences
Unsafe
Supervision
Preconditions
for Unsafe Acts
Unsafe
Acts
Latent Conditions
Latent Conditions
Latent Conditions
Active Conditions
Failed or Absent Defenses
Notes: HFACS is based on Reason’s Swiss Cheese Model of Human Error and is a data-driven analysis method originally developed for investigation of aviation aircrew accidents. It enables a retrospective analysis of existing data and it frames the incident in that context.
HFACS classifies human error into 17 causal categories which are organized around four tiers:
- Unsafe Acts of Operators
- Preconditions for Unsafe Acts
- Unsafe Supervision
- Organizational Influences
HFACS captures the system breadth and depth in describing behaviors not only from the individual level of performance, but also includes preconditions of the situations, supervisory activities and organizational influences. It first identifies the holes then finds ways to fill them.

## Slide 16: HFACS-ATC
Organization
Supervision
Preconditions
Controller
Latent Vulnerabilities
Latent Vulnerabilities
Latent Vulnerabilities
Separation Violation
Critical Human Error
Notes: HFACS was selected as an appropriate model for ATC and adapted to the ATC domain for retrospective analysis of operational errors (Scarborough & Pounds, in preparation).
The HFACS-ATC taxonomy incorporated the primary task the controller was engaged in at the time of the critical error, situational variables relevant at the time, and an organization of the Unsafe Supervision and Organizational Influences tiers to reflect the FAA’s particular organizational structure. In addition, each critical point of human error which could be identified in the text was identified and classified on all dimensions for that particular point in time. With this procedure, more than one human error could be identified for each OE, making for a possibly richer look at events which culminated in the OE.

## Slide 17
ORGANIZATION
CLIMATE
STRUCTURE
POLICIES & PROCEDURES
RESOURCE MGMT.
SUPERVISION
GENERAL SUPERVISION
PLANNING
CORRECTION OF KNOWN PROBLEMS
TEAMWORK
CONTRAVENTIONS
PRECONDITIONS
ATC CONDITIONS
ATC PRACTICES
SITUATIONAL FACTORS
ATC
DEFICIENCIES
PROCEDURE FOLLOWING
TASK
HFACS-ATC
Notes: The four-tier structure of HFACS was used. Some categories and definitions were adapted to capture air traffic control- related activities.
In HFACS-ATC, as with the original HFACS, the bottom two tiers (Controller and Preconditions) capture variables that exert a more direct influence on an individual controller’s performance.
HFACS-ATC used an expanded group of situational factors to capture events that could affect controller performance such as traffic and airspace characteristics, weather and equipment, and the ambient environment.
The top two tiers deal with supervisory control and organizational influences associated with operational errors. Teamwork, as a casual factor, was extended to the supervisory level.

## Slide 18: Task
RESULTS --
Notes: For all descriptives, the % given is over all critical points identified, not within groups, so they may not sum to 100% within a given category.
Task
A majority of the critical points were associated with three tasks: communicating with the pilot over radio frequency (63.7%), tower observation (17%), and coordination with other controllers (9.3%). The remaining critical points were distributed across eight other tasks. Three tasks were unused by the analysts: Materials Checking, Hand-off Relief-briefing, and Examination.

## Slide 19: Causal Factors @ Tiers
RESULTS --
Notes: Tier
Most critical points were classified in the Controller Tier (91.2% of total); fewer as Preconditions (7.4%), and very few (1.4%) as Supervision errors. No critical points were associated with causal factors in the Organizational Tier.

## Slide 20
Causal Factors @ Person
RESULTS --
Notes: At the individual Controller level, most critical points (86%) were associated with Deficiencies in performance, such as, in decision making or performance of skills.
  18%, as failures of decision making and problem solving
  63% as failures to adequately perform highly learned skills, such as vigilance (e.g., the controller failed to catch the pilot's inaccurate readback of the clearance) or memory recall (e.g., the controller forgot a clearance when coordinating a crossing departure).
  5% of total were misperceptions.
Failures in following procedures were associated with 5% of the critical points.
These results are partially an artifact of the current reporting process which focuses most attention at the level of the individual controller.
These results replicate the findings from the other research studies.

## Slide 21: Person Causal Factors @ Task
RESULTS --
Notes: To illustrate how this type of approach would provide added value for understanding incidents, the three tasks being associated most often with a critical point-- Controller-Pilot Communications, Tower Observation, and Coordination --were further examined at the level of the individual controller.
Controller-pilot communications (63.7%)
  59% were associated with individual deficiencies
    42% were skill-based errors (e.g., failure to catch an incorrect readback).
Tower Observation (17%)
  14% were associated with individual deficiencies ,
    13% were skill-based errors, such as failures of attention (e.g., the controller did scan prior to issuing a departure clearance).
Coordination (9.3%)
  6% were associated with individual deficiencies,
    5% were skill-based errors (e.g., failure to properly accomplish transfer of traffic to another position).

## Slide 22: Preconditions
ATC Conditions, such as
  expectation bias
  spatial confusion
  perceptual tunneling
  distraction
  integration failure
  cognitive fixation
  incorrect assumption
ATC Practices, such as
  poor teamwork
RESULTS --
Notes: Preconditions—sometimes also referred to as performance shaping factors—were associated with only 7% of the critical points. Again, this type of information is not currently routinely gathered during ATC incident investigations.
Controller’s conditions noted included:
  Mental States of--
  expectation bias, spatial confusion, perceptual tunneling
  distraction, integration failure, cognitive fixation, incorrect assumption
  Training and Experience--
  inadequate knowledge for position
  inadequate mentoring
Controller’s practices noted were relative to readiness to work.

## Slide 23: Situational Influences
Ambient environment
      noise
Distractions
      job related
      non-job related
Traffic and airspace/runway characteristics
      excessive traffic load
      unusual situation (emergency or high risk)
      airspace design characteristics (complexity, changes, etc.)
Equipment problems
RESULTS --
Notes: Situational influences--
ambient environment –
  noise
ambient distractions –
  job related
  non job related
traffic and airspace --
  excessive traffic load
  unusual situation (emergency or high risk)
  airspace design characteristics (complexity, changes, etc.)
equipment problems

## Slide 24: Conclusions - This Study
Replicated and extended
previous findings
As were previous findings, it was limited by using information recorded
in archival data
Revise…
Notes: Replicated
  The study replicated previous findings.
Extended
  Identified specific mental processes and situational factors to be addressed.
Revise
  The payoff for taxonomic analysis of incidents will come when quality data to better identify causal and contributory factors.
  Needed: Change the investigation and reporting system
Enabling higher order analyses
  So the analyst can begin to look at more specific information and the complex associations between constellations of factors. This approach would be particularly helpful in domains as complex and dynamic as ATC.

## Slide 25
Ground Actions
Ground- Controller Communications
Traffic & Airspace
Pilot-Controller Communications
Pilot Actions
Weather
Procedures & Orders
Documents & Materials
Personal Factors
Environment
Interpersonal & Social Factors
Supervision
Management
Team Factors
Workplace & HMI
Training & Experience
Organization
ATC Performance in a Complex Environment
Notes: The technique captures the complexity of the ATC environment.

## Slide 26: Cognitive Processing
INPUT
RESPONSE SELECTION
SENSORY RECEPTION
PERCEPTION
RESPONSE EXECUTION
OUTPUT
ATTENTIONAL CAPACITY
FEEDBACK
LONG
TERM
MEMORY
WORKING
MEMORY
THE
PICTURE
Notes: The technique also incorporates the individual controller’s thinking processes into the analysis.
By understanding these processes, we can begin to understand the thinking processes that support ATC performance and we also believe that we can begin to understand how situation awareness is gained, maintained, and lost—a variable that keeps reappearing in studies of runway safety.

## Slide 27
ATC
FLT
GROUND
Performance in a Complex
Environments
Notes: Recall that the definition of runway incursions encompasses also pilot deviations and vehicle/pedestrian deviations. Parallel JANUS techniques are being developed by CAMI researchers to capture the contributing and causal factors for pilots and ground/surface operations also.
To address the complexity of the problem.

## Slide 28
Thank you for your attention.
julia.pounds@faa.gov