## Slide 1
Un escenario de Incursión de Pista
“Causas y Recomendaciones…”
Cap. Sven Boewe
Flight Safety
GRUPO TACA

## Slide 2: Incursión de Pista - Definición
Toda ocurrencia en un aeropuerto relacionado con:
  Una aeronave
  Un vehículo
  Una persona
  Un objeto
en tierra y que crea un peligro inminente de colisión o que resulte en la perdida de adecuada separación con una aeronave en maniobra de despegue o aterrizaje.
* No existe definición internacional de Incursión de Pista..

## Slide 3
Por qué hasta ahora estamos
escuchando de este problema?
Es algo nuevo ?
?

## Slide 4
WW-I
Definitivamente NO…

## Slide 5
El problema de Incursiones de Pista
es un problema creciente,
mucho más serio de lo que pensamos,
y puede ser causado por diversas razones:

## Slide 6
B747 KLM – B747 Pan Am
Los Rodeos, Tenerife / 1977
(Fatalidades: 583)
CRM y fraseología inadecuados…
Video #1

## Slide 7
B737 US Air – Fairchild Metroliner
LAX, California / 1991
(Fatalidades: 34)
Baja conciencia situacional…
Video #2

## Slide 8
Fecha: 08 Oct 2001
Aerolínea: SAS
Vuelo No: SK686
Aeronaves: MD87/Citation II
Lugar: Milan, Italia
Fatalidades: 118
Visibilidad reducida…

## Slide 9
A320
Colombia / 2000
(separación fué de aprox. 150 pies!!!)
(Posibles fatalidades: +200)
Errores operacionales (ATC)…
Video #3

## Slide 10
B747 Korean Airlines – B747 China Airlines
Chicago O’Hara / 1999
(separación fué de 3 segundos y 75 pies!!!)
(Posibles fatalidades: +300)
O el simple descuido de una tripulación…
(Desviación de Piloto)
(para mencionar solo algunos)
Video #4

## Slide 11
La siguiente es una recreación de acontecimientos casi fatales, ocurridos en Providence, Rhode Island.
Vuelo 1448 de United Airlines, acaba de aterrizar con 1/2 milla de visibilidad (causada por neblina)…
Muchos de los “ingredientes” para un accidente por
Incursión de Pista estuvieron presentes:
- CRM y fraseología inadecuados
Baja conciencia situacional
Errores operacionales (ATC)
Quebranto en las comunicaciones
Baja visibilidad
No adherencia a SOP´s
Poca familiaridad con Aeropuerto

## Slide 12
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A

## Slide 13
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
TWR: United 1448, what´s your position ?
UAL: ...and ahh, we are clear of the runway on November by Bravo, United 1448.
TWR: United 1448, thank you, taxi to the ramp via taxiway November and Tango, report crossing Rwy 16.
UAL: Ok, N, T...will report crossing RWY 16, United 1448.
TWR: Wind 140 at 5
USAIR: Ground, USAir 2998 is holding short at FEDEX.

## Slide 14
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
M
A
TWR: US Air 2998 thank you
UPS: Ground UPS 27 taxi
TWR: UPS 27 Providence Ground, good evening, RWY 5R, taxi via taxiway V and RWY 23R, hold short RWY 16 , advise holding short.
UPS: Ok, we can´t take V at this time, we are facing the wrong way..., any chance of A, M and N?
TWR: UPS 27, you can expect that taxi, hold your position for now please, stand clear of all taxiways
UPS: Ok, we´ll hold our position here, on the ramp, over... UPS 27.

## Slide 15
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
TWR: USAir 1020, turn left taxiway N or A and report clear of the RWY please.
USAir: Roger looks like we´ve got N here, for USAir 1020.
TWR: USAir 1020, thank you, taxi to the ramp vía taxiway N and T, report crossing RWY 16.
USAir: N, T, to the ramp, report crossing RWY 16, ...and we are clear of 5 at this time, for USAir 1020 .
TWR: USAir 1020, thank you.
TWR: Fedex 1662 , RWY 5 R, fly RWY HDG, cleared for Takeoff.
Fedex: RWY HDG cleared for takeoff, on 5 R, ...ahhh, Fedex 1662.

## Slide 16
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
UAL: ...and 1448 is on N by the RWY here, we don´t see the ahh...., are we cleared to cross straight ahead on N?
TWR: United 1448, affirmative, cross RWY 16, join taxiway N and T on the other side.
UAL: N – T on the other side, United ahhh...1448.
TWR: USAir 1020 exert caution, 757 ahead just coming up on RWY 16, join taxiway N and T, taxi to the ramp.
USAir: Ok, we´re looking for the other airplane.
USAir: and we´re crossing N at B, did you want us to taxi A to the ramp?
TWR: USAir 1020, negative, that was just if you missed N on the rollout, taxi to the ramp, via taxiway N and T, report entering taxiway T please.

## Slide 17
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
USAir: Thank you, N – T, USAir 1020.
UAL: ...and ahhh, United 1448...., we´re approaching K here,...ahhh, uhh, mmmm,...
TWR: United 1448 ! You should´t be anywhere near K, hold your position please
JUST STOP !
UAL: Tower, this is United 1448 and we are currently on a RWY, I´m looking out to the right with a K, ahhh...we need to go on the K taxiway.
SOMEBODY JUST TOOK OFF!!!
TWR: United 1448, you where supposed to taxi via N and T, I need to know what RWY you are on, I can´t see anything from the TWR!
UAL: We, ahh..Maam, we are on 23 R and intersection of 16 and we did not connect on N, we are by K to our right and we just overshot K, we did not see it...

## Slide 18
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
TWR: Fedex 1662, contact departure…, good day.
Fedex: Fedex 1662, over to departure, so long...
[ Garbled Transmission ]
UAL: […] runway on 23L here...
TWR: United… STAND BY please!
TWR: USAir 2998, RWY 5R, fly runway heading, cleared for takeoff.
UAL: Maam..., I'm trying to advise you we are on an active RWY, United 1448 !!!
TWR: 23R is not an active RWY, it’s a taxiway when we are IFR or in the dark
[ Garbled Transmission ]
[???]: …we’ll stand clear of all runways until we figure this out.
TWR: EVERYBODY STAND BY PLEASE, RADIO SILENCE UNTIL I TALK TO YOU !!!

## Slide 19
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
UAL: …runway.
TWR: EVERYBODY STAND BY !!!
TWR: USAir 1020 hold your position please, I don’t know where the United is…, I'll figure it out in a minute.
USAir 1020: We are on T, for USAir 1020.
UAL: …our position United 1448, we are on 23R, we are looking at K straight ahead, if we can go straight, we can get on K and get off the RWY.
TWR: United 1448, stand by please ! DON’T TALK !!! I have other things I need to do !!!
UAL: Roger, Maam.
TWR: USAir 2998, RWY 5R fly runway heading, cleared for takeoff.
USAir 2998: Ahh…, Tower, USAir 2998, ‘till we figure out what’s going on down there, we are just gonna stay clear of all runways.

## Slide 20
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
TWR: USAir 2998, roger, hold short of RWY 5R. He’s not near the RWY, but you can hold short.
USAir 2998: OK
TWR: Tower, USAir 2998, isn’t going yet because I have a United, HE DOESN’T KNOW WHERE THE HELL HE IS !!! I'll take him back and I'll flash you when he’s ready.
TWR: USAir 1020, ahh…, are you at your gate ?
USAir 1020: ahh..., we are stopped as requested, on T.
TWR: USAir 1020, thank you.
TWR: United 1448, understand you are on RWY 23R. Have you gone past taxiway K and T ?
UAL: Maam, we’re on 23L and 16, and I'm facing into K, at this point, the nose is just over 23L!
TWR: Are you facing Northwest or Southeast ?

## Slide 21
5R
5L
34
23L
23R
Control Tower
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
UAL: We are facing…, we are heading…, for United 1448…, right now we are facing approximately 200 degrees on the heading…, I'm looking out the window, and I'm seeing a sign that says 23L to my right and a sign that says 16 to my left, and I have the other sign that says K to my right and to my left, we are on a current runway…, heading 200.
TWR: Stop all traffic until advised please.., United has NO IDEA of where they are ! Thank you.
TWR: United 1448, just taxi straight ahead, and let me know when you get to the next sign please...
UAL: Ok, we’re gonna go straight ahead, we’re gonna go up to K here.
TWR: United 1448, are you just turning onto RWY 23L right now ?
UAL: Yes we are, and we are going to go over, we are on 23…, we are currently exiting on…, we are coming up on K now.

## Slide 22
5R
5L
34
23L
23R
Control Tower
Terminal
Building
Northwest Ramp
16
C
C
B
C1
N
K
K
N
T
T
B
Providence, Rhode Island (KPVD)
B
K
A
TWR: United 1448, roger, turn right K and then slight left turn onto taxiway C, hold short runway 23R
UAL: …is ahh…, 150 and we are on K, we are clear of the RWY, we are approaching K1 and we are on K.

## Slide 23
Pero…,
cómo una tripulación tan experimentada
y con tanto entrenamiento puede verse
involucrada en este tipo de situación ?
?
?
?
?
?
?
?
?
?

## Slide 24
“There are no such things as accidents,
what we call by that name is the effect
of some cause which we did not see”
“Voltaire”
(“No existe tal cosa como un accidente.
Lo que llamamos por ese nombre son
los efectos de causas que no hemos visto”)
“Voltaire”

## Slide 25
Debemos entender este concepto:
Fallas Activas vs. Fallas Latentes
Fallas Activas: Cometidas por todos aquellos que se
encuentran en contacto directo con el
sistema (pilotos, ATC, mecánicos, etc.)
Fallas Latentes: Se derivan de decisiones u omisiones
en las esferas organizacionales o
gerenciales del sistema.

## Slide 26
Las “fallas activas” tienen un impacto directo e
inmediato, mientras que las “fallas latentes”
pueden permanecer durmientes por largos periodos,
en ciertos casos por varios años, antes de que se
combinen con “fallas activas” y eventos “detonantes”
causando así rupturas en las defensas del sistema.
“Beyond Aviation Human Factors”
D.Maurino – J.Reason – N.Johnston – R.Lee

## Slide 27
La gran mayoría de fallas activas
son el resultado de fallas latentes…
Debemos entonces “apuntar” a las
fallas latentes del sistema para así mitigar las activas !
Nuestra Meta

## Slide 28
Es importante que tanto las tripulaciones,
el ATC y en general todo el sistema,
aprendan a reconocer la magnitud del
problema de incursiones de pista.
Deben entender que cierta combinación de factores
crean un entorno altamente propenso
para generar errores…
“Behavior is a function of consequences”
Conciencia Situacional

## Slide 29
Cuadro Comparativo – Incursiones de Pista

## Slide 30
A mí NUNCA
me va a ocurrir una
Incursion de Pista…
PERCEPCION DEL PROBLEMA…
(por parte de las tripulaciones)
Notes: This presentation was prepared by the FSF ALAR Task Force as a product to help prevent approach-and-landing accidents (ALAs), including those involving controlled flight into terrain (CFIT).
January 2001

## Slide 31
FINISHED FILES ARE THE RE-SULT OF YEARS OF SCIENTIF- IC STUDY COMBINED WITH THE EXPERIENCE OF MANY YEARS
COUNT THE “F’s”
PERCEPCION…
(Conciente y subconciente)

## Slide 32
100%
APROXIMACION
Y ATERRIZAJE
CRUCERO
DESPEGUE
RODAJE
PUNTO DE SATURACION ANTROPOMETRICO
ESFUERZO
RENDIMIENTO
TIEMPO
Momentos de MENOR
carga de trabajo ( percibida? )
Esfuerzo Requerido

## Slide 33
Yerkes & Dobson
Graph
Carga de Trabajo / Nivel de tensión
Performance
Bajo
Moderado
Alto
Alto
V
E
R
D
E
A
M
B
A
R
A
M
B
A
R
R
O
J
O
R
O
J
O

## Slide 34
Yerkes & Dobson
Graph
Carga de Trabajo / Nivel de tensión
Performance
Bajo
Moderado
Alto
Alto
Nivel aceptable de
capacidad para
tareas críticas
Nivel aceptable
de tensión para
tareas críticas

## Slide 35
Yerkes & Dobson
Graph
Carga de Trabajo / Nivel de tensión
Performance
Bajo
Moderado
Alto
Alto
Nivel aceptable de
capacidad para
tareas críticas
COMPLACENCIA !
CONFUSION !
Incursión por
sobrecarga
Incursión por
complacencia

## Slide 36
Entrenamiento
Tripulaciones
ATC
Operadores de
Vehículos Terr.

## Slide 37
Entrenamiento (cont.)
Tripulaciones
(causantes del 50%-60% de eventos !)
Rotulación
Demarcación
Iluminación
SOPs (Comunicaciones, Cabina Estéril, Cartas de Aeropuerto “a mano”, etc)
Adecuada Familiarización
Adecuada uso de CRM

## Slide 38
Entrenamiento (cont.)
Tripulaciones (cont.)
Adecuado uso de CRM
También en tierra puede ser útil…
Video #5

## Slide 39
Entorno Operacional
Diseño de Aeropuertos
Avances Tecnológicos
(ATC)
Y otros…
Avances Tecnológicos
(Aeronaves)

## Slide 40
Cuidado con las
INCURSIONES DE PISTA
…aparentemente, ya no se limitan
solo a los Aeropuertos !
Y finalmente un último recordatorio:
Video #6

## Slide 41
“The high level of safety achieved in
scheduled airline operations lately,
should not obscure the fact that
most of the accidents that occurred
could have been prevented”
ICAO,
Accident Prevention Manual, 1984
Muchas gracias !