## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
AIRPORT INFRASTRUCTURE
Arturo Benito
Director Fleet Planning & Environment-IBERIA

## Slide 2: ISSUES
Minimum energy airside design
ATC co-ordination
Reduction of APU / GSE use
APU replacement

## Slide 3: MINIMUM ENERGY AIRSIDE DESIGN Target
Minimise taxi time to save fuel and emissions.
For Iberia:
1 minute of taxi per flight
=
3,000 tons of fuel per year

## Slide 4: MINIMUM ENERGY AIRSIDE DESIGN Strategy
Parking positions/terminals close to taxiways
Minimise taxiways length
Avoid taxi braking when possible

## Slide 5: ATC CO-ORDINATION Target
Minimise time between engine starting and beginning of taxi
Close co-ordination between:
  airport (ground movement)
  ATC (arrival/departure planning)

## Slide 6: ATC CO-ORDINATION LEONARDO Project
It will integrate existing management tools at CDG and MAD airports under real operating conditions
The partners are Aeroport de Paris (France), SICTA (Italy), NLR (Holland), AENA, Iberia, Indra, Ineco, Isdefe (Spain)

## Slide 7: COMMERCIAL AIRCRAFT TURN-AROUND
Typical turnaround: 0.5-3.0 hours
Operations:
  deplane/unload
  cleaning
  refuelling
  technical checks
Most of these tasks require energy supply by APU/GSE
  repairs
  catering
  enplane/loading
  pre-flight checks

## Slide 8: REPLACING APU/GSE Systems
Functions
Electricity
Air conditioning
Engine starting
Water supply truck
Replacements
50/60-400 Hz converters
Pre-conditioned air
Compressed air supplier
Water from general network

## Slide 9: REPLACING APU/GSE Savings
Typical APU emissions per turnaround (kg.)

## Slide 10: REPLACE STANDARD APU BY FUEL CELL Pros
Energy efficiency improvement by a factor of 2-3 times
Nearly elimination of pollutant emissions
Production of water for potential on-board use

## Slide 11: REPLACE STANDARD APU BY FUEL CELL Cons
Higher weight (compensated by water generation)
Higher price (probably will become less than APU’s in the future)
Jet fuel sulphur content is challenging
Slower start

## Slide 12: FUEL CELL ARCHITECTURE
Fuel Cell Stacks
DC
AC
Integrated Fuel Processor
Exhaust
Cabin Air
System
Controller
Comp.
Battery
Turb.
Jet Fuel
Water
Separator
Water

## Slide 13: FUEL CELL TIMING
Automotive manufacturers doing active research
Boeing: a light aircraft demonstrator powered by fuel cells (2003-2005)
NASA/Boeing program: fuel cell APU demonstrator (2006-2008)
Power density may increase in next 10-15 years to enable APU production

## Slide 14
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Thank you !