## Slide 1
Groundside Operational Opportunities
Zurich Airport
Emanuel Fleuti, Unique (Zurich Airport Ltd), CH-8058 Zurich
P: +41-43-816 21 81, F: +41-43-816 47 60, E: emanuel.fleuti@uniqueairport.com
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 2: Emissions at Zurich Airport
Air Traffic
Landside Traffic
Infrastructure
Handling
Emissions in the LTO-Cycle: Approach, Taxi, Take-off, Climbout
Engine start-up, APU, GPU, GSE, airside traffic, maintenance
Heating plant, building maintenance, con-struction
Landside road (rail) access (airport induced, 3 km range)
Emissions 2001
NOx VOC
80% 36%
9% 38%
8% 19%
3% 7%
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 3: Problem at Airports
Pollution Limits:
EU-Directives
National Limits
Constraints
Airport induced Emissions
+
Emissions of other Sources
=
Overall Pollution
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 4: Mitigation Planning
Problem Assessment
Defining the Aim
Evaluating and choosing
the measures
Controlling
It is important to find a solution to an existing problem, not a problem to an existing solution!
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 5: Mix of Measures
Technical Measures:
Filters, CC
Substitutes
Operational Measures:
Hours of operation
Maintenance, Handling Instructions
Economic Measures:
Incentives
Charges
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 6: Handling Measures
Handling
Installation and Use of Fixed Ground Power at all Terminal Stands:
- 12,170 t fuel (in 2001)
75 t NOx (= 60%)
(118,000 a/c cycles)
Potential of CNG vs Diesel / Gasoline:
40 t NOx/a (-40%)
Potential of Eco-Drive Courses:
10 t NOx/a (-10%)
implemented
planned
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 7: Infrastructure Measures
Infrastructure
Installation of CNG and LowNOx in Heating Plant :
- 30 t NOx (= 55%)
New processes in a/c maintenance:
- 150 t VOC (= 60%)
implemented
implemented
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 8: Landside Traffic Measures
Landside Traffic
Extended Passenger Services:
Fly and Rail to 100 stations
Train Ticket in Tour Package
Check-in at 36 Train Stations
implemented
Large Public Transport System:
International / National Trains
Local Trains (270 daily dept.)
Local Bus Lines (>500 daily dept)
= Modal Split of 39% overall
implemented
Airport Groundside Panel
Madrid 21-22 May 2002

## Slide 9: Summary
Systematic Approach reveals Key Issues
Defining Aims and Setting Targets is the Pusher
Planning of Measures is Teamwork
Implementation of Measures needs to be followed
Controlling is mandatory
It is important to find a solution to an existing problem, not a problem to an existing solution!
Airport Groundside Panel
Madrid 21-22 May 2002