## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Ground Support Equipment Emission Reduction Options
Randy Harrison
Director - Environmental Services
Delta Air Lines, Inc.

## Slide 2: Presentation
Overall strategy
Applicability of technology to equipment types and operation
Other initiatives
Conclusion

## Slide 3: Emission Reductions
No single solution
  Infrastructure requirements
  Operational requirements
  Equipment availability
  Technology availability
Cost considerations

## Slide 4: Electric GSE
Applicability
  Belt loaders
  Bag tractors
  Aircraft tractors *
  Forklifts
  Container loaders
  Cargo tractors
  *Limited Basis
Benefits/Challenges
  Zero emissions
  Lower maintenance costs
  Increased equipment reliability
  High infrastructure cost
  Additional ramp space
  Recharging

## Slide 9: Compressed Natural Gas
Applicability
  Bag tugs
  Belt loaders
  OEM type equipment (Ford, GM Etc)
  Forklifts
Benefits/Challenges
  Lower emissions (compared to gasoline - higher for HC and CO compared to diesel)
  Infrastructure (limited availability, high cost for fill stations)

## Slide 10: Liquid Petroleum Gas
Applicability
  Bag tractors *
  Belt loaders *
  OEM type equipment (Ford, GM, Etc.)
  Forklifts
  * Limited use
Benefits/Challenges
  Lower emissions (compared to gasoline - higher for HC and CO compared to diesel)
  Readily available
  Safety concerns (employee strains)
  Tank location
  Cost

## Slide 11: Gasoline/Diesel Retrofit with 2 or 3 Way Catalytic Converters
Applicability
  Diesel and closed-loop gasoline engines where kits are available
Benefits/Challenges
  Lower emissions
  Reduced fuel cost
  Open loop systems
  Engine run times
  Installation location and space on GSE
  Many different engines (many sizes and Mfg)

## Slide 12: Diesel Retrofit with Particulate Traps
Applicability
  All current and older model diesels where kits are available
Benefits/Challenges
  >85% particulate reduction
  Installation location
  Cost
  Maintenance
  Life span
  Not certified for all equipment
  Run time

## Slide 13: Fuel Cells Emerging Technology with Significant Potential
Possible Applicability
  Bag tugs
  Belt loaders
  Jet tractors
  Cargo tractors
  Container loaders
  Chargers
  OEM type equipment
Benefits/Challenges
  Zero emissions
  No charge time, fueling could be similar to conventional fueling
  Less invasive infrastructure
  Availability
  Technology, cost and timeline

## Slide 14: Solar Power Developing Technology
Applicability
  Fuel service carts
  Other GSE
Benefits/Challenges
  Zero emissions
  No infrastructure required
  Limited applicability
  Presently only used to assist other power sources

## Slide 16: Other Emission Reduction Initiatives
Tow-barless tractors
Lavatory carts
Fuel carts

## Slide 20: Conclusion
No one solution fits all needs
Technology is still developing
Aviation industry is utilizing what is available
Cost

## Slide 21
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Thank you !