## Slide 1
FUEL CONSERVATION
WG4 Workshop
Aviation Operational Measures
for Fuel & Emissions Reductions
Alain JOSELZON
AIRBUS

## Slide 2: FUEL CONSERVATION
BACKGROUND
A permanent and omnipresent objective for Airbus
Dedicated efforts made by Airbus
  in all fields of activity
  in every phase of product life
  in all parts of Aircraft
  in every phase of Aircraft operation
Experience accumulated jointly by Airbus, Suppliers and Operators has permitted to reach maturity in actually optimising fuel conservation
Incorporation of improvements in technologies, methodologies and modelling techniques, instrumentation, etc., as they become available
Recommendations recalled in these slides are for general info only and not meant to replace any existing specific document

## Slide 3: FUEL CONSERVATION
Dedicated efforts in all activity fields
Design, Production & Quality of A/C (aerodynamic smoothness, sealing, systems, equipment, engines, nacelles, weight, quality control processes) optimised to minimise fuel consumption & maximise perfo. retention
  Close cooperation with Eng./Nac. Manufact. & Suppliers
Training & Documentation contain targeted recommendations
  Specific brochures on fuel economy, cost index, etc.
In service support
  ad hoc support
  periodic or ad hoc visits of crews and specialists, audits
  operational conferences

## Slide 4: FUEL CONSERVATION
Dedicated efforts in every phase of product life (1)
Design/Production/Quality processes of Aircraft, Powerplant, Components (as indicated previously)
Development and Flight tests focusing on perfo. deterioration diagnosis and correction, e.g.:
  dedicated testing of Aircraft and nacelle sealing, etc.
  careful monitoring/analysis of performance gap
  corrective modifications defined and launched for Aircraft certification standard or earliest possible incorporation
  sophisticated modelling of a/c & engine performance, (esp. thrust vs thrust parameter relationship), adjusted and extrapolated to the full flight envelope (ambient conditions, speed, weight, etc.), leading to a consolidated perfo. baseline

## Slide 5: FUEL CONSERVATION
Dedicated efforts in every phase of
product life (2)
Aircraft and Engine Production acceptance processes
  Careful monitoring and data analysis (specific cases, trends & statistical analyses)
  Initial calibration and subsequent adjustments of In Flight Performance (IFP) computation programme as required (e.g. following incorporation of performance improved engines)
In service Support (including documentation & training)
  Supply of adequate A/C systems and software tools for A/C & Engine performance monitoring; data analysis; further actions as required
  Monitoring of A/C-Engines operational, maintenance and overhaul procedures efficiency (engine wash, coke cleaning, A/C cleaning, sealing restoration, rigging adjustments, etc.)

## Slide 6: FUEL CONSERVATION
Dedicated efforts in all parts of Aircraft (1)
Efforts on initial design by Aircraft & Engine Manufacturers to be pursued by the Operators with the support from the A/C & Engine Manufacturers
Aircraft (including Nacelles) Aerodynamic smoothness (steps & gaps) , Seals, Doors (rigging/sealing)
Aircraft Systems
  Control surface rigging adjustments
  FMS optimisation (optimum routes), best matching with ATC and Airport infrastructure systems (overall Air Traffic benefit)
Engines and Nacelles
  Clearance optimisation, erosion & FOD resistance, syst. reliability
  FADEC optimisation (engine control, system failure detection, engine performance monitoring)

## Slide 7: FUEL CONSERVATION
Dedicated efforts in all parts of Aircraft (2)
Weight minimisation and CoG optimisation
  Propulsion system weight, A/C ZFW minimised by design
  Typical recommendations to Operators:
    A/C loading: further aft CoG position increases specific range (but CoG must stay within allowable range)
    Avoid excess weight; eliminate unnecessary weight
    Minimise embarked/contingency fuel through accurate flight planning (individual route/A/C combination fuel consumption monitoring)
    Voluntary extra fuel transportation to be optimised (determine breakeven profitability point taking into account fuel price, additional fuel consumed, payload loss, turnaround time)

## Slide 8: FUEL CONSERVATION
Dedicated efforts in every phase of operation (1)
Ground running-Taxiing : typical recommendations
  limit use of APU whenever possible (saves APU fuel & life)
  Plan engine start-up in conjunction with ATC
  Taxiing with one (2) engine (s) out saves fuel but some drawbacks to be considered: operators must base their policy on airport config. (taxiways, runways, ramps, etc.)
Take-Off
  Derated and flexible Take-off benefit from reduced engine wear/efficiency retention outweigh the small increase in fuel consumption vs full thrust T/Off

## Slide 9: FUEL CONSERVATION
Dedicated efforts in every phase of operation (2)
Climb
  Optimum climb law is depending on the Aircraft, on selected modes and cost indices
  In general, it is not profitable to climb at high-speed laws except for time imperatives, neither to climb at very slow climb laws
  The 1st optimum FL is above the X-over altitude (transition from constant IAS to constant Mn). It depends on the A/C & on weight
  Optimum altitude (for time and costs) increases as weight reduces. Due to ATC constraints, step climbs performed to stay close to the optimum; FCOM and FMS refer
  Delaying climb to the next step should be avoided

## Slide 10: FUEL CONSERVATION
Dedicated efforts in every phase of operation (3)
Cruise
  Optimum cruise altitude and airspeed depend on Aircraft, weight, wind, and cost index (CI)
  Relationships link together for a given A/C: CI, FL, Mn, weight, time, fuel consumption, distance, wind
  Lowest fuel consumption is obtained at the lowest cost index (however the time penalty has to be watched)
  FMS optimises the flight plan (including the flight profile) accordingly, and the FCOM contains additional material to help the pilot in the optimisation process

## Slide 11: FUEL CONSERVATION
Dedicated efforts in every phase of operation (4)
Descent
  Fuel consumption increases significantly with airspeed and also in case of a premature descent
    Descent performance depends on A/C, weight and cost index
    The lower the cost index, the lower the speed, the less steep the descent path, the longer the descent distance, the greater the descent time, the earlier the top of descent (TOD) point, the lower the fuel consumption
    The FMS computes the TOD as a function of cost index

## Slide 12: FUEL CONSERVATION
Dedicated efforts in every phase of operation (5)
Holding
  Green dot speed is the one or 2 engine out operating speed in clean configuration; being approximately the best lift to drag ratio speed, it provides in general the lowest fuel consumption
    However, when weight increases and green dot speed exceeds the max recommended speed, it is advised to hold in config. 1 at S-speed (keeping clean conf. coupled with a speed reduction would save fuel but decrease the safety margin; it could become hazardous in turbulent conditions)
    There is an optimum holding altitude, but holding altitudes are often imposed by ATC
    Linear holding at cruise level and at green dot speed and in as clean as possible configuration should be performed whenever possible (early recognition of holding delay helps to plan so as to minimise penalty )

## Slide 13: FUEL CONSERVATION
Dedicated efforts in every phase of operation (6)
Approach
  Premature extensions (landing gear, slats, flaps) should be avoided to avoid fuel consumption penalty
  A decelerated approach saves fuel in comparison to a stabilised one, conditions and safety permitting

## Slide 14: FUEL CONSERVATION
Additional present opportunities
Progressive incorporation of new technologies, methodologies, modelling and test tools (see 1st slide)
Experience accumulated and achieved maturity (see 1st slide)
Aircraft family concept, extensive use of concurrent engineering processes, of virtual mock-ups, more sophisticated simulation testing means (software, laboratory, simulators), increased system reliability, reduce the ground and flight test time, the number of ferry flights, some of the continued airworthiness flight tests
FMS improvements and bad weather detection improvements
Maximised load factors, with optimised A/C /route combinations
RVSM (Reduced vertical separation minima) in Europe since Jan. 2002 allows to fly nearer the optimum altitude for fuel burn

## Slide 15: FUEL CONSERVATION
Projection
Current/projected trends
in overall fuel efficiency
at operators are encouraging

## Slide 16: FUEL CONSERVATION
Additional future opportunities
Continued progress expected in present opportunities
Electrical GSE
Ground transportation enhancements
Airport infrastructure enhancements
CNS/ATM and future associated A/C system enhancements
Weather forecast improvements
...

## Slide 17: FUEL CONSERVATION
Other considerations
In the design field, Airbus is involved in considerable research activities, currently in progress, relative to fuel consumption and emissions reduction. They are likely to have operational aspects associated with it.
Trade-offs
  emissions-emissions (e.g. NOx vs CO2)
  emissions-noise (e.g. Noise vs CO2 , Noise vs NOx)
Collaborative efforts (manufacturers, operators, airports, authorities, financiers, passengers) required to efficiently match supply air transport services to demand for passenger & cargo air transport