## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Non-Revenue Flying
Kevin M Morris
Manager Environment, British Airways

## Slide 2: Non-Revenue Flying
What is Non-Revenue Flying?
Post Maintenance
  Engine testing
Diversion/Positioning flights
Test Flights
Epilogue:
  Tales of the unexpected

## Slide 3: Non-Revenue Flying
Any flight that doesn’t make money!
Includes flights for:
  Training, Ferry, verification, positioning, testing, development, + Ground Engine running(?)

## Slide 4: Non-Revenue Flying
Some Non-Revenue flying is necessary, but it is expensive, uses fuel and creates unwanted emissions
Can sometimes be reduced or “managed” or coupled with commercial service

## Slide 5: Post Maintenance

## Slide 6: Verification of Maintenance
Result of some maintenance actions can not be accurately verified on the ground e.g.
  Engine re-light envelope
  Manual reversion
  Some emergency systems, etc.
Some flying may be necessary

## Slide 7: B 737 Manual Reversion
Check is required if control rods, system linkages are disturbed
  Check at FL350, switch off both control systems, manual trim out
  Recording of results allowed a check at 10 000 ft instead
  Resulting in approx. 1 hour reduction in flight time, and savings in fuel and emissions

## Slide 8: Engine Ground Running

## Slide 9: Engine Ground Running
Post maintenance action, e.g.
  Check starts
  Thrust reverser verification
  Leak tests
Reduce time of running
Reduce power setting
  To the minimum required

## Slide 10: Concorde Ground Runs
Following temporary suspension of C of A, Concorde engines run on a daily basis.
  Runs of 1 hour duration
    10 min at full reheat power
    Rest at high power
Problems with noise, fuel use

## Slide 11: Concorde Ground Runs
Reappraise requirements
Long term, not short term
  Reheat not necessary
  Push to high power, then reduce to a lower power
  Running time reduced
Approx. 80% reduction in fuel

## Slide 12: Diversions and Positioning

## Slide 13: Positioning Flights
Diversions are BAD NEWS!
Choice of alternate is important:
  Too close - both can have similar weather
  Too far - high cost in time and fuel for diversion and recovery
Choose wisely!

## Slide 14: Positioning Flights
Split operations, sometimes require positioning of aircraft
Positioning also required if Maintenance is carried out away from main base
Sometimes a commercial load can be carried (e.g. B777 delivery flight with cherries)

## Slide 15: Development, TI and Test

## Slide 16: Test Flying
Some test flying is necessary
  Required by Manufacturer (MM)
  Required by the Regulator
  Required by the airline
Sometimes possible to combine test flights
  e.g. Concorde noise with AWFT

## Slide 17: Test Flying - costs
Typical AWFT flight fuels:
    ATP - 2 000 kg
    B737/A320 - 6 000 kg
    B757 - 12 000 kg
    B767 - 12 000 kg
    B777 - 13 000 kg
    B747 - 30 000 kg
    Concorde - 78 000 kg
Other type probably less!

## Slide 18: Test Flights - Minimisation
B.I.T.E.
Do everything that’s possible on the ground
Record everything, and review Test during revenue flying (if possible!)
Construct logical test schedules

## Slide 19: B 737 Alternate Flap
Problem found with Boeing 737 alternate flap, during AWFT
Problem resolved, but UK CAA required verification flights
Agreed for ‘Management’ Pilots to use alternate system to lower flaps on commercial flights into LHR

## Slide 20: Test Flying
It is not always possible to recreate flight and pressurisation loads on the ground. For this reason,
Some defects can only be demonstrated....

## Slide 21: ....in the air!

## Slide 22
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Thank you !