## Slide 1
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
HOW TO SAVE FUEL BY LOSING TIME?
Jean-Pierre NICOLAON
EUROCONTROL - EEC

## Slide 2
IN ABSORBING ARRIVAL DELAYS LINEARY DURING DESCENT INSTEAD OF HOLDING STACK TECHNIQUE

## Slide 3: ARRIVAL TRAFFIC IS GENERALLY ORGANIZED THROUGH SUCCESSIVE LAYERS:
STEP 1
ARRIVAL SLOTS (AIRLINES SCHEDULES) ARE DETERMINED ACCORDING TO RUNWAY CAPACITY (TYPICAL VALUE 44 a/c PER HOUR FOR SPECIALIZED RUNWAY)

## Slide 4
STEP 2
DEPARTURE SLOTS (including overbooking) ARE ALLOCATED ACCORDINGLY BY ATFM (pretactical)

## Slide 5
STEP 3
ATC CONTROLLERS REFINE TRAFFIC SEQUENCES AS APPROPRPIATE (tactical)

## Slide 6
NOTE:
OVERBOOKING IS REQUIRED TO COMPENSATE UNPREDICTABLE, UNEXPECTED AND INACCURATE ELEMENTS such as:
  AIRLINES DELAYS
  FLIGHT CANCELLATIONS
  BAD WEATHER

## Slide 7: HOWEVER OVERBOOKING AND INACCURACY CAN INDUCE HOLDING BEFORE LANDING THOSE DELAYS COULD BE ABSORBED EITHER :
IN HOLDING STACK (e.g. London)
LINEARY (e.g. Paris CDG)

## Slide 8: ARRIVING TRAFFIC TO PARIS CDG + LE BOURGET

## Slide 9: ARRIVING TRAFFIC TO PARIS CDG

## Slide 10: ARRIVING TRAFFIC TO PARIS ORLY

## Slide 11
HOLDING STACK TECHNIQUE IS BEING USED AS AN AIRCRAFT TANK CLOSE TO RUNWAY FOR PREVENTING GAPS TO HAPPEN INTO LANDING SEQUENCES.
IT CAN BE USED EASILY WITHOUT ANY COMPUTER ASSISTANCE

## Slide 12
HOLDING STACK INDUCES SIGNIFICANT EXTRA FUEL BURN
IT ENABLES LONG DELAYS ABSORPTION CAPABILITY

## Slide 13
LINEAR HOLDING CAN ONLY ABSORB ‘REASONABLE’ DELAYS (5/7 minutes)
IT HAS TO BE COMPLEMENTED BY HOLDING STACK FOR LONGER DELAYS
IT IS VERY SUITABLE TO HUB SEQUENCES

## Slide 14
IT IS SAVING FUEL EVEN COMPARED TO NOMINAL TRAJECTORY
IT REQUIRES COMPUTER ASSISTANCE FOR EFFICIENT SEQUENCING AND SPACING

## Slide 15: SAVED FUEL BURN/ ABSORBED DELAYS
PROGRESSIVE SPEED REDUCTION PROFILE
SEGMENTED SPEED PROFILE
EXAMPLE OF AIRBUS A310 DESCENDING AT MINIMUM DRAG SPEED ACCORDING TO :

## Slide 16
TRANSITION ALTITUDE
STANDARD DESCENT PROFILE
M.;0,80 - 300 KT - 250 KT + HOLDING AT FL50
DESCENT PROFILE AT PROGRESSIVE REDUCED SPEED
DESCENT PROFILE AT SEGMENTED SPEEDS
HOLDING
PROFILE 

## Slide 17: TYPICAL SPEED SEGMENTS

## Slide 18: ABSORBABLE DELAYS DURING DESCENT ONLY

## Slide 19: FUEL BENEFITS COMPARISON/STACK VERSUS LINEAR

## Slide 20: EXAMPLE OF COMPUTER ASSISTANCE
INFORMATION GIVEN BY MAESTRO - ARRIVAL MANAGER
Current Time
Runway 25 (Le Bourget)
Runway 26 left
Time Scale
Runway 27 (North)

## Slide 21: SEQUENCE DETAILS
IAF (origin)
(S = Susin, M = Merue, L = Lorta)
Callsign
Aircraft Type
Time at IAF
Current Delay

## Slide 22: WHAT MAGNITUDE OF BENEFITS COULD BE PROVIDED BY LINEAR HOLDING ?
THIS IS DEPENDING UPON AIRPORT AND DEMAND COMBINATION
HOWEVER SOME TYPICAL VALUES ARE ALREADY AVAILABLE

## Slide 23
IN NORMAL CONDITIONS
LINEAR HOLDING ALLOWS FUEL SAVING OF
2x60’x85kg = 10,200 kg PER DAY AT PARIS ORLY
AND
3x110’x85kg=28,050kg PER DAY AT PARIS CDG
IN HEAVY SITUATION
AT PARIS ORLY (100’ min Delay)
60’ OF LINEAR HOLDING ARE SAVING
60’X85kg = 5,100kg
WHILE 40’ OF HOLDING STACK ARE INCREASING FUEL BURN BY 2,400kg
AT PARIS CDG (225’ min Delay)
60’x85kg=5,100kg ARE SAVED WHILE 165’x60kg =9,900kg ARE LOST

## Slide 24: CONCLUSIONS
LINEAR HOLDING REDUCES FUEL BURN
IT WORKS IN REAL LIFE
ADDITIONAL BENEFITS CAN BE OBTAINED BY LINEAR HOLDING:

## Slide 25
  REDUCTION OF FLIGHT TIME AT LOW ALTITUDE LOWERING NOISE
  REDUCTION OF FLIGHT TIME IN THE HOLDING STACK REDUCING RISK
LINEAR HOLDINGTHE WAY AHEAD

## Slide 26
AVIATION OPERATIONAL MEASURES FOR FUEL AND EMISSIONS REDUCTION WORKSHOP
Thank you !